## Slide 1: The Picopix Project
Xavier Llopart
On behalf of the LA-PicoPix design team

## Slide 2: Timepix4
2013
TIMEPIX3
2016
VELOPIX
2019
TIMEPIX4
Technology |  |  | 65nm – 10 metal
Pixel Size |  |  | 55 x 55 µm
Pixel arrangement |  |  | 4-side buttable 512 x 448
Sensitive area |  |  | 6.94 cm2
Readout Modes | Data driven (Tracking) | Mode | TOT and TOA
 |  | Event Packet | 64-bit
 |  | Max rate | 3.58x106 hits/mm2/s
 |  | Max Pix rate | 10.8 KHz/pixel
 | Frame based (Imaging) | Mode | CRW: PC (8 or 16-bit)
 |  | Frame | Not-zero-suppressed
 |  | Max count rate | ~5 x 109 hits/mm2/s
TOT energy resolution |  |  | < 1Kev
Time resolution |  |  | 195ps bin  ~60psrms
Readout bandwidth |  |  | 16x @10.24 Gbps
Minimum threshold |  |  | <500 e-
Radiation tolerance |  |  | NO
TIMEPIX4
2007
TIMEPIX
Notes: Questa e’ la funzionalita che vogliamo portare in velopix2 (verde)
Il problema e’ che non e’ radhard, TID e SEU
Alta occupancy non supportata

## Slide 3: The Picopix design
Picopix is a 256 x 256 pixels particle tracking detector readout ASIC with < 30 psrms timing resolution, on-chip clustering and data reduction, and readout up to 3.9 ∙109 clusters ∙ s –1
Target of the design:
Demonstrate the feasibility for a possible upgrade of the LHCb VELO Detector

## Slide 4: The Picopix design
Picopix is a 256 x 256 pixels particle tracking detector readout ASIC with < 30 psrms timing resolution, on-chip clustering and data reduction, and readout up to 3.9 ∙109 clusters ∙ s –1
Target of the design:
Demonstrate the feasibility for a possible upgrade of the LHCb VELO Detector
Other High Energy Physics potential applications:
Generic platform for hybrid pixel sensor for fast timing (LGADs, 3D, …)
Beam gas monitoring at the LHC accelerator
Rad-hard radiation monitoring systems
Other HEP applications (if including additional operating modes)
A possible starting point for a designs that can benefit of the developed methodology and critical blocks
4D STEM (Scanning Transmission Electron Microscopy)
Mass spectrometry
X-ray photon correlation spectroscopy
Medical applications (SPECT/PET)
Other potential applications:
Generic platform for sensor studies (Si, CdTe, GaAs,…) or SPADS?
X-ray and neutron imaging
Time-resolved photon processing science:

## Slide 5: The Picopix design  LA-Picopix
Why Large Area?
Precise timing (<50ps) in a large array introduces several additional challenges that need to be faced at the early stage  needs silicon prove on a full-size chip
⬥ Clock jitter ⬥ power distribution ⬥ IR-drop induced jitter ⬥ Data readout ⬥ Time corrections ⬥ etc.…
Wafers available  simplifies bumping and sensor development
A large-area prototype submission requires an engineering run >1.2 M$ but:
  Several potential users have shown interest:
    ⬥ Medipix collaboration ⬥ SY-BI Beam instrumentation ⬥ LHCb ⬥ others?
  An approach similar to the Medipix and RD53 Collaborations  An ASIC for multiple users

## Slide 6: The Picopix design
The first prototype targets directly the final architecture
Pixel matrix design :
Timing performances
Analog front-end
TDC resolution
Clustering functions
Data reduction
Pixel readout
Architecture and IPs :
Data readout
Control and monitoring
Clock distribution
High-speed links
On-chip biasing
Technology and power:
Power density (one of the main challenges)
SEE robustness
TID robust design
TSMC 28nm HPC+
Verification environment:
Full UVM verification environment
Formal verification
SEE verification
  facing at the early stages all the complexity of a full-scale design

## Slide 7: The Picopix ASIC organization
64 columns of 16 regions
Region
Region
Region
Region
Region
Region
•••
•••
•••
•••
•••
Region
Region
Region
Region
Region
Region
•••
•••
EoC
EoC
EoC
EoC
High speed links
Event sorter and builder
Packet processor
Control
Peri logic
PIXEL
PIXEL
PIXEL
PIXEL
TDC
ARBITRATION
SHARED LOGIC
SUPER-PIXEL
•••
•••
Data manager
Slow-control
Clock distribution logic
digital PLL
PIXEL REGION
Hierarchical units
Flat implementation
64 columns of 16 regions
Region
Region
Region
Region
Region
Region
•••
•••
•••
•••
•••
Region
Region
Region
Region
Region
Region
•••
•••
EoC
EoC
EoC
EoC
High speed links
Event sorter and builder
Packet processor
Control
Peri logic
PIXEL
PIXEL
PIXEL
PIXEL
TDC
ARBITRATION
SHARED LOGIC
SUPER-PIXEL
•••
•••
Data manager
Slow-control
Clock distribution logic
digital PLL
PIXEL REGION

## Slide 8: Analog FE in PicoPix by Viros Sriskaran
Analog Islands (2x2):
  ~30 µW/pixel and Qin-thr>~4ke-  <25 psRMS
  Optimized for negative input charges (e-)
  7-bit threshold DAC
  Novel on-pixel biasing power drop compensation
  2x2 pixels analog island: 52 x 48µm² :
    ~25% area in a 45 µm pitch
    ~17% area in a 55 µm pitch

## Slide 9: The Picopix TDC
Time-over-Threshold (ToT)
  Proportional to energy measure
  Used internally for ToA time-walk correction
  Can be transmitted within the packet in Tracking-ToT mode (and in raw-data mode)
Time of arrival (TOA)
  Coarse TOA  BxID
  Fine TOA  with 3.125ns resolution
  Ultra-Fine TOA  ~40ps bins (10 bits)
    Auto-calibrated TDC (each measurement)
    P, V, T, Rad and On-chip variations on a large-scale chip are critical for this resolution
Reference clock distribution is very critical!
  Pixel to pixel skew (static)
    TOA is corrected without requiring a calibration per channel outside of the chip!
  Clock jitter (dynamic)
    Simulation methodology for establishing IR-drop induced clock jitter [Gianmario Bergamin]
Design status: RTL and Physical design completed
  careful physical design, manual placement and routing to match timing
  post-layout extracted simulation

## Slide 10: Clock distribution
0
1
S0
0
1
S0
0
1
S0
0
1
S0
Full-chip DLL clock distribution
Unique clock source and full PVT controlled
Skewing clock allows quasi-static power consumption and strong IR-drop reduction
Allows control of clock phase with 3-5ps skew
Design status: RTL Complete – blocks implemented

## Slide 11: On pixel event processing ➞ Data reduction
 | 1 | 1 | 0 |  | 
 | 1 |  | 0 |  | 
 | 0 | 0 | 0 |  | 
Data filtered already at the level of the pixel-array
  Bandwidth reduction towards the periphery
  Significant power and IR-drop reduction
Further reduction and compression in the periphery
M
Arbitration logic
  Transmit only Master pixel packet (can be disabled)
  ToA on master provide the highest resolution
  Design status: RTL complete
Hit-Map:
  Hit-Map of all the pixels around the master
  Or Hit-Map of the super-pixels around the master (when transmitting all ToT)
  Design status: RTL complete
Advanced on-pixel data filtering:
  Digital filtering according ToT
  Possible to add filtering according ToA, Hit-Map shape, and others features extraction.
  Design status: To be done
Arbitration Logic

## Slide 12: On pixel event processing ➞ Data reduction
Data filtered already at the level of the pixel-array
  Bandwidth reduction towards the periphery
  Significant power and IR-drop reduction
Further reduction and compression in the periphery
Filtering disable
Filtering large clusters
Filtering small clusters
  Design Status: RTL complete
Clustering and filtering

## Slide 13: PixESL – Picopix studies
CERN EP R&D WP5

## Slide 14: Pixel-matrix data-path
  Pixel array readout by column
  Each super-pixel transmits to the next
  Columns of Super-pixels are organised in regions allowing reducing latency.
  Arbitration mechanisms for handling data transfer priorities
  Design Status: RTL almost complete
ARBITRATION
TDC PACKET
ARBITRATION
TDC PACKET
ARBITRATION
TDC PACKET
ARBITRATION
TDC PACKET
● ● ●
ARBITRATION
TDC PACKET
ARBITRATION
TDC PACKET
ARBITRATION
TDC PACKET
ARBITRATION
TDC PACKET
● ● ●
PIXEL REGION:
8 x 2 SUPER-PIXELS
PIXEL COLUMN:
ARBITRATION
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
● ● ●
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
● ● ●
ARBITRATION
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
● ● ●
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
SUPER-PIXEL
● ● ●
● ● ●
16
REGIONS
REGION
REGION

## Slide 15: Periphery data-path
81b
Full Time calibration:
  DLL clock skew calibration (Row and Column)
  Unique time-walk correction (programable)
  TOA event calibration (24.4ps bin)
  10b or 6b fine-time output
  Built-in TOA extender up to 32-bits(@40MHz)
  Digital T0Sync shift adjustment (24.4ps bin and 100ns range)
Event Filtering:
  Configurable TOT range
  Configurable TOA range
  Hitmap shape (single pixels, L shape, + shape,…)
On-chip XY decoding
Single packet formatting:
  To Sorter: 24-bit, 36-bit, 72-bit
  To FIFO: 72b_PC_iTOT, 72b_raw and Jumbo
Design Status: RTL ongoing
PACKET PROCESSOR

## Slide 16: Periphery data-path
Creates output packets Header + N*Packets
Design Status: RTL ongoing
Sort packets per BxID
  Cumulates packets over time and groups them in bins based on event tag
  Sorted data readout
Design Status: RTL ongoing
81b
EVENT SORTER
EVENT BUILDER

## Slide 17: Periphery data-path
Designed by the CERN EP R&D WP6 team
Design Status: First Silicon Prototype Available (DART28)
WP6 design roadmap is aligned with PicoPix project.
FEC – correct up to 30 consecutive bits
Effective data rate:
  With silicon photonics: 4 x 23.04 Gb/s = 92.16 Gb/s
  With electrical links: 4 x 11.52 Gb/s = 46.08
81b
HIGH-SPEED TRANSMITTER

## Slide 18: Picopix operating modes
CLUSTER FILTERING | 
Filter large clusters | Clusters large than 3x3 around master
Filter small clusters | Clusters smaller than 3x3
No filtering | Transmits all clusters
TRACKING MODE | 
Tracking mode | The packet includes: ▪ MASTER ADDRESS ▪ ULTRA-FINE TOA ▪ HIT-MAP
Tracking + ToT | The packet includes: ▪ MASTER ADDRESS ▪ ULTRA-FINE TOA ▪ HIT-MAP ▪ TOT OF ALL THE PIXELS
EVENT PACKET | Tracking mode |  | Tracking mode + ToT | 
 | Packet size | Max N of packets | Packet size | Max N of packets
Raw data format | 72 bits out-of-order | 1.28 GEVENTS s−1 (32 Bx−1) | 144 bits out-of-order | 640 MEVENTS s−1 (16 Bx−1)
Standard format | 36 bits SORTED | 2.56 GEVENTS s−1 (64 Bx−1) | 72 bits SORTED | 1.28 GEVENTS s−1 (32 Bx−1)
Reduced- format | 24 bits SORTED | 3.84 GEVENTS s−1 (96 Bx−1) |  | 
MASTER EXTRACTION | Tracking mode | Tracking mode + ToT
Send cluster master | Full 3X3 Hit-Map around master pixel | Full 3x3 Hit-Map around the super-pixel simplifying the off-chip re-clustering
Send all super-pixels | Local 2x2 Hit-Map within super-pixel | 
Main data-driven readout modes implemented:

## Slide 19: Picopix operating modes
FRAME-BASED MODE |  |  | 
 |  | Packet size | Max output rate
Particle counting | Integrate number of particle hits per pixel during the shutter-open period. Zero suppressed readout | 72 bits | 2.56 ∙ 109 Counters s−1 (64 counters / Bx)
Integral ToT | Integrate the Time-over-Threshold per pixel during the shutter-open period. Zero suppressed readout | 72 bits | 2.56 ∙ 109 pixels-TOT s−1 (64 pixels-TOT / Bx)
Main frame-based readout modes implemented:

## Slide 20: On-chip processor in Picopix
Take over low-computational task from the back-end (slow-control)
Automatize recurrent monitoring operations as bias monitoring, etc.
Calibration, threshold trimming, clock distribution calibration for precise data correction, etc.
Provide commands instead writing/reading registers
Possibility to reprogram it in any moment, making it very flexible for new applications
Toolkit for generating highly-customizable systems that can be integrated in radiation-tolerant ASICs
automates SoC assembly and verification
provides a radiation-tolerant verified IPs library
supports fault-tolerant extensions for redundancy and error correction.
hardware, verification and software toolchain support
SOCRATES - SoC RAdiation Tolerant Eco-System
CERN EP R&D WP5

## Slide 21: Summary of specifications
Technology |  | 28nm – 10 metal
Pixel Size |  | 49.5µm (tbc)
Pixel arrangement |  | 3-side buttable 256 x 256
Sensitive area |  | 1.606 cm2 (tbc)
Data driven (Tracking) | Mode | TOT and TOA on Master only
 | Event Packet | RAW: 64-bit TIME10bit: 28-bit TIME6bit: 24-bit
 | Max rate @ pixel matrix | 5.12x109 events/chip
 | Max average pixel rate | <78 KHz
 | Max single pixel rate | <20 MHz/pixel
Pixel clustering mode (can be turned off) | On-pixel clustering | Master + surrounding 8-bit hitmap for 3x3 events
 | On-pixel large cluster filter | Asynchronous filtering for events larger 3x3
 | On-pixel sub-pixel resolution | 256x256  512x512
 | On-pixel TDC | Shared for 4 pixels. TOA + TOT of Master only DCO autocalibration on-chip ~40ps bin(~11.5psrms)
 | Periphery cluster sorting and framing | YES
 | SuperPixel Counter | 4x12-bit counters  TOT on all pixels or photon counting
 | Periphery absolute on-chip time calibration | YES
Frame-based |  | YES zero-suppressed. 12-bit pixel counters (PC or iTOT)
Readout bandwidth |  | Up to 4x @12.8 or 25.6 Gbps (tbd)
Radiation tolerance |  | YES. TMR design
Chart: Simulated TOA Resolution

## Slide 22: Summary
LA-Picopix is a large-area Particle Tracking detector ASIC with < 30 psRMS timing resolution, on-chip clustering support, data-driven readout up to 3.9 ∙109 cluster ∙ s –1
LA-Picopix will allow demonstrating precise timing and functionalities on a large pixel array
  Target submission by end of 2025
Multiple operating modes and functionalities allow retargeting the chip for different applications, and some potential users have shown interest. Example of applications are:
▪ LHCb velo (main specifications) ▪ beam gas monitoring ▪ radiation monitoring ▪ X-Ray imaging ▪ 4D STEM ▪ X-ray photon correlation spectroscopy ▪ Mass spectrometry ▪ Medical applications (SPECT/PET) ▪ etc..
Progress in the CERN EP R&D projects suggests feasibility of integrating the outcome of multiple R&Ds into one proof-of-principle ASIC, fostering collaboration and resources consolidation:
  ▪ EP-Wp6 – High-speed links ▪ EP-Wp5.1 – Technology evaluation ▪ Wp5.2 – IP development
  ▪ EP-Wp5.3 – Intelligence on detector ▪ EP-Wp5.5 – interconnect solutions ▪ Wp5.4 – on-chip power converters
Focus → designing a versatile pixel ASIC in 28nm technology, accessible to multiple users.

## Slide 23: BACKUP MATERIAL

## Slide 24: 72-bit Non-Sorted Data Packets
72-bit RAW tracking (Data-Driven):
BxiD (TOA): 17-bit
UFTOA-10b RAW: bin size 24.4ps covers 25ns
Master Address: 16-bit pixel address
Hitmap: 8-bit around master pixel
TOA and TOT Raw data
1-bit pileup indicator
72-bit PC or iTOT (Frame Based, zero-suppressed)
Master Address: 16-bit pixel address
PC_iTOT_P0: 12-bit
PC_iTOT_P1: 12-bit
PC_iTOT_P2: 12-bit
PC_iTOT_P3: 12-bit
72-bit fine time TOA tracking (Data-Driven):
BxiD (TOA): 28-bit
UFTOA-10b: bin size 24.4ps covers 25ns
Master Address: 16-bit pixel address
Hitmap: 8-bit around master pixel
Master TOT: 8-bit
1-bit pileup indicator

## Slide 25: Jumbo (2x72-bit) Non-Sorted Data Packets
Jumbo raw tracking (Data-Driven):
  72-bit RAW packet:
  BxiD (TOA): 17-bit
  UFTOA-10b RAW: bin size 24.4ps covers 25ns
  Master Address: 16-bit pixel address
  Hitmap: 8-bit around master pixel
  TOA and TOT Raw data
  1-bit pileup indicator
72-bit TOT:
Master Address: 16-bit pixel address
TOT_P0: 12-bit
TOT_P1: 12-bit
TOT_P2: 12-bit
TOT_P3: 12-bit
Jumbo fine time TOA and TOT tracking (Data-Driven):
72-bit fine time TOA:
BxiD (TOA): 32-bit
UFTOA-10b: bin size 24.4ps covers 25ns
Master Address: 16-bit pixel address
Hitmap: 8-bit around superpixel
72-bit TOT:
Master Address: 16-bit pixel address
TOT_P0: 12-bit
TOT_P1: 12-bit
TOT_P2: 12-bit
TOT_P3: 12-bit

## Slide 26: Sorted Data Packets by BxiD (TOA)
Header
BxiD (TOA): @40MHz
STATUS: Readout mode, link config,…
Event Counter: Num of packets will follow
Other: TBD
3x 24-bit data
UFTOA-6b: configurable bin size (24.4 to 396ps)
Master Address: 16-bit pixel address
2-bit info:
  Sub-pixel: 2-bits calculated from Hitmap
  Pileup and on-time TOT Valid
  2-bit TOT
2x 36-bit data
UFTOA-10b: bin size 24.4ps covers 25ns
Master Address: 16-bit pixel address
Hitmap: 8-bit around master pixel
2-bit info:
  Pileup and on-time TOT Valid
  2-bit TOT
1x 72-bit data
UFTOA-10b: bin size 24.4ps covers 25ns
Master Address: 16-bit pixel address
Hitmap: 8-bit around master pixel or super-pixel
TOT_P0, P1, P2 and P3 in super-pixel: 9-bit TOT @320MHz
Pile-up: 1-bit pileup indicator

## Slide 27: IO + DART pads distribution [preliminary]
DART Hybrid (optical)
PIC
~2.4 mm
DART Hybrid (elec)
VDDA_CORE | 31
VSSA_CORE | 30
VDD_CORE | 27
VSS_CORE | 29

## Slide 28: High Speed Transmitter
25.6 Gbps Line Driver (PRBS7)
12.8 Gbps Line Driver (PRBS7)
Designed within EP R&D WP6
Design Status: First Silicon Prototype Available (DART28 Chip)
  All included blocks are fully functional.
  Excellent PLL jitter performance demonstrated (random jitter <300 fs rms).
  TID X-ray test showed no significant eye quality degradation up to 2 Grad at nominal power supply.
  The SEE heavy ion test campaign validated the TDC-based SEE recovery mechanism, preventing PLL unlocks.
  Successful integration and data transmission with silicon photonics demonstrated.
  Data transmission performance degraded at 25.6 Gbps (data-dependent jitter) due to Power Delivery Network limitations.
    Issue understood. Addressing it will require close collaboration between the ASIC design team and the module design team.
Next Steps:
  Increase modulation voltage (3.6V?) for micro ring modulator.
  Add temperature control unit for wavelength stabilization.
  Improve on-chip Power Delivery Network (PDN).
  Adapt data path and configuration interfaces to align with PicoPix project requirements.
WP6 ASIC design roadmap is aligned with PicoPix project.

## Slide 29: Analog FE in PicoPix by Viros Sriskaran
Analog Islands (2x2):
  ~30 µW/pixel and Qin-thr>~4ke-  <25 psRMS
  Optimized for negative input charges (e-)
  7-bit threshold DAC
  Novel on-pixel biasing power drop compensation

## Slide 30: The Analog Front-end
Digital
Buffering structure
Analog EOC
8-bit DACs
ANALOG PIXEL ISLAND
PERIPHERY

## Slide 31: Sub-pixel resolution
M[x][y]
+
hitmap
M[x][y+1]
M[x-1][y+1]
M[x][y]
M[x-1][y]
M[x][y-1]
M[x-1][y-1]
M[x+1][y+1]
M[x+1][y]
M[x+1][y-1]
Built in combinatorial algorithm to calculate center of gravity based on Master + hitmap
Selectable weight of Master allows to tune algorithm
For a 256x256 array  512x512 array
  16-bit + 8-bit  18-bit address

## Slide 32: Event sorting
Out-of-order hit packets
Event Sorter
Event frame of hit packets
Off-Chip
Datalinks
Proposed solution
Problem: Data-driven readout provides out-of-order packets
Proposed solution: Design an on-chip Event sorter module that accumulates hit packets over time and groups them in bins based on event tag
Goals:
  Ordered packet readout
  Fixed latency
  Data reduction

## Slide 33
Technology |  |  | 65nm – 10 metal
Pixel Size |  |  | 55 x 55 µm
Pixel arrangement |  |  | 4-side buttable 512 x 448
Sensitive area |  |  | 6.94 cm2
Readout Modes | Data driven (Tracking) | Mode | TOT and TOA
 |  | Event Packet | 64-bit
 |  | Max rate | 3.58x106 hits/mm2/s
 |  | Max Pix rate | 10.8 KHz/pixel
 | Frame based (Imaging) | Mode | CRW: PC (8 or 16-bit)
 |  | Frame | Not-zero-suppressed
 |  | Max count rate | ~5 x 109 hits/mm2/s
TOT energy resolution |  |  | < 1Kev
Time resolution |  |  | 195ps bin  ~60 psrms
Readout bandwidth |  |  | 16x @10.24 Gbps
Minimum threshold |  |  | <500 e-
Radiation tolerance |  |  | NO
The design can inherit several of the functionalities implemented in the TIMEPIX4 chip

## Slide 34: The digital PLL
LAYOUT OF THE dPLL
Design by: Vladimir Gromov, Arseniy Vitkovskiy (NIKHEF)
One digital-PLL per pixel-region
Generates 320MHz clock used for TDC
Required output jitter = 4 psRMS
Suppression of the time jitter of the column clock
  Efficiently suppresses fast (HF) phase noise present of the reference clock high-freq. input jitter.
  Good immunity to power supply ripples and noise
Design status : Prototyped in September 2023
  In the AMTest28 – Test chip prepared by the CERN ASIC Support Service for testing multiple 28nm IP designs
  Diced dies and test-bench available
  First test results are promising

## Slide 35: Slow-control
Custom serial control protocol
  Write packet:
  Read packet:
Allow control of periphery slaves and pixel-matrix
Scripted generation of configuration registers
  Instantiate and route registers in RTL
  Generate documentation
Design Status:
  RTL ready
  Verification and CI ready

## Slide 36: On-chip processor in Picopix
Take over low-computational task from the back-end (slow-control)
Automatize recurrent monitoring operations as bias monitoring, etc.
Calibration, threshold trimming, clock distribution calibration for precise data correction, etc.
Provide commands instead writing/reading registers
Possibility to reprogram it in any moment, making it very flexible for new applications
Toolkit for generating highly-customizable systems that can be integrated in radiation-tolerant ASICs
automates SoC assembly and verification
provides a radiation-tolerant verified IPs library
supports fault-tolerant extensions for redundancy and error correction.
hardware, verification and software toolchain support
SOCRATES - SoC RAdiation Tolerant Eco-System
CERN EP R&D WP5

## Slide 37: The SOCRATES platform
Hardware composition
Generate the top-level SoC
Integrate IP blocks
Infer interconnects (crossbars, adapters)
Software generation
Invoke RISC-V toolchain
Generate hardware abstraction layer (HAL)
Generate linker scripts
Verification
Functional testing environment
SystemC-UVM environment
FPGA prototyping
Implementation
Run synthesis and physical implementation flow on targets
Generate constraints
Advanced stage
Early stage
Ideas for the future
DEVELOPMENT STAGE:
SoCMake Build System
Radiation Hardening
Pre-verified IP-blocks library
Fault tolerant interconnects
radiation-hardened blocks
Software fault tolerance
Fault injection framework
Formal verification for TMR
Constraints for fault tolerance
  CERN EP R&D WP5 – Marco Andorno , Alessandro Caratelli , Davide Ceresa , Benoit Denkinger , Kostas Kloukinas , Anvesh Nookala

## Slide 38: SoCMake: a HW/SW Build System
SIMULATE
Verilator
Xcelium
VCS
IMPLEMENT
Cadence
...
FPGA EMULATE
Vivado
Software application
Register file and Interconnections (*.v)
Documentation - website (*.html, *.md)
UVM testbench (SystemC) and SEE injection utilities
Hardware abstraction layer
Config files for synthesis and implementation (*.yaml, *.tcl)
Top level HDL (*.v)
Software application
IP blocks and hardware accelerators (*.sv)
Linker scripts generation
*.sv
*.cpp
*.rdl
RDL toolchain
CMake based HW/SW build system for SoCs
Input configuration in SystemRDL
  Register Description Language extended for supporting SoC description
  Used as top-level architecture description
Rapid prototyping of SoCs:
  Quick composition of IP blocks into full systems
  Quickly build different architectures with different IP blocks, hardware accelerators or different CPUs
Open-source
  Toolkit: https://gitlab.cern.ch/socrates

## Slide 39: A an almost-fully generated SoC: TriglaV prototype
Goals:
Demonstrate (and develop) SOCRATES capabilities
Validate the toolkit and demonstrate the feasibility of using programmable logic inside front-end ASICs.
Test-drive the HEP 28nm Common Design Platform
Test the radiation performance and validate the design choices
Design strategy:
Fully generated with the SOCRATES toolkit
Target architecture: embedded controller for pixel readout ASICs
Radiation tolerant design
Implemented in 28nm bulk CMOS
focus on introducing observability and testability features to evaluate the radiation tolerance of the design under irradiation testing
Design submission:
MPW run in 28nm reserved for the 30th November 2024

## Slide 40: A an almost-fully generated SoC: TriglaV prototype
CPU choice: IBEX (Zero-risky) [1]
Fully triplicated in TriglaV – TMR formal verification and fault-injection
In parallel studies for selective protect CPU components and handle faults [2]
Memory Scrubbing and Protection Unit
Dual-port commercial SRAM
Bit interleaving, ECC (Hamming encoded 13-8)
Periodic scrubbing
APB-RT interconnect
encoded data and address – triplicated control
error correction double-error handling in software
RISC-V IBEX
CPU
MSPU
SRAM
SRAM
MSPU
SRAM
SRAM
Bootloader
Debug unit
JTAG
SOC control
PLIC
TIMERs
UART
GPIO
ASIC-specific peripherals
OBI TMR crossbar
iPOL2v3
On-chip resonant DCDC converter
EP R&D WP5.2
APB-RT interconnect
Design Status: MPW run in 28nm reserved for the 30th October 2024

## Slide 41: A fully generated SoC in Picopix
EoC 1
EoC 0
…
EoC N
EoC 1
EoC 0
Periphery control
Access to packet-processor
RISC-V IBEX
CPU
MSPU
SRAM
SRAM
MSPU
SRAM
SRAM
Bootloader
Debug unit
JTAG
SOC control
PLIC
TIMERs
OBI TMR crossbar
APB-RT interconnect
End-Of-Column slow-control units
Handles access to pixel-matric configuration registers
Serial protocol
Access data buffer for analysis
For decisions based on data
Periphery control
Control clock calibration
Access periphery slow-control
Bias monitoring
Design Status: Not started yet

## Slide 42: PixESL a virtual prototyping framework
CERN EP R&D WP5 D. Ceresa, F. Brambilla, J. Dhaliwal
Time-consuming
guidelines
limitations
NO structured feedback
Physics simulation
Specifications
Hardware design
Verification
guidelines
limitations
ref. model
ASIC limits
guidelines
limitations
Fast
Reference model
for verification and physical simulation
Validation
Verification
Specifications
Physics simulation
Hardware design
Verification
PixESL framework
Virtual prototype