## Slide 1: Lecture 2 Applications of Accelerators
Professor Emmanuel Tsesmelis
Principal Physicist, CERN
Visiting Professor, University of Oxford
Graduate Accelerator Physics Course
John Adams Institute for Accelerator Science
16 October 2024

## Slide 2: Introduction

## Slide 3
Accelerators are not only for particle physics
Accelerators Worldwide

## Slide 4
Cutting edge Research Infrastructures play a key role in a knowledge driven society
Knowledge is − and will be more and more − the most precious resource for a sustainable development
Accelerator Technologies and Innovation
Notes: 4

## Slide 5: Accelerators for Energy
Accelerator-Driven Subcritical System
  External source of neutrons to drive sub-critical reactor loaded with non-fissile fuel such as 232Th.
  Neutrons produced by high-power proton beam through spallation, breeding 233U causing it to fission.
  Cannot support self-sustaining chain reaction.
  232Th is widely-available natural resource.
  Released thermal power is 100 times that of beam energy.
  Turning off the accelerator stops the fission reaction.
Use of Th instead of U produces
less actinides.
The cycle produces much less long-lived
radioactive waste (e.g. Pu).
Enough Th is available to sustain
such systems for 10 centuries.

## Slide 6: Accelerators for Energy
ADSR & Radioactive Waste Transmutation
  ADSR neutrons interact with surrounding fuel material containing separated long-lived isotopes.
    Transmute these isotopes into shorter-lived products.

## Slide 7: Accelerators for Energy
International Thermonuclear Experimental Reactor (ITER)
  Ion beams to be part of plasma heating techniques for fusion
    Provide high current drive efficiency required magnetic confinement fusion facilities.
    Required tens of A of ion current at 1 MeV kinetic energy.

## Slide 8: Accelerators for the Environment
CLOUD experiment at the CERN PS
  Experiment using cloud chamber to study possible link between cosmic- rays and cloud formation.
    Studies suggest that cosmic- rays may have an influence on the amount of cloud cover through the formation of new aerosols (tiny particles suspended in the air that seed cloud droplets).
  Understanding the underlying microphysics in controlled laboratory conditions is a key to unraveling the connection between cosmic-rays, clouds and climate.
  First time high-energy physics accelerator used to study atmospheric and climate science.

## Slide 9: Accelerators for Security
X-ray Scanning of Cargo

## Slide 10: CERN’s technological innovations have important applications in medicine and healthcare
Accelerator technologies are applied in cancer radiotherapy with protons, ions and electrons.
Pixel detector technologies are
used for high resolution 3D colour X-ray imaging.
© CNAO
© marsbioimaging
Technologies applied
at CERN are also used in PET, for medical imaging and diagnostics.
© ENVISION / ENLIGHT
CERN produces innovative radioisotopes for nuclear medicine research.

## Slide 11
Accelerators for Medicine
X-ray Radiation Therapy
  Electron linacs for conventional X-ray radiation therapy (MV photons).
    X-rays have been used for decades to destroy tumours.

## Slide 12: Accelerators for Medicine
Hadrontherapy
  For deep-seated tumours and/or minimizing dose in surrounding healthy tissue use hadrons (protons, light ions).
  Accelerator-based hadrontherapy facilities.
  Based on medium-energy cyclotrons and synchrotrons for hadron therapy with protons (250 MeV) or light ion beams (400 MeV/u 12C-ions
Loma Linda Proton Treatment Centre
Constructed at FNAL
Established 1989
60 MeV protons
First hospital-based
proton therapy

## Slide 13: PIMMS @ CERN
Proton-Ion Medical
Machine Study (PIMMS) Study

## Slide 14: Accelerators for Medicine
The Bragg Peak

## Slide 15: Accelerators for Medicine
Charged particle energy loss in matter
The relativistic Bethe-Bloch formula

## Slide 16: Accelerators for Medicine
Medical Imaging
  Radioisotopes have become vital components in medicine.
    Produced at reactors or accelerators (cyclotrons or linacs).
  Positron Emission Tomography (PET)
    Requires positron emitter 18F
    From 7-11 MeV proton accelerator
  99Mo / 99mTc
    100 kW of 200 MeV protons impinging on depleted U target produce neutrons.
    Neutrons targeted on low-enriched U thus producing 99Mo.
PET Scan
Bone scans
indicating
increased
99mTc intake
due to
cancer growth

## Slide 17: Radiopharmaceuticals

## Slide 18
Neutrons & X-rays
Protein structure revealed with help of light sources
Neutron and X-ray imaging essential for studies of proteins and advanced materials.
2-d material (graphene)
ISIS and Diamond neutron and X-ray sources Harwell, UK

## Slide 19: Synchrotron Light Sources
Courtesy ESRF

## Slide 20: Synchrotron Light Sources

## Slide 21: The Electromagnetic Spectrum

## Slide 22: Rate of Energy Loss (1)
This EM radiation generates an energy loss of the particle concerned, which can be calculated using:
Electron radius
Velocity of light
Total energy
‘Accelerating’ force
Lepton rest mass
constant
Force can be written as: F = evB = ecB
Thus:
but
Which gives:

## Slide 23: Rate of Energy Loss (2)
Have:
Finally, this gives:
,which gives the energy loss
Interested in the energy loss per revolution for which need to integrate the above over one turn.
Thus:
Bending radius inside the magnets
Lepton energy
Gets very large if E is large !!!
However:

## Slide 24: Accelerators for Synchrotron Light

## Slide 25: X-ray Diffraction
25
Max von Laue
1914 Nobel Prize:
‘For his discovery of the
diffraction of X-rays
by crystals’
Constructive interference:
2 d sinθ = n λ

## Slide 26: X-ray Diffraction Today
26

## Slide 27
Diamond Light Source
Diamond Light Source, Harwell Science and Innovation Campus, UK
Diamond Light Source Beamlines

## Slide 28: Accelerators for Synchrotron Light
Protein Structures
  Proteins are biological molecules involved in almost every cellular process.
  The protein is produced, crystallised and illuminated by X-rays. The interactions between the X-rays and the crystal form a pattern that can be analysed to deduce the protein structure.
  Over 45,000 structures have been solved by the worldwide synchrotron community.
Protein
Data
Bank
The trimer of the Lassa nucleoprotein,
part of the Lassa virus

## Slide 29
Roger Kornberg’s Nobel Prize-winning determination of the structure of RNA polymerase has been described as a “technical tour de force.” The key to the visualization of this fundamental biological molecule in action was synchrotron radiation, supplied by the powerful X-ray crystallography instruments at the Stanford Synchrotron Radiation Laboratory.

## Slide 30
Protein Structure Revealed by Light Sources
HIV glycoprotein
yeast enzyme
mosquito
immune system

## Slide 31
4th Generation Light Source – Free Electron Laser

## Slide 32: European XFEL
European XFEL at DESY is a large-scale proto-type for the ILC
  100 cryomodules; 23.6 MV/m, accelerator length 2.1 km; 17.5 GeV
  Sucessfully started operation in 2017

## Slide 33: Accelerators for Neutron Science
Penetrate deep inside materials since they are deflected only from the nuclei of atoms.
Statistical observation of deflected neutrons at various positions after the sample can be used to find the structure of a material.
Loss or gain of energy by neutrons can reveal the dynamic behaviour of parts of a sample, for example dynamic processes of molecules in motion.
ISIS Spallation Facility (800 MeV) at RAL

## Slide 34: ISIS Accelerators and Targets

## Slide 35: Accelerators for Ion Beam Implantation
35
Ion implantation in semiconductor manufacture
Typical semiconductor fabrication: 140 operations, 70 involving ion implantation at specific sites in crystal
Ions accelerated to modest energies
  Depth of implant controlled by ion beam energy: typically 2  600 keV

## Slide 36: Ion Beam Implantation Products
36
36

## Slide 37: Radiocarbon 14C Formation & Decay

## Slide 38: Radiocarbon 14C Dating

## Slide 39: Accelerators for History & Culture Applications
Accelerator Mass Spectrometer
Radiocarbon
Dating

## Slide 40
Consideration of use
Fundamental knowledge
Niels Bohr
Thomas Edison
Louis Pasteur
Accelerator Science and Technologies

## Slide 41: Bibliography