## Slide 1
Summary VD and PiD detectors for FCC-ee
based on A. Andrezza, G. Boudoul, T. Papaevangelou,
E. Robuti, M. Rolo, S. Senyukov, D. Contardo/P. Schwemling
D. Contardo (IP2I)
FCC FRANCE & ITALY 2nd workshop, Venice, 4 - 6 November 2024

## Slide 2
S. Senyukov developments in TPSCo 65 nm processes
  “small electrodes, thin epi-layer (10 μm), large size (ALICE-ITS3)
  “OCTOPUS” DRD3/7 project goal demonstrate best approach/alternatives toward 3 μm
    process variants : STD ≃ 25 μm pitch, GAP ≲15 μm
    STD/GAP 100/5 ns timing precision targets
    Asynchronous readout, digitization few bits for STD higher pitch, pixel grouping for GAP lower pitch
+ The project has several international collaborators
different processes provide differtent charge sharing, few digitisation bits can improve resolution
Vertex Detector
target precision ≃ 3 μm and X/X0 /layer less than 0.1% at low power ≲ 50 mW/cm2
Monolithic CMOS technology is a unique solution to meet this performance

## Slide 3
M. Rolo developments in LFoundry 110 nm processes
  large electrodes, HR wafers, active thickness down to 50 μm
  ARCADIA-MD3
    pixels 25 x 25 μm2, matrix 512 x 512, 1.28 x 1.28 cm2 silicon active area, “side-abuttable”
      < 30 mW/cm2 at 100 MHz/cm2
      4.7 μm resolution with binary readout (not deconvoluted from telescope resolution)
Also studies of 10 μm pitch and grouping in mini-strips
4.7 μm
Vertex Detector
target precision ≃ 3 μm and X/X0 /layer less than 0.1% at low power ≲ 50 mW/cm2
Monolithic CMOS technology is a unique solution to meet this performance

## Slide 4
Vertex Detector mechanical designs
crucial to fully benefit from sensor performance (or to avoid over-designing)
S. Senyukov SEED large sensors in snail shape allowing overlaps
F. Palla stave concept
small sensors, 0.25% X/X0 /layer
complex MDI integration
large bent sensors 2 in layer 1-2, 4 in layer 3 and 4
improved X/X0, but fill factor and hermeticity issue
Several other common challenges
  airflow cooling
  stability
  services
  MDI integration
  accessibility

## Slide 5
Vertex Detector simulations
G. Boudoul, A. Andreazza
Provide guidance on overall configuration
can be parametric
  radius and lentgth of layers
  single versus double layers
  requirements / layer(disk) extended to outer pixel and wrapping layers…
old plot of CLD and IDEA vd on top of each others
Provide guidance for sensor and system R&D
need detailed geometries, full GEANT simulations
  operation condition, rates and occupancies at different sensor positions including background
    input to readout architecture
  realistic performance estimate with respect to
    sensor parameters, system design (X/X0, hermeticity, acceptance), mis-calibrations
Essential piece is development of a digitizer (started)
  produce realistic clusters for all tracks
    eg correct hit positions and occupancies
  should be usable in all sensor & detector configurations

## Slide 6
a layer at 15 cm would allow 3σ discrimination up to the 2 T-field cutoff of 0.66 GeV at 2.2 m
at 3T the momentum cut-off is 1 GeV at 2.2 m a ToF layer would be useful in front of the LGVD at 35 cm
position precision target in r/Φ 5(7) μm at .35(2.2) m
courtesy of R. Aleksan
30 ps
30 ps
30 ps
3σ
3σ
4σ
* Large Gas Volume Detectors (Drift CHamber or Time Projection Chamber)
Motivation for PID
Flavor physics, Higgs decays to fermions, HNL mass…
ToF ≃ 30 ps precision at ≃ 2.2(0.15) m provide 3σ π/K discrimination ≳ 3(0.66) GeV standalone
needed in the 1 GeV region to complete dE/dx and dN/dx in LGVD*
strong interest to have combined position and timing precision in a same sensor
courtesy R. Aleksan

## Slide 7
ToF PID / Tracking Layers
Monolithoc CMOS and LGADS
* the technology could be deployed in first layers of a Si/W elctromagnetic calorimeter and a LumiCal, ** not correcteed for time reference resolution
w/o gain
w/ gain
TPSCo 65 nm
modified with gap
10 μm epi., pitch 10 μm
63 ps precision
IP2I plans to develop
async. readout architecture
ToA/ToT at end of column
Mini CACTUS-V2 IRFU
LFoundry 150 nm,
175 µm, 0.5 x 0.5 mm2
≃ 60 ps precision
w/ gain layers started
ARCADIA-MADPIX M. Rolo
LFoundry 110 nm, w/gain
48 μm, 250 x 100 μm2
≃ 72 ps precision**
INFN-FBK LGADs E. Robuti
hybry design
50 μm, .45 x .45 mm2
≃15/50 μm/ps precision
New design pads
trench isolated
to control charge sharing
P. Schwemling/D. Contardo

## Slide 8
ToF PID / Tracking Layers
Monolithoc CMOS and LGADS
* the technology could be deployed in first layers of a Si/W elctromagnetic calorimeter and a LumiCal, ** not correcteed for time reference resolution
TPSCo 65 nm
modified with gap
10 μm epi., pitch 10 μm
63 ps resolution
IP2I plans to develop
async. readout architecture
ToA/ToT at end of column
Mini CACTUS-V2 IRFU
LFoundry 150 nm,
175 µm, 0.5 x 0.5 mm2
≃ 60 ps precision
w/ gain layers started
ARCADIA-MADPIX M.Rolo
LFoundry 110 nm, w/gain
48 μm, 250 x 100 μm2
≃ 72 ps precision**
INFN-FBK LGADs E. Robuti
hybry design, .45 x .45 mm2
≃15/50 μm/ps precision
New design pads trench isolated to control charge sharing determined
w/o gain
General MCMOS/LGAD technology problematics
Intrinsic time precision limit w/ and w/o gain layer
  versus pixel size/pitch - active thickness - capacitance
Position precision
  channel density versus position/timing performance (driving power)
low power premplification
Other MCMOS technology R&D
TJ 180 nm CASSIA CERN, w/ amplification ≃ 50 x 50 μm2
SiGe tecnnology UniGe (not commercial), w/o and w/ amplifications
MPGD - ex. Picosec T. Papaevangelou
30 – 35 ps precision

## Slide 9
ToF PID / Tracking Layers
Monolithoc CMOS and LGADS
* the technology could be deployed in first layers of a Si/W elctromagnetic calorimeter and a LumiCal, ** not correcteed for time reference resolution
TPSCo 65 nm
modified with gap
10 μm epi., pitch 10 μm
63 ps precision
IP2I plans to develop
async. readout architecture
ToA/ToT at end of column
Mini CACTUS-V2 IRFU
LFoundry 150 nm,
175 µm, 0.5 x 0.5 mm2
≃ 60 ps precision
w/ gain layers started
ARCADIA-MADPIX M.Rolo
LFoundry 110 nm, w/gain
48 μm, 250 x 100 μm2
≃ 72 ps precision**
INFN-FBK LGADs E. Robuti
hybry design, .45 x .45 mm2
≃15/50 μm/ps precision
New design pads trench isolated to control charge sharing determined
w/o gain
w/ gain
System aspects
Power management
  number of layers versus standalone performance and power sum
  X/X0 versus power
Mechanical structure and services similar as for VD
  stave design - sensor size and thickness tbd
  bent design – oriented to large and thin sensors

## Slide 10
ToF PID / Tracking Layers
Monolithoc CMOS and LGADS
* the technology could be deployed in first layers of a Si/W elctromagnetic calorimeter and a LumiCal, ** not correcteed for time reference resolution
TPSCo 65 nm
modified with gap
10 μm epi., pitch 10 μm
63 ps precision
IP2I plans to develop
async. readout architecture
ToA/ToT at end of column
Mini CACTUS-V2 IRFU
LFoundry 150 nm,
175 µm, 0.5 x 0.5 mm2
≃ 60 ps precision
w/ gain layers started
ARCADIA-MADPIX M.Rolo
LFoundry 110 nm, w/gain
48 μm, 250 x 100 μm2
≃ 72 ps precision**
INFN-FBK LGADs E. Robuti
hybry design, .45 x .45 mm2
≃15/50 μm/ps precision
New design pads trench isolated to control charge sharing determined
w/o gain
w/ gain
Simulation studies
operating conditions – rate and occupancies
position and timing precision requirements versus radius
(can influence technology choices)
effect of X/X0 versus radii and number of layers
physics benefit of inner radius timing

## Slide 11
Outlook
Sensor R&D
  different technologies shoud eventually converge on similar performance for VD
  technology alternative(s) to achieve PID/Tracking is (are) yet to be established
  work will continue in the first 3-4 years DRD period for comparative evaluations
  on longer term, 3D wafer stacking, finer foundry nodes, could shed new light for channel density and power consumption (DRD& mandate)
System aspects are crucial, they may limit the performance
  particularly for X/X0, MDI integration and systematic effects
Simulation studies are needed
  to guide R&D
  to define and refine detector configurations and requirments (as a function of r/𝜂)
  to assess effects of hermeticity, acceptance, mis-calibrations
France and Italy are developing complementary technologies
and system approaches, synergies can be exploited
EoIs foressen on VD, tracking Wrapping Layers and ToF/Tracking Layers

## Slide 12
Outlook
Sensor R&D
  different technologies shoud eventually converge on similar performance for VD
  technology alternative(s) to achieve PID/Tracking is (are) yet to be established
  work will continue in the first 3-4 years DRD period for comparative evaluations
  on longer term, 3D wafer stacking, finer foundry nodes, could shed new light for channel density and power consumption
System aspects are crucial, they may limit the performance
  particularly for X/X0, MDI integration and systematic effects
Simulation (mostly full) studies are needed
  to guide R&D
  to define and refine detector configurations
  to assess effects of hermeticity, acceptance, mis-calibrations
France and Italy are developing complementary technologies
and system approaches, synergies can be exploited
EoIs foressen on VD, tracking Wrapping Layers and ToF/Tracking Layers
Monolithic CMOS
common technology matrix
A. Andreazza
can be connected to system and simulation aspects