## Slide 1: Resistive Plate Chamber for the Muon apparatus
Acknowledge
Many thanks to Bencivenni, Giacomelli, Laktineh, Lee, Poli Lener, Ramos for useful discussions and support.
On behalf of the RPC community and participants to RPC2024

## Slide 2
RPC2024 conference outlook
Standard RPC
Multigap RPC
Statement from prof. Santonico

## Slide 3
Study Eco-friendly mixtures
Evolution of “standard RPC”
Decrease gas gap
Decrease electrode thickness
Double gap concept, decrease the charge on a single gap, study new electrodes
Improve front end to achieve order 10 fC threshold sensitivity and low noise
Detector
Fron-end
Operation

## Slide 4
The ATLAS RPC upgrade for LHC
New thin-gap RPCs (1 mm)
Improved time resolution (0.4 ns) for time-of-flight measurements
Courtesy of Paolo Camarri
Gas-gap thickness: reduced from 2 mm to 1 mm.
Electrode thickness: reduced from 1.8 mm to 1.4 mm
New gap layout
1 mm gap

## Slide 5
The ATLAS RPC upgrade for LHC
Courtesy of Luca Pizzimento
New electronics

## Slide 6
The ATLAS RPC upgrade for LHC
Timing
Time resolution applying the time walk correction ∼ 330 ps with a mono-gap RPC
Performance of the BIS78 RPC detectors: a new concept of electronics and detector integration for high-rate and fast timing large size RPCs
ATLAS Collaboration - Luca Pizzimento (Rome U., Tor Vergata and INFN, Rome3)
Performance of new generation of Resistive Plate Chambers operating with alternative gas mixtures
Nucl.Instrum.Meth.A 1066 (2024) 169580
Giorgia Proto, N. Bangaru, F. Fallavollita, O. Kortner, H. Kroha
Efficiency

## Slide 7
Gas-gap thickness: reduced from 2 mm to 1.4 mm.
Sub-ns time resolution
High background capability up to 2 kHz/cm2
Innovative FEB with low sensitivity threshold ( below 50 fc)
1.4 mm gap
Double side strip readout for XY recostruction
FEB based on ASIC petiROC2C, specially designed by
OMEGA group
Courtesy of Maxime Gouzevitch
The CMS RPC upgrade for LHC

## Slide 8
Space resolution on x coordinate
Timing
Absolute time resolution of a two chambers system: 780 ps
Courtesy of Maxime Gouzevitch
The CMS RPC upgrade for LHC

## Slide 9
Efficiency plateau at 2.3 kHz/cm2 background rate.
Efficiency plateau at 1.0 kHz/cm2 background rate.
Courtesy of Jules Vandenbroeck, Mehar Ali Shah
The CMS RPC upgrade for LHC

## Slide 10
Courtesy of Alessandro Rocchi
R&D: glass phenolic laminate (Roma2)
Phenolic glass properties:
Electrical Resistivity, Average value: 2-4 x 1012 Ωcm
Dielectric Constant, Average value: 5.10
Dielectric Breakdown, Average value: 30000 V
Detector features
Gap configurations: 2 parallel/single gap
Electrode thickness: 0.4 mm
Gas-gap thickness: 0.2 mm
Active surface: 8 cm x 30 cm
Spacer lattice: 3 cm x 3.5 cm
Electrode material: phenolic glass

## Slide 11
Courtesy of Alessandro Rocchi
R&D: glass phenolic laminate (Roma2)
Rate capability at GIF++
A rate capability of approximately 2 kHz/cm2 (ABS 10) at 75% efficiency is observed
Time resolution on the H8 beam line
√𝟐
𝝈
𝝈𝒕 = = 𝟏𝟕𝟎 𝒑𝒔
All channels

## Slide 12
Courtesy of Alessandro Rocchi
R&D: glass phenolic laminate (Roma2)
𝜎𝑠 =
0.77
√2
𝑚𝑚 = 0,5430,016 𝑚𝑚
Space resolution with the charge centroid method
Perspective for tracking – timing – high-rate capability
        Reduce the graphite resistivity
                Reduce the strip pitch
        Reduce the phenolic glass resistivity by optimizing production processes and selection.

## Slide 13
R&D: 1 mm gas gap (Bari-KODEL)
Double gap HPL equipped with CMS front-end
1 mm gap thick and 1.4 electrode thick
92% efficiency up to ∼ 2.2 kHz/cm2
Working point average ∼ 6 kV
Courtesy of D. Ramos

## Slide 14
R&D: 500 mm Glass RPC (Bari-KODEL)
50x50cm2 prototype double gap glass RPC with gas thickness of 500 um under test for fast timing RPC prototype.
Preliminary signal study by using CAEN digitizer DT5742, strip PCB 5 mm pitch and cosmic trigger
jitter = time_thr – time_0
Study jitter distribution @ 4 kV with standard CMS mixture
Preliminary: 220 ps
Courtesy of D. Ramos

## Slide 15
R&D: new melamine electrodes (KODEL)
Thin melamine sheets (ρ ~ 1.5 ⅹ 1011 Ω cm) and polycarbonate sheet to support the gas gaps
New RPC electrode material (Melamine sheet):
Thinner gas gap volumes to achieve a better time resolution (~ 300 ps or better)
2 mm thick gas volume RPCs → 1 mm thick gas volume RPCs
→ In next R&D, 0.5 mm thick gas volume RPCs
Thinner RPC electrode for higher rate capability (> 5 kHz cm-2)
Hopefully NO oil varnishing needed
Why NOT soda-lime glass instead? (commonly used for timing RPCs)
Resistivity ~ 1012 Ωcm → Too high to be used at high-rate environment
→ The rate capability at best ~ 1 kHz cm-2
Too fragile to make large sized trigger RPC gaps
0.5 mm or 1 mm thick Polycarbonate
300 ~ 500 μm thick Melamine
+ Phenol
Graphite coating on
a PC plate
Glued to be one piece
Courtesy of K. Lee

## Slide 16
R&D: new melamine electrodes (KODEL)
Small 1-mm thick gas-volume double-gap RPC made of 500 μm-thick melamine-based sheets
Active area of the detector: 26.4 x 26.4 cm2
Strip pitches
5 mm to address a 1 ~ 2 mm position resolution
11 mm for typical RPC triggers
Surface resistivity of graphite ~ 500 kΩ/sq
Absence of good front-end-electronics with a time resolution better than 100 ps
→ Unable to check the time characteristics of the detectors
11 mm pitch strips (read only 24 strip among 32 strips)
Digitization threshold = 0.33 mV (~ 50 fC)
HVWP = HV(abs 95%) + 100 V = 5.71 kV
Efficiency @HVWP = 0.972, εmax = 0.990
Mean cluster size @WP = 2.5
Noise rate ~ 10.8 Hz cm2 @ 23.1 oC
Courtesy of K. Lee

## Slide 17
R&D: glass electrodes (Lyon, Tsinghua)
Standard glass RPC have low-rate detection capability (a few hundreds of Hz/cm2)
Tsinghua has developed a low resistive glass 1010 Ω · cm ( doped glass with metal components) and a very high surface uniformity, with a roughness below 10 nm
REF. F. Lagarde et al 2016 JINST 11 C09006
Limitation (30 cm x 30 cm) is a problem
Courtesy of I. Laktineh

## Slide 18
R&D: plastic electrodes (Lyon)
PVdF and PEEK are very stable and chemically inert thermoplastic
New kind of PVdF developed with the help of PolyOne (Germany). Doped with CNT we achieved a bulk resistivity of 1011-12 W cm.
New charged PEEK developed with the help of Krefine (Japan).
Doped with BC a bulk resistivity of 108-9 W cm was achieved.
A few small detectors were made using doped PVdF plates of 2-3 mm thickness. An excellent efficiency is obtained with cosmic, but resistivity is not low enough for reaching high rate.
Plates made with charged PEEK were produced reaching 108-9 W cm which could allow reaching rates of hundreds of kHz/cm2, but some homogeneity issues are still there.
More efforts and funding are needed to finalize this material.
AIDA2020
Courtesy of I. Laktineh

## Slide 19
R&D: Sustainable RPC operation
Eco-friendly mixtures requirements: Low GWP, low toxicity, not flammable, detector performance comparable with standard one. Actions:
Replace C2H2F4 with HFO
Addition of CO2
SF6 still needed but studies on replacement on going
HFO moves the operating voltage (WP) at much higher values, so the the addition of CO2 helps in limiting this increase. For thin gap RPC (es. sub-mm gaps), this might be less important
 | TFE (%) | HFO (%) | CO2 (%) | iC4H10 (%) | SF6 (%) | GWP | CO2e (g/l)*
STD | 95.2 | - | - | 4.5 | 0.3 | 1485 | 6824
ECO2 | - | 35 | 60 | 4 | 1 | 476 | 1522
ECO3 | - | 25 | 69 | 5 | 1 | 527 | 1519
Density (g/l) | 4.68 | 5.26 | 1.98 | 2.69 | 6.61 | - | -
GWP | 1430 | 7 | 1 | 3 | 22800 | - | -
*GWP with respect to CO2, and their CO2e, in grams, for one litre of mixture
Courtesy of RPC EcoGas@GIF++ collaboration

## Slide 20
R&D: Sustainable RPC operation
Efficiency single gap HPL RPC 2mm vs 1mm
Single gap (2.0mm)
Courtesy of RPC EcoGas@GIF++ collaboration

## Slide 21
A physics case: Long Lived Particles
The ANUBIS proposal
Courtesy of Oleg Brandt
Instrument with RPC the ATLAS roof

## Slide 22
A physic case: Long Lived Particles
Courtesy of Aashaq Shah
The proANUBIS demonstrator with LHC data

## Slide 23
Facility productions
General Tecnica (Italy) has produced the gas gaps for ATLAS phase I and CMS Barrel. It is now producing the new ATLAS RPC gas gap for phase II. Also ready to respond to R&D requests.
KODEL@Korea University has produced the gas gaps for CMS forward (still in production). Also, the group significatively active in R&D activity. Under discussion the future of the mass production facility. Input from scientific community needed.

## Slide 24
Facility productions (new entries)
University of science and technology of China (USTC) is undertaking a major effort to set up a gas gap production facility for the ATLAS RPC. Preparatory work is over. Ready for production.
Max Plank Institute (MPI) has recently put in operation a new facility for the ATLAS gas gap production. Also, the MPI group has started to establish two additional manufacturers:

## Slide 25
Conclusion
Detector performance such as: rate capability of 4-5 kHz/cm2, time resolution of 200-300 psec, space resolution of 400-500 mm are easily achievable with the present technology for “standard RPC”. Improvement of at least a factor of 2 is within reach. Inputs from community on FCC muon detector baseline are needed.
Additional R&D should be performed on novel material for electrodes and assembly procedure for thin gas gas RPC (0.2-0.5 mm)
The eco-gas puzzle needs some special effort, but there is the evidence that operation with thin gas gaps would facilitate the definition of a proper eco-friendly mixture
Several facilities are now in operation and can respond to possible call for production
DRD1 has offered a unique platform for collaborative network and could facilitate the discussion for possible FCC muon detector ideas