## Slide 1
Positron source optimization
with GIOTTO and a sub-harmonic buncher
A. Bacci, M. Rossetti Conti & I. Drebot (on ICS)
Istituto Nazionale di Fisica Nucleare
2nd FCC Italy & France Workshop, 4-6 November 2024, Venice, Italy
Notes: Good, afternoon, I thank the organizers for this contribution to the INFN-Milano activities on FCC

## Slide 2
INFN-MI activities on Positron Sources optimization
focusing more on the methods than on one the specific case
  GIOTTO AI code, the main tool applied to the source beam line optimization
  The most relevant results obtained in this activity
----- the latest news -----
The use of a low-frequency buncher to improve the e+ capture
Optimizations by “orchestrating” an array of solenoids on the AMD field profile
One-slide on Illya Drebot contribute about BD with ICS in the FCC main ring
Conclusions
2
  Index

## Slide 3
from 2007
  GIOTTO AI code for beam line optimization
3
Genetic Interface for OpTimizing Tracking with Optics
Notes: Invited @ ERL UN MESE FA
In principle it can drive a generic code, or python script
keyikey

## Slide 4
Our activity main Goal: start from IJClab SOTA layout and with GIOTTO & our BD expertise to push the optimization @ its maximum
We kept frozen initial positron distrib.: “Amor5X0_E6GeV_Spot0.5mm_Emxy15um_OutputPositrons_Astra.ini”;
The only modification: an Astra’s flag to consider the beam extraction from the target
  2022/23 Collaboration with IJClab
Example of an of the optimization we performed
We tested both: HTS (PSI – like) and AMD
and more cavities: 2 GHz mode ; SW-TW 1.3 GHz; 3 GHz SLAC-type
1
2
3
4
5
6
7
4
M. Rossetti Conti
Notes: Positron yeld

## Slide 5
Bz-plateau= 0.55T
Optimization magnetic field profile
HTS – Mag. Device field profile
Genetic knobs: +3
Bridge coil : position
Bridge coil 1: field
Bridge coil 2: field
a bridge solenoid
Bz-Hyperbole completion
  GIOTTO bridge coils optimization test
5
Notes: Two Helmholtz coils. We built the field profile with superfish

## Slide 6
GIOTTO now optimizes particle distribution subsets within specific windows (6D)
Macroparticles: 136 k
here within the first bucket optimization (z-cut, pz-cut).
In green, the dead particles; in violet, the live ones
  A new GIOTTO feature: the window optimization
6
two RF buckets

## Slide 7
  GIOTTO window optimization results
22-end
meanwhile
few months ago
+
+
7

## Slide 8
----- the latest news -----
8
Notes: Last weeks news

## Slide 9
  The use of a low-frequency buncher to improve the e+ capture
The idea: in the frame of ERL-INFN BriXSinO project
1.3 GHz vs 650 MHz vs 433 MHz vs 325 MHz
Bunchers Comparison: Performance vs frequencies
Paper under submission
9
Notes: The buncher has a lot of benefits on BD
Buncher under constructon in Milano

## Slide 10
  Focus on the low-frequency buncher
Lower frequency buncher:
  a more linear field == a lower chromatism
  cavities with large irises == larger particles acceptance
10
Notes: Raccontare che è una comparazione tra 4 diversi piani trasversi al centro del buncher cambiando la frequeza del buncher Le emittanze sono dopo il buncher

## Slide 11
Study of two cases for a buncher injecting an L-band LINAC 2GHz, cavities :
A low vph 325 MHz buncher cavity ~ 1/6 of 2 GHz
A 500 MHz buncher as first trapping device cavity for L-banc 2GHz acc. cavities
325 MHz Buncher 0.7
2) 500 MHz Buncher
1) 325 MHz Buncher 0.7
Low Bunchers exploit modified Bessel function, for non-linear distribution corrections
11
  Focus on the low-frequency buncher & low vph
Notes: Light speed
Dire bene dove si piazza il buncher!!!

## Slide 12
  Focus on low vph and β < 1 positron
Low Bunchers exploit modified Bessel function, for non-linear distribution corrections
325 MHz Buncher 0.7
2) 500 MHz Buncher
1) 325 MHz Buncher 0.7
Distribution leaving the target
12

## Slide 13
89% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 56.7 MeV (45.0% ∆E/E)
εn,x=52 103 mm-mrad
σx= 16 mm
σz= 11 mm
88.9% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 57.1 MeV (45.3% ∆E/E)
εn,x=53 103 mm-mrad
σx= 16 mm
σz= 11 mm
  Low-frequency buncher results 325 vs 500 MHz
325 MHz Low-vp
500 MHz
13

## Slide 14
45% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 8.9 MeV (7.9 % ∆E/E)
εn,x=12.4 103 mm-mrad
σx= 8 mm
σz= 1.9 mm
to be boosted and compared with the ring acceptance
  Low-frequency buncher results 325 MHz
325 MHz
89% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 56.7 MeV (45% ∆E/E)
εn,x=52.0 103 mm-mrad
σx= 16 mm
σz= 11 mm
14
Notes: È stato un nostro esercizio, ma chiarmaente ci dobbiamo confrontare con la parte che veramente entrerà nel Damping Ring che è nota, ma non l’abbiamo ancora inserirla in questi conti

## Slide 15
#21 Gens/knobs list
- 1x φinj 325 MHz Buncher
- 18x single coils Bz
- 2x array of coils ⓲ & ⓲ (each powered together) Bz
  The solenoids array used for the optimization
⓲
⓲
15
A GIOTTO peculiar multidimensional problem: 21 Knobs
  Two cases: -large windows optimization- & -narrow windows opt-

## Slide 16
  As GIOTTO directed the solenoids -large window opt-
The AMD field map
89% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 56.7 MeV (45% ∆E/E)
εn,x=52 103 mm-mrad
σx= 16 mm
σz= 11 mm
Previous: the only AMD
90% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 54.6 MeV (43% ∆E/E)
εn,x=52 103 mm-mrad
σx= 16 mm
σz= 11 mm
16
+

## Slide 17
  As GIOTTO directed the solenoids -narrow window opt-
17
The previous slide one
45% of extracted e+ in 1st RF bucket
E=126 MeV
∆E = 8.9 MeV (7.9 % ∆E/E)
εn,x=12.4 103 mm-mrad
σx= 8 mm
σz= 1.9 mm
44% of extracted e+ in 1st RF bucket
E=125.8 MeV
∆E = 8.0 MeV (6.3 % ∆E/E)
εn,x=10.0 103 mm-mrad
σx= 7.7 mm
σz= 1.8 mm
The previous Bz profile
The new Bz profile

## Slide 18
  Bunch intensity control & diagnostics via ICS in the FCC main ring
Work in progress
﻿﻿ Improve the IP of LASER VS e-/e+ beams inside the bending magnet.
﻿﻿Find the optimum between bunch charge reduction VS emit. degradation.
﻿﻿ e-/e+ energy optimization exploiting the IP within a dispersion region
﻿﻿ Beam halo reducing exploiting Donuts-shaped laser beam. In proposal experiment @ FACET-II (SLAC)
Use high-energy scattered photons (25 & 150 GeV) paving the way for new discoveries as the Primakoff production of pseudoscalar particles,. Collaboration with FTX group, LUXE experiment @ DESY.
ICS can equalize the charge of colliding beams avoiding the Flip-Flop instability.
Several % of bunch charge can be removed in the first 400 beam ring loops.
18
ICS = Inverse Compton Scattering
Illya Drebot

## Slide 19
Optimization achieved:
  We believe, we have pushed our optimizations close to the maximum achievable limits (FF saturated). The method can be still applied to different layouts.
  There is under study with IJCLab a comparison between AI GA methods with AI ML Bayesian methods.
The Buncher capability:
  The use of a buncher is promising to enhance the capture, still in the early stages. We used a 50 mm iris with a gradient of 15 MV/m. Still in realistic feasibility study, including integration with magnetic devices, are still missing.
Planning optimization test of the crystal target at P3 (PSI): crystal target conceptual design in an HTS-based configuration (within the FCC-ee injector collaboration and with Ferrara-INFN group)
Genetic Optimizer in Control System: A genetic optimizer will eventually be integrated directly into the control system for real-time machine optimization, as currently implemented in the STAR project at the University of Calabria.
  Conclusions
19