## Slide 1
S5-like Demo Cell
Update on Solenoid Design
Mattia Castoldi, Lucio Rossi, Giuseppe Scarantino, Marco Statera
11/October/2024
MuCol-WP8 integration meeting

## Slide 2
Outline
MuCol Deliverable Report D8.1 solenoid data
Study of the engineering limits of D8.1 configuration
Solenoids design optimization strategy
Minimum focusing strength error configuration analysis
Mechanical analyses: stand-alone and lattice operational modes
Reduced-current configuration analysis

## Slide 3
S5 demo cell analysis: MuCol Deliverable Report D8.1
Beam optic studies on S5 cell assumed ideal solenoids and dipoles.
Results presented in the Deliverable Report D8.1.
An engineering design of the stage magnets is needed.
field profile on axis
profile on axis

## Slide 4
S5 demo cell: magnets design
Design for the target field required by the optics.
Magnets must be optimized starting from the proposed solenoid configuration.
Motivation: excessive peak field values on the coil section.
MuCol deliverable report D8.1 parameters
*Same solenoid shifted to larger radius, increasing current to keep same profile
Excessive field at the coil section!!
Geometrical radial constraints not satisfied*.
(RF cavity aperture, cryostat thickness, dipole radial thickness)

## Slide 5
MuCol D8.1 Report configuration: excessive stresses
The engineering limits were investigated on the S5 cell solenoid parameters reported in the MuCol Deliverable Report D8.1.
Limit for a feasible solenoid design:
Minimum Current Margin: 15.3%
MuCol deliverable report D8.1 parameters
Max Hoop Stress: 1.2 GPa
Stresses are the limit!

## Slide 6
Solenoids optimization strategy: lattice configuration
Divide the coil section in two to reduce the peak field and optimize their shape to produce the same target field.
Parametric sweep of the coil geometrical parameters: combinations.
2
1
z1
λ
w1
w2
t2
t1
z
Coil scheme & geom. parameters considered:
Cell mid-plane
Begin of the cell
Nota Bene:
Periodicity accounted in the stage modelling.
Symmetry condition on the cell mid-plane

## Slide 7
Constraints
Constraints: ” “
Coil
z
Internal (minimum) radius solenoid
15 mm
10 mm
40 mm
Gap for thermal insulation and mechanics (coil-external boundary)
Inner mechanics of the solenoid
250 mm
800 mm
275 mm
Inner radius of the dipole
Dipole overall thickness
Gap for waveguide
Other constraint:
Aspect ratio of the coil section:
1/3 < wx/tx < 3
Dipole
Coil subdivision
220 mm
Inner radius of the cryostat
(30 + 250 + 30) mm
Value updated to 200mm in WP8 meeting #22

## Slide 8
Optimization targets
The search of the optimal solenoid configuration should target the following:
  Minimum peak field on the coil section.
  Minimum RMS error of the axial field w.r.t. the target field expansion.
  Minimum error on the focusing strength on the cell length (integral of along the cell axis).
  From results considerations: maximum B2 field harmonic component.
2 configuration found:
Minimum RMSE.
Optimized: lower peak field.
+1%
-1%
Focusing Strength error within 1%
Each point corresponds to a unique combination of the geometrical parameters
RMSE=0.554T
RMSE=0.325T

## Slide 9
Results
Lower peak field configuration: RMSE = 0.554 T.
Peak field still high, but improved w.r.t. single coil stack (>40T)!
Computed field disaligned w.r.t. the target…
N.B:
6D stage lattice considered!
Coil Parameters | 
Current Margin [%] | 30.9
Minimum Critical current [A] | 582
Temperature Margin [K] | 27.2
Total magnetic energy in cell [MJ] | 47.4

## Slide 10
Mechanical Analysis: No prestress, no radial constraints
Mechanical analysis of the free-expanding coils.
Limiting hoop stress values!
Resulting force on the coils points towards the center of the cell (attractive force).
No radial constraints applied.
The coils are not self-sustaining
Coil Axial Forces:
Coil A: 47.5 MN
Coil B: -119 MN
Net Force:
-71.5 MN
N.B:
6D stage lattice considered!
>> Limit value of 0.3 %
Coil B
Coil A
Hoop Stress [MPa]
Hoop Strain [%]
Axial Stress [MPa]

## Slide 11
Prestress Study: Pressure on free boundary (I)
7.8 MN
39 MN
160 MPa
51 MPa
Free radial expansion, pre-stress added as an external uniform pressure acting on the plane.
Parametric sweep of the applied force on the boundary stopped when hoop stress started to get negative values. Last step: 39 MN on Coil1, 7.8 MN on Coil2.
Max hoop stress still >700 MPa . Max hoop strain 0.5% > limit hoop strain!
First approach: avoid negative hoop stress values!
N.B: 6D stage lattice considered!

## Slide 12
Prestress Study: Pressure on free boundary (I)
Free radial expansion, pre-stress added as an external uniform pressure acting on the plane.
Parametric sweep of the applied force on the boundary stopped when hoop stress started to get negative values. Last step: 39 MN on Coil1, 7.8 MN on Coil2.
Max hoop stress still >700 MPa . Max hoop strain 0.5% > limit hoop strain!
First approach: avoid negative hoop stress values!
N.B: 6D stage lattice considered!
Max hoop strain > 0.3 %...

## Slide 13
Prestress Study: Pressure on free boundary (II)
27.5 MN
55 MN
225 MPa
180 MPa
Free radial expansion, pre-stress added as an external uniform pressure acting on the plane.
Parametric sweep of the applied force on the boundary stopped when hoop strain < 0.3% reached... BUT negative hoop stress. Last step: 55 MN on Coil1, 27.5 MN on Coil2.
Max hoop stress 393 MPa / -269 MPa. Max hoop strain 0.28% < limit hoop strain!
Approach: hoop strain < 0.3% !!
N.B: 6D stage lattice considered!
\

## Slide 14
Prestress Study: Pressure on free boundary (II)
Free radial expansion, pre-stress added as an external uniform pressure acting on the plane.
Parametric sweep of the applied force on the boundary stopped when hoop strain < 0.3% reached... BUT negative hoop stress. Last step: 55 MN on Coil1, 27.5 MN on Coil2.
Max hoop stress 393 MPa / -269 MPa. Max hoop strain 0.28% < limit hoop strain!
Approach: hoop strain < 0.3% !!
N.B: 6D stage lattice considered!
\
Max hoop strain < 0.3 % !!

## Slide 15
Mechanical Analysis:stand-alone demonstrator
Results for the stand-alone demonstrator stage.
This case is representative of the steady-state condition on an S5 stage following a fault shutdown on subsequent stages.
Test: no prestress, no radial constraints.
Applied prestress needs to be increased:
Apply 85 MN on Coil1 and 51 MN on Coil2 to have a peak hoop strain value of 0.29%. Still negative hoop stress regions.
Peak field increased to 30 T

## Slide 16
Mechanical Analysis:stand-alone demonstrator
Results for the stand-alone demonstrator stage.
This case is representative of the steady-state condition on an S5 stage following a fault shutdown on subsequent stages.
Test: no prestress, no radial constraints.
Applied prestress needs to be increased:
Apply 85 MN on Coil1 and 51 MN on Coil2 to have a peak hoop strain value of 0.29%. Still negative hoop stress regions.

## Slide 17
Reduced-current solenoid for first integration excercise
Considering the required field targets, the proposed solenoid configuration still does not respect the mechanical limits of HTS-based coils.
A reduced-current configuration has been studied: (25% reduction).
The magnet design and cell integration has been conducted on this configuration. The displayed results does not meet the requested field targets on the beam axis.
Both configurations (stand-alone, lattice) has been considered in the mechanical design.
Two separated AISI 316LN steel restraining collars has been added: in case of stand-alone stage operation, the coil-structure deformation will be contained by the most external SS ring.
R
Z
Coils
Cu collars
SS restraining cylinders
Reduced peak field on axis: 6.5 T.

## Slide 18
Reduced-current solenoid for first integration excercise
Considering the required field targets, the proposed solenoid configuration still does not respect the mechanical limits of HTS-based coils.
A reduced-current configuration has been studied: (25% reduction).
The magnet design and cell integration has been conducted on this configuration. The displayed results does not meet the requested field targets on the beam axis.
Both configurations (stand-alone, lattice) has been considered in the mechanical design.
Reduced peak field on axis: 6.5 T.
Figures of Merit | Value
RMS difference [T] | 1.67
Reduction on Integral along the axis [%] | 47.03
Figures of Merit | Value
RMS difference [T] | 1.67
 | 47.03

## Slide 19
Reduced-current solenoid design: lattice operation (I)
The mechanical design of the S5-like solenoids converged to a 25% reduced current configuration.
To limit the stresses in the solenoids in lattice operation, SS collars must be fit on the 10 mm Cu rings containing the coils. A 50 mm SS collar is needed for coil A, 25 mm SS collar for coil B.
A 0.8 mm interference between the two collars is required to contain the stresses in a self-sustaining coil configuration.
Coil stress components: lattice configuration
Coil A
Coil B
Stresses are within the mechanical limits!

## Slide 20
Reduced-current solenoid design: lattice operation (II)
The Von Mises stress was assessed in the Cu collars and SS restraining rings.
The resulting stresses are compatible with the elastic limits of the materials considered.
The total radial displacement is needed to determine the radial gap with the external SS ring required for the stand-alone cell operation.
Cu collars
SS restraining rings
Total displacement
Stresses are within the mechanical limits!

## Slide 21
Reduced-current design: stand-alone operation (I)
The load conditions in the stand-alone cell operation are remarkably different to the analyzed lattice configuration.
To limit the stresses in stand-alone operation, additional SS collars must be fit on the coils structure. Addittional 50 mm SS collar is needed for coil A, 75 mm SS collar for coil B.
A 0.8 mm interference between the two collars is assumed.
Coil stress components: lattice configuration
Coil A
Coil B
Stresses are within the mechanical limits!

## Slide 22
Reduced-current design: stand-alone operation (II)
The Von Mises stress was assessed in the Cu collars and SS restraining rings.
The resulting stresses are compatible with the elastic limits of the materials considered.
The total radial displacement has been assessed on the structure.
Cu collars
SS restraining rings
Total displacement
Stresses are within the mechanical limits!

## Slide 23
Reduced-current design: support structure design
The coil support structure has been designed to sustain the coil axial forces in the two configurations: stand-alone, lattice.
Thick AISI 316LN shell is needed to sustain the axial forces in normal out-of-cell direction.
Even in the reduced-current configuration, the mechanical design of the support structure is not trivial.
Coil Axial Forces | Coil A/Coil B Value [MN] | Net Force Value [MN]
Lattice configuration | -27 / +67 | +50
Stand-alone configuration | -55 / +35 | -20
Stand-alone configuration: Von Mises Stress [Mpa]
Lattice configuration: Von Mises Stress [Mpa]
z
positive force (cell center)
negative force (outward cell direction)
Coil A
Coil B

## Slide 24
Summary and next steps
The magnet design for the S5-like demonstrator cell looks challenging, in particular from a mechanical point of view.
The search for an optimized solenoid configuration, respecting the required focusing strength, converged to the two-coil-subdivision configuration presented.
The mechanical limits of the materials constituting the assembly are not respected, thus a reduced-current configuration has been studied.
A 25% coil current reduction (from to ) decrease the coil stresses within their mechanical limits: a collar and support structure design has been proposed.
The support structure design still presents criticalities to be solved, the stresses appear excessive, requiring 60 mm Inconel bolts and a thick shell (with associated increased cost and manufacturing complications…).
Further iterations are needed, both on the magnets design and on the cell integration study!

## Slide 25
Thank you for your attention!