## Slide 1
Въведение във физиката на детектори на елементарни частици

## Slide 2
Формиране на сигнал
Всяка заредена частица, преминаваща през среда, оставя след себе си възбудени атоми, двойки електрон-йон (в газови среди) или двойки дупка-елетрон (в твърди тела).
Възбуждане:
Фотоните излъчени от възбудени атоми в прозрачна среда могат да бъдат детектирани посредством полупроводникови фотонни детектори или фотоумножители.
Йонизация:
Прилагайки електрично поле в обема на детектора, електроните и йоните произведени в процеса на йонизация се движат разнопосочно и индуцират сигнал върху металните електроди. Тези сигнали се четат от подходяща предна електроника.

## Slide 3
Детектори, регистриращи възбудени атоми  Сцинтилатори

## Slide 4
Фотоните се рефлектират към краищата на сцинтилатора.
Световоди отвеждат фотоните към фотоумножителите, където фотоните се конвертират в електрически сигнал.
Поради отличната разделителна способност по време (<1ns) времето на пристигане, или времето за прелитане, могат да бъдат измерени много прецизно  Тригер, Time of Flight.
Сцинтилатори
Сцинтилатор
ФЕУ
Световод

## Slide 5
Typical Geometries:
UV light enters the WLS material
Light is transformed into longer wavelength
Total internal reflection inside the WLS material
‘transport’ of the light to the photo detector
Сцинтилатори

## Slide 6
Сцинтилаторите се използват масово поради:
  Добре формиран и бърз отговор  1 до 100ns
Основни характеристики на ФЕУ:
Умножение (зависи от приложеното напрежение): 108 to 1010
Ефективност за детектиране на фотони: < 20%
For very good PMs: registration of single photons possible.
Пример: 10 първични електрона, Умножение 107 108 електрона накрая за време  10ns, I=Q/T = 108*1.603*10-19/10*10-9= 1.6mA.
Пад върху 50  съпротивление  U=R*I= 80mV.
e-
g
стъкло
PC
Полупрозрачен фотокатод
Фотоумножители

## Slide 7
Формиране на сигнал
Всяка заредена частица, преминаваща през среда, оставя след себе си възбудени атоми, двойки електрон-йон (в газови среди) или двойки дупка-елетрон (в твърди тела).
Възбуждане:
Фотоните излъчени от възбудени атоми в прозрачна среда могат да бъдат детектирани посредством полупроводникови фотонни детектори или фотоумножители.
Йонизация:
Прилагайки електрично поле в обема на детектора, електроните и йоните произведени в процеса на йонизация се движат разнопосочно и индуцират сигнал върху металните електроди. Тези сигнали се четат от подходяща предна електроника.

## Slide 8
q
q
A point charge q at a distance z0
Above a grounded metal plate ‘induces’ a surface charge.
The total induced charge on the surface is –q.
Different positions of the charge result in different charge distributions.
The total induced charge stays –q.
-q
-q
The electric field of the charge must be calculated with the boundary condition that the potential φ=0 at z=0.
For this specific geometry the method of images can be used. A point charge –q at distance –z0 satisfies the boundary condition  electric field.
The resulting charge density is
(x,y) = 0 Ez(x,y)
(x,y)dxdy = -q
I=0
Principle of Signal Induction by Moving Charges

## Slide 9
q
If we segment the grounded metal plate and if we ground the individual strips the surface charge density doesn’t change with respect to the continuous metal plate.
-q
-q
V
I1(t) I2(t) I3(t) I4(t)
The charge induced on the individual strips is now depending on the position z0 of the charge.
If the charge is moving there are currents flowing between the strips and ground.
 The movement of the charge induces a current.
Principle of Signal Induction by Moving Charges

## Slide 10
Детектори, работещи на базата на йонизация
Газови детектори:
  Нишкови камери (Wire Chambers)
  Дрейфови камери (Drift Chambers)
  Време-проекционни камери (Time Projection Chambers)
Твърдотелни детектори:
  Транспорт на електрони и дупки в твърди тела
  Силициеви детектори (Si- Detectors)

## Slide 11
Gas Detectors with internal Electron Multiplication
E
Ions
Electrons
Principle: At sufficiently high electric fields (100kV/cm) the electrons gain energy more than the ionization energy  secondary ionization etc. etc.
  dN = N α dx α…Townsend Coefficient
  N(x) = N0 exp (αx) N/ N0 = A (Amplification, Gas Gain)
  Avalanche in a homogeneous field:
  Problem: High field on electrode surface
   breakdown
  In an inhomogeneous Field: α(E)  N(x) = N0 exp [∫α(E(x’))dx’]

## Slide 12
Wire Chamber: Electron Avalanche
Electric field close to a thin wire (100-300kV/cm). E.g. V0=1000V, a=10m, b=10mm, E(a)=150kV/cm
Electric field is sufficient to accelerate electrons to energies which are sufficient to produce secondary ionization  electron avalanche  signal.
Wire with radius (10-25m) in a tube of radius b (1-3cm):
b
b
a
Wire

## Slide 13
Multi Wire Proportional Chamber
Classic geometry (Crossection), Charpak 1968 :
One plane of thin sense wires is placed between two parallel plates.
Typical dimensions:
Wire distance 2-5mm, distance between cathode planes ~10mm.
Electrons (v5cm/s) are collected within  100ns. The ion tail can be eliminated by electronics filters  pulses of <100ns length.
For 10% occupancy  every s one pulse
 1MHz/wire rate capabiliy !
 Compare to Bubble Chamber with 10 Hz !

## Slide 14
In order to eliminate the left/right ambiguities: Shift two wire chambers by half the wire pitch.
For second coordinate:
Another chamber at 900 relative rotation
Signal propagation to the two ends of the wire.
Pulse height measurement on both ends of the wire. Because of resisitvity of the wire, both ends see different charge.
Segmenting of the cathode into strips or pads:
The movement of the charges induces a signal on the wire AND on the cathode. By segmentation of the cathode plane and charge interpolation, resolutions of 50m can be achieved.
Multi Wire Proportional Chamber

## Slide 15
Cathode strip:
Width (1) of the charge distribution  distance between Wires and cathode plane.
‘Center of gravity’ defines the particle trajectory.
Avalanche
Multi Wire Proportional Chamber

## Slide 16
Drift Chambers
In an alternating sequence of wires with different potentials one finds an electric field between the ‘sense wires’ and ‘field wires’.
The electrons are moving to the sense wires and produce an avalanche which induces a signal that is read out by electronics.
The time between the passage of the particle and the arrival of the electrons at the wire is measured.
The drift time T is a measure of the position of the particle !
By measuring the drift time, the wire distance can be increased (compared to the Multi Wire Proportional Chamber)  save electronics channels !
E
Scintillator: t=0
Amplifier: t=T

## Slide 17
Electric Field  1kV/cm
Drift Chambers, typical Geometries
U.Becker Instr. of HEP, Vol#9, p516 World Scientific (1992) ed F.Sauli

## Slide 18
y
z
x
E
B
drift
charged track
Wire Chamber to detect the tracks
gas volume
Time Projection Chamber (TPC):
Gas volume with parallel E and B Field.
B for momentum measurement. Positive effect: Diffusion is strongly reduced by E//B (up to a factor 5).
Drift Fields 100-400V/cm. Drift times 10-100 s.
Distance up to 2.5m !

## Slide 19
STAR TPC (BNL)
Event display of a Au Au collision at CM energy of 130 GeV/n.
Typically around 200 tracks per event.
Great advantage of a TPC: The only material that is in the way of the particles is gas  very low multiple scattering  very good momentum resolution down to low momenta !

## Slide 20
Gas Ne/ CO2 90/10%
Field 400V/cm
Gas gain >104
Position resolution s= 0.25mm
Diffusion: st= 250mm
Pads inside: 4x7.5mm
Pads outside: 6x15mm
B-field: 0.5T
Largest TPC:
  Length 5m
  Diameter 5m
  Volume 88m3
  Detector area 32m2
  Channels ~570 000
ALICE TPC: Detector Parameters

## Slide 21
TPC installed in the ALICE Experiment

## Slide 22
First 7 TeV p-p Collisions in the ALICE TPC in March 2010 !

## Slide 23
First Pb Pb Collisions in the ALICE TPC in Nov 2010 !

## Slide 24
GEMs & MICROMEGAS
GEM
Thin metal-coated polymer foils
70 µm holes at 140 mm pitch
F. Sauli, Nucl. Instr. and Methods A386(1997)531
MICROMEGAS
Narrow gap (50-100 µm) PPC with thin cathode mesh
Insulating gap-restoring wires or pillars
Y. Giomataris et al, Nucl. Instr. and Meth. A376(1996)239

## Slide 25
Detectors based on Ionization
Gas detectors:
  Wire Chambers
  Drift Chambers
  Time Projection Chambers
  Transport of Electrons and Ions in Gases
Solid State Detectors
  Transport of Electrons and Holes in Solids
  Si- Detectors
  Diamond Detectors

## Slide 26
Silicon Detector
Velocity:
μe=1450 cm2/Vs, μh=505 cm2/Vs, 3.63eV per e-h pair.
~33000 e/h pairs in 300μm of silicon.
However: Free charge carriers in Si:
T=300 K: e,h = 1.45 x 1010 / cm3 but only 33000 e/h pairs in 300m produced by a high energy particle.
Why can we use Si as a solid state detector ???

## Slide 27
doping
p
n
Doping of Silicon
In a silicon crystal at a given temperature the number of electrons in the conduction band is equal to the number of holes in the valence band.
Doping Silicon with Arsen (+5) it becomes and n-type conductor (more electrons than holes).
Doping Silicon with Boron (+3) it becomes a p-type conductor (more holes than electrons).
Bringing p and n in contact makes a diode.

## Slide 28
At the p-n junction the charges are depleted and a zone free of charge carriers is established.
By applying a voltage, the depletion zone can be extended to the entire diode  highly insulating layer.
An ionizing particle produces free charge carriers in the diode, which drift in the electric field and induce an electrical signal on the metal electrodes.
As silicon is the most commonly used material in the electronics industry, it has one big advantage with respect to other materials, namely highly developed technology.
Si-Diode used as a Particle Detector !

## Slide 29
Zone without free charge carriers positively charged.
Sensitive Detector Volume.
Under-Depleted Silicon Detector
n
p
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
+
-
Zone with free electrons. Conductive.
Insensitive to particles.
Electric Field

## Slide 30
Zone without free charge carriers positively charged.
Sensitive Detector Volume.
Fully-Depleted Silicon Detector
n
p
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
+
-
Electric Field
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 31
300mm
SiO2
passivation
readout capacitances
ca. 50-150 mm
Silicon Detector
Fully depleted zone
N (e-h) = 11 000/100μm
Position Resolution down to ~ 5μm !

## Slide 32
Silicon Detector
Every electrode is connected to an amplifier 
Highly integrated readout electronics.
Two dimensional readout is possible.
CMS Outer Barrel Module

## Slide 34
CMS Tracker

## Slide 35
Z2 electrons, q=-e0
Interaction with the atomic electrons. The incoming particle loses energy, and the atoms are excited or ionized.
Interaction with the atomic nucleus. The particle is deflected (scattered) causing multiple scattering of the particle in the material. During this scattering a Bremsstrahlung photon can be emitted.
In case the particle’s velocity is larger than the velocity of light in the medium, the resulting EM shockwave manifests itself as Cherenkov Radiation. When the particle crosses the boundary between two media, there is a probability of the order of 1% to produced and X ray photon, called Transition radiation.
Electromagnetic Interaction of Particles with Matter
M, q=Z1 e0

## Slide 36
Ускорител на заредени частици - в нашия случай протони
Сблъскване на частици - енергия на взаимодействието:
  Е = Е(сноп 1)+ Е(сноп 2)
Най-висока енергия на сблъсъците на LHC досега:
  Е = 13 [TeV] = 2 x 6.5 [TeV] (2015 - 2018 г.)
Проектна енергия на LHC:
  Е = 14 TeV
Връзка (превръщане) между енергия и маса: E = mc2
При сблъсъка на сноповете от протони се раждат много нови частици.
По-тежките частици са нестабилни и се разпадат бързо до по-леки частици, които можем да измерим.
Детектори на Големия адронен ускорител на насрещни снопове

## Slide 37: Експериментът CMS

## Slide 38
Експериментът CMS (Run1&2)
(Компактен мюонен соленоид)
Соленоидален магнит
Суперпроводяща намотка
Магнитно поле: 3.8 Т във вътрешността, затворена от магнита
~1.8 T извън магнита
Електромагнитен калориметър
Кристали от оловен волфрамат
Адронен калориметър -
тип сандвич
Стомана(в централната част)
или месинг(в затварящите части)
и пластмасови сцинтилатори
Железен хамут на детектора;
През неге се затварят магнитните силови линии.
Вътрешен треков детектор – две основни системи: Силициев пикселов детектор
Силициев микрострипов детектор
Мюонна система - централна част: Камери с дреифови тръби (DT)
Камери със съпротивителна плоскост (RPC)
Мюонна система –
затварящи части:
Катодни стрипови
камери (CSC)
Камери със
съпротивителна
плоскост (RPC)
Тегло 12.5 t
Диаметър 15 m
Дължина 21.6 m

## Slide 39: Движение на заредена частица в магнитно поле
S
N
Соленоидално магнитно поле
Траекторията на заредена частица се закривява в магнитно поле.
Ако гледаме срещу посоката на магнитното поле,
положително заредените частици ще се отклоняват по посока на часовниковата стрелка,
а отрицателно заредените в обратна посока.
В приложението iSpyWebGl, посоката на магнитното поле във вътрешността на магнита е по посока на оста Z. В основния xy изглед, оста z е насочена към наблюдателя.

## Slide 40: Определяне на импулс и заряд - Вътрешен треков детектор
Сигналите от вътрешния треков детектор, позволяват да се реконструират техните траектории. Големината на закривяване на техните траектории позволяват определянето на техния импулс по формулата r ~ p/B, където r [m] е радиусът на кривината, p [GeV/c] – импулсът на електрона, а B [T] е магнитното поле.

## Slide 41: Определяне на импулс и заряд - Вътрешен треков детектор
http://cms.cern/detector/identifying-tracks

## Slide 42: Измерване на енергия - калориметрична система

## Slide 43: Детектиране на електрони, позитрони и фотони Електромагнитна лавина във вещество
Два процеса на загуба на енергия в плътна среда за е± с Е>1GeV или фотони:
излъчване на фотон от заредена частица (примерно е+ или е-) при движение в полето на ядро от средата
раждане на е+е- двойки от фотон, в полето на ядро от средата
Кристал от оловен волфрамат и лавинни фотодиоди, използвани в ECAL на CMS
Енергията на частицата, инициирала лавината е пропорционална на броя изсветени фотони

## Slide 44
ECAL - електромагнитен калориметър на CMS
(в ляво)
HCAL - адронен калориметър на CMS
(в дясно)

## Slide 45: Калориметрична система ектромагнитен (ECAL) и адронен калориметър (HCAL)

## Slide 46: Мюонна система на CMS (Run1 & Run2)

## Slide 47: Мюонна система на CMS (Run1 & Run2)
DT (Камери с дрейфови тръби)
CSC (Катодно стрипови камери)
RPC (Камери със съпротивителна плоскост)

## Slide 48
https://cms.cern/detector/detecting-muons

## Slide 50: Как се регистрира частици със CMS
Силициев детектор:
  Регистрира попадения на електрически заредени частици.
Електромагнитен калориметър:
  Регистрира електрони, позитрони и фотони
  Те отлагат пълната си енергия в него
Адронен калориметър
  Регистрира адрони, които отлагат пълната си енергия в него
Мюонна система:
  Регистрира електрически заредени частици, преминали през всички останали системи и магнита.
  Ние предполагаме, че такива могат да бъдат само мюоните.
Комбинираме информацията от отделните детекторни системи!

## Slide 51: Липсваща енергия
Частици, които не могат да бъдат регистрирани с нашия детектор
  Неутрино - трябва ни много по-голям детектор
  Частици, които не познаваме
Но ние може да направим оценка какво количество енергия или импулс са отнесли тези частици!
Величината, който ще използваме в нашия анализ се нарича Missing Energy и съдържа в себе си сумата от енергиите, отнесени от всички частици, които не сме успели да регистрираме и измерим.
А също и информация за посоката, в която е отнесена тази енергия.
Забележете, липсващата енергия може да е отнесена от повече от една частица!

## Slide 52
Благодаря за вниманието!