## Slide 1: How do we manage 40K machines in the CERN Computer centre
Zhechka Toteva (CERN/IT)
CERN – 18/09/2025

## Slide 2: Outline
CERN Computer Centre (CC) in numbers
Overview of the CERN network and data storage
Overview of electricity and cooling
WLCG is couple of numbers
Configuration management at CERN IT
CERNMegabus@CERN
  Architecture
  Overview of major implemented use cases
  CERN Computer Centre (CC) power cut management

## Slide 3: CERN Computer Centre (CC) in numbers

## Slide 4: Computing network
250 routers, 4100 switches, 1200 Wi-Fi points
35 000 km optical fibre (only ~5 000 less than the equator length)
Wigner Data centre in Hungary
  1200 km distance
  with three 100 Gb/s

## Slide 5: Data storage
50 Pbytes / year from LHC
  + 25 Pbytes / year from non-LHC experiments
RECORD: August 2018: 13.8 Pbytes of data written on tape (of which 11.56 is LHC data)
  More than 2 PB read/write daily
Tape drives faster than disks; but slower in mounting (latency)
  90 K disk drives (of which 10-15% are SSD, providing less than 10% capacity)
  SSDs are 5-10 times more expensive than spinning disks
www.cern.ch/eos
www.cern.ch/castor

## Slide 6
https://filer‐carbon.cern.ch/grafana/dashboard/db/castor‐dashboard?orgId=1

## Slide 8: Electricity and cooling
2.7 MW consumption (+ ~ 1 MW cooling) from maximum 3.5 MW
  480 KW diesel generators
Protected by UPS
  Enough to start the diesel generators
  Enough to shut down non-critical machines*
Cooling
  Chilled air via silver ducts enters the false floor and the into the closed server aisles
  Water-cooled racks in the vault in the basement

## Slide 9: WLCG – Worldwide LHC computing grid
More than 170 data centres in 42 countries with about 800,000 cpu cores
  CERN provides about 20% of the WLCG resources
  Allows more than 10,000 physicists to access LHC data
  >250,000 jobs run concurrently on the Grid
  Storage is about 400 PB disk and 400 PB of tape globally
  In 2016, global transfer rates have regularly exceeded 35GB/s
Key facts and numbers (http://information-technology.web.cern.ch)
www.cern.ch/wlcg
www.cern.ch/wlcg-public

## Slide 10: Configuration management at CERN IT
TEIGI Tool suite
43 000 Puppet managed machines
Certification Manager
AI-TOOLS
CERNMegabus
…

## Slide 11
Thanks Config team fro the slide

## Slide 12: CERNMegabus at CERN IT
CERNMegabus
The CERNMegabus architecture is based on the publisher-consumer model and utilises the CERN IT messaging infrastructure
The publisher and the consumer services comprises of building blocks
  configured with Puppet
  to use the CERNMegabus python libraries
Installed on all Puppet managed machines in the CERN CC
A service that provides for instant communication between services

## Slide 13: CERNMegabus architecture
The CERNMegabus architecture is based on the publisher-consumer model and utilises the CERN IT messaging infrastructure
Affected service “B”
External program
Central CERN IT ActiveMQ brokers
4. Execute reactive actions
Change service ”A”
1. Subscribe for message
2. Publish message
3. New message

## Slide 14: Already our clients
TEIGI Tool suite
(roger)
43 000 Puppet managed machines
CERNMegabus
CERN Computer Centre Power Cut Management
IT Monitoring
CASTOR
EOS
DNS Load Balancing
CLOUD
BATCH

## Slide 15: From roger to EOS/CASTOR/Puppet HAProxy
castor-lhcb-headnode-Y
Set castor-lhcb-disknode-X in read-only mode
Central CERN IT ActiveMQ brokers
4. Execute `modifydiskserver Disab castor-lhcb-disknode-X `
Set roger state of castor-lhcb-disknode-X to disabled
Subscribe for topic /topic/roger.**group.castor and hostgroup selector in message
2. Publish message to /topic/roger.**group.castor
3. Message de-queued
In practice - I
{"new": {"update_time": "1538633786", "updated_by": “blueuser", "hostname": “castor-lhcb-disknode-X", …, "appstate": "disabled"}, "old": {"update_time": "1538633774", "updated_by": “somebody", "hostname": "castor-lhcb-disknode-X “, …, "appstate": “production"}
hostgroup header: `castor-lhcb-diskservers`
~1 sec

## Slide 16: CERN CC Power Cut event
Electrical grid
UPS
~ 20 min
Power back
t
1. Preserve data
Shutdown
(all machines which we can)

## Slide 17: CERN CC Power cut event detection
ccpcoX programmatically detects power cut/power back event

## Slide 18: UPS and PLC

## Slide 19: CERN CC Power cut event detection algorithm
UPS 1
PLC
UPS 2
UPS 3
UPS 4
UPS 5
Modbus
0
1 0
1
1
1
0
01
0
1
0
1
..
Data collection
module1
module5
module2
...
...
...
...
...
Decision making algorithm

## Slide 20: CERN CC Power cut tests
During mid-annual power cut test on the 2nd of July, 2018
  Detected power cut
  Notified the subscribed machines
  Shutdown the machines, which had been predefined to be shutdown
  Detected the power back
  Notified the machines, which had been predefined to wait
Presented at CHEP’18

## Slide 21: From CERN CC UPS PLC to CERN CC shutdown
Any Puppet managed machine in CC*
Log power cut events in /var/log/powercut.log
Central CERN IT ActiveMQ brokers
4. Execute
`std_log --path=XYZ`
ccpcoX programmatically detects power cut/back event
1. /topic/ccco.notif
2. Publish message to /topic/ccco.notif
3. Message de-queued
In practice - IV
message = {'powercut_now': True, 'elapsed_time': 0, 'simulation': False}
~2 min*
2 mins after detection!

## Slide 22: Thanks
THANKS for listening and ENJOY your visit at CERN
Zhechka