## Slide 1
Overview of the LHC performance in Run 3
Major LHC events and performance in 2023 and 2024
Prospects for 2025 & 2026
Status of HL-LHC preparation
Reyes Alemany Fernandez, CERN
Beams department – Accelerator and Beam Physics group

## Slide 2: LHC in 2023
21.04.2023
1st stable beam of 2023
Mar-Apr
Jun-Jul
May
Aug-Sep
Oct-Nov
31.08.2023 (B)
08.09.2023 (A)
2 x injection protection device (TDIS) vacuum leak.
Stop p+ operation!
26.09.2023: 1st stable Pb ion beam
End Sep – Early Oct
ALICE background issue followed by studies and solution
October
Beam loss induced SEU causing trips, quenches, etc.
Studies, Lumi levelling
25.05.2023
RF finger module issue.
Intensity limited to 1.6x1011 p+/b
~4 days downtime
17.07.2023
Fallen tree in VD causing power glitch, magnet quench, and leaking bellow between cold mass and insulation vacuum
~50 days of downtime
12.05.2023
1st collisions 2374 bunches

## Slide 3: LHC RF Finger Module Issue
Vacuum pressure
2023: Pressure spikes within the vacuum sector A4L1 during the fill ID 8828 (1.63⋅1011 p/b – 2358 bunches)  beam dumped during the ramp (BLM)
Beam intensity
Bunch length
Beam energy
VGI.628.4L1.X.PR
~ 4 days of downtime for repair
Total number of modules present in LHC = 1819
Inspections in 2023 of 212 mm type revealed 8 degraded modules
Full replacement in 2023 not possible
Replacement strategy staged in YETS23-24 (47/71) and YETS24-25
Signs of overheating
Visual inspection  annealed/plasticized spring on the 212 mm vacuum module due to localized temperature increase to more than 500°C
RF fingers
Spring is damaged where RF fingers separation is non-conform
Mitigation for 2023 & 2024:
Bunch intensity limited to 1.6⋅1011 p+
Bunch length kept above 1.2 ns
25.05.2023
YETS: Year End Technical Stop
Pressure (mb)
10-11
10-7

## Slide 4: LHC Inner Triplet (IT) Bellow Leak
Magnet Quench due to electrical perturbation
  ‘Normal’ high pressures in the He lines during the magnet quench created a small hole (1 mm2) in an edge welded bellow (non-conform) with major consequences (vacuum vessel pressure degraded and below reparation)
Quick repair in-situ with partial cryogenic warm-up
~50 days of downtime
Similar events possible on triplets and mainly in Q1-Q2 interconnection until LS3
Inspection not possible without warm-up
But warm-up poses a significant risk due to a thermal cycle of irradiated triplets
IT.L8
Consolidation of IP2 and IP8 IT proposed in LS3
(IP1 and IP5 replaced by HL-LHC upgrade)
17.07.2023

## Slide 5: LHC TDIS (Target Dump Injection Segment)
Machine protection devices used during injection – regularly moving in and out
  Located in front of IP2 (ALICE) for beam 1 and IP8 (LHCb) for beam 2
  Each TDIS contains 3 modules with 12 edge welded bellows per TDIS
Two leaks appeared on separate bellows of the same TDIS (IP8) within 1 week
  Both varnished and blocked in out position
Root cause: misspecification of the bellow, causing wear-out after 2-3 years
Intensity per injection severely limited  End of high-intensity p+ physics Ion run extended p-p reference run moved to 2024
Module A
Module B
Module C
beam
Bellows
Mitigation:
Both TDIS replaced by (non-conform) spares during YETS23-24 (expected life-cycle covers the year of operation)
YETS24-25 replace by conform spares (based on refurbished TDIS with new bellows)
31.08.2023 (B)
08.09.2023 (A)
(E)YETS: (Extended) Year End Technical Stop

## Slide 6: Other limitations in Run 3 that require LHC parameters and configuration optimization
Electron cloud and cryogenics load  limits bunch pattern
Radiation to inner triplets  change of optics
LIMITATIONS

## Slide 7: Electron cloud and cryogenics load
Synchrotron radiation
SEY > 1!!
e- accelerated by the intense e.m. field of the next p+ bunch
Cascade effect
Heat load  at the limit of cryogenic system
Pressure rise
Beam instabilities
Emittance growth
The additional 10% scrubbing leaves room to increase the number of bunches and bunch intensity:
  2400 bunches with 1.8e11 p+/b with trains of 4-5x36b in reach
SEY: Secondary Emission Yield
Heat load evolution in 2024
LHC sector
~10% heat load reduction between Apr & Sep!
SEY: Secondary Electron Yield
hc: LHC half-cell ~53 m
Under the eﬀect of the cloud itself, conditioning of the copper surface of the LHC beam pipes is expected, decreasing thus the SEY of the surface. Such a process seems therefore to be hindered in some parts of the LHC ring.

## Slide 8: Ensuring the Longevity of the IT until LS3
The problem: collision debris (mainly pions) capture in the IT
IT: Inner Triplet
IR: Insertion Region, IP: Interaction Point
RP: Reverted Polarity
IT R1
The consequence: reduced lifetime of magnets  change needed before LS3
The mitigation: from nominal (FDF) to Reverse Polarity (DFD) optics
Main drawback: risk of radiation damage for the first module of D1 of both sides of IP1
Exchange with spare should be considered for the YETS25-26
Moderate risk for 2025: Replacement of a spare →7 weeks of work in the tunnel Possibility to run with the first D1 module disconnected (~1 shift of work in the tunnel), increasing the strength of the remaining 5 modules (per IP side) and the MCBHX3
IR5: Nom-H
IR5: RP-V
Mitigation in 2025: IP5 RP-V, IP1 Nom-V, Xang rot IP1&5)
D1: separation dipole
FDF: Focusing Defocusing Focusing
DFD: Defocusing Focusing Defocusing
p-p @√s=14 TeV
85 mb inel xs
Mitigation applied in 2024 in IP1
IR1: Nom-V
IR1: RP-H
Distance from IP (m)
20
30
40
50
Peak dose (MGy)
20
30
40
Failure
Peak dose IP D1 (MGy)
20
60
40
80
100
120
140
Run 1
Run 2
Run 3
Integrated lumi (fb-1)
Moderate damage

## Slide 9: 2023 & 2024 LHC Performance
2023 summary:
  p+ period best availability 76%, stable beams for physics 52%
  Many long-term faults  target 75 fb-1/exp not reached
2024 summary:
  Highest production rate ever - up to 1.5 fb-1/24h
  Peak luminosity at ~2.1x1034 cm-1s-1
    Limited by cryogenic cooling capacity in the IT
2024

## Slide 10: The 2023 & 2024 ion runs

## Slide 11: 2023 LHC Lead Ion Run Performance
TCLD: Target Collimator Long Dispersion suppressor in IR7
BFPP: Bunch Free Pair Production
IR: Insertion Region
Ion run relied on several new concepts all successfully used in operation
  Slip-stacked 50 ns beams from injectors to provide higher intensity
  Crystal collimation to handle higher intensity without quenches
  TCLD collimators (HL-LHC equipment) & BFPP bump in IR2 to allow full luminosity for ALICE
  BFPP bump in IR8 to allow higher LHCb luminosity
Several problems encountered
  Background in ALICE experiment – mitigated in 2023
  High beam losses in the ramp – mitigated in 2024
  Beam losses due to 10 Hz orbit oscillation – culprit found and fixed!
  Single-event upsets on quench protection system – mitigated in 2024

## Slide 12: 2024 LHC Ion Run Performance
2024 Production
  ALICE, ATLAS, CMS: average 1.9 nb-1
  LHCb: doubled 2023 production in half the time  achieved!
2024
2023
IP1,2,5: Remains 1.45 nb-1 to be collected in 2025&2026
Experiments’ expectations for the full Run 3
  ATLAS/CMS/ALICE
    5.35 nb-1 for full Run3
  LHCb
    1 nb-1 but strong request for higher target (x2)
Excellent injectors performance:
Higher bunch intensities than LIU target
Higher transmission efficiencies than before
LIU: LHC Injectors Upgrade

## Slide 13: 2025 & 2026 schedules
18.09.2024 Research Board approved the update of Run3/LS3/Run4 schedule:
  Short YETS25-26 (08.12.2025 to 23.02.2026)
  Run LHC until end of June 2026 with Heavy Ion run taking place in June
  End of LHC Run 3 date on Monday 29th June 2026 (SPS North Area physics continues)
Run 3
LHC LS3(*)
LHC Run 4
(*) LS3 Injectors is shorter
2025 scheduled (approved)
138 days of p+ physics
2 days of Vdm
25 days Pb run end of 2025
NO pp ref run
O-O and p-O collisions last week of June
2026 scheduled (info)
66 days of p+ physics
2 days of Vdm
25 days Pb run in June (PbPb or pPb)
NO pp ref run
YETS: Year End Technical Stop
Vdm: Van der Meer scan for luminosity calibration

## Slide 14: Status of HL-LHC preparation

## Slide 15: HL-LHC parameters
2.3·1011 p+/bunch
2.1 μm ℇnx,y
25 ns bunch spacing
β*= 0.15 m (β*= 0.5 m @LHC)
Virtual peak lumi with crab 1.7·1035 cm-2s-1
LHC p+ Lumi Levelled @ 5·1034 cm-2s-1
Pile up = 131
LHC Injectors Upgrade
27 km
= 4.5 km
@IT
5 km
10 km
km
@IT
High gradient magnets:
Stronger focusing
Large aperture
Only possible with new technology
IP
IT
IT: Inner Triplet
IP: Interaction Point
LHC
HL-LHC

## Slide 16
HL-LHC parameters
But, larger beam size at the IT  larger crossing angle to avoid beam-beam interactions (need of large aperture)
Crab-cavities are the solution
IP
Lumi = Lumiideal * Spaghetti-Loss Factor
Lumiideal = f(Nb↑,Ib↑,ε↓,β*↓)
Crossing angle = φ
If Spaghetti-Loss Factor is not cured 
LHC  φ/2 = 285 µrad  F ~ 85%
HL-LHC  φ/2 = 590 µrad  F ~ 30%

## Slide 17: Magnets Nb3Sn
Good progress across all key technologies
US and CERN magnet production well underway
Inner Triplet String testbed taking shape
  Infrastructure in place and magnets starting to be installed
The Inner Triplet String Testbed – focus for 2025
The IT String will deliver the first complete experience of installing and operating the IT zone
LHC NbTi 12 kA
HL-LHC Nb3Sn  16.5 kA (ultimate 17.5 kA)

## Slide 18: Preparing for the Inner Triplet String Test
Tracing on the floor:
  Beamlines, pillars, jumpers, beam pts, jacks, anchors, …
  Robotic solutions for tracing to reduce time
Magnet support jacks - installation and alignment
First magnets aligned
  Q2a and D1 in place and aligned in Nov 2024
IT STRING tracing
IT STRING – D1 placed and aligned
Tracing robotic solutions testing
IT STRING jack alignment

## Slide 19: MgB2 superconducting link
The flexible, double-wall, corrugated cryostat:
19 MgB2 SC cables in a single assembly, twisted together to form a compact bundle
Can transfer altogether a DC current of about 120 kA at ~20 K
The first Cold Powering System for the HL-LHC Triplets has been successfully validated: cryogenic, electrical and mechanical performance all met design parameters
Today in an advanced phase of series production
Nb3Sn quadrupoles
NbTi correctors
SC D1
SC: Super Conducting
D1: separation dipole

## Slide 20: Crab Cavities
Delays in RFD cavities jeopardizes completion of RFD cryomodules in-time for LS3 installation
Mitigation strategy being worked on
5 DQW cryomodules (Europe)
5 RFD cryomodules (North America)
Increasing the number of collisions in the HL-LHC

## Slide 21: Civil Engineering Complete
Point 1
Point 5

## Slide 22
Updated Schedule for HL-LHC

## Slide 23
Conclusions

## Slide 26: Spares

## Slide 27: Setting the scene
LS2
RUN 3
LS3
RUN 4
RUN 2
2021 - 2026
HL-LHC upgrades
installation
HL-LHC commissioning
and exploitation
Injectors RUN 2 achieved parameters SPS ejection:
1.2·1011 p+/bunch
2.6 μm ℇnx,y
25 ns bunch spacing
Integrated LHC luminosity
~140 nb-1 @6.5 TeV
(per high lumi experiment)
LIU & 1st phase of HL-LHC
- New Linac 4 @160 MeV H-
- Booster injection @160 MeV and extraction @2 GeV
- PS injection @2GeV, RF system upgrade, etc
- SPS RF system upgrade, etc
Injectors LIU targets SPS ejection
2.3·1011 p+/bunch
2.1 μm ℇnx,y
25 ns bunch spacing
LHC p+ Lumi Levelled
@ 5·1034 cm-2s-1
2015 - 2018
LHC 2024 operation
3 x 36 bunches BCMS
1.6·1011 p+/bunch
Integrated lumi ~125 nb-1 @6.8 TeV
(per high lumi experiment)
2.45·1011 p+/bunch
1.66 μm ℇnx,y
Achieved in MD, not yet operational
SPS ejection
LIU & 1st phase of HL-LHC commissioning
and exploitation
≥ 2030
ℇnx,y : normalized transverse emittance
LIU: LHC Injectors Upgrade

## Slide 28: LHC in 2024
Mar-Apr
Jun-Jul
May
Aug-Sep
Oct-Nov
Reverse Polarity optics
commissioned (~ +1 week)
First Stable Beams @6.8 TeV 5th April (3 days early)
LHCb VELO closed for the 1st time
1200 bunches on 14th April
(10 days early)
Record ion Run
1.9 nb-1 Target
BCMS: Batch Compression and (bunch) Merging and (bunch) Splitting
First injection: 8th March (3 days early)
Beam position around the 27 km
H (mm)
V (mm)
BCMS beams May
Normalized emittance
2.0 µm
Date
Apr
May
Operating with 1.6⋅1011 p+/bunch
Bunch length control/target
Limit RF module heating risk
Very stable physics production
Bunch length (ns)
Time
5’
Stable Lumi Production
Summer period
Beyond the 110 fb-1 target
Average lumi (nb-1)
110 nb-1
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
pp reference run 28th Oct – 2nd Nov
Integrated lumi over expectations
Delivered int lumi (pb-1)
30 Oct
1 Nov
3 Nov

## Slide 29: RF burst disk
Mitigation to reduce the risk:
Installation of fast depressurizing valves to back up the warm recovery line
Similar events may still happen given small pressure margin between opening of safety valve and burst disk, which is necessary to able to protect the RF cavities against major events, for which the bust disks were foreseen
Trigger event  power cut in point 4 following a wrong manipulation after issue with compensator
Afterwards: well-known chain of events:
  the RF cavities are automatically isolated from the He input and output lines, consequently the cryomodule pressure increases due to the static heat loads the safety valves open and maintain the pressure around 1.9 bar
Unfortunately, two of the new burst disks installed during YETS22-23 did not withstand the pressure and opened
A test campaign on the spare disks confirmed that likely these two disks were outliers
02.04.2023

## Slide 30: LHC in 2024
Operating in 2024 with known weak modules
  47 of 71 replaced in YETS23-24
  Remaining modules to be replaced YETS24-25
Beam induced power depends on bunch intensity and bunch length
  Bunch intensity limited to 1.6⋅1011 p+ in 2024
    Run 3 max = 1.8 ⋅ 1011 p+/b
  Bunch length control throughout the cycle
Dealing with Limitations – RF Finger Modules
Bunch length B1 (ns)
Bunch length B2 (ns)
(E)YETS: (Extended) Year End Technical Stop
Time from start of acceleration (s)
Time from start of acceleration (s)
3.3 min

## Slide 31: Performance optimization
Move to BCMS Beams
  Filling scheme based on 3x36b patterns imposed by heat load limitation from electron cloud
  Intensity limited to 1.6⋅1011 p+/bunch by RF fingers
  Emittance: could be improved with BCMS
Optimised BCMS since May
  Higher bunch brightness
    Smaller emittance beneficial for reducing losses at injection
BCMS Beam for the LHC in the PS
BCMS: Batch Compression and (bunch) Merging and (bunch) Splitting
Normalized emittance (µm rad)
Apr
May
Jun
Jul
Aug
Sep
Oct
Instantaneous lumi (Hz/µb)
Time (s)
Stable beams
BCMS
Time along PS cycle
6 bunches
3 bunches
9 bunches
18 bunches
36 bunches

## Slide 32: Outlook for the LHC in 2025
2025 Schedule
  2025 luminosity target will be comparable to 2024 (target 110 nb-1)
  Short Oxygen run mid-year and Pb Ion Run to end the year
Ensuring longevity of the IT Magnets
  Full reversed polarity gives best outlook but would stop any forward physics
  Compromise is flipping the crossing plane with nominal powering in IR1 and reversed polarity in IR5
    Good background conditions for FASER and SND
    PPS rotated to allow data taking to continue
  Several magnets still reach estimated limits if 2025 and 2026 are good production years
Moving to Flat Optics
  Recovers luminosity loss due to limitation of aperture in triplet with flipped crossing plane
IT: Inner Triplet
FASER: Forward Search Experiment (close to IP1)
SND: Scattering and Neutrino Detector (close to IP1)
PPS: Precision Proton Spectrometer (close to IP5)

## Slide 33: Beam screen heat load forecast @HL-LHC era
HL-LHC prediction in S78
for 5x48b @ 2.3e11 ppb & 7 TeV
 280 W/hc > Cryo limit [225 W/hc]
Fill #8471 in 2022
(measured 5x36b)
Objective after Beam Screen (BS) treatment
2.3
Cryo Limit expected for Run4
The LHC cryogenic capacity is limited and cannot be easily increased Money, surface/underground available space, energy…
From Run 4, heat loads applied to cryogenics will significantly increase LHC intensities ↑↑  Sync. Rad + Image Current + e-cloud ↑↑
The proposed mitigation strategy is :
“Treat” in situ a fraction of BS around the LHC to reduce the e-clouds
This treatment must be done in LS3
Under the eﬀect of the cloud itself, conditioning of the copper surface of the LHC beam pipes is expected, decreasing thus the SEY of the surface. Such a process seems therefore to be hindered in some parts of the LHC ring.
Simulations without considering any BS treatment and fitting the current heat load measurements in 2022 for 5x36b
“Treat”: remove CuO + increase surface carbon concentration + surface passivation on 100 selected half-cells

## Slide 34: Key ingredients for the HL-LHC upgrade
A technologically “intense” upgrade project
New IT quadrupoles, Nb3Sn
Civil engineering
Crab Cavities
Crystal collimation
Low impedance collimators
  Superconducting links
Injection and dump upgrades
…
2
2
3
4
5
6
1

## Slide 35: Preparing the Collider-Experiment Interface
Protecting the machine from collision debris
  Moving into the production phase for both the TAXS (secondary particle absorber) the TAXN (neutral particle absorber)
  Mock-up area heavily used to train and test
    Very soon house full setups of both ATLAS and CMS

## Slide 36: LHC layout & beam production

## Slide 39: Other limitations in Run 3 that require LHC parameters and configuration optimization
Besides: RF fingers modules  limits bunch intensity and bunch length
Electron cloud and cryogenics load  limits bunch pattern
Radiation to inner triplets  change of optics
LIMITATIONS