## Slide 1
LHCb VELO U2
Mechanical concept

## Slide 2
Investigating several aspects of the U2 VELO mechanical concept
  Motion system compatible with "iris" RF-shield (linear motion version...)
  Vacuum interface and feedthrough
  Possible approach for the separation of "clean" and "outgassing" part of the module
  Possible approach for "VELO separation from beam pipe"
Some of the assumptions:
  VELO acceptance down to low eta but "LHCb acceptance" up to 270mrad
==> primary vacuum tank can have a radius as low as 21cm @ 800mm
  Try to use "off the shelf" components for the vacuum interface (bellows, feedthrough)
  Try to keep motion and flexes out of the primary vacuum
In the following the base hypothesis is a 4 flange "iris" system:
  Vacuum interface similar for a 2-halves system (while U1 motion can be reused)
  Based on square modules but compatible with module tiling a la "concentric layout
Introduction

## Slide 3
The vessel
Primary vacuum
Diameter 500mm
Insulation vacuum volume
Outer Diameter 1200mm

## Slide 4
Mechanical drive system
SKF Kaydon’s KH precision
slewing ring bearing
Applications:
Radar Antennas
Machine tool tables
Medical devices
Bevel gearbox coupled
to a balls screw
Rotation of the slewing ring bearing generates a linear movement
Motor

## Slide 5
Mechanical drive system

## Slide 6
Mechanical drive system
Module flange feedthrough (number of modules per flange can be optimised).
CF15 Bellow
Motion transmission in the primary vacuum
Vacuum load on flange ~ 2 Kg
Piezo legs linear actuators
Fine alignment devices
"iris" with linear motion
“Iris” with rotation may also work

## Slide 7
Module outgazing
Screen covering the outgazing parts ?
Pumping orifice, “dirty primary vacuum”
Small slit, cold substrate doesn’t touch

## Slide 8
Services feedthrough
Modules flanges primary vacuum
. All feedthroughs must be UHV CF type (copper joint)
. Optimisation of the number of outlets to reduce the risk of leakage
)
Pumping orifice, “dirty primary vacuum”
Flanges services insulation vacuum.
. HV, LV, optical, CO2, Vacuum ….
(Can be with O-rings)

## Slide 9
Vacuum layout
Primary vacuum Head (SMOG3?)
Insulation vacuum flange
Insulation door

## Slide 10
VELO X and Y motion
Bellows placed at the extremity
will absorb a tiny movement +/-5mm
X motion should be added to the VELO support frame
Y
X

## Slide 11
Isolate the VELO primary Vacuum
A challenge for the RF/Vacuum group and the VAT company
DN 800
Light RF contact mechanism
RF all metal gate valve: needed for the bake out.

## Slide 14: Can this technology be adapted to a large valve, With low material budget ?
VAT 47.1 Extreme High Vacuum RF All-Metal Gate Valve. - VAT Valves
DN 800

## Slide 15: Motion bearing standard SKF production