## Slide 1
SuperKEKB RF Gun System and Operation Status
Rui Zhang (KEK ACCL-5, Injector Group)
2024.12.02. @CERN

## Slide 2
Introduction of KEK, SuperKEKB & Linac injector
SuperKEKB RF gun system
  RF gun cavity
  Photocathode
  Laser system of RF gun
Recent achievements and 2024ab commissioning status
Summary and outlook
Contents

## Slide 3
Self Introduction
03-34
Mt. Tsukuba
Ph. D course: 2010.04-2013.12, Department of Physics and Astronomy, Shanghai Jiao Tong University (SJTU)
  Novel thermal management in solid-state laser
  Multi-function nonlinear laser
  Micro-nano optics
Post doctoral researcher: 2014.04-2016.03, Injector Group, ACCL Division V, KEK
  Development of combination technology for Yb:YAG thin disk laser
  Improvement of RF gun thin disk laser system for SuperKEKB
  Cryogenic laser experiment
Assistant professor: 2016.04-now, Injector Group, ACCL Division V, KEK
  Nd/Yb hybrid laser system for SuperKEKB RF gun
  Synchrotron radiation monitor
  Spatial and temporal reshaping for laser beam
  Improvement of photocathode quantum efficiency
  Fast laser abort system
Hobbies: Badminton, Volleyball, Travel, Origami, Anime, Bonsai, Horticulture…

## Slide 4
Location of KEK
04-34
Mt. Tsukuba
Tokyo
Ibaraki Prefecture
KEK Tsukuba Campus
KEK Tokai Campus

## Slide 5
Tsukuba Campus of KEK
05-34
Tsukuba Hall
Oho Hall
Fuji Hall
Nikko Hall
PF
PF-AR
DR
Linac
J-arc
Mt. Tsukuba
KEK Tsukuba Campus

## Slide 6
SuperKEKB Project
06-34
Upgrade of KEKB B-factory
High-luminosity electron-positron collider
Asymmetric-energy electron-positron double-ring collider
Main ring is composed of
  Low Energy Ring (LER)
  4.0 GeV Positron 3.6 A
  High Energy Ring (HER)
  7.0 GeV Electron 2.6 A
Positron damping ring
Design Luminosity: 8.0x1035 cm-2s-1
  40 times maximum luminosity of KEKB
  Twice beam current of KEKB
  Squeezed βy* with nano-beam collision
Y. Funakoshi, IPAC2022, Bangkok, 2022.06

## Slide 7
SuperKEKB Project
07-34
Tsukuba Hall
New luminosity world record in 2022: 4.71 x 1034 (cm-2s-1)

## Slide 8
SuperKEKB Project
08-34
 | KEKB achieved |  | SuperKEKB 2022 June 22nd |  | SuperKEKB design | 
 | LER | HER | LER | HER | LER | HER
Ibeam [A] | 1.637 | 1.188 | 1.363 | 1.118 | 3.6 | 2.6
Bunches Number | 1585 |  | 2249 |  | 2500 | 
Ibunch [mA] | 1.033 | 0.7495 | 0.606 | 0.497 | 1.440 | 1.040
βy* [mm] | 5.9 | 5.9 | 1.0 | 1.0 | 0.27 | 0.30
ξy | 0.129 | 0.090 | 0.0398 | 0.0278 | 0.0881 | 0.0807
Luminosity [1034cm-2s-1] | 2.11 |  | 4.71 |  | 80 | 
Integrated Luminosity [ab-1] | 1.04 |  | 0.40 |  | 50 | 

## Slide 9
General Layout of SuperKEKB Linac
09-34
M. Satoh, the 26th KEKB Accelerator Review Committee, 2022.12.16

## Slide 10
Top view
Side view
Thermionic DC e- gun (GU_AT)
e- beam for e+ production: 13 nC (KBP for positron generation)
e- beam study: 1 nC (JBE)
PF injection: 0.1 - 0.3 nC (QFE)
PF-AR injection: 0.1 - 0.3 nC (ARE)
RF gun (GR_A1)
e- : 0.1 - 5 nC (KBE for HER injection)
Primary RF gun
Pulse bends in 24o line
Pulse to pulse beam switching for RF e- gun/thermionic e- gun
RF gun (GR_AS)
Backup for HER injection (Under studying)
Electron Source Part of Linac
10-34
R. Zhang, the 120th B Factory Project Committee, 2021.10

## Slide 11
 | Electron HER 7 GeV | Positron LER 4 GeV
Normalized Emittance | 40 / 20 [μm] | 100 / 15 [μm]
Energy Spread | 0.07% | 0.16%
Bunch Charge | 4.0 nC | 4.0 nC
SuperKEKB Requirements
A stable electron beam with high charge and low emittance is essential for SuperKEKB
11-34

## Slide 12
SuperKEKB RF Gun
12-34
R. Zhang, the 23rd KEKB Accelerator Review Committee, 2019.07
Requirements
4 nC electron charge generation capability
10 μm emittance preservation
Long term continuous operation
4 nC Beam Operation
Less space charge effect
  Longer pulse: 10 - 20 ps
Essential strong focusing field
  Preserves the low emittance from the RF gun
Stable long-time operation
  Lower electric field: < 100 MV/m
Side coupler or cut disk gun cavity structure is preferred

## Slide 13
S-band RF Gun System for SuperKEKB
RF gun cavity: strong focusing electric field & high acceleration efficiency
Quasi travelling wave side coupler (QTWSC): A1 primary RF gun
Cut disk travelling wave structure (CDTWS): A1 secondary RF gun
Photocathode: long lifetime & comparable high QE
Medium QE with long lifetime: 10-4 - 10-3 @266nm > 1 year
Metal composite: Ir2Ce or Ir7Ce2
Laser: simple, stable, spatial & temporal reshaping
Laser active material pumped by laser diode directly
  Yb-fiber & Neodymium (Nd) doped crystal (Nd:YAG): A1 ground laser hut
  Yb-fiber & Ytterbium (Yb) doped crystal (Yb:YAG): A1 underground laser hut
Temporal and spatial reshaping for minimum energy spread and emittance
13-34
R. Zhang, the 23rd KEKB Accelerator Review Committee, 2019.07

## Slide 14
RF Gun in Linac A1 Section
14-34

## Slide 15
The 120th B Factory Project Committee
A1 primary RF gun
QTWSC
In beam line
A1 secondary RF gun
CDSTW
Perpendicular to the beam line
Under studying
15-34
M. Yoshida, LCG Meeting, 2021.10
RF Gun in Linac A1 Section
A1 primary RF gun
A1 secondary RF gun

## Slide 16
QTWSC RF Gun Design
Common SC RF Gun
QTWSC RF Gun
Properties of QTWSC (5 nC case)
Gun exit
16-34
M. Yoshida, the 26th KEKB Accelerator Review Committee, 2022.12

## Slide 17
Photocathode for RF Gun
Iridium Cerium Alloy Photocathode
17-34
R. Zhang, Linac Meeting, 2021.01

## Slide 18
Photocathode for RF Gun
Characteristics of photocathodes
Quantum efficiency ranking:
KEK Ir7Ce2 > KOBELCO Ir2Ce >
KOBELCO Ir7Ce2 > KEK Ir2Ce
Sparking probability:
KEK Ir7Ce2 < KOBELCO Ir2Ce
The adoption of KEK Ir7Ce2 began with the 2021ab commissioning phase
Achievable bigger size (>12 mm)
Iridium Cerium Alloy Photocathode
18-34
R. Zhang, Linac Meeting, 2021.01

## Slide 19
Laser System for RF Gun
Yb Single Mode Fiber
Amplifier 1
Semiconductor Optics Amplifier (SOA)
114 MHz  10 MHz
Yb Single Mode Fiber
Amplifier 2
Menlo Orange 1 (1030 &1064 nm)
Menlo Orange 2 (1030 & 1064 nm)
Home made ANDi type 1064 nm
EO Pulse Picker
10 MHz  1- 50 Hz
Double bunch
Beam splitter 50:50
1st Nd:YAG Laser Line with 5 Stages Rod Amplifiers (High power 5th stage)
YCOB in 1st Laser Line 1064 nm  532 nm
BBO in 2nd Laser Line 1064 nm  532 nm
Beam Polarizer
Combination for Two Laser Lines
Beam Polarizer
Division for Two Laser lines
BBO in 1st Laser Line 532 nm  266 nm  DOE
BBO in 2nd Laser Line 532 nm  266 nm  DOE
Fiber
Oscillators (114 MHz)
Fiber
Amplifiers (10 MHz)
Nd:YAG Rod Laser
Amplifiers (1-25 Hz)
Wavelength Conversion & Spatial Reshaping
Yb Single Mode Fiber
Amplifier 3
MEMS Switch
3 In 1 Out






Ground Laser Hut
 Tunnel RF Gun Box
Transporting Line for
Two Lasers (11 m long)




RF Gun
Injection From Two Windows

2nd Nd:YAG Laser Line with 5 Stages Rod Amplifiers (High power 5th stage) with delay line
Upstream
Downstream
Yb-Fiber and Nd:YAG Hybrid Laser System
19-34
R. Zhang, the 23rd KEKB Accelerator Review Committee, 2019.07

## Slide 20
Laser System for RF Gun
Yb-Fiber and Nd:YAG Hybrid Laser System
1st Nd:YAG rod amplifier stage
2nd stage
3rd stage
5th stage
Laser from fiber stage
To BBO for green laser
④
①
②
③
⑤
20-34
R. Zhang, the 23rd KEKB Accelerator Review Committee, 2019.07
4th stage
Pockels cell

## Slide 21
Laser System for RF Gun
Yb-Fiber and Nd:YAG Hybrid Laser System
Green Lasers
A1 Ground Laser Hut
GS_A1 Room
Klystron A1 Gallery
Tunnel A1 Part
0o RF Gun
Thermionic Gun
Laser Transporting Line (LT)
24o Line
A1 Chicane
1st Laser Line
2nd Laser Line
LT
21-34
R. Zhang, the 9th SuperKEKB Long-term Operation Plan Meeting, 2021.10

## Slide 22
Laser System for RF Gun
Yb-Fiber and Nd:YAG Hybrid Laser System
22-34
R. Zhang, the 9th SuperKEKB Long-term Operation Plan Meeting, 2021.10
FHG
FHG
Position sensor
Position sensor
Piezo mirror mount
Piezo mirror mount
Injection shutter

## Slide 23
Laser System for RF Gun
Yb-Fiber and Nd:YAG Hybrid Laser System
23-34
R. Zhang, the 9th SuperKEKB Long-term Operation Plan Meeting, 2021.10

## Slide 24
Laser System for RF Gun
Two Laser Beams Incidence Mode for Better Beam Quality
2nd line
HWP
HWP
Polarizer
Delay line
11 m long transporting line
A1 ground laser hut
Tunnel optics table
BBO
0o RF gun
90o RF gun
BBO
BBO
Flip mirror
HWP
Polarizer
Laser with vertical polarization, laser with horizontal polarization, HWP: half wave plate
e- beam
1st line
Simple illustration for 2 lasers incidence (out of ratio)
24-34
R. Zhang, the 23rd KEKB Accelerator Review Committee, 2019.07
60o injection
60o injection

## Slide 25
Laser System for RF Gun
Spatial Reshaping for Lower Emittance
Diffractive Optical Element for producing high-quality electron beams
Principle: Diffraction optics by lens and micro-configuration
Desired intensity distribution can be realized (phase coding)
World’s first application of a DOE in the UV laser section
6mm
3mm
25-34
R. Zhang, the 9th SuperKEKB Long-term Operation Plan Meeting, 2021.10

## Slide 26
Laser System for RF Gun
Spatial Reshaping for Lower Emittance
Application of DOE in the 1st laser line since 2020c and in the 2nd laser line since 2021c
Elliptical flat-top spatial distribution on the photocathode surface (LA: 6 mm, SA: 3 mm) for generating low-emittance electrons and preventing RF gun discharge
2nd laser after DOE
1st laser after DOE
1st laser before DOE
2nd laser before DOE
26-34
R. Zhang, the 9th SuperKEKB Long-term Operation Plan Meeting, 2021.10
R. Zhang, IPAC2022 Bangkok, 2022.06

## Slide 27
Laser Pointing Stability
27-34
R. Zhang, N. Toyotomi (Mitsubishi SC), the 120th B Factory Project Committee, 2021.10
2021c Operation Status & Achievements

## Slide 28
Laser Pointing Stability
28-34
R. Zhang, N. Toyotomi (Mitsubishi SC), the 120th B Factory Project Committee, 2021.10
2021c Operation Status & Achievements
A1 Ground Laser Hut
Tunnel Optics Table
Position sensor
Piezo mirror mount
Position sensor

## Slide 29
Better Laser Pointing Stability
Measured in 2019.06 without DOE & laser position feedback
Measured in 2021.06 with DOE & laser position feedback
H 2σ: 48.04±0.51 μm
V 2σ: 46.08±0.69 μm
H 2σ: 24.30±3.06 μm V 2σ: 10.08±0.46 μm
Laser pointing stability at virtual photocathode
Laser position feedback system
29-34
R. Zhang, N. Toyotomi (Mitsubishi SC), the 120th B Factory Project Committee, 2021.10; IPAC2022 Bangkok, 2022.06
2021c Operation Status & Achievements

## Slide 30
Best Emittance Record for the SuperKEKB Commissioning
Wire scanner @ B-sector
Two lasers incidence mode
2 nC from the RF gun
The best record so far
Wire scanner @ B-sector
Wire scanner @ BT
Wire scanner @ BT
Best record
30-34
2022ab Operation Status & Achievements

## Slide 31
2024c Operation Status & Achievements
Stable and Continuous RF-gun Injection for HER
HER e- beam injection
Stable and continuous e- beam operation for injection
  2 nC 25 Hz double bunch
Comparable higher injection efficiency in 2024c commissioning
No trend of photocathode QE degradation
Reliable laser system and feedback system
  Position feedback
  Laser pulse energy feedback
  RF phase feedback
Stable 4-ring simultaneous injection
31-34
HER injection efficiency
Electron charge @ injection point
HER injection background
Electron beam current

## Slide 32
Stable and Continuous RF-gun Injection for HER
32-34
2024c Operation Status & Achievements
HER e- beam injection
Stable and continuous e- beam operation for injection
  2 nC 25 Hz double bunch
Comparable higher injection efficiency in 2024c commissioning
No trend of photocathode QE degradation
Reliable laser system and feedback system
  Position feedback
  Laser pulse energy feedback
  RF phase feedback
Stable 4-ring simultaneous injection

## Slide 33
33-34
Future Operation Study
3 nC and 4 nC Electron Beam Study for Future Commissioning
 | 3 nC | 3 nC (2-bunch) |  | 4 nC
εx (μm) | 23.196 ± 4.325 | 32.454 ± 4.285 | 17.191± 2.875 | 39.816 ± 5.749
εy (μm) | 16.068 ± 2.431 | 30.914 ± 5.290 | 29.902 ± 5.711 | 25.983 ± 7.894
Emittance Status at B-sector*
* B sector wire scanner is the nearest one after the RF-gun
3 nC 2-Bunch Beam
4 nC Beam
New RF gun cavity will be installed in July 2025
  Better vacuum level
  Lower emittance for 3 nC and 4 nC beam
Yb:YAG laser system with temporal reshaping for electron beams with lower emittance and energy spread
New injection pattern investigation for higher charge HER injection (7 bunch injection)

## Slide 34
Summary & Outlook
THANKS
The SuperKEKB RF-gun system is performing well in the current commissioning
An upgraded laser system is being used to generate a 4 nC electron beam for the upcoming commissioning
A new laser system with temporal reshaping will be implemented to generate a high-charge electron beam with superior quality
A new injection pattern is currently under investigation
34-34

## Slide 37
Yb:YAG Disk Laser and Nd:YAG Rod Laser
LONG-TERM OPERATION PLAN of LASER SYSTEM for RF GUN
Nd:YAG rod laser
Yb:YAG thin disk laser
Good thermal management and modern laser design
Necessary multi-pass for amplification
Used in Phase I
Poor stability and complex adjustment
Not suitable for accelerator long term operation
Mediocre thermal management
Single or double-pass for efficient amplification
Used in Phase II and III
Good stability
Simple adjustment and fast recovery during trouble case
Yb:YAG disk thickness: 1 mm
Nd:YAG rod length: 80~95 mm
12-27
Yb:YAG disk laser head
Nd:YAG rod laser amplifier module

## Slide 38
Partial Reflection Mirror
S1: PR@260nm R=5%
S2: AR@260nm R<0.2%
Input UV laser
Partially reflected laser for monitoring
Transmitted UV laser
Transmitted UV laser
Rear surface reflected laser  ghost beam

## Slide 39
Gaussian Beam v.s. Flat-top Beam
Intensity (a.u)
Beam Size
Beam Size

## Slide 40
Route B: New Ytterbium-doped YAG (Yb:YAG) laser system
LONG-TERM OPERATION PLAN of LASER SYSTEM for RF GUN
Design layout of Yb:YAG rod laser system
Yb:YAG thin disk laser
Good thermal management
Needs several pass for amplification
Used in Phase I
Poor stability
Complex adjustment
Not suitable for accelerator operation
Nd:YAG rod laser
Mediocre thermal management
One or two pass for efficient amplification
Used in Phase II and III
Good stability
Simple adjustment and fast recovery
thickness: 1 mm
length: 80~95 mm
length: 20 mm
28-32

## Slide 41
Route B: New Ytterbium-doped YAG (Yb:YAG) laser system
LONG-TERM OPERATION PLAN of LASER SYSTEM for RF GUN
Current fiber oscillator is available to both Nd:YAG and Yb:YAG laser
Low thermal effect of Yb:YAG laser due to low quantum defect
Available pulse stacking technology for low energy spread electron beam generation
t
I
Nd:YAG Laser
t
I
Yb:YAG Laser
Fiber Oscillator
27-32

## Slide 43: Streak Camera Test Data by 2 Lasers
2 lasers mode
1st laser
2nd laser

## Slide 44
For High Quality e-
24-26
Laser Spatial Reshaping
Laser Temporal Reshaping
r
I
Laser spatial distribution
Phase space
x
x’
Linearity
Emittance
Laser beam shaper for flat-top
For Nd and Yb laser
Under purchasing
Pulse stacking by birefringent crystals
Demonstrated in Nd laser
Will be used in Yb:YAG laser for real flat
t
I
t2
t1
t1
x
x’
t2
Phase space
Laser spatial distribution
t
I
Yb:YAG laser
t
I
Nd:YAG laser

## Slide 45: Updates in 2020
Temporal reshape: Pulse stacking for low energy spread
Pulse stacking setup made by a crystal array
(birefringent effect of crystal)
Two stages stacking system made by YVO4 crystals
Input laser pulse with temporal Gaussian shape (FWHM~10 ps)
Output laser pulse with temporal rectangular shape (FWHM~40 ps)
Input Nd:YLF mode lock laser pulse with 9.4 ps FWHM width
Achieved laser pulse by stacking
* Supported by Dr. Yosuke Honda
17-20

## Slide 46: RF-Gun for 5 nC
Space charge is dominant.
  Longer pulse length : 20 - 30 ps
Stable operation is required.
  Lower electric field : < 100MV/m
Focusing field must be required.
  Solenoid focus causes the emittance growth.
  Electric field focus preserve the emittance.
Total
Space charge
RF
Epaxial coupled cavity : BNL
Annular coupled cavity : Disk and washer / Side couple

## Slide 47: Energy spread reduction using temporal manipulation
Gaussian
Square
5nC
10nC
15nC
20nC
20nC
15nC
10nC
5nC
5nC electron
15nC
Primary beam for positron production
t
t
Energy spread of 0.1% is required for SuperKEKB synchrotron injection.

## Slide 48: Required laser pulse energy
5nC
Ce2Te
ATF
Offline measurement
P-polarization
Offline measurement
S-polarization
Normal injection (old 3-2)
Inclined injection
Charge( C )
Laser power ( J )
QE=10-3
QE=10-4
QE=10-5
Current laser energy(500μJ)

## Slide 49
Field
Focusing field
Accelerating field
Focusing field
Field
Given force
Given force
Focusing field
Focusing
field
=> 集束力
Pill-box cavity
Annular coupled cavity with nose
Accelerating field
Accelerating field
Beam
Beam
Accelerating field
Accelerating field
Accelerating field

## Slide 50
INJECTOR GROUP STATUS
Arisen issues in 2021ab
Serous discharge  Uniform laser intensity distribution and smooth RF conditioning
Performance deterioration of RF-gun window  Component analysis of deposits
Unavailable 2-bunch injection  Sufficient RF conditioning and adjust the RF pulse width, improve the emittance of the 2nd bunch beam
Not achieved charge at BT end > 2 nC  Next page
Achievements and Issues in 2021ab
M. Yoshida, Linac Technology Meeting, 2021.08
R. Zhang, 2021.08
Photocathode used in 2021ab
Gun window used in 2021ab

## Slide 52: YCOB CRYSTAL at LINAC
From Prof. YQ Zheng’s Slide, the 1st KEK and SICCAS nonlinear optics forum, Tsukuba, May 28, 2018