## Slide 1
A probabilistic approach for characterization studies
M. Magistris, A. Gomes, R. Neugebauer, E. Stamati
CERN
ARRAD GT1 - libération des matériaux au CERN

## Slide 2: Outline
Clearance criteria
Challenges
Systematic approach
Probabilistic approach
Conclusions

## Slide 3: Clearance criteria
Specific activity
Contamination
Dose-rate

## Slide 4: Challenges
Particles: protons, pions, neutrons, electrons….
Particle energy: eV to TeV
Timescale: months to decades

## Slide 5: Challenges
Different materials, each with different activation properties
Accelerator components with complex shapes, which can affect radiation measurements
Mixed items from multiple particle accelerators

## Slide 6: Systematic approach
Systematic study of all possible activation scenarios:
Geometry
Radiological history
Material composition
Boundary scenario
5,000,000 activation scenarios
Sensitivity study

## Slide 7: Systematic approach
Total gamma counting: classification based on a reference fingerprint (or nuclide vector)
How can we choose the most penalizing fingerprint?...
... with a Figure Of Merit!
The most penalizing scenario was used for classification at the exit of accelerators.
FOM
T. Frosio and al., Classification of radiological objects at the exit of accelerators with a dose-rate constraint, Applied Radiation and Isotopes
See presentation by Frederic Aberle!

## Slide 8: Probabilistic approach
In the systematic approach:
- every activation scenario has the same probability
- we classify based on the most penalizing scenario
In the probabilistic approach:
- every scenario has a given probability
- we classify based on a risk analysis
We extract the probability distributions from our database....
... and translate them into an input file, ready for computations.

## Slide 9: Probabilistic approach
Design:
We extract a population of virtual waste items based on the probability distributions
Operation:
ActiWiz computes the radiological properties of every virtual item

## Slide 10: Probabilistic approach
Virtual items can be grouped together into packages
Analysis:
We define the TGC signal LL_eq, below which an item is conventional

## Slide 11: Probability distributions Example of massive pieces
Beam energy
Mass:
Entire waste item
Individual components making up the waste item

## Slide 12: Radiological properties Example of metallic waste
Dose-rate:
Near the entire waste item
Near individual components making up the waste item
1 nSv/h
See the invisible (< 1 nSv/h)
Analyze properties of components (e.g. plastic) based on DR of the entire item
Mass
Invisible

## Slide 13: Radiological properties Example of massive pieces
Proton energy
Facility:
The probability depends on the age and size of the facility
The probability distribution ensures that likely scenarios are well represented

## Slide 14: Machine learning Example of electric cables
Confidence 95.45%
Classification:
Logistic regression models the probability of a binary outcome y based on the variable x
  Conventional (Negative) y=0
  Radioactive (Positive) y=1
Simulations:
ActiWiz computes the Co-60 equivalent and the classification for every activation scenario
An item with Co-60eq = 0.041 Bq/g is classified “negative” with 4.55% error.

## Slide 15: Machine learning Example of electric cables
Confidence 95.45%
Confidence 99%
If we wish our confidence to increase by <4% ...
... our threshold would decrease by 2x
Sensitivity:
We can quantify our level of confidence when performing clearance
See presentation by Andrea Gomes and Andrea Camerini!

## Slide 16: Conclusions A probabilistic approach for clearance
Use available of data on material and waste
Select scenarios with 0.01 < LL < 100 and DR < 1 uS/h (i.e. discarding scenarios irrelevant for clearance)
Focus computational on the most relevant scenarios
Thanks to uncertainty propagation, and by using training vs testing sets, we can make a quantitative comparison of different models and evaluate their prediction accuracy.

## Slide 17: Conclusions A probabilistic approach for clearance
As we move to continuous probability distribution and as we discard irrelevant scenarios, we can:
  Concentrate our computational efforts on the cases with the highest impact, therefore:
  Improve our computational "return of investment" (ROI), therefore:
  Benefit from better accuracy, therefore:
  Reach high confidence levels, because….
  …we explore the phase space where it matters.

## Slide 18
Thank you for your attention