## Slide 2: HI-ECN3 Target complex CERN – ESS exchange Lund 20th September 2024
Jean-Louis GRENARD - CERN - HI-ECN3 WP4 Target complex

## Slide 3: What do we call Target Complex?
The target area
  Target station which contain the target
  Associated shielding
  The space to perform target maintenance activities (inspections, replacement, repair…)
  Remote handling equipment (crane, spreaders, mobile robots)
  Confinement(s)
The target service building
  Air handling units
  Cooling stations
  Controls systems
  The space to perform preparation for target (and other activated components) final disposal and possibly post irradiation examination

## Slide 4: BDF/SHiP Target & Complex
New
Service Building
~ 1000 m2
ECN3
Beam Dilution System
New
Access Shaft
(material only)
88 m2
TCC8
Existing
Access Shaft
48 m2
B918
B911
New Target Complex
containing the Beam Dump Target

## Slide 5: BDF Target complex integration
Target area
Confinement wall
Access chicane
Mobile Shielding
Above Coil Shielding
Magnetized
shielding
Water cooled proximity shielding
Target
Upstream Shielding
Collimator
Target station
SHIP experiment
Diluted Proton beam from SPS
Space for shielding temporary storage
Beam instrumentation
Vacuum confinement

## Slide 6
BDF Target complex integration - shielding
~12m
~8m
~4,8m
~ 180 m³ (~1400t) of cast iron + US1010
~ 360 m³ (~800t) of concrete / marble

## Slide 7: BDF Target complex integration extraction
Concept similar to the ISIS target station

## Slide 12
Installation of lifting tool
which include shielding

## Slide 23: Target station vacuum confinement
Overall dimensions: ~6.36 x 2.05 x 2.95 m
Can be fully fabricated and tested at a contractor premisses
Primary vacuum to optimize air activation around target
(Water containment in case of water leak)

## Slide 24: Target station vacuum confinement
Utilities feedthroughs
Mechanical design ready to build a prototype
Design of radiation tolerant gaskets
Decommissioning plan

## Slide 25: BDF Target complex integration extraction
Trolley mounted on full stainless steel chain action rollers

## Slide 26: BDF Target complex integration extraction
Extraction / insertion mechanism based on a motorized rigid chain
This will be installed on purpose in case of target exchange

## Slide 27: Space requirement for target exchange
~30m

## Slide 28: Maintenance of the target complex - few ideas
Target exchange
  Connections of utilities located in ‘’human’’ accessible environment
  Remote handling features for the connections
  Support of remotely controlled crane and ROVs
  Size reduction for final disposal by shearing
  Transfer from the underground to surface in shielded casks
n-TOF target#2 pipes reduction with ROVs

## Slide 29: Target Complex handling
Existing overhead travelling crane 30t capacity replaced
  Redundancy on the 3 movements of the crane
  Integration of a video system
  Integration of a positioning system for the 3 movements
  Off-board control cubicles
  Cable festoon routing
  Remote tools connection on the hook
  Auxiliary hoist
  Investigation on possibility to optimize crane size
  Ongoing specification

## Slide 30: The target service building
Nuclear ventilation system of the target complex
  Air handling units, filters, dehumidifiers (outside)
Target cooling systems
  Pumps, Filters, Heat exchanger, Cooling instrumentation, He circulation system
  Target controls systems
  Target monitoring (sensors), Target control valves, vacuum vessel confinement
  Service cell / hot cell
  Buffer area
Safety systems
Electrical distribution system
Control and safety systems
(Evaporator)
~1000m²

## Slide 31
Shielded buffer zone
Material access
Cooling equipment
Service cell
with a movable roof
Power room
Personnel access
New lorry access
Service building – ground floor
HotCell

## Slide 32: Service building – 1rst level
30t overhead traveling crane
Control racks
Mobile shielded hatches
Filter room

## Slide 33: HI-ECN3 service cell - context
HI-ECN3 project need to have a facility to prepare objects for final disposal
  BDF target
  Proximity shielding
  Hadron stopper coil
  Why do we need a specific facility to prepare HI-ECN3 object for final disposal (waste packaging)?
  Level of radiation (~few Sv/h after 1year of cool down)
  Characteristics of materials (W)
  Presence of radiological critical spallation products
  Size and weight of the objects doesn’t fulfil elimination path requirement towards PSI (container size limitation)
  Understanding of failure modes to improve future designs
  Lessons learnt from waste packaging of highly radioactive objects (ISOLDE target, LHC TDE, n_TOF spallation targets)
  Currently such facility does not exist at CERN
Main justification

## Slide 34: Service cell definition - design
Prelimiary discussion with master slave manipulator manufacturer
→Check of volumes in integration model

## Slide 35: Service cell definition – BDF target waste packaging draft sequence

## Slide 36
Service building within the BDF/SHiP complex

## Slide 37: Systems failure scenarios
Evaluation required for operation and maintenance scenarios
  Water and/or He leak
  Vacuum leak
  Fire
  Ventilation
  Cooling
  Extraction system
  Handling tools

## Slide 38: Subjects of concern – Target station
Did you have any elastomers (for gaskets?) in areas with (high) radiation dose?
Did you have any lubricant in areas with (high) radiation dose?
Did you have any place where you have implemented measure to prevent cold welding (typically on rolling elements)
How have you qualified sub systems? And to which extend have you over stressed your systems?
How have you prevented the pollution of the target vessel during installation? To which extend all your systems are sensitives to dust and corrosion?

## Slide 39: Subjects of concern – Cooled shielding
What has made de decision for ESS to move towards a cooled shielding made out of stainless steel?
What is the chemical composition of the stainless steel shielding?
Did you encountered any difficulties during production?
What QA checks have you performed typically for the quality of the welds?
Have you identified several suppliers for those blocks? Could share the name of your suppliers?

## Slide 40: Subjects of concern - Hotcell
How have you define the process and workflow for the hotcell?
What is the strategy for the final disposal of the target wheel?
Did you intend to separate each individual W block from the wheel?
How dose the design of the hot cell and associated process have defined the target?
What has made decision to built a hotcell without lead glass window (Just operating with cameras)
How did you guarantee the air tightness of the hotcell when you insert equipment?
What are your constrains in term of final packaging for waste disposal? (Package type, shielded container)
What are the standards you have used to design the hotcell?
Did you intend to use your hot cell else than for the target facility?

## Slide 41: Subjects of concern – Support building
From which standards (as a nuclear facility) have you based your design?
Which systems are covered by secured network (UPS and/or diesels generators)?
What is the strategy in case of power outage?

## Slide 42
Thank you

## Slide 43: Spares slides

## Slide 44: Target Complex in an existing facility
CERN
Prevessin site
CERN
Meyrin site
SPS
ring
SPS extraction
towards North Area
ECN3
Implementation in the SPS North Area ECN3 designed at construction in 70’s for a High Intensity (NAHIF)
Currently used by NA62 experiment
SPS North Area beam lines and associated infrastructure being currently consolidated
Would require the dismantling fraction of current beam line, target station, the experiment
Only one target station can be accommodated in the cavern

## Slide 45: The TCC8 area
TCC8 cross section (length 170m)
8m soil
~10m bellow ground

## Slide 46: Target station vacuum confinement
500 mm
120 mm
Skin thickness: 30 mm
Grid of HE 100 M beams (each 120 mm tall) crossing each other at 90º, 500 mm separation
Skin thickness: 30 mm
Boundary condition: floor beams fixed to the floor in the vertical direction.
Max displacement 3 mm
Max VM stress in the sheet: ~200 MPa local peak, lower elsewhere
Max utilization factor of the beams:0.49
Buckling factor: 0.82
Simplified analysis using 1-d beams and 2-d shell elements
More detail vessel design