## Slide 2: Radiation Protection Considerations for HI-ECN3
C. Ahdida, G. Mazzola, G. Dumont WP6 - Radiation Protection & Safety
ESS - CERN Meeting, ESS, Lund, Sweden 20th September 2024

## Slide 3
Overview of RP Challenges at HI-ECN3
Target Complex Design Optimization
Target Studies
Outline

## Slide 4
CERN’s SPS North Area
HI-ECN3 at ECN3
Key beam parameters of BDF/SHiP
 | BDF
Intensity (p/spill) | 4×1013
Spill duration (s) | ≥1
Cycle length (s) | ≥7.2
Avg. beam power (kW) | 356
Average intensity (p/s) | ≤5.6×1012
Annual POT | 4×1019
Duration (years) | 15
Total POT | 6×1020
8m soil
TCC8 cross-section
High Intensity ECN3 (HI-ECN3) project for a new state-of-the-art high intensity experimental facility in ECN3
    exploiting the available high intensity SPS 400 GeV/c proton beam
    benefiting from an existing cavern of comfortable size incl. its infrastructure
    using the advantage of the shielding created by the soil
RP challenges
    High beam energy and intensity as well as high POT leading to high prompt radiation and activation levels
    Proximity to surface, experimental and public areas
    Losses during beam transfer (not covered here)

## Slide 5
Target Complex Optimization

## Slide 6
RP studies based on FLUKA MC simulations were performed for a design optimization of BDF/SHiP@HI-ECN3
ALARA approach Optimization required to ensure that exposure of personnel to radiation and radiological impact on environment are As Low As Reasonably Achievable
Prompt radiation Reduce prompt radiation to comply with radiation area classification in the surrounding accessible areas as well as the 1 mSv limit at the CERN fence
residual radiation Limit activation of target and experimental area to reduce residual dose rates to be compatible with an adequate area classification
Air and soil activation Reduce activation of air and its releases into the environmental. Limit soil activation (3H<1000 Bq/kg, 22Na<50 Bq/kg) and transfer to groundwater
Environmental impact Reduce environmental impact from prompt radiation and releases of activated air to fulfill CERN’s dose objective for the public of <10 uSv/year
Radiation area classification
BDF/SHiP design optimization

## Slide 7
Stainless steel
Concrete
US1010
Cast iron
Target complex & muon shield, Created using FLAIR [4]
Moraine
TCC8
W-TZM target
Magnetic part of hadron stopper 1.6 T
11 m
Moraine
1.6 m
1.6 m
8 m
Muon shield 1.7 T
ECN3
A detailed BDF/SHiP target complex together with the muon shield was implemented in FLUKA
Optimized BDF dump with reduced shielding and re-use of existing, already activated TCC8/TT7 shielding blocks, while maintaining SHiP physics performance
Shielding embedded in vacuum vessel
FLUKA geometry includes the full underground TCC8/ECN3 cavern and surrounding galleries, tunnels, rooms, etc.
Ground profile data from CERN’s Geographic Information System and technical drawings were used to model the surrounding ground
FLUKA hosted by CERN [1-3]
4.8 m
Floor shielding (13.3 m3)
1 m
Vacuum vessel
Muon shield
~180 m³ of cast iron + US1010
~360 m³ of concrete
BDF/SHiP FLUKA model

## Slide 8
Cross-sectional view
Side view
Along y-axis
Shielding design is well optimized for the prompt radiation
Annual limit of Non-designated Area on CERN domain and at CERN fence (1 mSv/y) as well as dose objective for members of the public (10 uSv/y) is by far met
Avg. intensity of 5.6×1012 p/s
(-20 cm < x < 80 cm)
(13260 cm < z < 134380 cm)
(-20 cm < x < 80 cm)
(13260 cm < z < 13380 cm)
Prompt radiation in target area

## Slide 9
Cross-sectional view, target level
Along x-axis, working height
Upstream of vessel w/o upstream shielding Preliminary worst case manual intervention scenario
The shielding design contains well the high residual dose rates reaching in the central target region several 10 Sv/h after 1 month of cool-down
The residual dose rates outside the shielding are < 1 µSv/h
1 month cool-down
x [0,40]
x_beam = 26 cm
Shielding removed
After removal of the shielding upstream of the vessel, residual dose rates of several 100 µSv/h are expected
Supervised Radiation Area on the sides
Further optimization by movable shielding
Total PoT 6×1020
(13240 cm < z < 13390 cm)
(15 cm < y < 45 cm)
(13240 cm < z < 13390 cm)
1 month
(-15 cm < x < 80 cm)
Residual radiation in target area

## Slide 10
Air and soil activation
Specific activity of 3H and 22Na in the soil below TCC8 (most critical area)
3H
22Na
Air activation
Thanks to floor iron shielding, 3H and 22Na activity concentrations in the soil are below respective design limits
A hydro-geological study is underway, which will allow to refine the design limits and possibly allow to reduce the required shielding
Total PoT 6×1020
PoT 4×1019 per year
Activation of air in target complex area were studied
Production of radionuclides evaluated with FLUKA in combination with ActiWiz [5]
CASE 1: build-up of radionuclides during operation w/o air extraction and 30 min cooldown time before air release
CASE 2: constant immediate release of air (worst-case for upper limit of environmental impact)
Flush of target complex with fresh air before any access to reduce specific airborne radioactivity to be compatible with 0.1 CA
Exposure of members of the public due to air releases is negligible
1 Person working 40h/w, 50w/y with standard breathing rate in activated air with CA = 1 receives 20 mSv
1

## Slide 11
BDF Target Studies

## Slide 12
Baseline Design (CDS) – Water cooled, W + TZM cladded w/ Ta2.5W
Pursued during the comprehensive design phase → C. Ahdida et al., SPS Beam Dump Facility - Comprehensive Design Study, CERN-2020-002
Prototype + test with beam + Post irradiation examination
BDF Target baseline design

## Slide 13
Longitudinal cut along the target
The residual dose rates of the target were studied for 5 years of operation (now 15 yrs) and different cool-down times
The highest dose rates are in the order of 100 Sv/h after 4 hours of cooling and a few Sv/h after 1 year
Even after 30 years, dose rates at 40 cm still of the order of a few mSv/h → dedicated storage place in facility for irradiated target
For radioactive transport the max. dose rate level at any point on the external surface of a package shall not exceed 2 mSv/h
Thick iron cask (~30 cm thick) for transportation and storage as well as during handling
Total PoT 4×1019 (5 yrs)
4 hours cool-down
1 year cool-down
30 years cool-down
1 day cool-down
Residual Radiation – baseline CDS target

## Slide 14
LA multiples of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
CDS target radionuclide inventories
Total PoT 2×1020 (5 yrs) + 1 month cool-down
Target | Material | Mass [kg] | Multiple LL | Multiple LA | A [Bq]
CDS | W | 695 | 1.9E+08 | 2.6E+08 | 9.2E+14
 | TZM | 271 | 1.1E+09 | 8.4E+07 | 1.8E+14
 | Ta | 28 | 1.7E+11* | 6.9E+08 | 9.8E+14
*Dominated (99.9%) by Ta-182 (115 d half-life)

## Slide 15
BDF target prototype w/ in total 14 h irradiation in TCC2, leading to 2.4E16 PoT
Target activation was measured and compared to FLUKA simulations showing excellent agreement
Cooling water activation was estimated w/ FLUKA
Estimated residual dose rate after 1h of cooling at 40 cm from the cartridge is 18.7 mSv/h, while the PMI monitor measured 16.9 mSv/h
Both samples showed the presence of high-Z spallation products some of them could have been produced in the target materials
Water-cooling filter with debris was analysed via EDX
  No peaks were found for Ta, W, Mo or Ti
  Metallic particle (Al, Ca, Fe, Cl, Fe, Cr)
Benchmark of residual dose rates (mSv/h)
Radionuclides in water samples
Water samples were analysed by liquid scintillation and gamma spectrometry
Prototype Target Tests

## Slide 16
Baseline Design (CDS) – Water cooled, W + TZM cladded w/ Ta2.5W
Investigation of alternative claddings (Nb, Nb-1Zr, Nb-10Hf-1Ti)
Alternative BDF target design studies
Alternative designs currently being studied in the TDR
Enclosed compact
Cu + W Target
W Helium cooled Target
D = 33 cm, L = 201 cm
Investigation of radionuclide inventories
Expected to be less critical from a radiological point of view

## Slide 17
Cladding materials:
  Tantalum –16.6 g/cm3
  Nb (ASTM R04210 – Type 2) – 8.6 g/cm3
  Nb-1Zr (ASTM R04261 – Type 4) – 8.6 g/cm3
  Nb-10Hf-1Ti (ASTM R04295) – 8.86 g/cm3
Total PoT 2×1020 (5 yrs), 1y cool-down
Total PoT 2×1020 (5 yrs)
Residual dose rates (uSv/h)
No difference in the residual dose rates for the various Nb claddings
Includes residual dose rates from surrounding material
Waste classification as FA-MA waste to be disposed of in Switzerland (no open pathway so far for such activation of Ta/Nb)
* LMA: Acceptance Activity Limits, if activity levels < LMA candidate for elimination in France
Alternative Claddings
Nb-94 half-life of 20300 yrs

## Slide 18
Baseline Design (CDS) – Water cooled, W + TZM cladded w/ Ta2.5W
Investigation of alternative claddings (Nb, Nb-1Zr, Nb-10Hf-1Ti)
Alternative BDF target design studies
Alternative designs currently being studied in the TDR
Enclosed compact
Cu + W Target
W Helium cooled Target
D = 33 cm, L = 201 cm
Investigation of radionuclide inventories
Expected to be less critical from a radiological point of view

## Slide 19
Total PoT 2×1020 (5 yrs) + 1 month cool-down
Target | Material | Mass [kg] | Multiple LL | Multiple LA | A [Bq]
Large W | W | 3178 | 1.3E+08 | 8.2E+08 | 3.7E+15
 | TZM1 | 219 | 4.0E+07 | 1.8E+06 | 5.0E+12
CDS | W | 695 | 1.9E+08 | 2.6E+08 | 9.2E+14
 | TZM | 271 | 1.1E+09 | 8.4E+07 | 1.8E+14
 | Ta | 28 | 1.7E+11* | 6.9E+08 | 9.8E+14
*Dominated (99.9%) by Ta-182 (115 d half-life)
See backup slides for list of radionuclides
When comparing the W parts of the two targets, the multiple of LA and total A are a factor 3-4 higher (mainly due to the higher mass) for the large W target than the CDS target
There are only few percent differences between the TZM quantities
The Ta cladding of the CDS target exhibits mostly the highest values
Radionuclide inventories comparison
LA for short-cool-down times:
For 1h (4h), Hf-178m (4s half-life) produced via Ta-178m (2.36h half-life) is dominant (48%)
For 1d, Gd-148 (74y half-life) becomes most important (38%) (as for 1 month)
1TZM cladding layer
Also Iodine can make volatile molecules with Cobalt, Hafnium and Tantalum

## Slide 20
Summary & Questions
Main radiological aspects regarding an implementation of BDF/SHiP in ECN3 were investigated
First shielding design for an optimization of exposure of personnel to radiation and radiological impact on environment
Further detailed studies and optimization in the Technical Design Phase until end of 2025 to achieve first beam on target in 2030
Questions
  What potential release of radionuclides from the target to the He loop do you expect? How do you plan to mitigate the contamination?
  How do you account for H-3 out-diffusion?
  What are your plans for radioactive waste management (characterization, conditioning, waste packaging, shielding, elimination)
  Do you foresee any destructive works on the activated target/surrounding elements?

## Slide 22
[1] Website: https://fluka.cern
[2] C. Ahdida, D. Bozzato, D. Calzolari, F. Cerutti, N. Charitonidis, A. Cimmino, A. Coronetti, G. L. D’Alessandro, A. Donadon Servelle, L. S. Esposito, R. Froeschl, R. García Alía, A. Gerbershagen, S. Gilardoni, D. Horváth, G. Hugo, A. Infantino, V. Kouskoura, A. Lechner, B. Lefebvre, G. Lerner, M. Magistris, A. Manousos, G. Moryc, F. Ogallar Ruiz, F. Pozzi, D. Prelipcean, S. Roesler, R. Rossi, M. Sabaté Gilarte, F. Salvat Pujol, P. Schoofs, V. Stránský, C. Theis, A. Tsinganis, R. Versaci, V. Vlachoudis, A. Waets, M. Widorski, New Capabilities of the FLUKA Multi-Purpose Code, Frontiers in Physics 9, 788253 (2022)
[3] G. Battistoni, T. Boehlen, F. Cerutti, P.W. Chin, L.S. Esposito, A. Fassò, A. Ferrari, A. Lechner, A. Empl, A. Mairani, A. Mereghetti, P. Garcia Ortega, J. Ranft, S. Roesler, P.R. Sala, V. Vlachoudis, G. Smirnov, Overview of the FLUKA code, Annals of Nuclear Energy 82, 10-18 (2015)
[4] V. Vlachoudis, FLAIR: A Powerful But User Friendly Graphical Interface For FLUKA, in Proc. Int. Conf. on Mathematics, Computational Methods & Reactor Physics (M&C 2009), Saratoga Springs, New York (2009)
[5] H. Vincke, C. Theis, ActiWiz – optimizing your nuclide inventory at proton accelerators with a computer code, Progress in Nuclear Science and Technology (2014)
[6] P. Vojtyla, Models for assessing the dosimetric impact of releases of radioactive substances from CERN facilities to the environment – Air, CERN Internal report (2021)
Bibliography

## Slide 23
Activities of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Activities multiples – CDS target

## Slide 24
LL multiples of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Multiples of Swiss Clearance Limits (LL)
CDS Target

## Slide 25
Activation of water from cooling circuits was estimated
Shielding estimate around demineralization cartridges was performed assuming Be-7 to be stopped, but no target debris
  → 50 cm cylindrical concrete shielding was foreseen and for the roof of the area 165 cm concrete
Remaining water in circuit mostly contains H-3 with a concentration of around 0.5 GBq/l per year of operation
Due to the high H-3 production in the target (~18 TBq during 5 yrs operation), a significant contribution to the H-3 concentration in the water can come from H-3 out-diffusion from the target disks and subsequent trapping in the cooling water
In case of 1% of out-diffusion every 2 months (best guess, no data available) and 100% trapping, the H-3 concentration from out-diffusion amounts to ~60 MBq/l every 2 months
The exchange of cooling water (1 m3) in one year would result in ~220 GBq of H-3 activity
PoT 1×1019 (1 yr)
Total Activity (Bq) for H-3 and Be-7
Results above do not take out-diffusion from target into account
Water activation – CDS

## Slide 26
Alternative cladding materials
Material: |  | Niobium | Nb-1Zr | Nb-10Hf-1Ti |  | 
 |  | (ASTM R04210 | (ASTM R04261 | "C103" |  | 
 |  | Type 2) | Type 4) | (ASTM R04295) |  | 
Density (g/cm3): |  | 8.6 | 8.6 | 8.86 |  | 
Composition: | C | 0.01 | 0.01 | 0.015 |  | 
Max Weight % | N | 0.01 | 0.01 | 0.01 |  | 
 | O | 0.025 | 0.025 | 0.025 |  | 
 | H | 0.0015 | 0.0015 | 0.0015 |  | 
 | Zr | 0.02 | 0.8-12 | 0.7 |  | 
 | Ta | 0.3 | 0.5 | 0.5 |  | 
 | Fe | 0.01 | 0.01 | - |  | 
 | Si | 0.005 | 0.005 | - |  | 
 | W | 0.05 | 0.05 | 0.5 |  | 
 | Ni | 0.005 | 0.005 | by difference |  | 
 | Mo | 0.02 | 0.05 | - |  | 
 | Hf | 0.02 | 0.02 | 9-11" |  | 
 | Ti | 0.03 | 0.03 | 0.7-1.3" |  | 
Reference: |  | [1] | [2] | [3] |  | 
[1] | https://www.navstarsteel.com/niobium-sheet.html |  |  |  |  | 
[2] | https://www.tantalum-niobium.com/niobium/nb-1zr-wire-rod.html |  |  |  |  | 
[3] | Ximenes Franqueira R., Internal communication, (2021) |  |  |  |  | 

## Slide 27
Total PoT 2×1020 (5 yrs) + 1 month cool-down
Tungsten – Total Activity (Bq)
Tungsten – Multiple of LL
Tungsten – Multiple of LA
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Tungsten part
Radionuclide inventory of large W target

## Slide 28
Total PoT 2×1020 (5 yrs)
Tungsten – Multiple of LA
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
1 hour
1 day
Radionuclide | Halflife | 1h
Hf-178m | 4s | 1.2E+09
Gd-148 | 74.60y | 4.3E+08
W-187 | 23.9h | 3.2E+08
W-185 | 75.1d | 1.9E+08
Hf-172 | 1.87y | 1.5E+08
Ta-182 | 114.7d | 3.8E+07
Sum of all |  | 2.52E+09
Radionuclide | Halflife | 1d
Gd-148 | 74.60y | 4.3E+08
W-185 | 75.1d | 1.9E+08
W-187 | 23.9h | 3.2E+08
Hf-172 | 1.87y | 1.5E+08
Ta-182 | 114.7d | 3.8E+07
Yb-169 | 32.0d | 1.7E+07
Ta-183 | 5.1d | 1.7E+07
Hf-175 | 70.0d | 1.3E+07
Sum of all |  | 1.13E+09
For 1 h of cool-down, Hf-178m is dominant (48%) and wrt. to 1 month of cool-down also W-187 and W185 are relevant (Hf-178m comes from the decay of Ta-178m (2.36h half-life)
For 4 hours of cool-down, the important radionuclides are as for 1 hour
For 1 day of cool-down, Gd-148 becomes most important (38%)
Large W target – LA for short cool-down
Tungsten part

## Slide 29
Cross-sectional cut at the target
4×1013 p / 7.2 s
Longitudinal cut at the target
Along z – Large W target vs. CDS target
1.4 m
2 m
The highest dose rate are observed in the upstream part of the large W target with a sharp decrease towards its downstream end, which will lead to a significantly higher activation in the upstream than the downstream part of the target
The max. dose rate reached in the large W target is with ~3.2e13 uSv/h about a factor 2.6 higher than what is reached at maximum in the CDS target
Prompt radiation for large W target

## Slide 30
Beam transfer
TT7 shielding recovery
TCC8 dismantling
Shielding recovery from discontinued CERN PS Neutrino Facility (PSNF)
~100 m3 std. cast iron blocks
~50 m3 non-std cast iron blocks
~3 MCHF, investment <1/3
Residual H*(10)
Radioactive waste zoning
Several RP studies for the high intensity SPS-ECN3 beam transfer were performed
This includes studies for a bridge above the TDC85 transfer tunnel near ECN3
Prompt H*(10)
Various beamline and shielding configurations were investigated
Dismantling of the highly radioactive TCC8 target area in 2026
Evaluation of residual dose rates and radio-nuclide inventories for operational RP as well as radioactive transport and waste studies
TCC8
Residual H*(10)
Some additional studies

## Slide 31
Muon prompt radiation aboveground downstream ECN3
Worst-case immediate air release (CASE 2) yields 3 nSv/year (main contributors: N-13, Ar-41, C-11, O-15) and is thus well below the annual dose objective of CERN
Exposure of members of the public due to air releases is negligible
Dose from air releases
Used max. dose coefficients from different age groups [6]
Positions of nearby population groups
Effective dose estimates
Dose from stray radiation
Release point
Annual limit of Non-designated Area on CERN domain and at CERN fence (1 mSv/y) as well as dose objective for members of the public (10 uSv/y) is by far met
CERN fence
H-3 release due to air activation of ~80 kBq
PoT 4×1019 per year
Annual effective dose from muons
Environmental impact