## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to broadcast them online to all registered students and to post them without any further processing on the CAS website.
The author hereby confirms that the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.
Copyright statement and speaker’s release for video publishing

## Slide 3: Basic Mathematics and Units
Rende Steerenberg – CERN BE/OP

## Slide 4: Contents
Vectors & Matrices
Differential Equations
A word on the units we use

## Slide 5
Vectors & Matrices
Differential Equations
A word on the units we use

## Slide 6: Scalars & Vectors
Scalar, a single quantity or value
Vector, (origin,) length, direction

## Slide 7: Coordinate systems
(x,y) Cartesian coordinates
r is the length of the vector
y
x
r

θ gives the direction of the vector
(r, ) Polar coordinates
r
A vector has 2 or more quantities associated with it

## Slide 8: Vector Cross Product
θ
b
a
a × b
The cross product a × b is defined by:
Direction: a × b is perpendicular (normal) on the plane through a and b
The length of a × b is the surface of the parallelogram formed by a and b
a and b are two vectors in a plane separated by angle θ

## Slide 9: Cross Product & Magnetic Field
Force
B field
Direction of current
The Lorentz force in a pure magnetic field expression
The reason why our particles move around our “circular” machines under the influence of the magnetic fields
“Normal conducting & perm. magnets” by Jeremie Bauche
“Transverse Beam Dynamics” by Bernhard Holzer
Today & Tue.
Today

## Slide 10: Lorentz Force in Action
charge = 2e
Magnetic Field
Velocity ‘v’
charge = -e
charge = e
Particle with
mass ‘m’
The higher the energy of the beam the larger the radius of curvature

## Slide 11: A Rotating Coordinate System
It travels on the central orbit
Vertical
Horizontal
Longitudinal
y
s or z
x
q

## Slide 12: Magnetic Rigidity
Bρ is called the magnetic rigidity, and if we put in all the correct units we get:
Bρ = 33.356·p [kG·m] = 3.3356·p [T·m] (if p is in [GeV/c])
As a formula this is:
Which can be written as:
Momentum
p=mv
Like for a stone attached to a rotating rope
e
p
e
mv
B
=
=
r
mv
evB
F
=
=
r
2
Radius of curvature

## Slide 13: Moving a Point in a Coordinate System
To move from one point (A) to any other point (B) one needs control of both Length and Direction.
Rather clumsy !
Is there a more efficient way of doing this ?
2 equations needed !!!
y
x
A
B

## Slide 14: Matrices & Vectors
So, we have:
Rows
Columns
Let’s write this as one equation:
A and B are Vectors or Matrices
A and B have 2 rows and 1 column
M is a Matrix and has 2 rows and 2 columns

## Slide 15: Matrix Multiplications
This matrix multiplication results in:
Equals
This implies:
This defines the rules for matrix multiplication
Is this really simpler ?

## Slide 16: Moving a Point & Matrices
x
y
x1
x3
x2
y3
y2
y1
1
3
2
Lets apply what we just learned and move a point around:
M1 transforms 1 to 2
M2 transforms 2 to 3
This defines M3=M2M1

## Slide 17: Matrices & Accelerators
We use matrices to describe the various magnetic elements in our accelerator.
  The x and y co-ordinates are the position and angle of each individual particle.
  If we know the position and angle of any particle at one point, then to calculate its position and angle at another point we multiply all the matrices describing the magnetic elements between the two points to give a single matrix
Now we are able to calculate the final co-ordinates for any initial pair of particle co-ordinates, provided all the element matrices are known.

## Slide 18: The Unit Matrix
Xnew = Xold
Ynew = Yold
There is a special matrix that when multiplied with an initial point will result in the same final point.
The result is :
The Unit matrix has no effect on x and y

## Slide 19: Going Backwards
What about going back from a final point to the corresponding initial point ?
or
For the reverse we need another matrix M-1
The combination of M and M-1 does have no effect
M-1 is the “inverse” or “reciprocal” matrix of M.
such that

## Slide 20: Calculating the Inverse Matrix
If we have a 2 x 2 matrix:
Then the inverse matrix is calculated by:
The term (ad – bc) is called the determinate, which is just a number (scalar).

## Slide 21: Example: Drift Space Matrix
A drift space contains no magnetic field.
A drift space has length L.
x2 = x1 + L.x1’
L
x1’
x1
x1’ small
}

## Slide 22: A Practical Example
or
Changing the current in two sets of quadrupole magnets (F & D) changes the horizontal and vertical tunes (Qh & Qv).
This can be expressed by the following matrix relationship:
Change IF then ID and measure the changes in Qh and Qv
Calculate the matrix M
Calculate the inverse matrix M-1
Use now M-1 to calculate the current changes (ΔIF and ΔID) needed for any required change in tune (ΔQh and ΔQv).

## Slide 23
Vectors & Matrices
Differential Equations
A word on the units we use

## Slide 24: The Pendulum
Lets use a pendulum as example
The length of the pendulum is L
It has a mass m attached to it
It moves back and forth under the influence of gravity
L
M
Lets try to find an equation that describes the motion of the mass m makes.
This will result in a Differential Equation

## Slide 25: Differential Equation
Restoring force due to gravity is
-M g sinθ
(force opposes motion)
M
L
Mg

θ is small
L is constant
The distance from the centre = Lθ (since θ is small)
The velocity of mass M is:
The acceleration of mass M is:
Newton: Force = mass x acceleration

## Slide 26: Solving a Differential Equation
and
Differential equation describing the motion of a pendulum at small amplitudes.
Find a solution……Try a good “guess”……
Differentiate our guess (twice)
Put this and our “guess” back in the original Differential equation.

## Slide 27: Solving a Differential Equation
Oscillation amplitude
Oscillation frequency
Now we have to find the solution for the following equation:
Solving this equation gives:
The final solution of our differential equation, describing the motion of a pendulum is as we expected :

## Slide 28: Position & Velocity
The differential equation that describes the transverse motion of the particles as they move around our accelerator.
The solution of this second order describes oscillatory motion
For any system, where the restoring force is proportional to the displacement, the solution for the displacement will be of the form:

## Slide 29: Phase Space Plot
Plot the velocity as a function of displacement:
x
x0
x0
It is an ellipse.
As ωt advances by 2 π it repeats itself.
This continues for (ω t + k 2π), with k=0,±1, ±2,..,..etc

## Slide 30: Oscillations in Accelerators
x = displacement
x’ = angle = dx/ds
ds
x’
x
dx
x
s
Under the influence of the magnetic fields the particle oscillate

## Slide 31: Transverse Phase Space Plot
x
φ
φ = ωt is called the phase angle
X-axis is the horizontal or vertical position (or time).
Y-axis is the horizontal or vertical phase angle (or energy).
This changes slightly the Phase Space plot
X’
Position
Angle

## Slide 32: Transverse Phase Space Plot
Horizontal Phase Space
We distinguish motion in the Horizontal & Vertical Plane
x
φ
x’
y
φ
y’
Vertical Phase Space

## Slide 33: Transverse Emittance
To be rigorous we should define the emittance slightly differently.
Observe all the particles at a single position on one turn and measure both their position and angle.
This will give a large number of points in our phase space plot, each point representing a particle with its co-ordinates x, x’.
beam
x’
x
emittance
acceptance
The emittance is the area of the ellipse, which contains all, or a defined percentage, of the particles.
The acceptance is the maximum area of the ellipse, which the emittance can attain without losing particles
Symbol: e
Expressed in 1s, 2s,..
Units: mm mrad

## Slide 34
Vectors & Matrices
Differential Equations
A word on the units we use

## Slide 35: Relativity
CPS
velocity
energy
c
SPS / LHC
Einstein:
energy increases
not velocity
}
PSB
Newton:

## Slide 36: The Units we use for Energy
The unit eV is too small to be used today, we use:
  1 KeV = 103, MeV = 106, GeV = 109, TeV = 1012
The energy acquired by an electron in a potential of 1 Volts is defined as being 1 eV

## Slide 37: Energy: eV versus Joules
The unit most commonly used for Energy is Joules [J]
In accelerator and particle physics we talk about eV…!?
The energy acquired by an electron in a potential of 1 Volt is defined as being 1 eV
1 eV is 1 elementary charge ‘pushed’ by 1 Volt.
1 eV = 1.6 x 10-19 Joules

## Slide 38: The Energy in the LHC beam
The energy in one LHC beam at high energy is about 400 Million Joules
This corresponds to the energy of a TGV engine going at 160 km/h
...... but then concentrated in the size of a needle

## Slide 39: Energy versus Momentum
Einstein’s formula:
which for a mass at rest is:
The ratio between the total energy and the rest energy is
Then the mass of a moving particle is:
We can write:
Momentum is:
The ratio between the real velocity and the velocity of light is

## Slide 40: Energy versus Momentum
Therefore the units for
  momentum are: MeV/c, GeV/c, …etc.
  Energy are: MeV, GeV, …etc.
Attention:
  when β=1 energy and momentum are equal
  when β<1 the energy and momentum are not equal
Energy
Momentum

## Slide 41: A Practical Example (PSB-ISOLDE)
Kinetic energy at injection Ekinetic = 1.4 GeV
Proton rest energy E0=938.27 MeV
The total energy is then: E = Ekinetic + E0 = 2.34 GeV
We know that
, which gives γ = 2.4921
We can derive
, which gives β = 0.91597
Using
we get p = 2.14 GeV/c
In this case: Energy ≠ Momentum

## Slide 42: A Practical Example (PSB-PS)
Kinetic energy at extraction Ekinetic = 2 GeV
Proton rest energy E0=938.27 MeV
The total energy is then: E = Ekinetic + E0 = 2.94 GeV
We know that
, which gives γ = 3.128
We can derive
, which gives β = 0.948
Using
we get p = 2.79 GeV/c
In this case: Energy ≠ Momentum

## Slide 43
Pure mathematics is, in its way, the poetry of logical ideas.
Albert Einstein