## Slide 1: Normal-Conducting and Permanent Accelerator Magnets
CERN Accelerator School
BASIC CAS, 10th March 2025
Jérémie Bauche
CERN

## Slide 2: Acknowledgements
The first part of these slides, dedicated to the magnetic fields theory and electromagnets, is mostly from previous lectures from Thomas Zickler and Davide Tommasini, with some additions.
The second part, on permanent magnets, has been prepared based on material from Pierre Thonet (CERN), Gael Le Bec (ESRF), Johannes Bahrdt (Helmholtz Zentrum Berlin), and Ben Shepherd (STFC Daresbury Laboratory).
A big THANK YOU to all of them!

## Slide 3: Scope of this lecture
  About 5000 ‘room temperature’ magnets (50 000 tonnes) are installed in the CERN accelerator complex, in about 20 km of beam lines
  There is a large variety (about 500 different types), with different technologies to address different needs
  Today, we will mainly focus on ‘room temperature’ magnets i.e., normal-conducting (iron-dominated) electro-magnets, and on permanent magnets

## Slide 4: Outline
    Producing magnetic fields
      Why and how?
      Analogies with other domains
    Magnet technologies
      Technology classifications
      Electro-magnets (EM)
        EM components
        Magnet topologies and use in accelerators
      Permanent magnets (PM)
        Materials
        PM types in accelerators
        Comparison PM vs. EM
        Tuneable PM
    Spare slides

## Slide 5: Outline
    Producing magnetic fields
      Why and how?
      Analogies with other domains
    Magnet technologies
      Technology classifications
      Electro-magnets (EM)
        EM components
        Magnet topologies and use in accelerators
      Permanent magnets (PM)
        Materials
        PM types in accelerators
        Comparison PM vs. EM
        Tuneable PM
    Spare slides

## Slide 6: Why do we need magnets?
Interaction with the beam
  guide the beam to keep it on the orbit
  focus and shape the beam
Lorentz‘s force:
  for relativistic particles, B and E effects are equivalent if
  to produce effect of B = 1 T you need E = 3∙108 V/m = 300 MV/m !
  … practical limitation of E is only a few MV/m  use magnetic fields!
Cartoon by B.Touschek
„Right hand rule“ scheme as shown for positive charges
( is reversed for negative charges!)
„Left hand rule“ with this scheme also works!
My mnemonic is “F.B.I.” where I replace by which stands as a flow (current) of positive charges

## Slide 7: Maxwell‘s equations
Gauss‘ law for electricity:
Gauss‘ law of flux conservation:
Faraday‘s law of induction:
Ampere‘s law:
In 1873, Maxwell published "Treatise on Electricity and Magnetism" where he summarized discoveries of Coulomb, Øersted, Ampere, Faraday, Gauss et. al. in 4 mathematical equations:
James C. Maxwell
Notes: D = electric displacement
E = electric field
ε0 = dielectric constant of free space
J = current density
= electric charge density
Summarizes discoveries of Coulomb, Øersted, Ampere, Faraday, et. al. in four mathematical equations:
DIVERGENCE
1) Gauss's law of electricity describes the relationship between a static electric field and the electric charges that cause it: the net outflow of the electric field through any closed surface is proportional to the charge enclosed by the surface.
2) Gauss’ law of flux conservation: The total flux entering a closed surface equals the total flux exiting the same region – and there are neither sources nor sinks. In other words: the net magnetic flux out of any closed surface is zero and there are no "magnetic charges" or magnetic monopoles.
CURL
3) Faraday’s law: The induced electromotive force in any closed circuit is equal to the negative of the time rate of change of the magnetic flux through the circuit.
4) Ampere’s law: The line integral of the magnetic field around a closed loop is proportional to the electric current flowing through the loop (plus a term taking time-dependent electrical fields into account).
IF WE FOCUS TO MAGNETOSTATICS, as there are no time dependent fields, the equations for the electric and the magnetic parts become uncoupled, and we will need only 2 out of the 4 Maxwell equations:
First, we need Gauss’ law of flux conservation: Divergence B = 0 which means that the net magnetic flux out of any closed surface is zero
And second, we need the first part of Ampere’s law: Curl H = J which means that the line integral of the magnetic field around a closed loop is proportional to the electric current flowing through the loop. The second term for time-dependent electrical fields can be ignored in magnetostatics.
D = electric displacement
E = electric field
ε0 = dielectric constant of free space
J = current density
ρ = electric charge density

## Slide 8: Magnet vocabulary
IEEE defines the following terms and units:
Magnetic field:
  H (vector) [A/m] (1 Oersted = 79.58 A/m)
  magnetizing force produced by electric currents
Magnetic flux density or magnetic induction:
  B (vector) [T or kg/(A·s2)] (1 Gauss = 10-4 T)
  density of magnetic flux driven through a medium by the magnetic field
  Note: flux or induction is frequently referred to as "Magnetic Field“
Permeability:
  H and B relate by the constitutive law for materials: B = µH
  µ = µ0 µr
  permeability of free space µ0 = 4·π·10-7 [(V·s)/(A·m) or (kg·m)/(A·s2)]
  relative permeability µr (dimensionless): µair = 1; µiron > 1000 (not saturated)

## Slide 9: Producing the magnetic field
Maxwell & Ampere:
„An electrical current is surrounded by a magnetic field“
https://lewebpedagogique.com/
https://lewebpedagogique.com/
„Corkscrew “ (or „Right hand”) rule applies…
And this time, no “left” alternative!

## Slide 10: Analogy of electromagnetism with other domains
Generator
voltage supply
lamp (resistor)
wires
current
pump
hydraulic resistor
pipes
water flow
Hydraulic circuit
Electrical circuit
Magnetic circuit
Load
air gap
Transmission line
Flow

## Slide 11: Analogy of electromagnetism with other domains
Similar analogies exist with mechanics, electrostatics…

## Slide 12: Outline
    Producing magnetic fields
      Why and how?
      Analogies with other domains
    Magnet technologies
      Technology classifications
      Electro-magnets (EM)
        EM components
        Magnet topologies and use in accelerators
      Permanent magnets (PM)
        Materials
        PM types in accelerators
        Comparison PM vs. EM
        Tuneable PM
    Spare slides

## Slide 13: Magnet technologies
Magnets
Permanent magnets
Superconducting
Normal-conducting
Electro-magnets
adjustable field amplitude
zero electrical resistance
no ohmic losses
very high current densities
require cryogenic cooling
adjustable field amplitude
limited by the ohmic losses
dissipated power to be removed
only moderate current densities
require air or water cooling
fixed field amplitude
do not require powering
do not require cooling

## Slide 14: Magnet technologies
Magnets
Permanent magnets
Superconducting
Coil dominated
Normal-conducting
Iron dominated
Coil dominated
Iron dominated
Electromagnets
PM dominated
Iron dominated
SC cos theta dipole
Superferric dipole
NC cos theta dipole
NC dipole
PM Halbach dipole
PM quadrupole

## Slide 15: Coil dominated – Iron dominated
In coil-dominated magnets, the magnetic field in the aperture is shaped by the position of the conductors respectively the current distribution around the aperture
-> often superconducting



In iron-dominated magnets, the magnetic field is shaped by the geometry of the poles, which are surfaces of constant scalar potential
-> often normal-conducting
B1: normal dipole
B1: normal dipole
B2: normal quadrupole
B2: normal quadrupole

## Slide 16: Outline
    Producing magnetic fields
      Why and how?
      Analogies with other domains
    Magnet technologies
      Technology classifications
      Electro-magnets (EM)
        EM components
        Magnet topologies and use in accelerators
      Permanent magnets (PM)
        Materials
        PM types in accelerators
        Comparison PM vs. EM
        Tuneable PM
    Spare slides

## Slide 17: Iron dominated electromagnets
They represent the large majority of magnets in accelerators
They are mainly composed of
An electric circuit (coils) which produces the magnetic field
A magnetic circuit (yoke) which:
  confines the magnetic flux in the circuit to avoid stray flux
  shapes the magnetic field distribution in the region of interest
  enhances the magnetic effect induced by currents in the coils

## Slide 18: Creating the magnetic field
Flux lines represent the magnetic field
Coil colors indicate the current direction

## Slide 19: Confining the magnetic field
Coils hold the electrical current
Iron holds the magnetic flux

## Slide 20: Shaping the magnetic field
From Gauss’ law, Ampere’s law and the constitutive relation, we can derive that the flux lines in free space always meet a material with infinite permeability perpendicular to the surface (“surface of constant scalar potential”)
Conversely: If we can shape a material with infinite permeability such that its surface is everywhere perpendicular to our desired field configuration, then the only field that can exist around the material will be this desired field!

## Slide 21: Enhancing the magnetic field
I = 32 kA
Bcentre = 0.09 T
I = 32 kA
Bcentre = 0.80 T (for 50 mm of aperture)
The presence of a magnetic circuit can increase the flux density in the magnet aperture by factors!

## Slide 22: Excitation current in a dipole
Ampere’s law and with
leads to
assuming, that B is constant along the path
If then
then:

## Slide 23: Permeability
Chart: Excitation current NI [kA]
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
without iron | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
with iron (constant permeability) | 0 | 2.5 | 5 | 7.5 | 10
with iron (non-linear) | 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.45 | 1.6 | 1.7 | 1.8 | 1.88 | 2.2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5
Ferro-magnetic materials: high relative permeability (µr >>1), but not constant
Permeability: correlation between magnetic field strength H and magnetic flux density B
Consequence 1:
The path in the iron can no longer be fully neglected
Consequence 2: The flux lines will no longer meet the iron perpendicularly, creating field imperfections
Saturation: Increase of B above 1.5 T in iron requires non-proportional increase of H

## Slide 24: Ideal vs. real magnets
Ideal magnets have infinite permeability, and the poles are extended to infinity in all directions
Real magnets have high, but finite and non-linear permeability, and the poles are truncated to provide space for the coils

## Slide 25: Dipole
Purpose: bend or steer the particle beam
Applications: synchrotrons, transfer lines, spectrometry, beam scanning
Equation for normal (non-skew) ideal (infinite) poles: y =
 straight line with h = gap height
Magnetic flux density in aperture: B
 η ≈ 0.98 for non-saturated yoke
Magnetic flux density components: Bx = 0; By = B1 = const. (for “normal” dipole, i.e. H)
S
N

## Slide 26: Quadrupole
Purpose: focusing the beam (horizontally focused beam is vertically defocused)
Equation for normal (non-skew) ideal (infinite) poles: =
 hyperbola with r = aperture radius
Magnetic flux density in aperture: B
(η ≈ 0.98 for non-saturated yoke)
Magnetic flux density components: y ; x (for “normal” quadrupole)
S
S
N
N

## Slide 27: Sextupole
Purpose: correct chromatic aberrations of ‘off-momentum’ particles
Equation for normal (non-skew) ideal (infinite) poles:
(r = aperture radius)
Magnetic flux density in aperture: B
(η ≈ 0.98 for non-saturated yoke)
Magnetic flux density components: xy ; (“normal” sextupole)
S
N
S
S
N
N

## Slide 28: Summary of magnet types
Pole shape | Field distribution | Pole equation | B | Bx , By
 |  | y =  r =  h/2 | B = | Bx = 0 By = B1 = const.
 |  | 2xy =  r 2 | B | y x
 |  | 3x 2y –y 3 =  r 3 | B | xy /
 |  | 4(x 3y – xy 3) =  r4 | B | /
Pole shape | Field distribution | Pole equation | B | Bx , By
 |  | y =  r =  h/2 |  | Bx = 0 By = B1 = const.
 |  | 2xy =  r 2 |  | 
 |  | 3x 2y –y 3 =  r 3 |  | 
 |  | 4(x 3y – xy 3) =  r4 |  | 

## Slide 29: Conventional NC magnet layouts
Excitation coils carry the electrical current creating H
Iron yoke guide, enhance and shape magnetic flux
Auxiliaries for cooling, interlock, safety, alignment, ...
Tapered poles
Straight poles
Figure-of-eight
or
Collins
H-type
C-type
O-type
or
Window frame

## Slide 30: Outline
    Producing magnetic fields
      Why and how?
      Analogies with other domains
    Magnet technologies
      Technology classifications
      Electro-magnets (EM)
        EM components
        Magnet topologies and use in accelerators
      Permanent magnets (PM)
        Materials
        PM types in accelerators
        Comparison PM vs. EM
        Tuneable PM
    Spare slides

## Slide 31: Permanent magnet materials
In 600 b.C., stones of “magnetite” (iron oxide) found in Magnesia area, in Greece.
Most popular PM materials:
AlNiCo: alloy of Al, Ni, Co
Ferrites: ceramic compound mixing iron oxide and one (or more) of Sr, Ba, Mn, Ni, Zn
Rare earths: Lanthanides group (elements 57 to 71 in periodic table)
For accelerator magnets:
Samarium-Cobalt: SmCo5 and Sm2Co17 (Variants exist with Cu, Fe or Zr instead of Co)
Neodymium-Iron-Boron: Nd2Fe14B
Courtesy: Vacuumschmelze GmbH
Notes: AlNiCo is capable to produce up to 1.2 T in a closed magnetic circuit, but the flux density drops drastically when the magnetic circuit is open, what makes it impractical for accelerator magnets.

## Slide 32: PM characteristics
Distinction “soft” and “hard” (i.e. PM) magnetic materials: Hc soft < 200 Oe < Hc hard
BHmax is the maximum possible energy product, i.e. the capacity to produce magnetic field
Br is the maximum flux density that the PM can achieve in a closed magnetic circuit
Hcb is the coercivity which tells how much opposite H field is needed to cancel the Br
Hcj is the intrinsic coercivity which tells how much opposite H field is needed to fully demagnetize the magnet
For accelerator magnets:
Samarium-Cobalt:
  Br ≈ 1.1 T ; Hcb ≈ 10 kOe ; BHmax ≈ 32 MGOe (Sm2Co17)
  Good radiation and corrosion resistance
  Small temperature coefficient: -0,03 to -0,05 %/°C
Neodymium-Iron-Boron:
  Br ≈ 1.5 T ; Hcb ≈ 12 kOe ; BHmax ≈ 52 MGOe
  Strong magnetic field
  Larger temperature coefficient: -0,09 to -0,12 %/°C
BHmax
b
.
.
.

## Slide 33: Magnet technologies
Magnets
Coil dominated
Iron dominated
Electro-magnets
PM dominated
Iron dominated
Permanent magnets
The position of the conductors define the field pattern
The position of the iron poles define the field pattern
The position of the permanent magnet blocks define the field pattern (Halbach)
The position of the iron poles define the field pattern

## Slide 34: PM-dominated magnets
Halbach: field pattern defined by position and orientation of PM blocks
Evaluation of dipole field:
B ≈ Br . cos(π/M) . ln(R/r)
Br: remanent field
M: number of segments
R: external radius
r: internal radius
Magnets are placed around aperture with magnetization axis oriented along the flux line path (low ext. stray field)
 Very compact designs
 Sensitive to magnetization orientation of PM blocks
Klaus Halbach
Halbach designs: dipole (left), quadrupole (centre), sextupole (right)
PM dipole design of FASER experiment – P. Thonet
LINAC 4 PM quadrupole

## Slide 35: Iron-dominated PM
The field pattern is defined by the iron pole geometry (like in an iron-dominated EM)
The PM blocks only provide the magnetization of the magnetic circuit
Field quality is independent of errors of magnetization orientation of the PM blocks
Field amplitude can be increased w.r.t. Br of PM block with tapered poles
N-tof separation dipole – P. Thonet
AD target quadrupole – P. Thonet

## Slide 36: Comparison EM vs. PM
PM have significant advantages over EM, but also some limitations for their use in accelerator magnets
Main advantages of PM:
  No power consumption
  No powering and cooling infrastructure
  Fail safe and maintenance free
  Relatively compact and cheap
Main limitations of PM:
  Fixed field
  Field stability (T° dependence)
  Safety (magnetic hazards)

## Slide 37: Tuneable PM
Magnets
Electro-magnets
Fixed field
Permanent magnets
Hybrid magnets
Tuneable field
the magnetic circuit geometry is static
the field amplitude is tuned by powering auxiliary coils
the magnetic circuit geometry is variable
the field amplitude is tuned by modifying the magnetic circuit (with controllers, motors and mechanical linkage)

## Slide 38: Mechanically tuneable PM
Mechanical modification of the magnetic circuit to tune the field amplitude
Can be made in two ways:
 Changing the reluctance of the magnetic circuit:
  Moving yoke pieces (1)
 Deriving the magnetic flux to a parallel circuit:
  Moving yoke pieces (2)
  Moving the PM blocks (3)
Main limitations:
  Management of the forces and tolerances
  Reliability and time response of motors
  Cost (magnet and control system)
(3) ZEPTO quad. B. Shepherd
(1) AD target quad. – P. Thonet
(2) SPring-8-II dipole T. Watanabe, et al.

## Slide 39: Hybrid EM - PM
Combining coils with PM blocks in the same magnetic circuit to create a hybrid magnet
Main advantages:
  Main field can be tuned to a significant part of the nominal (up to ± 20 - 30 %)
  PM temperature dependence can be compensated by the coils
Main limitations:
  Risk of demagnetizing the PM blocks
  In designs where the PM and coils are in series in the magnetic circuit, the coil ampere-turns scale with the gap for the PM
CLIC final focusing quadrupole – A. Vorozhtsov, M. Modena

## Slide 40: Literature
CAS proceedings, Fifth General Accelerator Physics Course, University of Jyväskylä, Finland, September 1992, CERN Yellow Report 94-01
International Conference on Magnet Technology, Conference proceedings
Iron Dominated Electromagnets, J. T. Tanabe, World Scientific Publishing, 2005
Magnetic Field for Transporting Charged Beams, G. Parzen, BNL publication, 1976
Magnete, G. Schnell, Thiemig Verlag, 1973 (German)
Field Computation for Accelerator Magnets: Analytical and Numerical Methods for Electromagnetic Design and Optimization, S. Russenschuck, Wiley-VCH, 2010
Practical Definitions & Formulae for Normal Conducting Magnets, D. Tommasini, Sept. 2011
CAS proceedings, Magnetic measurements and alignment, Montreux, Switzerland, March 1992, CERN Yellow Report 92-05
CAS proceedings, Measurement and alignment of accelerator and detector magnets, Anacapri, Italy, April 1997, CERN Yellow Report 98-05
The Physics of Particle Accelerators: An Introduction, K. Wille, Oxford University Press, 2000
CAS proceedings, Magnets, Bruges, Belgium, June 2009, CERN Yellow Report 2010-004
CAS on Magnets, Sankt Polten, Austria, November 2023
Design and manufacturing of three permanent magnet dipoles for FASER experiment, Pierre Thonet, TE-MSC seminar, https://indico.cern.ch/event/1010394/

## Slide 41: Many thanks for your attention! … more information is available in the spare slides!

## Slide 42: Spare slides

## Slide 43: Hysteresis cycle
Hysteresis loop of (ferro-)magnetic materials:
First magnetisation (“virgin curve”):
  Dotted line
Saturation
  No more amplification of B by the material
Remanence:
  Residual magnetic flux density when H = 0
Coercive force
  Necessary opposite H to cancel remanence
Hysteresis loop
  Relation of B to H when the material is excited sequentially to +H and –H. The surface corresponds to the dissipated power of the hysteresis losses

## Slide 44: Design process
Field strength (gradient) and magnetic length
Integrated field strength (gradient)
Aperture and ‚good field region‘
Field quality:
    field homogeneity
    maximum allowed multi-pole errors
    settling time (time constant)
Operation mode: continous, cycled
Electrical parameters
Mechanical dimensions
Cooling requirements
Electro-magnetic design is an iterative process:
Collect input data
Analytical design
Numerical 2D/3D simulations
Mechanical design
Drawings & specifications
Magnet
Beam Optics
Power
Cooling
Vacuum
Survey
Integration
Safety
Certification
Transport
A magnet is not a stand-alone device!

## Slide 45: Costs and optimization
Focus on economic design!
Design goal: Minimum total costs over projected magnet lifetime by optimization of capital (investment) costs against running costs (power consumption)
Total costs include:
Attention:
Decreasing current density means:
increasing coil cross section
increasing material (coil & yoke) cost
increasing manufacturing cost
But:
decreasing capital costs for power converter and cooling system
decreasing operation costs
capital costs of magnets
capital costs of power converters
capital costs of power distribution
capital costs of cooling system
operation costs of power converters
operation costs of cooling system

## Slide 46: Massive vs. laminated yokes
Historically, the primary choice was whether the magnet is operated in persistent mode or cycled (eddy currents)
+ no stamping, no stacking
- time consuming machining, in particular for complicated pole shapes
- difficult to reach similar magnetic performance between magnets
+ less expensive for prototypes and small series
+ steel sheets less expensive than massive blocks
+ steel properties can be easily tailored
+ uniform magnetic properties over large series
- expensive tooling
+ less expensive for larger series

## Slide 47: Yoke manufacturing
Stamping laminations
Stacking laminations into yokes
Gluing and/or welding
Assembling the yoke parts

## Slide 48: Excitation coils manufacturing
Conductor insulation
Coil winding
Ground insulation
Epoxy impregnation
Testing
Conductor selection
Notes: []

## Slide 49: Coil cooling
Cooling is required to remove the dissipated electrical power from the coils
(Temperature acceptance of typical insulating materials is ~60°C)
Air cooling by natural convection:
  Only for low densities: j < 1 to 2 A/mm2, depending on coil size
  Cooling enhancement
    Heat sink with enlarged radiation surface
    Forced air flow (cooling fan)
  Only for magnets with limited strength (e.g. correctors)
Direct water cooling:
  Typical current density j ≤ 10 A/mm2
  Requires demineralized water (low conductivity) and hollow conductor profiles

## Slide 50: NC-magnets in the 1950-60s
CERN PS (1959), 25 GeV, 628 m
Combined function magnet: dipole + quadrupole + higher order multi-poles
Water cooled main coils + Figure-of-Eight windings + Pole-face windings
Magnetic field B: 0.014 T – 1.4 T
100 + 1 magnets in series
Notes: Let’s have a look back in the history of normal-conducting accelerator magnets:
Certainly, a milestone in the construction of synchrotrons is the CERN Proton-Synchrotron (PS), which is still in operation after more than 60 years!
The PS is a combined function machine, built in the late 50s, consists 100 + 1 magnet connected in series. A PS main magnet unit was built from 10 laminated blocks sitting on a common girder, water cooled main coils made of hollow aluminium conductor, which power the dipole and the quadrupole field simultaneously and can produce a magnetic field between 0.014 T and 1.4 T.
In addition, there are so called “Figure of Eight” windings which can adjust the quadrupole field gradient in a small range around the working point without changing the integrated bending field.
On top of the poles are additional actively powered windings, called “Pole Face Windings” (PFW) for sextupole correction. These PFW provide also compensation for a non-uniform field attenuation due to eddy currents in the vacuum chambers with a set of passive windings which are connected to a resistor network.

## Slide 51: NC-magnets in the 1970s
CERN SPS (1976), 7 km, 450 GeV
744 H-type bending magnets with B = 2.05 T

## Slide 52: NC-magnets in the 1980s
LEP (1989), 27 km
Cycled field: 22 mT (20 GeV injection) to 108 mT (100 GeV)
5.75 m long ‘diluted’ magnet cores: 30% Fe / 70% concrete
Four water cooled aluminium excitation bars
Max. current: 4.5 kA

## Slide 53: NC-magnets even in the LHC …
Double-aperture LHC quadrupole
LHC Main Dipole
What about the future…?

## Slide 54: Circular Colliders
Chart: Circumference [m]
| 3 | 12 | 2.7 | 12 | 22 | 18 | 300 | 2000 | 768 | 27000 | 240 | 366 | 2200 | 3000 | 98 | 768 | 24 | 240 | 100000 | 54000
Lepton colliders | 0.83503 | 1.0017 | 0.43503 | 2.335 | 1.6684 | 2.335 | 16.6684 | 66.6684 | 20.0017 | 346.6684 | 7.335 | 20.0017 | 30.0017 | 26.6684 | 2.335 | 20.0017 | 3.335 | 6.335 | 583.335 | 400.0017
Hadron colliders | 108.0815 | 1053.122 | 3003.125 | 3269.7918 | 853.1209 | 23336.4598 | 3069.7917 | 46669.7932 | 166669.7933 | 116669.7933

## Slide 55: Future challenges
Large scale machines:
  Investment cost: material, production, transport, installation
  Operation costs: power consumption & cooling
  Reliability & availability
High energy beams and intensities:
  Ionizing radiation impact on materials and electronics
Hadron colliders:
  High magnetic fields
Lepton colliders (circular & linear):
  Alignment & stabilization
  Compact design & small apertures
Future accelerator projects bear a number of financial and technological challenges in general, but also in particular for magnets …
“2-Beams Modules” with 41848 DBQ and 4274 MBQ magnets
Machine-Detector Interface (MDI) with the FF system

## Slide 56
Twin-aperture dipole
Twin-aperture quadrupole
FCC energy efficient magnets
About 24000 magnets will be needed for the booster and collider of FCC-ee!
Energy saving: Ampere-turns recycled  50% less power consumption
Cost saving: 50% less units to manufacture, transport, install, align
  Simple and reliable: few components
  Simple yoke design and coil layout  low manufacturing costs
  No coil inter-turn insulation (dipoles)
Compact: small dimensions, less material

## Slide 57: Production of sintered PM blocks
The crystals of the base materials have an “easy axis” of magnetic orientation
Final magnetization direction will follow the one defined by initial orientation!

## Slide 58: Assembly of PM
The assembly of a PM based accelerator magnet is generally not straight forward
It requires:
Measurement of the PM blocks properties
  Field amplitude and direction (Helmholtz coils)
Possibly, a sorting of the PM blocks
  Compensating field errors in PM dominated magnets
Specific tooling
  To deal with the magnetic forces
  The magnet is always on!
Magnetic measurements
  Polarity checks during assembly
Packaging
  Safety during transport
PM dipole design of FASER experiment – P. Thonet
Helmholtz coils