## Slide 1: Plasma Wakefield Acceleration and the AWAKE Experiment at CERN
Edda Gschwendtner, CERN
CAS course on Basics of Accelerator Physics and Technology
10 – 14 March 2025, Ferney-Voltaire, France

## Slide 2: Conventional Acceleration Technology
Very successfully used in all accelerators (hospitals, scientific labs,…) in the last 100 years.
LHC cavity
2
  (invention of Gustav Ising 1924 and Rolf Wideroe 1927)
E. Gschwendtner, CERN
Typical gradients:
  LHC: 5 MV/m
  ILC: 35 MV/m
  CLIC: 100 MV/m

## Slide 3: Circular Accelerators
To discover new physics: accelerate particles to even higher energies
Conventional RF cavities ok for circular colliders:
beam passes accelerating section several times.
Limitations of electron-positron circular colliders:
Circular machines are limited by synchrotron radiation in the case of electron-positron colliders.
These machines are unfeasible for collision energies beyond ~350 GeV in case of FCCee.
Notes: For hadron colliders, the limitation is magnet strength. Ambitious plans like the FCC call for 16 T magnets in a 100 km tunnel to reach 100 TeV proton-proton collision energy.

## Slide 4: Linear Colliders
 48 km
CLIC, electron-positron collider with 3 TeV energy
Favorable for acceleration of low mass particles to high energies.
Limitations to linear colliders:
Linear machines accelerate particles in a single pass. The amount of acceleration achieved in a given distance is the accelerating gradient. This number is limited to 100 MV/m for conventional copper cavities.
Particle energy = accelerating gradient*distance
e.g. accelerate electrons to 1 TeV (1012 eV):
100 MeV/m x 10000 m or
100 GeV/m x 10 m
Accelerating cavities
Stanford Linear Collider
50 GeV  3.2 km

## Slide 5: Accelerating Gradient
5
E. Gschwendtner, CERN
Accelerating fields are limited to <100 MV/m
In metallic structures, a too high field level leads to break down of surfaces, creating electric discharge.
Fields cannot be sustained; structures might be damaged.
Conventional RF Cavities
Plasma is already ionized or “broken-down” and can
sustain electric fields up to three orders of magnitude higher gradients
 order of 100 GV/m.
 ~1000 factor stronger acceleration!
Plasma Acceleration

## Slide 6: Plasma Wakefield Acceleration
100 MV/m  100 GV/m
MC
10 TeV
The high gradient of plasma wakefield acceleration makes this technology very interesting for reducing the size (and cost) for future linear colliders.

## Slide 7: Plasma Wakefield Acceleration
PLASMA is the 4th state of matter
Quasi-neutrality: the overall charge of a plasma is about zero. Collective effects: Charged particles must be close enough together
that each particle influences many nearby charged particles.
Electrostatic interactions dominate over collisions or ordinary gas kinetics.
Plasma WAKEFIELDS are the fields created by collective motion of plasma particles are called.
ACCELERATION of charged particles when they experience an electric field.
Strength of the acceleration:
‘Accelerating gradient’ : ~MV/m

## Slide 8: How to Create a Plasma Wakefield?
surfer
boat
lake
Analogy:
lake  plasma
Boat  particle beam (drive beam)
Surfer  accelerated particle beam (witness beam)
E. Gschwendtner, CERN

## Slide 9: How to Create a Plasma Wakefield?
What we want:
Longitudinal electric field to accelerate charged particles.
Using plasma to convert the transverse electric field of the
drive bunch into a longitudinal electric field in the plasma.
The more energy is available, the longer (distance-wise) these
plasma wakefields can be driven.
Charged particle bunches or laser beam carry almost purely transverse Electric Fields.
drive-beam
Boat
Our Tool:
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e
e
e
e
e
e
e
e
e
e
Single ionized rubidium plasma
Lake
e-
e- acceleration
Surfer

## Slide 10: Principle of Plasma Wakefield Acceleration
Drive beam (boat):
Laser drive beam
Charged particle drive beam
Plasma wave/wake excited by relativistic particle bunch
Plasma e- are expelled by space charge force
Plasma e- rush back on axis
Ultra-relativistic driver – ultra-relativistic wake  no dephasing
Acceleration physics identical for LWFA, PWFA
plasma wavelength λpe = mm-scale

## Slide 11: Where to Place the Witness Beam (Surfer)?
Accelerating for e-
Decelerating for e-
Focusing for e-
Defocusing for e-
e-
Longitudinal and transverse wakefields are π/2 out of phase.
 Only ¼ of the electron oscillation length is focusing and accelerating for charged particles!

## Slide 13
Plasma Wakefield, Density Scaling
Drive bunch traveling inside a plasma perturbs the plasma electron distribution.
 oscillation with
c
ωpe
2π
λpe
=
Maximum accelerating gradient increases with increasing plasma density.
Plasma electron wavelength decreases with increasing plasma density.
The plasma oscillation leads to a longitudinal accelerating field:
The maximum accelerating field (wave-breaking field) is:
Example: npe = 1x1018 cm-3  EWB = ~100 GV/m  λpe = ~30 µm
Example: npe = 7x1014 cm-3 (AWAKE)  EWB = 2.5 GV/m  λpe = 1.2 mm

## Slide 14: Seminal Paper 1979, T. Tajima, J. Dawson
Use a plasma to convert the transverse space charge force of a beam driver into a longitudinal electrical field in the plasma

## Slide 15: State-of-the-Art
9.2 GeV in 30 cm  30.7 GeV/m
BELLA, Berkeley Lab, USA
A. Picksley et al., PRL 133, 255001 (2024)
Laser Driven
I. Blumenfeld et al, Nature 455, p 741 (2007)
42 GeV in 85 cm  52 GeV/m
FACET, SLAC, USA
Electron Driven
Transfer efficiency 42+/-4% with 0.2% energy spread, up to 70% with energy spread increase
C.A. Lindstrøm et al., Phys.Rev.Lett. 126, 014801 (2021)
FLASHForward, DESY
Electron Driven
A. Maier et al., Phys. Rev. X 10, 031039 (2020)
Stable 24hr operation
LUX laser plasma accelerator, DESY
Laser Driven
FEL lasing amplification of 100 reached at 27nm wavelength
Laser Driven based FEL: First demonstration
500 MeV electrons from LWFA
W.T. Wang, K. Feng, et al., Nature, 595, 561 (2021)
Electron Driven based FEL: First demonstration
R. Pompili et al., Nature 605, 659-662 (2022)
94 MeV electrons from PWFA
FEL lasing at 830 nm
Since then two more groups: Soleil/HZDresden, Berkeley
China
Sparc-Lab
Notes:     FLASHForward: ≲ 1.25 GeV energy with a few 100 pC at ~100 fs rms bunch duration, up to 1MHz repetition rate, few kW average power
    63ns

## Slide 16: State of the Art and Goals for HEP Collider
 Requires international, multi-dimensional R&D efforts.
ESPP 2020:
Plasma R&D Roadmap
US Snowmass and P5
R&D Efforts

## Slide 17: Towards Higher Energies – Electron/Laser Drivers
Electron/laser driven PWA: need several stages, and challenging wrt to relative timing, tolerances, matching, etc…
  effective gradient reduced because of long sections between accelerating elements….
Witness beam
Drive beam: electron/laser
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Drive beams (Boat):
Lasers: ~40 J/pulse
Electron drive beam: 30 J/bunch
Witness beams (Surfers):
Electrons: 1010 particles @ 1 TeV ~few kJ
To reach TeV scale:

## Slide 18: Towards Higher Energy – Proton Drivers
Witness beam
Drive beam: protons
Plasma cell
Proton drivers: large energy content in proton bunches  allows to consider single stage acceleration:
  A single SPS/LHC bunch could produce an ILC bunch in a single PDWA stage.
Drive beams (Boat):
Lasers: ~40 J/pulse
Electron drive beam: 30 J/bunch
Proton drive beam: SPS 19kJ/pulse, LHC 300kJ/bunch
Witness beams (Surfers):
Electrons: 1010 particles @ 1 TeV ~few kJ
To reach TeV scale:
With existing proton beams the energy frontier with electrons can be reached!
SPS p+ (450 GeV): accelerate to 200 GeV electrons.
LHC p+ can yield to 3 TeV electrons.
A. Caldwell et al., Nature Phys. 5, 363–367 (2009)
Witness bunch energy along plasma.
1 TeV proton driver

## Slide 19: Proton Bunch as a Drive Beam
  In order to create high wakefield amplitudes, the drive bunch length must be in the order of the plasma wavelength.
  CERN SPS proton bunch: very long! (sz = 6 - 10 cm)  much longer than plasma wavelength (l = 1mm)
   Would create only small wakefield amplitudes.

## Slide 20: Self-Modulation of the Proton Bunch
Density modulation on-axis  micro-bunches.
  Micro-bunches separated by λpe.
  Resonant wakefield excitation
  Large wakefield amplitudes
Initial transverse wakefields
Periodic focusing/defocusing fields
Radial bunch and plasma density modulation
Stronger wakefields
Full modulation
Self-Modulation Instability:
 Immediate use of SPS proton bunch for driving strong wakefields!
p+ bunch

## Slide 21
The AWAKE Experiment

## Slide 22: AWAKE is an International Collaboration
Strong commitment from 19 institutes

## Slide 23: AWAKE’s Strong Scientific and Educational Output
> 70 papers related to AWAKE
> 90 Conference proceedings and papers
CERN Teacher Program
AWAKE courses and seminars
USPAS, JUAS, CAS
23 AWAKE Collaboration papers in high-level journals
> 28 PhD students
> 11 Master students
> 20 Post-docs
Outreach: Newspapers, TEDX, …
 5 doctoral thesis prizes, 2 early career awards!

## Slide 24: AWAKE at CERN
E. Gschwendtner, CERN
The only proton driven plasma wakefield acceleration experiment worldwide.
High energy gain possible because the high-energy driver is available today.
Advanced WAKEfield Experiment
Accelerator R&D experiment.
Unique facility driving wakefields in plasma with 400 GeV proton bunch from the SPS.
Accelerating externally injected electrons to GeV scale.

## Slide 25: AWAKE at CERN
AWAKE experiment
beam dump
~1100m
SPS
LHC
protons
~1000m
Control
room
~50m
AWAKE
AWAKE installed in CERN underground area

## Slide 26: AWAKE has a Well-Defined Program
p+ self-modulation
2 GeV e- acceleration
RUN 1 (2016-2018)
e- acceleration to several GeV,
beam quality control, scalability
RUN 2 (2021-2033)
First applications >2034
 Move from proof-of-concept towards an accelerator

## Slide 27: AWAKE Experiment until Today
p+ self-modulation
2 GeV e- acceleration
RUN 1 (2016-2018)
e- acceleration to several GeV,
beam quality control, scalability
RUN 2 (2021-2033)

## Slide 28: AWAKE Experiment and Results
Ti: Sapphire Laser
Ti:Sapphire
500mJ
120 fs
10m Plasma source in AWAKE tunnel
Rubidium vapour
Density: 1014 – 1015 cm-3
Density uniformity < 0.2%
400 GeV
3x1011 p
400ps
750m proton beam line

## Slide 29: AWAKE Experiment and Results
400 GeV
3x1011 p
400ps
AWAKE Collaboration, Phys. Rev. Lett. 122, 054802 (2019).
M. Turner et al. (AWAKE Collaboration), Phys. Rev. Lett. 122, 054801 (2019).
M. Turner, P. Muggli et al. (AWAKE Collaboration), Phys. Rev. Accel. Beams 23, 081302 (2020)
F. Braunmueller, T. Nechaeva et al. (AWAKE Collaboration), Phys. Rev. Lett. July 30 (2020).
A.A. Gorn, M. Turner et al. (AWAKE Collaboration), Plasma Phys. Control Fusion, Vol. 62, Nr 12 (2020).
F. Batsch, P. Muggli et al. (AWAKE Collaboration), accepted in Phys. Rev. Lett. (2021)
#1: Demonstration of Seeded Self-Modulation of the Proton bunch
400 GeV
3x1011 p
400ps
750m proton beam line
Ti: Sapphire Laser
10m Plasma source in AWAKE tunnel
Ti:Sapphire
500mJ
120 fs

## Slide 30: AWAKE Experiment and Results
Laser line
Electron source
Diagnostics and booster structure
Transfer line
20 MeV electron line
Diagnostics

## Slide 31: Results: Electron Acceleration
No accelerated electrons
Accelerated electrons
Convert pixel-size and dipole setting to energy
Acceleration up to 2 GeV has been achieved.
Charge capture up to 20%.
AWAKE Collaboration, Nature 561, 363–367 (2018)
E. Gschwendtner, CERN
#2: Demonstration of Electron Acceleration in Plasma Wakefield

## Slide 32: Run Results – Stabilizing Large Wakefield Amplitudes
Introducing a density step in the plasma cell
stabilization of the micro-bunches
Increased wakefield amplitudes after SSM saturation
New Rubidium vapour source with density step installed in 2023
Length: ~ 10 m, independent electrical heater of 50 cm from 0.25 to 4.75 m, Step height up to ±10%
10 diagnostic viewport  to measure light emitted by wakefields dissipating after the passage of the proton bunch
K. V. Lotov, Physics of Plasmas 22, 103110 (2015)
K. V. Lotov and P. V. Tuev 2021 PPFC 63 125027

## Slide 33: Run 2b - Stabilizing Large Wakefield Amplitudes
Effect of density step in the plasma source
Optimizing the proton bunch self-modulation
Accelerated electrons
AWAKE Collaboration

## Slide 34: Other Scientific Results
AWAKE
collaboration
All milestones achieved – plus additional ones.
  Relevant studies for general plasma wakefield acceleration concepts.
Wakefield growth due to SM
M. Turner et al. (AWAKE Collaboration), ‘Phys. Rev. Lett. 122, 054801 (2019).
Ion motion, Sim/Meas
preliminary
M. Turner, CERN, AWAKE Collaboration
Seeding with relativ. ionization front
F. Batsch, P. Muggli et al. (AWAKE Collaboration), Phys. Rev. Lett. 126, 164802 (2021).
Seeding with electron bunch
L. Verra et al. (AWAKE Collaboration), Phys. Rev. Lett. 129, 024802 (2022)
Beam-hose instability
T. Nechaeva, et al. (AWAKE Collaboration), Phys. Rev. Lett. 132, 075001 (2024).
Filamentation instability
L. Verra, et al. (AWAKE Collaboration), Phys. Rev. E 109, 055203 (2024).

## Slide 35: AWAKE: What’s Next?
e- acceleration to several GeV,
beam quality control, scalability
RUN 2 (2021-2033)

## Slide 36: AWAKE Run 2 – Electron Beam Quality
Expected accelerated electron beam parameters:
Normalized emittance: (2-30) mm mrad
Qe = 100 pC
dE/E: 5-8 %
Run 2c: E ~ 4-10 GeV in 10 m
Demonstrate electron acceleration and emittance control of externally injected electrons.
E. Gschwendtner, CERN
Self-modulator plasma
Accelerator plasma
on-axis e-beam injection
New electron beam: 150 MeV, 200 fs, 100 pC, σ = 5.75 µm
bunch length shorter than plasma wavelength
On-axis injection, Blow-out regime, Beam loading: reach small ∂E/E, Match electron beam transverse properties to the plasma
Start in 2029
Notes: beam size at injection of 5.75 µm (for an emittance of 2 µm and beta of 4.8 mm)

## Slide 37: Preparing for AWAKE Run 2 during LS3
CERN Neutrino Gran Sasso area content (~600m3):
~500 large shielding blocks (0,05-0,6 mSv/h)
A few high dose-rate elements (50mSv/h)
70-meter-long aluminum He-tank
Various supports, ducts…

## Slide 38: AWAKE Run 2: New Layout, New Components
Laser system
 Installation during LS3

## Slide 39: AWAKE Run 2: New Layout, New Components
Laser system
 Physic Run starts in 2029 after LS3

## Slide 40: AWAKE Run 2 – Demonstrate Scalability
Development of scalable plasma sources to 100s meters length with sub-% level plasma density uniformity
E. Gschwendtner, CERN
Scalable plasma source
Self-modulator plasma
Accelerator plasma
Expected accelerated electron beam parameters:
Normalized emittance: (2-30) mm mrad
Qe = 100 pC
dE/E: 5-8 %
Run 2c: E ~ 4-10 GeV in 10 m
Run 2d: E > 10 GeV in 10+ m
1m Helicon Plasma Source
10m Discharge Plasma Source  prototype successfully tested in 2023

## Slide 41: Once AWAKE Run 2 is Demonstrated
First applications >2034

## Slide 42: First Applications of AWAKE Technology
Requirements on emittance are moderate for first applications.
    First applications to high energy physics for 50 GeV beam:
      Beam-dump experiments to e.g. search for dark photons.
      Use for collider, e.g. ep collider, which would be like a low-luminosity LHeC.
      Interaction with high-power laser to investigate strong-field QED.
        Can investigate new region with high energy.
        Currently no competitors.
        Only modest laser needed.
        Increasing laser power  probe more phase space.
Experimental conditions modeled on NA64 experiment.

## Slide 43: Collider Concepts Based on Plasma Wakefield
J. Farmer, A. Caldwell, A. Pukhov, 2024, arXiv:2401.14765
e+ e- collider, 250 GeV c.o.m.
proton driven
 international, multi-dimensional R&D efforts
E. Adli et al., 2013, arXiv:1308.1145
e+e- collider, 1 TeV c.o.m., electron driven
E. Gschwendtner et al. (AWAKE Collaboration), Symmetry 2022,14,1680
Fixed target dark matter experiment.
50 GeV electrons, proton-driven
C.B.Schroeder et al., 2023, JINST 18 T06001, arXiv:2203.08366
e+ e- collider, 1 TeV c.o.m., laser driven
B. Foster, R. D’Arcy, C. Lindstrom, 2023, New J.Phys. 25 093037
e+e- collider, e+ 31GeV (conventional), e- 500 GeV (electron driven)
HALHF
250 GeV c.o.m.

## Slide 44: Summary
Plasma wakefield acceleration have demonstrated significant achievements and an enormous potential. Reaching higher energies (>10 GeV) with plasma wakefield acceleration require either plasma staging when using laser/electron drive beams, or using a proton driver in a single plasma source such as in AWAKE.
The AWAKE Run 2 experiment exploits the unique possibilities of the CERN injector complex, adds to the diversity of the CERN experiments and addresses key challenges relevant for plasma-based accelerator community.
The community has moved from proof-of-concept towards designing accelerators for applications and colliders. Coordinated R&D programs take shape within the Particle Physics planning exercises. Technology R&D is crucial to advance the programs.