## Slide 1: Linear Imperfections
Jörg Wenninger
CERN Beams Department
Operation group / LHC
CAS course on
Basics of Accelerator Physics and Technology,
10 – 14 March 2025

## Slide 2
Introduction
Imperfection - sources
Orbit perturbations
Linear imperfections, geology and vibrations
Summary

## Slide 3: Accelerator lattice cell
An accelerator is typically build using a number of basic ‘cells’.
The cell layouts of accelerators come in many variants.
For today we consider a simple FODO cell containing:
  Dipole magnets to bend the beams,
  Quadrupole magnets to focus the beams,
  Beam position monitors (BPM) to measure the beam position,
  Small dipole corrector magnets for beam steering.
beam
Schematic of a ½ cell
Quadrupole
(focussing)
Quadrupole
(de-focussing)
Dipole
Dipole
Beam position monitor
Beam position monitor
Dipole corrector
Dipole corrector

## Slide 4: Dipole magnet
The dipole has two magnetic poles and generates a homogeneous field providing a constant force on all beam particles – used to deflect the beam.
  A dipole corrector is just a small version of such a magnet, dedicated to steer the beam.
Fx
x
Horizontal deflection
By
Fy
x
Vertical deflection
Bx
Lorentz force:
orthogonal to the speed and magnetic field directions
x
y
90 rotation

## Slide 5: Quadrupole magnet
A quadrupole has 4 magnetic poles.
A quadrupole provides a field (force) that increases linearly with the distance to the quadrupole centre – provides focussing of the beam.
  Similar to an optical lens, but a quadrupole is focussing in one plane, defocussing in the other plane.
Force pushes the particle towards the center  focussing
Force pushes the particle away from the center  defocussing

## Slide 6: Recap on beam optics
Quantities related to a beam optics in a circular accelerator will be needed for the lecture:
  The betatron function (b) that defines the beam envelope,
    Beam size / envelope is proportional to b
  The betatron phase advance (m) that defines the phase of an oscillation.
LHC optics at injection
zoom
zoom
one cell

## Slide 7: Recap on beam optics
Consider a particle moving in a section of the accelerator lattice. The focussing elements make it bounce back and forth.
This periodic oscillation is called the betatron oscillation.
…
one cell
one cell
Another section of the accelerator
Another section of the accelerator

## Slide 8: Recap on beam optics for pedestrians
The number of oscillation periods over one machine turn is called the machine tune (Q) or betatron tune.
  In this example Q is around 2.75 – 2 periods and ¾ of a period.
With a coordinate change (from longitudinal position in meters to betatron phase advance in degrees) this ‘rocky’ oscillation is transformed into a sinusoidal oscillation.
  Convenient and simple way to analyse the beam motion.
Betatron phase m
1 period
1 period
1 period
Longitudinal coord. s
position
position/b

## Slide 9: Physical and normalized coordinates
Example of coordinate transformation for trajectory in a LEP arc lattice
Physical coordinate : the is the real trajectory !
y position versus longitudinal position
Normalized coordinate :
y position normalized to  versus longitudinal position
Normalized coordinate :
y position normalized to  versus phase advance
De-focusing quadrupoles
Focusing quadrupoles
Observe how focusing quadrupoles bend the beam towards y = 0, while the opposite holds for de-focusing quadrupoles

## Slide 10
Introduction
Imperfection - sources
Orbit perturbations
Linear imperfections, geology and vibrations
Summary

## Slide 11: Imperfections
The first step in the design phase of an accelerations consists in building an “ideal” accelerator where all magnets have nominal fields and are perfectly aligned along the design trajectory.
But the designer must soon confront the real world, and tolerances on errors (= imperfections) must be defined to provide specifications for component design, manufacturing and alignment.
  What is the precision on field quality?
  What is the precision and stability of the power converter that feeds current into a magnet?
  What is the tolerance on the component alignment?
  What about vibrations, ie non-static errors?
  …
This lecture will discuss the impact of the simplest form of imperfections, the linear imperfections.
  And among the linear imperfections, I will focus on imperfections due to dipole fields.

## Slide 12: From model to reality - fields
The physical units of the machine model defined by the accelerator physicist must be converted into magnetic fields and eventually into currents for the power converters that feed the magnets.
Imperfections (= errors) in the real accelerator optics can be introduced by uncertainties or errors on:
  Beam momentum, magnetic field model and power converter regulation.
Example of the LHC main dipole calibration curve
Magnet strength
(angle, focal length…)
Magnetic field or gradient
(T, T/m, T/m2…)
Requested current
(A)
Beam momentum
Magnet
calibration curve (transfer function)
Power converter
Actual magnet current
(A)
Accelerator physicist

## Slide 13: From the lab to the tunnel

## Slide 14: From model to reality - alignment
To ensure that the accelerator elements are in the correct position the alignment must be precise – to the level of micrometres for a linear collider like CLIC !
  At the CERN hadron machines we aim for accuracies of around 0.1-0.3 mm.
The alignment process implies:
  Precise measurements of equipment in the laboratory with reference to the element alignment markers used by the survey group: for example, the magnetic axis.
  Precise in-situ alignment (position and angle) of the element in the tunnel.
Alignment errors (and vibrations) are a common source of imperfections.

## Slide 15: A good attitude in the tunnel
Always remember that accelerator components in the CERN tunnels are carefully aligned, please treat them with respect !
Please use the ladder !
(also, for your own safety)

## Slide 16
Introduction
Imperfection - sources
Orbit perturbations
Linear imperfections, geology and vibrations
Summary

## Slide 17: Imperfection – undesired deflection
Linear imperfections are the simplest form of machine errors involving dipole and quadrupole fields – we will focus today solely on dipole fields.
The presence of an unintended deflection along the path of the beam is a first category of imperfections.
This case is also in general the first one that is encountered when beam is first injected into a machine, or when a beam is launched into a linac.
The dipole orbit corrector is added to the accelerator cells to compensate the effect of unintended deflections.
  With the orbit corrector we can generate a deflection of opposite sign and amplitude that compensates locally the imperfection.
What are causes of unintended deflection?

## Slide 18: Unintended deflection
The first source is a field error (deflection error) of a dipole magnet.
This can be due to an error in the magnet current or in the calibration table (measurement accuracy etc).
  The imperfect dipole can be expressed as a perfect one + a small error.
=
+
real dipole
ideal dipole
small dipole error
A small rotation (misalignment) of a dipole magnet has the same effect, but in the other plane.
=
+
real dipole
ideal dipole
small dipole error

## Slide 19: Unintended deflection
=
+
real quadrupole
ideal quadrupole
The second source is a misalignment of a quadupole magnet.
  The misaligned quadrupole can be represented as a perfectly aligned quadrupole plus a small deflection.
small dipole error
No magnetic field on the beam axis
Non-zero magnetic field on the beam axis !

## Slide 20: Effect of a deflection
We set the machine tune to an integer value:
  Q = n N
Turn no 1
Turn no 2
Turn no 3
Turn no 4
Deflection
Particle direction
When the tune is an integer number, the deflections add up on every turn !
  The amplitudes diverge, the particles do not stay within the accelerator vacuum chamber.
  We just encountered our first resonance – the integer resonance that occurs when Q = n N

## Slide 21: Effect of a deflection
We set the machine tune to a half integer value:
  Q = n+0.5, n N
Turn no 1
Deflection
Particle direction
For half integer tune values, the deflections compensate on every other turn !
  The amplitudes are stable.
  This looks like a much better working point for Q!
Turn no 2
Turn no 3
Turn no 4

## Slide 22: Effect of a deflection
We set the machine tune to a quarter integer value:
  Q = n+0.25, n N
Turn no 1
Deflection
Particle direction
For quarter tune values, the deflections compensate every four turns !
  The amplitudes are stable.
  Also a reasonable working point for Q!
Turn no 2
Turn no 3
Turn no 4

## Slide 23: Many turns reveal something
Q = n + 0.5
Q = n + 0.4
Q = n + 0.3
Q = n + 0.2
Q = n + 0.05
The particles oscillate around a stable mean value (Q ≠ n)!
The amplitude diverges as we approach Q = n  integer resonance
Q = n + 0.1
Q = n
Let’s plot the 50 first turns on top of each other and change Q.
  All plots are on the same scale

## Slide 24: The closed orbit
The stable mean value around which the particles oscillate is called the closed orbit.
  Every particle in the beam oscillates around the closed orbit.
  As we have seen the closed orbit ‘does not exist’ when the tune is an integer value.
The general expression of the closed orbit x(s) in the presence of a deflection q is:
oscillating term
kink at the location of the deflection
divergence for Q = n
amplitude modulated by the envelope b
Orbit response

## Slide 25: Closed orbit example
Example of the horizontal closed orbit for a machine with tune Q = 6 + q.
The kink at the location of the deflection () can be used to localize the deflection (if it is not known)  can be used for orbit correction.
Q = 6.5
Q = 6.2
Q = 6.1
Q = 6.9
Q = 6.7

## Slide 26: A deflection at the LHC
In the example below for the 26.7km long LHC, there is one undesired deflection, leading to a perturbed closed orbit.
BPM index along the LHC circumference
Beam position x (mm)
This is what you see in the control room
Where is the location of the deflection?

## Slide 27: A deflection at the LHC
Beam position x/b
To make our life easier we divide the position by b(s) and replace the BPM index by its phase m(s)  to normalized coordinates.
Can you localize the deflection?
Betatron phase m

## Slide 28: A more realistic case at LHC
Now a more realistic orbit with 100’s of deflections.
How do we proceed to correct?

## Slide 29: Orbit correction
Nowadays there are two main approaches for orbit correction:
  Matrix inversion algorithms relying on the knowledge the response R(s).
    R(s) is measured or calculated.
    Popular algorithms: MICADO and SVD (Singular Value Decomposition), both come with many variants.
  Machine learning with a neural network that is trained to find a solution.
    The training may be based on data or on a model, or on continuous reward-like training.
Inversion algorithms have the advantage of higher intrinsic flexibility (correction quality and flexibility, noise reduction,…), they can be reused at different machines without need for tuning – they are in a sense ‘universal’.
  Good convergence even for error on b of 30%.
Machine learning based technique are adapted to situations where models are difficult to establish, change over time, for example in low energy machines and some linacs. A model trained on a certain machine cannot be reused elsewhere.

## Slide 30: LHC orbit correction example
The raw orbit at the LHC can have huge errors, correction reduce the errors by > factor 20.
  Tuning the LHC orbit takes ~2-4 hours for both beams and planes (with fine features around experiments)
MICADO & SVD
LHC vacuum chamber
44 mm
34 mm
50 mm
Corrected horizontal orbit of ring 1
At the LHC a good orbit correction is a key to good performance !
Uncorrected horizontal orbit of ring 1
50 mm

## Slide 31
Linear imperfection,geology
and vibrations
Image: NASA/NOAA
Deep Space Climate Observatory (DSCOVR) satellite

## Slide 32: Static and dynamic
So far, we have considered the imperfections (deflections) as “static”.
In the real world, imperfections evolve over time:
  The ground is moving around components  quadrupoles deflections will vary over time.
  The current sources of a magnet may not deliver a perfectly constant current, for example due to regulation ripple or imperfect filtering (50 Hz and many of its harmonics).
  …
The problem of imperfections, for example those impacting trajectories and orbits, is dynamic, extending over a large frequency range.

## Slide 33: Vibrating Earth
The ground below our feet is in constant movement over a large range of frequencies.
  Slow deformations due to tectonic movements, daily deformations due to tides,
  Vibrations due to ocean waves, seismic activity, human activity…
  The amplitudes generally decrease at higher frequencies.
C. Collette et al, PRAB 13, 072801
The integrated ground movement due to noise > 1 Hz is ~1-20 nm.
  This is (seems) to be a very small number.
  No problem for LHC…
  Can be problematic for FCCee or for a linear collider, due to the very tiny vertical beam emittances (sizes).
Ground motion spectrum of the LHC tunnel
1 nm
Ocean wave peak
Vertical scale corresponds to (amplitude)2 ~ power
1s
10s
0.1s
1 mm

## Slide 34: Accelerator component girders
The mechanical properties of components and of girders have an important impact on the stability due to mechanical resonances !
Example for a mock-up of the FCCee quadrupole assembly (for simulation benchmarking)
The movement of the quadrupole is amplified by up to a factor 100 at certain frequencies
Ground
Quadrupole
Improvements needed !!
Amplitudes are driven by the support jacks

## Slide 35: Civil engineering impact
HL-LHC has built huge underground structures in LHC points 1 and 5.
Civil engineering is not famous for working ‘quietly’ !
Noise and vibrations !
~100 m underground
LHC beam line = LHC magnets
CMS experiment cavern

## Slide 36: Civil engineering impact
In the early part of the CE work, a lot of soil was moved around and compacted while LHC was operating.
Ground compactors compact soil by… vibrating.
…and they managed to shake the beams colliding at the IP ~100 m underground.
Mechanism:
The vibrations with frequencies ~20 Hz were transmitted through 100 m of rock to the tunnel magnets and their girders which resonate in the frequency range 8-22 Hz.
The resonant excitation generated micrometer amplitude beam movements that were clearly visible on the CMS experiments luminosity (= rate of collisions).
Luminosity = collision rate
vibrations
Beam loss rates

## Slide 37: Waves from earthquakes
L. Braille (Purdue U.) / The IRIS (Incorporated Research Institutions for Seismology) consortium
Different types of body (Pressure, Shear) and surface waves (Raleigh, Love), multiple paths and reflections produce a complex signature of earthquakes at seismic measurement stations – also at accelerators like the LHC.

## Slide 38: Costa Rica earthquake (2012) – LHC as seismograph
A magnitude 7.6 earthquake in Costa Rica (05/09/2012 @ 14:42:10 UTC) ‘struck’ the LHC with stable colliding beams.
  Arrival of the first waves at CERN ~15:06 UTC.
The arrival of the different waves can be observed on the radial beam position – equivalent to ~0.5-1 mm circumference oscillations.
The stable collisions continued while the waves moved across the ring.
1 hour !
P
Surface waves
zoom

## Slide 39: Vibrating quadrupoles at LHC?
For many years, a class of rare beam loss events remained un-explained at the LHC.
Signature: the beams suddenly oscillate transversely at 8-10 Hz leading to beam abort due to beam losses exceeding tolerable thresholds.
The analysis of the orbits before beam loss (see earlier slides) pointed in all cases to well defined source, consistent with micrometer amplitude oscillations of a single quadrupole.
  The LHC quadrupole have mechanical resonances in the range 8-20 Hz.
  The sources are not randomly distributed, in 2023 there were only 2 locations for 7 events.
  What could be a trigger ???
Max orbit change in such events (modulated at ~10 Hz)
Source point

## Slide 40: LHC vibrating quadrupoles (2)
One location was instrumented with vibrations sensors in February 2024.
Observations…
The offline analysis of many signals pointed eventually towards a cryogenic valve used to re-pressurize the cold magnets with liquid Helium at 3.5 bar. Refill frequency depends on … leaks.
Vibration of the cryostat at 8 and 10 Hz !

## Slide 41: Slow ground movements – days to years
In large tunnels (LEP/LHC, future FCC) geology has an important impact.
Geological fault lines can degrade the stability locally by more than an order of magnitude.
  From ~70 mm drift / year in ‘quiet’ areas to many mm around active faults.
R. Pitthan, CLIC note 422
LEP(LHC) map with fault lines
Evolution of LEP element positions from 1993 to 1999 (one line / year)

## Slide 42: FCC tunnel preparation
The 91 km long FCC tunnel placement must be studied carefully (location, depth) to minimize the complications due to geologic structures (change of rock type, fault lines, lakes and rivers, ...
  Depth is ~200-400 m compared to 50-140m for LHC.
  Ongoing measurement campaign (seismic with vibrating trucks, test drilling).
Tribune de Geneve, 19.12.2024

## Slide 43: Earth tides
Tide bulge of a celestial body of mass M at a distance d
q = angle(vertical, the celestial body)
induces surface deformations and affects the water levels of the oceans, like a deformed ballon.
Such Earth tides alter the accelerator circumferences:
The Moon contributes 2/3, the Sun 1/3.
Not resonance-driven (unlike Sea tides !).
Accurate predictions possible (~%).
LEP tide predictions for Nov. 1992
The relative circumference change amounts to ~10-8 ~ 1 mm – resolution ~ 0.01-0.001 mm.
Gravitational wave detectors achieve sensitivities of ~10-21 !

## Slide 44: LHC circumference observations
Tides are observed very clearly on the LHC circumference by measuring the mean radial (=horizontal) beam position.
Tide observations (from orbit changes) over one week at 4 TeV in 2016
(expressed in energy change Dp/p)
Earthquake in New Zealand
The pressure waves induce a modulation of the circumference
Measurements
dp/p
10-4
Model

## Slide 45: Summary
Magnetic field and misalignments errors of accelerator components induce errors on the beam orbits over a large frequency range.
The errors are often sufficiently large that modern machines operate poorly or not at all.
Fortunately, ever improving tools and algorithms have been developed over the past 50 years to correct errors.
To minimize the imperfections from the start it is important to have:
  the best possible magnet (component) design,
  carefully measured magnetic fields,
  precise power converters,
  the best possible machine alignment,
  a quiet environment.
Thank you for your perfect attention !