## Slide 1: RF Systems
H. Damerau
CERN
12 March 2025
CAS Basics of Accelerator Physics and Technology

## Slide 2
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 3
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 4
Introduction
What is below?
How are RF signals generated which make the beam feel comfortable?
The radiofrequency (RF) system transforms a string of magnets into an accelerator
Cavity most is the most visible part of an RF system
  On top of the RF system food chain
  Interacts directly with beam
Cavity
Power amplifier
Low-level RF
system
Beam
Beam

## Slide 5
Frequency and wavelength ranges
100 kHz 3 km
1 MHz 300 m
10 MHz
30 m
100 MHz
3 m
1 GHz
30 cm
10 GHz 3 cm
100 GHz
3 mm
SPS 200 MHz
PS main RF system
PS longitudi- nal damper
CLIC 12 GHz
Long wave
Medium/ short wave
VHF
Microwave links

## Slide 6
Amplitude ranges
1 mV
1 mV
1 V
1 kV
1 MV
1 GV
LEP: 3.6 GV total
LLRF systems
Signals from beam pick-ups
ILC and CLIC: several TV
LHC: 16 MV
Cooled hadron beams (ELENA)
Electron light
sources
SLS
LHC
Low/Medium energy hadron RF

## Slide 7
Particle velocity depends on its type:
Old television set (30 kV): Electrons at 30% of c0
            Protons just at 0.7%
Small synchrotron (500 MeV): Electrons at 99.99995%
              Protons at 75.8%
Most electron accelerators at ‘fixed’ frequency
Particle velocity
p+
e-
p+
e-

## Slide 8
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 9
Accelerator type
Linear
(single pass)
RF system for high-energy accelerators
Hadrons
Electron
Maximum RF voltage, constant velocity
Maximum RF voltage, variable velocity
Circular
(multi-pass)
Compensate synchrotron radiation losses
Sweep frequency with beam
Hadrons
Electron
*Exceptions (rare) exist
*

## Slide 10
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 11
Limits to maximum gradient
Kilpatrick 1957,
f in GHz, Ecrit in MV/m
Wang & Loew, SLAC-PUB-7684, 1997
Surface electric field in vacuum
1000
500
200
100
50
20
10
0.01
0.1
1
10
100
f [GHz]
Ecrit [MV/m]
High frequencies generally preferred for large gradient
E. Jensen

## Slide 12
Why not high RF frequencies all the time? | 
Transverse beam size and aperture Particles are getting faster during acceleration | RF cavity scales with lRF = 1/fRF fRF must sweep Tunable or wideband cavities Technology only below ~100 MHz
Choice of RF frequency
500 MHz
1.5 GHz
  RF frequencies below ~200 MHz for
  Some hadron linear accelerators
  Cyclotrons
  Low- and medium energy hadron synchrotrons
  RF frequencies above ~200 MHz used for
  Linear accelerators
  Electron storage rings
  High energy hadron storage rings

## Slide 13
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 14
Minimum voltage requirement
(for circular accelerators)
The RF system must compensate
Energy gain per turn due to changing magnetic field, B
: bending, : average radius

## Slide 15
(for circular accelerators)
The RF system must compensate
Energy loss, e.g., due to synchrotron radiation (electrons or positrons)
Minimum voltage requirement
(mp/me)4 = 18364 ~ 1.1 ∙ 1013 times less for protons

## Slide 16
RF system expected to provide given energy gain
On-crest acceleration
Used in some linear accelerators
Insufficient in a circular accelerator
More voltage provided to avoid on-crest acceleration
Off-crest acceleration
Needed for circular accelerator
Higher voltage for given energy gain
Minimum voltage requirement


## Slide 17
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 18
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 19
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 20
Cavity parameters
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
R
C
L
Z(w)
with

## Slide 21
Cavity parameters
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
R
C
L
Z(w)
with

## Slide 22
Cavity parameters
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
Resonant circuit can also be described by R, R/Q, w0 or any other set of three parameters
R
C
L
Z(w)
Dw

## Slide 23
Cavity parameters
Most common choice by cavity designers w0, R, R/Q – why?
Resonance frequency, w0
  Exactly defined for given application, e.g. hfrev
Shunt impedance, R
  Power required to produce a given voltage without beam
“R-upon-Q”, R/Q
  Defined only by the cavity geometry
  Criterion to optimize a geometry
  Detuning with beam proportional to R/Q

## Slide 24
Why R/Q?
Charged particle experiences cavity gap as capacitor
Cavity geometry with small R/Q to reduce beam loading
q
Cavity
Beam induced voltage

## Slide 25
RF wavelength large below ~10 MHz: >30 m
Would need huge cavities  too large for accelerators
Line resonators: l/4 resonator
  Short circuit on one side  Voltage is zero
  Open end on other  No current but voltage
Why is this resonator so common in particle accelerators?
RF cavities in low frequency range
Voltage
Current
Transmission line, impedance ZL
l/4 length
Z(w)
Short- circuit

## Slide 26
Coaxial structure with inner conductor as beam pipe
RF cavities in low frequency range
Z(w)
Accelerating gap, isolated
Beam axis
Short- circuit
Still rather long geometry, 7.5 m at 10 MHz
Add capacitive or inductive shortening
Plate capacitor
Ferrite inductivity

## Slide 27
Capacitive loading
Add capacitor at gap of cavity to shorten the resonator
Significantly reduces cavity size
Fixed frequency only
Small losses due to capacitor
Cavity in vacuum
NSLS, 52.88 MHz
DESY PIA, 10.4 MHz, inner cond.
Outer cond.
~1 m
M. Nagl

## Slide 28
Inductive loading with magnetic material shortens resonator from tens of meters to a device, lossy though
Inductive loading
CERN PSB Finemet cav., 0.6-18 MHz
CERN PS, double gap, 2.8-10 MHz
Additional advantage: permeability of ferrite can be controlled by DC bias current  variable inductivity
  Cavity with programmable resonance frequency
  Essential for hadron acceleration in low-energy accelerators
M. Paoluzzi

## Slide 29
Remove inner conductor from coaxial set-up
The resonator becomes a pill-box cavity
The basis for cavity resonators
Further increase frequency
Electric field, TM010-mode
Magnetic field, TM010-mode
E. Jensen
Beam axis
Beam axis
DORIS cavity

## Slide 30
Example: 400 MHz cavities in LHC
Reduce beam loading in RF cavities
Shunt impedance, R, low for small R/Q with normal conducting cavities  superconducting cavities in LHC
Bell shape: R/Q ~ 44 W, 400 MHz
28 cavities, 5.3 MV/m
16 MV/beam

## Slide 31
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 32
Attack inductivity or capacitance of resonator, or combined
Coupling loop forms transformer with resonator inductivity
Coupling power into a cavity magnetically
C
Lc
M
RF power
L. Stigelin
Main coupler PSI cyclotron
~1 MW at 50 MHz
R
L
A. Rodchenko

## Slide 33
Attack inductivity or capacitance of resonator, or combined
Capacitive divider to gap to transform generator impedance to cavity shunt impedance
Beam also couples capacitively via the gap
R
C
L
Cc
Beam
Coupler of CERN PS 40 MHz
Coupler forms one half of capacitor with the gap
Coupling power into a cavity electrically
RF power

## Slide 34
Attack inductivity or capacitance of resonator, or combined
Coupling power into a cavity electrically
R
C
L
Cc
Beam
300 kW power coupler of LHC 400 MHz cavities
Coupler antenna transmits directly into the cavity
RF power
RF power
Most common electrical coupler

## Slide 35
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 36
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 37
Power to accelerate beam  Wanted
Compensate beam-induced voltage  Refl. P
Compensate electrical losses in cavity  Heat
Compensate electrical losses in distribution  Heat
How much power is required?
(ideally)
Pout = g ∙ Pin or Vout = ∙ Vin

## Slide 38
Cathode and filament
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
e-
e-
e-
e-
e-
Ua*
anode
e-
e-
e-
e-
e-
e-
Basics of grid tube
Ia
From diode to tetrode amplifier
E. Montesinos
*For tube amplifier designs voltages are named U instead of V

## Slide 39
Ia
Cathode and filament
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
e-
e-
e-
Ua
anode
Basics of grid tube
From diode to tetrode amplifier
E. Montesinos

## Slide 40
Cathode and filament
e-
e-
e-
Ua
anode
Ug1 control grid
e-
e-
e-
e-
Triode
  Modulating the grid voltage proportionally modulates the anode current
  Transconductance
    Voltage at grid
    Current at anode
  Limitations
    Parasitic capacitor from anode to control grid (g1)
    Tendency to oscillate
Basics of grid tube
From diode to tetrode amplifier
E. Montesinos
https://en.wikipedia.org/wiki/Triode

## Slide 41
Cathode and filament
e-
e-
e-
Ua
anode
Ug1 Control grid
e-
e-
Basics of grid tube
Ug2 Screen grid
Tetrode
  Screen grid
    Positive (lower anode)
    Decouple anode and g1
    Higher gain
  Limitations
    Secondary electrons
    Anode treated to reduce secondary emission
e-
e-
e-
e-
From diode to tetrode amplifier
E. Montesinos
https://en.wikipedia.org/wiki/Beam_tetrode

## Slide 42
Example: Tetrode amplifier driving SPS RF
Two transmitters, 2  1 MW at 200 MHz (almost continuous)
Eight tetrodes per amplifier
RS2004 tetrode
Amplifier trolley
Complete transmitter
E. Montesinos

## Slide 43
In a push-pull circuit the RF signal is applied to two devices
  One of the devices is active on the positive voltage swing and off during the negative voltage swing
  The other device works in the opposite manner so that the two devices conduct half the time
  The full RF signal is then amplified
Needs two different type of devices
Basics of RF solid state amplifiers
NPN BJT
PNP BJT
Vin
VDC
Vout
E. Montesinos
BJT: Bipolar Junction Transistor

## Slide 44
Another push-pull configuration is to use a balun (balanced-unbalanced)
  Power splitter, equally dividing the input power between the two transistors
  Balun keeps one port in phase and inverts the second port in phase
Since the signals are out of phase only one device is On at a time
This configuration is easier to manufacture since only one type of device is required
Basics of RF solid state amplifiers
Vdc
Input balun
(Unbalanced-Balanced)
Output balun
(Balanced-Unbalanced)
0 ⁰
0 ⁰
180 ⁰
180 ⁰
NPN BJT
NPN BJT
Vin
Vout
E. Montesinos
NXP Semi- conductors AN11325 2-way Doherty amplifier with BLF888A

## Slide 45
Example: Soleil 45 kW, 352 MHz
DU1029UK
Electron storage ring running at 352 MHz
600 W, 300 VDC/30 VDC converter
330 W amplifier module

## Slide 46
1.6 MW at cavity input
Example: SPS
200 MHz solid state amplifiers: 2  1.6 MW peak power, 2  16 towers per amplifier
E. Montesinos
80 modules per tower, 1280 modules with 5120 transistors per amplifier
Presently the largest RF installation in a particle accelerator
From LLRF
1/16 splitter

## Slide 47
How to choose the right RF amplifier?
Prefer tube amplifier, when | Prefer solid-state amplifier, when
Amplifier must be installed in the accelerator tunnel Expecting important spikes from beam induced voltage Large output power of a single device is required, without combiners Not much space is available High peak power in pulsed mode Amplifier must be compact and/or close to cavity | Amplifier can be located in non-radioactive environment Circulator can be installed to protect the amplifier Delay due to unavoidable combiner stages is little issue Sufficient space can be made available Continuous operation Amplifier can be separate from the cavity
Mostly no hard criteria  decide on case by case basis

## Slide 48
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 49
Generate the right RF signal
Get amplitude, frequency and phase right

## Slide 50
Electronic phase-locked loop
VCO
RF
Slow signal
Frequency re-generation and multiplication
Voltage controlled oscillator (VCO) locked in phase to input
fout, fout
fin, fin
Df
fVCO
Loop filter, H(w)
~fin - fVCO
Fixed phase relationship: fout – fin = const.
Locked frequencies: fout = fin

## Slide 51
fin, fin
Df
Electronic phase-locked loop
Loop filter, H(w)
VCO
RF
Slow signal
Lock two signals: frequency re-generation and multiplication
Voltage controlled oscillator (VCO) locked in phase to input
fout, fout
fVCO
~fin - fVCO
1
n
Fixed phase relationship: fout/n – fin = const.
Optional divider: fout = n · fin

## Slide 52
RF
source
Beam phase
Df
-
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
Direct digital synthesizer (DDS)
RF
Slow signal
h frev (digital)
fRF
Loop filter
h · frev, from B, p
ferr ~Df

## Slide 53
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
Phase-locked loop with beam phase as reference for RF system
fout = fin ± Df
fRF
Loop filter
h · frev, from B, p
Precision VCO
RF
Slow signal
h frev (digital)
ferr ~Df
Direct digital synthesizer (DDS)
RF
source

## Slide 54
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
Fast control of RF frequency to cavities (no slow corrections)
fout = fin ± Df
Precision VCO
fRF
Loop filter
h · frev, from B, p
RF
Slow signal
h frev (digital)
ferr ~Df
Direct digital synthesizer (DDS)
Move the wave!
RF
source

## Slide 55
Effect of beam phase loop at injection
Example: Injection of a bunch from PS Booster into PS
Essential in hadron accelerators to keep RF locked to beam
How does this look like in longitudinal phase space?
90° error, phase loop off
90° error, phase loop on
Bucket centre
Bucket centre

## Slide 56
Effect of beam phase loop at injection
Bunch in rigid bucket, no loop
Injection with phase loop
Essential in hadron accelerators to keep RF locked to beam
Even large transients (injection, transition) are controlled
Only minor longitudinal perturbation

## Slide 57
Summary
RF system parameters
  Choose frequency and voltage wisely
Parameters of RF cavities
  R, R/Q
  No ‘one-size fits’ all
Power amplifier
  Tube or solid-state based
Beam control as global feedback
  Beam phase
The beam is the reference - make it feel comfortable!

## Slide 58
Thank you very much for your attention!

## Slide 59
A big Thank You
to all colleagues providing support, material and feedback
Maria-Elena Angoletta, Philippe Baudrenghien, Thomas Bohl, Giorgia Favia, Jörn Jacob, Erk Jensen, John Molendijk, Eric Montesinos, Gerry McMonagle, Mauro Paoluzzi, Damien Perrelet, Bernhard Schriefer, Lukas Stingelin, Fumihiko Tamura, Frank Tecker, Daniel Valuch and many more…

## Slide 60
References
D. Boussard, Design of a Ring RF System, CERN SL/91-2 (RFS, rev.), 1991, http://cds.cern.ch/record/1023436/files/CM-P00065157.pdf
E. Montesinos, Accelerators for Medical Applications - Radio Frequency Powering, CERN-2017-004-SP, http://cds.cern.ch/record/2315172/files/1804.08535.pdf
R. Garoby, Low level rf building blocks, CERN-1992-003, 1991, http://cds.cern.ch/record/225609/files/CM-P00059483.pdf
J. W. Wang, G. A. Loew, Field Emission and RF Breakdown in High-Gradient Room-Temperature Linac Structures, SLAC-PUB-7684, 1997, http://www.slac.stanford.edu/cgi-wrap/getdoc/slac-pub-7684.pdf
W. D. Kilpatrick, Criterion for vacuum sparking designed to include both rf and dc, Rev. Sci. Instrum. 28 (1957), 1957, http://inspirehep.net/record/44645
H. Damerau, Radio-Frequency (RF) Systems, CAS, Introduction to Accelerator Physics, https://arxiv.org/abs/2108.06237

## Slide 61
If exact RF frequency not critical, choose standard value
Off-the-shelf RF components easily available in frequency ranges used by industry
Exchange of developments and equipment amongst research laboratories
Some standard frequencies
Accelerator | Frequency
Hadron synchrotrons (PSB, PS, JPARC RCS, MR) | <10 MHz
Hadron accelerators and storage rings (RHIC, SPS) | ~200 MHz
Electron storage rings (LEP, ESRF, Soleil) | 352 MHz
Electron storage rings (DORIS, BESSY, SLS,…) | 499.6…499.8 MHz
Superconducting electron linacs and FELs (X-FEL, ILC) | 1300 MHz
Normal conducting electron linacs (SLAC) | 2856 MHz
High-gradient electron linac (CLIC) | 11.99 GHz

## Slide 62
RF power amplifier
E. Jensen
Power capability of commercially available amplifier types

## Slide 63
Advantages | Disadvantages
Large beam aperture Long RF buckets, large acceptance Wide-band or wide range tunable cavities possible Power amplification and transmission straightforward | Bulky cavities, size scales 1/f, volume 1/f3 Lossy material to downsize cavities Moderate or low acceleration gradient Short particle bunches difficult to generate
Advantages | Disadvantages
Large beam aperture Long RF buckets, large acceptance Wide-band or wide range tunable cavities possible Power amplification and transmission straightforward | 
Why choose a low RF frequency?
  RF frequencies below ~200 MHz for
  Some hadron linear accelerators
  Cyclotrons
  Low- and medium energy hadron synchrotrons

## Slide 64
Advantages | Disadvantages
Cavity size scales 1/f, volume 1/f3 Break down voltage increases High gradient per length Particle bunches are short | Maximum beam available aperture scales 1/f No technology for wide-band or tunable cavities Power amplifiers more difficult Power transmission losses
Advantages | Disadvantages
Why choose a high RF frequency?
  RF frequencies above ~200 MHz used for
  Linear accelerators
  Electron storage rings
  High energy hadron storage rings

## Slide 65
Bucket area dependence on stable phase
In a circular accelerator the area in energy-time phase space (bucket area) depends on the stable phase
Below transition, fS = 0…90°
Above transition, fS = 90°…180°
Typical synchronous phase with respect to 0° or 180°
  Hadron accelerators: < 40°
  Electron storage rings: ~ 20°

## Slide 66
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 67
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
  Local feedback
Low-level RF system
  Beam phase control
Summary
Outline

## Slide 68
Antennas work in transmission and reception
RF cavities transfers energy to the beam, but it also works in the opposite, unwanted direction
Reciprocity

## Slide 69
Energy transfer from cavity to beam, but from beam to cavity
Both, RF generator and beam can induce voltage in cavity
Reduce beam induced voltage by reducing R, but not efficient
  Obviously needs more power  $$$
Feedback to decrease the apparent impedance for the beam
  Use amplifier to counteract beam induced voltage
C
Reduction of cavity impedance
Drive
Beam
Final amp
R
L
IG
IB

## Slide 70
Energy transfer from cavity to beam, but from beam to cavity
Both, RF generator and beam can induce voltage in cavity
Compare drive signal (no beam) with gap (beam and generator)
Amplify inverted difference
Reduction of cavity impedance
Drive
Beam
Final amp
L
IG
IB
FB ret.
+
V
-
+
C
R

## Slide 71
Gain [dB]
Frequency [MHz]
Transfer function with and without feedback
~24 dB
Example: 10 MHz RF system in CERN PS
Feedback gain of 24 dB
Equivalent impedance, Zeq(w) reduced
Impedance for amplifier remains unchanged, Z(w)
Cavity, amplifier with feedback
Z(w)
Zeq(w)
Asymmetric cavity optimized for energy flow to beam

## Slide 72
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase