## Slide 1: Present status of ELENA sources and possible modifications
Jose A. Ferreira, Alex Sinturel, Iker Lobato
14/10/2024

## Slide 2: Present status
Primary pump supplied by TE-VSC
  XDS35i, Last service 2022
TMP: TPH 2200 (1 spare?)
  Last service 2021
  Controller TCP5000 (1 spare)
  Manual venting
Gauges Leybold
  TTR211 Pirani
  Penning vac
Valves
  DN250 ISO-F from VAT isolating the source
  Valve DN63 ISO-K isolating the primary pump
Controls
  Interface developed by Julich, not compatible with CERN remote system

## Slide 3: Required modifications
Safety aspects linked to H2 pumping must be addressed => Dilution and inert purge.
Integrate protections in case of vacuum failure (i.e. stop H2 injection). Define interface with gas injection.
Integrate the vacuum equipment in VSC control and SCADA application
Standardize equipment with focusing on operational cost reduction (maintenance intensive design)

## Slide 4: Required modifications
H2 injection between 0.1 to 0.6 sccm -> <0.01 mbar×l/s => Minimum continuous inert purge (N2) 0.25 mbar×l/s
Required pump with gas purge, i.e. ACP28 gas purge 3.7e3 sccm or explore option to run with ballast (1.2m³/h).
Inert gas pressure to be monitored in case required
HSE shall approve the solution

## Slide 5: Required modifications
Dry primary pump, low maintenance and including H2 dilution, i.e. ACP28G
Isolation, venting and leak detection valves.
TMP
  MAG 1300ip or Mag 2200iP with automatic venting
  Low maintenance and possible spare compatible with injection pumping groups.
Gauges and TPG300

## Slide 6: Budget
Mechanical parts
  Package 1:
    1 TMP Version 2200 + spare
  Package 2:
    1 TMP Version 2200
    Spare TMP from differential pumping
Controls
TOTAL:
  Package 1 + Controls : 65kCHF
  Package 2 + Controls : 47kCHF

## Slide 7: Operation
Intervention shall be agreed with TE-VSC in advance (no calls the same day unless real unexpected issues)
Venting supervised by TE-VSC
Gas injection managed by BE-ABP or BE-OP with interfaces to VSC control system for safe operation (tbd)
This is the minimum proposal. If agreed final decision from Paolo => Modifications during LS3? Timing?