## Slide 1: Dynamic Aperture Updates

## Slide 2: Topics
Updates on dynamic aperture with beam-beam and errors
  Update from previous talk
General points on dynamic aperture

## Slide 3: Recap
Previously shown beam-beam has very low impact on DA with
  Single multipole lens in between two IPs
  Identical multipole lenses between all IPs
  Lattice with misalignment and orbit + tune correction (Yi Wu)
  IP waist and beta modified
Dynamic aperture evaluated using largest ellipse

## Slide 4: Dynamic Aperture: Largest Ellipse
Define dynamic aperture as largest possible ellipse (in X,Y plane) that only contains stable particles. Developed with A. Piveteau
Allows get quantifiable dynamic aperture to scan parameters

## Slide 5: Simulation Set-up
Load FCC-ee tt lattice without perturbations from MADX
Perturb lattice in MADX and import to Xsuite
Taper lattice
Compute 6D Twiss in Xsuite
Install (WS) beam-beam elements in Xsuite
  B2 same/mirrored parameters as B1
Compute DA metric – Largest Ellipse
Repeat without beam-beam

## Slide 6: Alignment Errors
Test impact of alignment errors on dynamic aperture
  Focus on vertical alignment errors of:
    Sextupoles - introduction of coupling and optics beating
    Quadrupoles – same as sextupoles + introduction of orbit + dispersion effects
Random errors with increasing standard deviation
  Applied to quadrupoles or sextupoles
  20 identical errors seeds with and without beam-beam
  Compute average and standard deviation of dynamic aperture for each error size
  Compare individual seeds too

## Slide 7: Results

## Slide 8: Results
Very small impact of beam-beam element on average dynamic aperture
Most error seeds have very similar dynamic aperture in both cases
  Shown next to each other in plot
  Few cases with differences
    Interesting to study these behaviour of these seeds
    Need to understand how beam-beam interacts with these errors

## Slide 9: Topics
Updates on dynamic aperture with beam-beam and errors
  Update from previous talk
General points on dynamic aperture

## Slide 10: Position and Angle Dependence of DA
Typically DA simulations set up as:
    Over many turns different combinations of and sampled
  In one location – typically point of symmetry without dispersion e.g. in RF section
    At low amplitudes holds throughout machine so no locationation dependence
FCC-ee (especially at tt) different
  Few turns before motion is damped
  Highly non-linear
    Especially at large amplitudes ( in DA)
    Especially in areas of strong sextupoles

## Slide 11: Investigation
Understand dependence of DA on initial conditions
  Non-zero initial and
  Initiating in various locations around the ring (with zero and )
Strategy:
  Create multiple particles with different and and determine survival percentages
  Project particles to different location and determine DA

## Slide 12: Angle Scan

## Slide 13: Angle Scan

## Slide 14: Angle Scan

## Slide 15: Angle Scan

## Slide 16: Angle Scan

## Slide 17: DA Angle Scan
DA computed at different amplitudes at RF marker
Each amplitude probed using 256 particles
  16 angles in
  16 angles in
100 turns in tt lattice
Colour indicating fraction of survived all 100 turns
  Yellow = 100%
  Dark Blue = 0%
Dots representing survival of particles
  “Classical DA”
No Radiation

## Slide 18: DA Angle Scan
DA computed at different amplitudes at RF marker
Each amplitude probed using 256 particles
  16 angles in
  16 angles in
100 turns in tt lattice
Colour indicating fraction of survived all 100 turns
  Yellow = 100%
  Dark Blue = 0%
Dots representing survival of particles
  “Classical DA”
Radiation

## Slide 19: DA Location Projection
Strategy:
  For each amplitude:
    Check and label stability:
      Generate 256 particles at RF marker (FRF.1)
      Track each particle 100 turns
    Project:
      Create same particles and track to different locations
      Determine particles with minimum
      Determine linear from local Twiss
    Plot new particle amplitude and stability

## Slide 20: Projection of DA
Track

## Slide 21: Projection of DA
Track

## Slide 22: Projection of DA
Track

## Slide 23: Projection of DA
Closest particle to , represents DA @
Track

## Slide 24: Projection of DA
Closest particle to , represents DA @
Track

## Slide 25: Projection of DA
Closest particle to , represents DA @ , with amplitude
Track

## Slide 26: Particle projection – Drift Downstream
Green = particles initiated at RF marker
Blue = Particles downstream
Orange = Closest particle to x’ = 0

## Slide 27: Particle projection – IP
Green = particles initiated at RF marker
Blue = Particles downstream
Orange = Closest particle to x’ = 0

## Slide 28: DA Location Projection
Strategy:
  For each amplitude:
    Check and label stability:
      Generate 256 particles at RF marker (FRF.1)
      Track each particle 100 turns
    Project:
      Create same particles and track to different locations
      Determine particles with minimum
      Determine linear from local Twiss
    Plot new particle amplitude and stability

## Slide 29: IP.1

## Slide 30: IP.4

## Slide 31: IR Quad outside Crab Sextupoles

## Slide 32: IR Quad outside Crab Sextupoles

## Slide 33: Arc Quadrupole

## Slide 34: Arc Quadrupole

## Slide 35: Same marker ½ turn later (FRF.2)

## Slide 36: Same location 1 turn later…

## Slide 37: Conclusions and Next Steps
DA highly dependent on initial conditions
  Need to be careful when evaluating DA
    Intrinsic property when simulating with radiation
  Especially important when optimising DA
    Might just lead to weakening of sextupoles at certain phase advances from initiation point
  Solution – evaluate DA at multiple angles in phase space
    Number of angles to be determined – convergence or analytical considerations
Next steps
  Repeat with LCC lattice – maybe less extreme non-lienearities
  Explore with multipole errors and beam-beam distorting linearity at lower amplitudes