## Slide 1
IFAST Prototyping Activity
REX Resonant EXtraction Improvements:
Final Achievements
Work Package 5 Task 3
Peter Forck & Rahul Singh (GSI) on behalf of the consortium
4th Annual Meeting / 9th April 2025

## Slide 2
Challenge for slow Extraction from Synchrotrons
Schematics for knock-out extraction:
Slow extraction: Gentle beam excitation at 3rd order resonance
Beam physics: Extraction as ‘slow losses’ for 1 … 10 s
Particle crosses stability boarder sequentially
Exponential amplitude growth during ‘transit time’
 50 … 1000 turns to reach septum for extraction
Stored beam horizontal phase space at electrostatic septum
x
x’
ele.-stat. septum
thickness
last spiral step xstep
after 3 turns
transit time Ttransit
extr.
channel
Knock-out extraction:
Transverse excitation
diffusion of core to separatrix
Signal-induced fluctuations
Sextupoles: non-linear fields
Ion’s amplitude growth per turn
 Ttransit & xstep
Unintended quadrupole current ripple
 tune ripple
 bursts extracted
Problem: Sensitivity to any unintended resonance condition, e.g.:
Change of tune: unintended quadrupole current ripple
Stochastic amplitude excitation of ‘knock-out’ extraction
Mitigation research within IFAST-REX with two directions:
Improved technical devices
 Improved power supply measurement for magnets
 TRL 7 reached
 Novel transverse excitation for knock-out extraction
 TRL 7 reached
Beam stabilization simulation & experimental validation:
 Simulation and experimental validation
 Tailored beam-based tests
separatrix
X
X’
Phase-
space
Approaching
3rd order
resonance
X’
X

## Slide 3
General: Beam Fluctuations for slow Extraction
Example: C6+ at 300 MeV/u at GSI, quadrupole scan, 2.5 s extraction called ‘spill’; coasting & bunched beam
Slow extraction: Gentle beam excitation at third order resonance
Problem: Fluctuations of the extracted beam (before systematic optimization)
Improvement by bunching:
Medical facility: Readout time typ. 100 µs used since years; however, improvement required
GSI & CERN: Not acceptable for nuclear & particle physics as related to detector deadtime
Time domain:
20 µs readout interval
cmean=35
Duty factor: norm. fluctuations
for the readout interval (here = 20 µs)
coasting beam
Poisson limit
bunched beam
Poisson
limit
Large fluctuation
 ‘bad’ spill
Small fluctuation  ‘good’ spill
Coefficient of variance:

## Slide 4
Results:
Measurement of ion arrival versus rf & ion time interval:
Costing beam: Quite ‘non-Poisson’
Beam: Bi68+ 300 MeV/u
frf = 3.62 MHz
Beam: frf = 4.96 MHz
Bunched beam extraction Urf = 3.1 kV
Coasting beam extraction
mean interval = 1/rmean
measure
time 2 µs
mean interval = 1/rmean
measure
Poisson
time 2 µs
time 200 ns
Poisson
extraction 10 s
Bunched beam: wider interval distrib.  better duty factor
Bunched beam: Short ‘bunches’,  1/3 of stored bunch
 acceptable for med. facilities,
 but not at GSI & CERN fix target exp.
time rel.
to rf
coasting
Spill Detector Development Measurement Example : Arrival Time with TDC
Large fluctuation
 ‘bad’ spill
Small fluctuation  ‘good’ spill
Topic: Bunched beam extraction
GSI measurement
T. Milosic et al., IBIC’21
J. Yang et al., IBIC’22
Remark: Possible mitigation by bunching at  80 MHz

## Slide 5
Topic: Spill micro-structure dependence on signal type for knock-out extraction
by GSI with contributions by HIT, CERN and MedAustron for coasting beam
Such systematic comparison performed for the first time!
Multi-band excitation types and comparison to traditional single band: Tests at COSY (FZ-Jülich)
However: Different rf excitation power required
Noise++ is good compromise
Large power from rf-amplifier (typ. 2x400 W), see below
Noise at baseband
Noise at 3 bands
Noise at baseband plus
sine at two harmonics
Large fluctuation,
 ‘bad’ spill
small fluctuation,
 ‘good’ spill
Experiment: Investigation of Extraction Signal Type
P. Niedermayer, R. Singh.,
Scientific reports, 14, 10310 (2024)

## Slide 6
Simulations by Xsuite and explanation
Simulation: Single particle tracking (COSY parameters)
Beam dynamics: Non-linear Hamiltonian
as representation of particle transverse energy
(Kabayashi Hamiltonian description)
Normalization to separatix value Hsep
Distance to separatix and dynamic evolution
Results:
Prior to extraction, distance from separatrix varies
Crossing separatrix depends on excitation type
Large distance and fast crossing preferred
Less sensitive to separatrix variation
Less sensitive power supply ripple
Better spill micro-structure achieved
Topic: Spill micro-structure dependence on signal type for knock-out extraction
by GSI with contributions by HIT, CERN and MedAustron
Normalized horizontal phase space:
Particle density shortly before extraction
Normalized Hamiltonian 5 ms prior to extraction:
power supply
ripple
Simulation: Investigation of Extraction Signal Type
P. Niedermayer, R. Singh.,
Scientific reports, 14, 10310 (2024)

## Slide 7
Topic: Spill micro-structure dependence on harmonics of betatron-frequency
by GSI and HIT; measurement at HIT with coasting beam C6+ 251 MeV/u, excitation by phase-shift keying RBPSK
Such systematic comparison performed for the first time!
 multi-band preferred
Hardware: Software Defined Radio & new high-bandwidth rf-amplifier from Barthel HF Technik
Experiment: Investigation of high Harmonics Excitation
Systematics for harmonics of betatron frequency excitation:
 higher harmonics preferred
Orange: lower side-band
Fluctuations for dual harmonics excitation:
Blue: upper side-band
Red: upper & lower side-band
Large fluctuation
 ‘bad’ spill
Small fluctuation  ‘good’ spill
Fluctuations for single harmonics excitation:
Blue: upper side-band
Orange: lower side-band
P. Niedermayer et al. (GSI & HIT)
In preparation for Phys. Rev. Accel. Beams
& arXiv:2503: 11285v1

## Slide 8
Capability for counting experiments: characterization by particle’s delay
 High harmonics lead more uniform distribution
Experiment: Investigation of high Harmonics Excitation
P. Niedermayer et al. (GSI & HIT)
In preparation for Phys. Rev. Accel. Beams
& arXiv:2503: 11285v1
Many pile-ups
Few pile-ups
Topic: Spill micro-structure dependence on harmonics of betatron-frequency
by GSI and HIT; measurement at HIT with coasting beam C6+ 251 MeV/u, excitation by phase-shift keying RBPSK
Integral distribution of particle interval:
Base-band
7th harm.
Pile-ups as a function of harmonics:
Pile-ups scheme:
1st
pulse
2nd
pulse
signal
trigger level
 separated
almost overlap
Pile-up
Hardware: Software Defined Radio & new high-bandwidth rf-amplifier from Barthel HF Technik
Such systematic comparison performed for the first time!

## Slide 9
Technology: Control of Knock-out Excitation
Control hardware: Universal Software Defined Radio USRP:
Low-cost commercial hardware
High performance ADC & DAC
Highly customizable due to large FPGA
Software:
Flow-graph design by as Open Software
Very complex signals generation exp. tests with reasonable effort
Shift of several application to FPGA
 Latency after trigger significantly improved
 Contribution to GNU-based software by GSI
P. Niedermayer and R. Singh, IBIC’22 & ‘23
Signal generation (GSI,MedA,HIT)
Universal software defined radio
USDR Ettus X310
DAC: 16 bit, 200 MS/s
Analog bandwidth: > 100 MHz
Max. output voltage 1.8 V
FPGA: 400k cells, clock rate 200 MHz
Topic: Technical realization for ko extraction control
by GSI and HIT, with contributions by MedAustron
USRP
ADC/DAC with FPGA
PC
DSP with GNU Radio
control
rev. freq.
trigger
excitation
signals
data
180°
stripline
kicker
1800 spitter
ampl.
beam
Signal chain
Collaboration efforts at GSI and MedAustron, for test at HIT (due to legal issues)  Operational at GSI (& HIT), tests at MedAustron
TRL 7 reached (only TRL 6 promised)

## Slide 10
Application: Extension for Control of Knock-out Excitation
Technology used additionally for feedback on 1 ms range
Control hardware & software: Feedback loop on USRP:
Shift of several application into FPGA
Latency significantly improved to 30 µs
300 Hz overall bandwidth achieved
 Contribution to GNU-based software by GSI
Topic: Feedback for macro-spill improvement
by GSI with contributions by HIT
only feedforward
feedforward and feedback
2
Particle rate [108/s]
Extraction time [s]
0
1
2
3
5
4
0
1
rf-power evolution
 large rf-power required
1.5
0.5
Extraction time [s]
0
1
2
3
5
4
only feedforward
feedforward and
feedback
Improved macro- & micro-structure
P. Niedermayer et al., IPAC’25 (in preparation)

## Slide 11
USRP
ADC/DAC with FPGA
PC
DSP with GNU Radio
control
rev. freq.
trigger
excitation
signals
data
180°
stripline
kicker
1800 spitter
ampl.
beam
Signal chain
Technical development by company Barthel HF Technik plus GSI & HIT
Topic: Technical realization for knock-out amplifier:
High power required (due to broadband exc. & feedback)
Higher voltage by pure capacity load (instead 50 )
Immunity against reflection from capacitive load (!)
Achieved parameters | Value | Remark
Frequency range | 0.1 … 20 MHz | Broadband !
Output power | 500 W | Lager power
Gain | 56 … 58 dB | Flatness 2 dB !
Input impedance | 50  | 
2nd harmonics distortion | -35 … -15 dBc | 
Output impedance | 50  | Can be operated with any load impedance!
Output reflection VSWR | < 3:1 | 
Electrode capacitive load | 50 pF typ. | Total power reflection
Output reflection VSWR | < 3:1 | 
Mechanics, cooling | 19" rack, air | 
Technology: RF Power Amplifier Achievements

## Slide 12
Achievements:
Gain: 57 dB for -30 … 0 dBm input,
Gain flatness: < 2 dB for 0.1 … 20 MHz reached
Thermal drift: Below 0.5 dB for
Reflection: Special precautions successfully tested
Status:
Two amplifier produced
Characterized by company Barthel and at HIT
Enabled innovative beam measurement for high harmonics
TRL 7 reached (only TRL 6 promised)
 Final milestone D5.3 for month 46 reached
2dB
Gain flatness: versus for 0.1 … 20 MHz
30 dB
frequency
[MHz]
Technical development by company Barthel HF Technik plus GSI & HIT
Topic: Technical realization for knock-out amplifier
USRP
ADC/DAC with FPGA
PC
DSP with GNU Radio
control
rev. freq.
trigger
excitation
signals
data
180°
stripline
kicker
1800 spitter
ampl.
beam
Signal chain
Technology: RF Power Amplifier Achievements

## Slide 13
Technical development by company Bergoz Instrumentation plus GSI & CERN
Accelerator physics: Spill fluctuation caused by quadrupole current ripple, i.e. AC ripples , bandwidth 10 Hz…40 kHz
Topic: High dynamic range current measurement device providing (!) in the presence of kA
Novelty: Additional AC transformer for 10 Hz … 40 kHz
Sensitivity for AC part:
Challenges: AC-component on strong DC offset
 magnetic core saturation for A
Solution: Two transformers
DC transformer measures & used for compensation
compensation accuracy 
Goal: AC transformer for power supply ripple measure
Methodology: Production of large dynamic range AC current measurement device by company Bergoz
split-core
DC transformer
magnet current
(= DC & AC ripple)
ACCT
electronics
A
D
digital
output
power supply
magnet
digital control
Compensation
winding for DC
additional
AC transformer
+
-
DC meas.
IFAST-REX deliverable
Technology: Transformer for Power Supply Ripple Determination

## Slide 14
Technical development by company Bergoz Instru. plus GSI & CERN
Development: Prototype by Bergoz as novel device
DC part: For AC transformer mag. saturation compensation
Split core of 1500 windings
Standard Hall probe Honeywell SS495A1
AC part: Core with 1500 windings
Analogue part comparable to beam current ACCT
Reference fluxgate DCCT
Prototype sensor
Reference fluxgate DCCT electronics
Prototype electronics
Precision voltmeters
Detailed tests:
At Bergoz: up to 400 ADC
plus ~10-3 power supply ripple
At CERN in 2023-25:
up to 5 kADC with
typical power supplier
Technology: Realization of the Transformer
110 mm
260 mm
Windings:
1500 turns

## Slide 15
Technology: Achievements for the Transformer
Technical development by company Bergoz Instru. plus GSI & CERN
Achievement:
Transfer function measurement for = -5 … +5 kADC at CERN
 Separation of DC & AC part achieved independent on
DC feedback
AC response
Transfer function Imeas / Iprim [dB]
+10
0
-20
-40
-80
-60
100
Frequency [Hz]
10-1
102
101
103
104
105
Improvement with respect to 1st prototype
= -5 … +5 kADC
Desired working range: 8 Hz … 40 kHz
105
Linearity & noise measurement for = -5 … +5 kADC
Achieved AC noise:
@1 kA , i.e. better than specified (
i.e. factor 10 to 30 better than DCCT !
Significant improvement
compared to 1st prototype in year 2023!
 TRL 7 reached via tests at CERN
(TRL 6 promised)
 Final deliverable reached !
Remark: Hz lines from network
Hz lines from DCCT
Amplitude spec. density []
100
105
Frequency [Hz]
101
103
102
104
10-4
10-2
100
102
reference DCCT
Maximal dc-current IDC = 5 kADC
novel sensor
101
10-1
10-3
100
Frequency [Hz]
101
103
102
104
Amplitude spec. density []
10-4
10-2
100
102
reference DCCT
Zero dc-current = 0 kADC
novel sensor
10-3
10-1
101

## Slide 16
Dissemination of Results 2024-25
Refereed publications including IFAST-REX Acknowledgement 2024-25:
P. Niedermayer, R. Singh (GSI), ‘Excitation Signal Optimization for Minimizing Fluctuations in Knock Out Slow Extraction’,
Scientific Reports, 14, 10310 (2024)
Philipp Niedermayer, Rahul Singh (GSI), ‘Excitation of nonlinear second order betatron sidebands for Knock Out slow extraction at the 1/3 resonance’,
Rev. Accel. Beams 27, 082801 (2024)
E.C. Cortes Garcia, P. Niedermayer, R. Singh, R. Taylor, E. Benedetto, E. Feldmeier, M. Hun, T. Haberer (HIT, GSI, CERN, SEEIIST),
‘Interpretation of the horizontal beam response near the third integer resonance’, Phys. Rev. Accel. Beams 27, 124001 (2024)
P. Niedermayer, R. Singh and E. Feldmeier (GSI, HIT), Knock-out slow extraction using betatron sidebands at high harmonics,
in preparation for Phys. Rev. Applied (2025)
Earlier publications: See talk Annual Meeting 2024
Six theses by IFAST-REX consortium members:
Pablo A. Arrutia Sota, ‘Advanced RF techniques for CERN's future slow-extracted beams’, PhD Thesis Keble College, University of Oxford, 2024
Thomas Bass, ‘A Comparative Analysis of Simulations and Experimental Outcomes: Slow Extraction Driven by RF Transverse Excitation at the CERN Proton Synchrotron’, Master Thesis Royal Holloway, University of London
Florian Kühteubl, ‘Slow Extraction Optimization for the MedAustron Synchrotron’, PhD Thesis Technical University Vienna, 2024
Philipp Niedermayer, ‘Transverse excitation for beam diagnostics and slow extraction from synchrotrons’, PhD Thesis Goethe University Frankfurt
Rebecca Taylor, ‘Slow Extraction: Upgrades for Next Ion Medical Machines at FLASH timescales’, PhD Thesis Imperial College London, Physics Department, 2024
Jiangyan Yang, ‘Exploration of slow extraction beam quality and improvements at SIS18’, PhD Thesis Goethe University Frankfurt am Main, 2025

## Slide 17
Summary for IFAST-REX
Experiments, simulation, and interpretation:
Beam dynamics simulation: Deep insight to non-linear process of slow extraction
Ground-breaking experiments performed with dedicated excitation and feedback & broad to operational usage
Network with intensive discussion between participants (in particular for Xsuite simulations)
Knock-out extraction control and amplifier:
Control by versatile capability of SDR implemented, contributions to GNU-based software
Rf-amplifier manufactured; speciality: broadband gain-flatness & immunity against reflections suited for capacitive load
Novel transformer:
Prototype successfully commissioned, can be very useful for further applications
Next step following IFAST: Stabilization of quadrupole power supply or tune correction (e.g. with air-coil quadrupole)
Further work for slow extraction micro-structure:
Experiments performed at several facilities, significant improvements demonstrated and operational
e.g. CERN & MedAustron: Empty bucket channelling, COSE, rf-knock-out, ML methods; CERN & GSI: Improved diagnostics
SAC recommendations:
Transverse emittance studies: Not performed systematically; will be done in future. However, users don’t complain presently
Further applications of novel transformer possible!
Deliverable report D5.3 submitted in March 2025 as foreseen  mission accomplished
IFAST-REX contributes significant to technical developments and networking !

## Slide 18
Thank you for your attention
The valuable work of all collaborators are warmly acknowledged
Main contributors:
Barthel: M. Barthel
Bergoz: L. Dupuy, F. Stulle
CERN: P. Arrutia Sota, M. Basto, M. Fraser, M. Pari, F. Velotti
CNAO: A. Mereghetti, M. Pullia
GSI: P. Forck, P. Niedermayer, R. Singh, S. Sorge, A. Stafiniak, J. Yang
HIT: C. Cortes, E. Feldmeier, A. Peters
MedAustron: F. Kühteubl, D. Prokopovich, C. Schnitzer
SEEIST & Tera-Care: E. Benedetto, R. Taylor

## Slide 19
Backup slides

## Slide 20
General: Beam Fluctuations for slow Extraction
Example: C6+ at 300 MeV/u at GSI, quadrupole scan, 2.5 s extraction called ‘spill’; coasting & bunched beam
Slow extraction: Gentle beam excitation at third order resonance
Problem: Fluctuations of the extracted beam (before systematic optimization)
Improvement by bunching:
Medical facility: Readout time typ. 100 µs used since years; however, improvement required
GSI & CERN: Not acceptable for nuclear & particle physics as related to detector deadtime
Time domain:
50 Hz &
harmonics
fcut
synchrotron freq.
& harmonics
coasting beam
bunched beam
Frequency domain:
20 µs time resolution
cmean=35
Duty factor: norm. fluctuations
coasting beam
Poisson limit
bunched beam
Poisson
limit
Large fluctuation
 ‘bad’ spill
small fluctuation  ‘good’ spill
Coefficient of variance:

## Slide 21
Coasting Beam Extraction versus bunched Beam Extraction
Results:
Bunching improves the micro-spill significantly,
here bunching frequency facc  4 MHz
Lower value concerning the cut-off frequency in the Fourier-Trans.
Value of maximum-to-average depends on readout period ( = sampling freqeuncy)
However:
Also ‘bunches’ are extracted (see below). Some users do not want to have this!
Experiment: C6+, 300 MeV/u: Measured by particle counting scintillator, readout period 20 µs
EPAC‘2000
Large fluct.
 bad spill
small fluct.  good spill
50 Hz & harmonics
fcut
(decrease by factor 2)
synchrotron freq.
& harmonics
coasting beam
bunched beam
coasting beam
bunched beam

## Slide 22
Typical Duty Factor for different Facilities for operational Parameters
Time [s]
Time [s]
Time [s]
Time [s]
Duty factor
Duty factor
Facility E
trans. ko, bunched
Facility B
trans. ko, bunched
betatron (longi), coasting
Facility B
Facility C
tune scan, coasting
Facility C
tune scan, bunched
Facility D
trans. ko, bunched
Facility A
tune scan, channelling
Facility F
trans. ko, bunched
Time [s]
Time [s]
Time [s]
Time [s]
Facility | Ex. meth. | Beam | Improvement | Duty fac. Ft
A | Tune scan | coasting | Rf-chan. | 0.948
B | Trans. ko | Bunched | Air-core quad | 0.713
 | Betatron, | Coasting | Rf-chan | 0.774
C | Tune scan | Coasting | Tune wobble | 0.951
 | Tune scan | Bunched | - | 0.983
D | Trans. ko | Bunched | - | 0.947
E | Trans. ko | Bunched | Rf-chan. | 0.895
F | Trans. ko | Bunched | Air-core quad. | 0.918
Performed by Florian Kühteubl et al. (MedAustron) for same sample period of ms (but different extr. duration)
Duty factor describes normalized fluctuations  the larger the duty factor the better the beam
Result: - Different beam quality caused by power supplier quality
- Various active beam stabilizations in operation and under test

## Slide 23
Typ. Frequency Spectrum for different Facilities for operational Parameters
Frequency [Hz]
Frequency [Hz]
Frequency [Hz]
Frequency [Hz]
Amplitude
Amplitude
Facility E
trans. ko, bunched
Facility B
trans. ko, bunched
betatron , coasting
Facility B
Facility C
tune scan, coasting
Facility C
tune scan, bunched
Facility D
trans. ko, bunched
Facility A
tune scan, channelling
Facility F
trans. ko, bunched
Frequency [Hz]
Frequency [Hz]
Frequency [Hz]
Frequency [Hz]
Performed by Florian Kühteubl et al. (MedAustron) for same sample period of 10 ms
Comparison different facilities with same sample rate: Frequency spectrum 0…500 Hz
 Characterization of power supplier quality and beam reaction for typical ( = user-defined) conditions
Results:
50 Hz related lines; depends strongly on power supplier type
Different beam reaction (broadband)
Differences (expected)
coasting  bunched beam
 Beam characterization for simulation
 Requirements & methods of
counteraction

## Slide 24
Technology can be further used for feedback on 1 ms range
Control hardware & software: Feedback loop on USRP:
Shift of several application to FPGA
Latency significantly improved to 30 µs
300 Hz overall bandwidth achieved
 Contribution to GNU-based software by GSI
Topic: Feedback for macro-spill improvement
by GSI with contributions by HIT
Milestone & deliverable for rf-control exceed
Extraction time [s]
0
1
2
3
4
5
Particle rate [108/s]
0
1
2
GSI: Feedback plus improved Noise++:
Significant improvement for micro- & macro spill achieved
Automated parameter optimization successfully tested
In first operational stage at GSI now
HIT: Feedback plus improved Phase Shift Keying BPSK:
Comparable system at HIT in operation
However, less performant due medical device requirements
Automated optimization
using PyBOBYQA algorithm
Steps (= required extraction cycles)
coeff. of variance cv @5ms
Experiment: Extension for Control of Knock-out Excitation

## Slide 25
Experiment: Knock-out Extraction Signal Spectrum Dependence
E.C. Cortes Garcia et al. IPAC’22 &
E.C. Cortes Garcia et al. NIM A 167137, 2022
P. Niedermayer el. al. IPAC’23
Topic: Spill micro-structure dependence on multi-band signals for knock-out extraction
by HIT & GSI with contributions by CERN and MedAustron
Signal | Qex,1 | Qex,2 | Qex,3 | Qex
1 | -- | 0.327 | - | 0.009
3 | 0.321 | 0.327 | 1.327 | 0.001
Horizontal tune at HIT Qx= 1.6789 at end of acceleration
Excitation close to tune & harmonics fex,i = Qex,i x frev
Excitation spectrum influences:
Separatrix crossing
Diffusion from the beam towards core
Result: Strong dependence on excitation spectra
Optimization performed in 2023 (HIT, GSI, MedA)
Versatile signal generation
Large power and bandwidth from amplifier
Improvement by multi-band excitation !

## Slide 26
Experiment: Investigation of Extraction Signal Type
Topic: Spill micro-structure dependence on signal type for knock-out extraction
by GSI with contributions by HIT, CERN and MedAustron
Noise at baseband
Noise at 3 bands
Noise at baseband plus sine at two harmonics
Large fluctuation
 ‘bad’ spill
small fluctuation,
 ‘good’ spill
Systematic for excitation types: Tests at COSY (FZ-Jülich)  Significant influence systematically investigated
Such systematic comparison performed for the first time!
Spill characterization via statistical moments:
Coefficient of variance
Spill duty factor
P. Niedermayer, R. Singh.,
Scientific reports, 14, 10310 (2024)

## Slide 27
Technical development by company Bergoz Instrumentation plus GSI & CERN
Accelerator physics: Spill fluctuation caused by quadrupole current ripple, i.e. AC ripples , bandwidth 10 Hz…40 kHz
Topic: Development and integration of high dynamic range current measurement device providing (!)
Goal: Production of large dynamic range AC current measurement device by company Bergoz
Parameter for additional control | Main Quad SIS100
Magnet current specification | 
DC current min. IDC,min & max. IDC,max | 1 kA & 10 kA
DC current ramp gradient rI | 6000 A/s
Ramp time Δt | 0.1 … 1 s
AC modulation rel. min. IAC,min/IDC & max. IAC,max/IDC | 10-4 & 10-2
AC modulation absolute min. IAC,min max. IAC,max | 0.1 & 100 A
Measurement requirements | 
Measurement duration ttot | 20 s
Bandwidth fmin … fmax | 10 Hz … 40 kHz
Total dynamic range l | >120 dB
Measurement resolution flat-top relative IAC/IDC | 10-7
Measurement uncertainty UI | 0.1% - 1 %
Methodology: Test device produced by Bergoz
Transformer for Power Supplier (WG1): Specification

## Slide 28
Micro-Spill Improvements by high Frequency Bunching
High frequency bunch with  80 MHz (variable) for tune scan at GSI
Goal: Less fluctuations on 100 µs scale but fast repetition of particle to avoid pile-ups
Accelerator physics: Bunching with high harmonics leads to large synchrotron tune
Result: Improvement achieved, but influence related to synchro-betatron resonances, e.g.
 Variation in duty factor and particle arrival
Duty factor weighted with count rate:
Large fluctuation
 ‘bad’ spill
Small fluctuation  ‘good’ spill
Duty factor of one spill
Weighted duty factor
for different rf power

## Slide 29
Micro-Spill Improvements by high Frequency Bunching
Quantitative confirmation by simulations
 Usage depends user’s requirement
Particle arrival relative to rf
High frequency bunch with  80 MHz (variable) for tune scan at GSI
Goal: Less fluctuations on 100 µs scale but fast repetition of particle to avoid pile-ups
Accelerator physics: Bunching with high harmonics leads to large synchrotron tune
Result: Improvement achieved, but influence related to synchro-betatron resonances, e.g.
 Variation in duty factor and particle arrival

## Slide 30
Slow Extraction Workshop 2024
Organized by MedAustron & GSI, sponsored by IFAST
Goal: Expert meeting for all aspects of slow extraction
Frame: International workshop started 2016 at GSI
Date: 11th to 15th Feb. 2024 in Wiener Neustadt, Austria
Subjects: Facility Overview, Spill Ripples & Beam Quality,
Hardware and Machine Protection,
Managing Extraction Efficiency, Septa Development,
Optimization & Machine Learning, MedAustron tour
Program: 60 talks, 7 discussions, 1 tutorial, 10 posters
Participants: 63 from Europe, US, Japan, China
https://indico.gsi.de/event/18184/
Result:
All major experts participated
Very intense discussion and knowledge transfer
Recognition of IFAST-REX contribution
Follow-up workshop at BNL mid 2025