## Slide 1: Electron-beam based neutron sources
Laurence Wroe (CERN, ATS-DO) laurence.wroe@cern.ch
Javier Olivares-Herrador, Andrea Latina, Steinar Stapnes, Walter Wuensch 4th iFAST Annual Meeting, Krakow, Wednesday 9th April 2025

## Slide 2
Contents:
  Neutrons: Applications; Supply and Demand; Production
  Electron-beam based neutron sources: Compact & Beyond
Introduction
Additional resources:
  https://indico.gsi.de/event/19422/contributions/81834/
  https://indico.cern.ch/event/1459602/
  Publication in review – watch this space
Aim: Outline the considerations and performance of electron-beam based neutron sources at both compact and larger scales.

## Slide 3
Wide-range of applications
  Scientific
  Industrial
  Medical
Neutron Applications
BNCT = Boron Neutron Capture Therapy NP = Nuclear Physics Research RP = Radioisotope Production IR = Irradiation experiments
Data from [1], [2]

## Slide 4
Scientific [3]:
  Over 4,000 peer-reviewed neutron scattering publications each year
Industrial / societal [4]:
  Energy storage – in-operando testing for next generation batteries
  Materials – measurements of stresses for material advancement
  Environment – in-operando testing of next generation solar-cells
  Security – analysis of single-event effects
Medical:
  Drug discovery – non-destructive and deep probing of biological samples (e.g. proteins)
  BCNT – 33 facilities worldwide [5]
Demand for Neutrons
Neutron beam-time usage averaged over ILL, ISIS, and LLB
Taken from [4]
  Oversubscription rate to neutron beamtime of between 2 and 5 times.
  Acknowledged underexploitedness and underservedness of industry.

## Slide 5
Nuclear Research Reactors (stats for power > 1 MW [6])
  91 in operation
  17 planned / under construction
  But 182 shutdown / decommissioned
Spallation Sources
  11 in operation
High Neutron Flux
FRM I nuclear reactor, Munich, 1957
“…the neutron community therefore faces the very real prospect of having very few operational neutron sources in Europe by 2030.” [4]
ESS, Lund

## Slide 6
Compact Accelerator Neutron Sources (CANS) can offer a solution for a medium flux scale
  More scalable because of a lower cost, complexity, infrastructure
  Tailored to specific application to compensate for a lower-flux
Medium Neutron Flux
Example of a conceptual design of VULCAN (Versatile ULtra Compact Accelerator-based Neutron source)

## Slide 7
Hadron accelerators generate neutrons directly through:
  Spallation (> 100 MeV, 1-2 GeV more optimal)
  1-stage nuclear reaction (< 100 MeV)
    e.g.
Accelerators – Hadron vs Electron
Electron accelerators predominantly generate neutrons through:
  A primary Bremsstrahlung reaction
  Then a secondary photoreaction
Photonuclear cross-section W(g,n)
Taken from [7]
Let’s compare the technologies!

## Slide 8
Turnkey solution for generating cold / thermal neutrons (λ ~ Å; v ~ 1 km/s)
  optimised for stress measurements in an industrial setting
  also suitable for neutron powder diffraction measurements within a university campus
VULCAN – An Electron-based CANS
DAES SA
Danish Technology Institute
Xnovo

## Slide 9
Why electron-driven?
  Neutron yield per kW of beam power is comparable between a 35 MeV electron beam and a < 10 MeV proton beam
  Electron acceleration to 35 MeV is relatively simple and cheap
  High-gradient accelerating technology can be utilised for a compact accelerator design
  High-gradient accelerating technology is compatible with the desirability of a pulsed particle beam for time-of-flight neutron measurement
VULCAN – Technology Choice

## Slide 10
CERN-DAES collaboration (2023-2025) delivering:
  Conceptual design of the electron accelerator
  Proof of concept of DAES’ target-moderator-reflector assembly in CERN’s CLEAR accelerator
DAES are seeking funding for the fabrication of a first machine
Project VULCAN – Status
The VULCAN prototype TMR

## Slide 11
“Is a high-gradient electron linac a suitable driver for neutron production?”
Studies undertaken that:
  Determine the electron beam specification achievable with:
      Accelerators based on high-gradient S-band technology
      Accelerators based on high-gradient X-band technology
  Model neutron production with calculated electron specification
  Characterise the unmoderated neutron spectrum
  Compare with state-of-the-art neutron facilities
Electron-Beam Based Neutron Sources

## Slide 12
Example Findings
High-energy, high-intensity electron linacs can provide bright neutron beams to a specification comparable to proton-linac and spallation sources
Neutron production is a trade-off between beam power, cost, and length

## Slide 13
Conclusions
There is an ever-increasing need for neutron sources, yet the supply is predicted to diminish as facilities shut down
Electron-based neutron sources can be suitable for generating medium-fluxes as small-scale CANS and higher-fluxes as much larger machines
Aim: Outline the considerations and performance of electron-beam based neutron sources at both compact and larger scales.
Thank you for listening! Please do not hesitate to ask me questions now or later

## Slide 14
Bonus Slides

## Slide 15
Bonus Slides

## Slide 16
Bonus Slides