## Slide 1: The double target holder
Benji, Rug, Stef

## Slide 2: Design criteria for the new target holder
Targets need to be much smaller
Reflection target necessary to continue the present tests
but the reflection target should be installed under an angle to the direction of flight,- like the 2018 target
Transmission target for starting the tests of Ps formation in forward direction
Minimize the steering of pbars, positrons and Laser as much as possible ie, by moving the A0 target electrode we should shift form reflection to transmission target.
It should be thermally isolated to keep the heat load to the magnets minimal
apply bias voltages of a few 100V
Facilitate maintenance, and easy changes of targets

## Slide 3
Electrons from the 5T
Active area of the 1T MCP
(25mm)
Inferred size of the
1T electrodes (30mm)
Present target

## Slide 4
P-bars from the 5T
Position of the new target

## Slide 5
P-bars from the 5T
Position of the new target

## Slide 6
New target holder ring
3D printed copper
Laser ~8mm diameter at the target
P-bars 4mm diameter
Reflection target 3x4.5mm
Transmission target 3x3 mm
The double target holder

## Slide 7
The double target holder
Reflection target
Transmission target
Positrons,
Pbars and
Laser
do not move when
Switching targets

## Slide 8
A possible technical solution from the PCB lab in CERN:
(they also made our Cupper-Beryllium double-grid on the Grid-Cryo-Motor)
Cupper Beryllium foil 0.4mm
Cupper Beryllium foil 0.2mm
Transmission Target ~ 3 um

## Slide 9
Reflection target holder:
Cupper Beryllium foil 0.3mm
Reflection target 0.5 mm
Cupper base 2.0mm
The target does not have to
perfectly cut

## Slide 10: Still to be done
add adequate mechanical clamps to hold the targets securely in place
  test the transmission target holder under cryogenic conditions
add heater and temperature sensor to the ring
add thermal insulation in order to keep it at RT without heating the environment too much
integrate to the existing trap infrastructure:
  new cable management with new connectors for easier maintenance
  shift the optical elements for the laser a few mm further downstream
3D print / or micro water jet cut the elements
test the heating of the targets with an infra red camera in a vacuum setup

## Slide 11
Short support plate
(fixed with 4 screws to the trap support plate)
Optical unit
Alignment motor unit
The modular design of the trap extension:

## Slide 12
Target size 3x3mm in comparison
SMA HF connector