## Slide 1: Sustainability of Particle Accelerators with focus on high intensity
Mike Seidel
Paul Scherrer Institute and EPFL, Switzerland
CERN Accelerator School
June, 2025, Borovets

## Slide 2
energy related research
use of critical materials
grid energy consumption
energy sources / procurement
life cycle management & recycling
water consumption
research infrastructure system efficiency
mobility &
business travel
heating & waste heat recycling
office/lab energy consumption
efficient technologies
Sustainability = Meeting the needs of the present without compromising the ability of future generations.
(one of many debated formulations)
construction GHG emissions

## Slide 3: Energy Consumption - Motivation
The world energy consumption has been continuously rising, reaching ca 19 TW today.
As a science community we rather want to contribute to solutions and not be part of the problem.
School Strike for Climate
Wikipedia
Earth
Moon
Tides
example from nature:
the Earth-Moon system dissipates 3.8 TW power from the rotation energy of earth
[Williams, Boggs, 2016]
includes all sources

## Slide 4: Community Activities on Sustainability
2014-17: EUCARD-2, WP Energy Efficient Accelerator Technologies
https://www.psi.ch/enefficient
2017–21: ARIES, Work Package Efficient Energy Management
https://www.psi.ch/aries-eem
2021–25: I.FAST, Work Package Sustainable Concepts
https://www.psi.ch/scat
ICFA panel on sustainable accelerators, chair: Thomas Roser (BNL)
https://icfa.hep.net/icfa-panel-on-sustainable-accelerators-and-colliders/
 consult websites for link collection to workshops and documentation

## Slide 5: Accelerator driven Research Infrastructures (RI)
grid power
primary beam
auxiliary systems
conversion target
undulators/magnets
colliding beam insertion
…
primary beam production
conversion to specific secondary radiation
protons
ions
electrons
neutrons, muons, neutrinos
exotic particles
X-rays
high level goal:
Science output per grid power, per operating/investment cost.
radiation to
experiments
accelerator

## Slide 6: Accelerator Concepts and Technologies [with emphasize on energy efficiency]
Proton Drivers with high intensity applications
Synchrotron Light Sources and FELs
Particle Colliders
Resonators and high Power RF Systems
Accelerator Magnets and Power Supplies
Cryogenic Systems
Component Cooling, Air Conditioning, Vacuum, Instrumentation … and other aux. systems
concepts, RI‘s
technologies

## Slide 7: Proton Driver Accelerators … and best attainable Grid-to-Beam efficiency?

## Slide 8: Megawatt Proton Driver Concepts
Yakovlev, FNAL, invited talk, IPAC 2017
Workshop: Efficiency of Proton Driver Accelerators, 2016, PSI
https://indico.psi.ch/event/3848/
 | technology | application
spallation neutron source SNS | s.c. linac + accumulator ring | pulsed neutrons
J-PARC Complex | rapid cycling synchrotron 3GeV (and main ring 30GeV) | pulsed neutrons, neutrinos, muons and more …
PSI High Intensity Proton Accelerator | isochronous cyclotron | CW neutrons, muons, ultra cold neutrons

## Slide 9: J-PARC Complex
RCS provides an economic solution to reach high energy of 3GeV; C=348m
is needed as injector for main ring to 50GeV
25Hz cycling allows to achieve 1MW for neutron and muon production
grid to beam efficiency is limited by losses from the cycling magnetic fields (ca 3%)

## Slide 10: Mitigate energy loss in cycling synchrotrons (Yoshi Kurimoto,KEK)
Increasing Repetition Rate from 0.4 Hz to approximately 1 Hz
< 1.3 s
Issue：Large power variation @ AC main grid
磁気エネルギーの流れ
~D140MW
2.56sec cycle
1sec cycle
Not allowed by Tokyo Electric Power Company
Energy Recovery with Bank Capacitor
Requirement : Energy Storage
concerns main ring in J-PARC, but applicable also to other cycling synchrotrons
use energy storage system to recover field energy from magnets

## Slide 11: Spallation Neutron Source SNS (ORNL)
superconducting linac accelerates H- to 1GeV at 60Hz repetition rate
accumulator ring compresses the pulse from 1ms to 0.7s by stripping injection of H-
pulsed neutrons are needed for many types of research and are advantageous over CW neutrons (reactor or PSI cyclotron)
however, grid to beam efficiency is limited by pulsed operation of s.c. linac (ca 9%)
 see later discussion on s.c. linacs

## Slide 12: PSI High Intensity Proton Accelerator
Ring Cyclotron 590MeV
2.4mA / 1.4MW
diameter: 15m
SINQ
spallation source
proton therapie center [250MeV sc. cyclotron]
dimensions:
120 x 220m2
meson production targets
isochronous cyclotron: no cycling of magnets/RF; but CW beam
low frequency RF, 50MHz, thus efficient
large and bulky magnets cover wide radius variation of beam (to R=4.5m)
1.4MW record beam power; low bunch charge through CW

## Slide 13: Power flow in PSI’s High Intensity Proton Accelerator
public grid ca. 10MW
required for p beam: 7.8MW
RF Systems 4.1MW
Magnets
 2.6MW
aux.Systems
Instruments
 3.3MW
Beam on targets
1.4MW
heat  to river, to air
neutrons
muons
cryogenics
conversion chain to beam power
offset power for aux. systems
finally heat

## Slide 14: Copper Resonators in PSI’s Ring Cyclotron
f = 50.6MHz; Q0 = 4,8104; Umax=1.2MV (presently 0.85MV)
transfer of up to 400kW power to the beam per cavity; a total of 4 cavities
Wall Plug to Beam Efficiency (RF Systems): 32% [AC/DC: 90%, DC/RF: 64%, RF/Beam: 55%]
hydraulic tuning devices (5x)
resonator inside

## Slide 15: Comparison: Megawatt p-Drivers
facility | accelerator type | Economy | Energy Reach | Power Reach | operational complexity | grid-to-beam Efficiency
SNS | superconducting linac | -- | ++ | ++ | ++ | 9%
J-PARC | rapid cycling synchrotron | ++ | ++ | - | - | 3%
PSI | isochronous cyclotron | + | -- | + | - | 18%
Megawatt class facilities operating today:
optimized for application, not efficiency!
590 MeV, 1.4 MW

## Slide 16: PSI: Improving Conversion Efficiency to secondary Radiation
measure | gain
Zr cladding instead steel | 12%
more compact rod bundle | 5%
Pb reflector | 10%
inverted entrance window | 10%
total gain factor | 1.42
color code: neutron density on same scale (MCNPX)
old
new
beam
beam
Example: neutron production target at PSI

## Slide 17: ESS: Improving Conversion Efficiency to secondary Radiation
Example: neutron production target at ESS
L.Zanini et al (2019):
Brightness increase by using low-dimensional moderators.
The flat moderators adopted for ESS offer a clear brightness increase with respect to the original TDR design based on volume moderators: the cold brightness increases by more than a factor of 2.5 with respect to the original design for ESS.

## Slide 18: Best attainable Grid-to-Beam efficiency with superconducting linac technology.

## Slide 19: Superconducting Linac : High Efficiency Potential example: PIP-II design of Fermilab
operating regime | avg. RF power | cryogenic power | avg. beam power | grid-to-beam Efficiency
PIP-II pulsed operation | 1.44MW | 1.19MW | 17.6kW | 0.7%
PIP-II CW operation | 9.10MW | 1.83MW | 1.60MW | 15%
PIP-II base parameters:
H-, 800MeV, 2.0mA, part of Fermilab complex
aim: neutrino production (1MW @ 60..120GeV)
CW operation as upgrade path
highest efficiency
[from presentation B.Chase, Y.Yakovlev, 2018]
not efficient in pulsed operation:

## Slide 20: Low Loss Superconducting Resonators
3‘000 church bell
50‘000 Cu resonator
21010 s.c. resonator
1
105
1010
Q0 = quality factor
 e-folding decay and resonance width
high Q resonators, 1.3GHz, 2K, FNAL
[A.Grassellino, A.Romanenko et al, 2013]
example:
Ua = 20MV, (R/Q) = 609, Q0 = 21010, Ib=2mA
Pdissip = 33 W
Pbeam = 40.000 W
dissipated power:
but: cryogenic efficiency!

## Slide 21: Cryogenic Efficiency
best possible coefficient of performance (COP):
Wc = amount of work required to remove heat Qin at cold temperature T
T0 = 293K
T = 2K
Qin
Wc
[S.Claudet et al, CERN 2013]
factor 3!
 lower COP is better !

## Slide 22: COP Factor: compare heating of houses
best possible coefficient of performance (COP):
T = 308K (35C)
T0 = 273K (0C)
Qout, Qin
W
in theory: COPCarnot = 8.8
in practice: COP = 3…5
in this case  higher COP is better !

## Slide 23: Powerflow s.c. Linac – Minimum System Example for a Single Cavity
GRID
AC/DC/RF/guide
RF  0.4 .. 0.6
cryogenics
COP  1000
beam
Pdissip
PRF
power balance:
regime | Ib [mA] | Q0 | RF | Pbeam [kW] | grid-to-beam Efficiency
TDR, CW | 2.0 | 21010 | 0.44 | 40.0 kW | 30%
high Q | 2.0 | 31010 | 0.44 | 40.0 kW | 33%
high current | 4.0 | 31010 | 0.65 | 80.0 kW | 50%
considered:
one 650MHz cavity
Ua = 20MV
l = 1.1m
ignored: cavity detuning, <1, regulation overhead, aux. systems …
extrapolation

## Slide 24: Energy Efficient Accelerator Technologies

## Slide 25: Supercondactivity in Particle Accelerators
the main concepts in accelerators: bending of trajectories and energy gain by RF fields, profit from energy efficient superconducting technology
DC field: cooper pairs move frictionless
zero losses
example: MRI magnet with cold switch
RF field: cooper pairs move frictionless, but carry mass that is accelerated back and forth
 imperfect shielding of RF field in material
 dissipation from «normal» electrons in RF field
 very small but non-zero losses
Magnets
RF Resonators

## Slide 26: Technology R&D: Superconducting RF at higher temperature
promising R&D: Nb3Sn coated cavities at Cornell
4.2 vs. 2.0K  efficiency
[M.Liepe, Cornell, IPAC‘19]
S Posen et al 2021 Supercond. Sci. Technol. 34 025007
record cw gradient in Nb3Sn-coated, Eacc = 24 MV/m
Cornell, FERMILAB
 simplicity, cost, efficiency, smaller size
To be published
DESY, Hamburg U.
aim for sustained SRF accelerator technology
10y Goal: >70 MV/m with a Q0 of 1x1010 and at 4K
contact: M.Wenskat, DESY
G. Deyu et al., „Al2O3 coating of Superconducting Niobium Cavities with thermal ALD“, in preparation
SMART recipe leads to a Tc of 15.4 K on Nb-samples coated with 15 / 25 nm of AlN / NbTiN

## Slide 27: Efficient RF Power Sources
Example: SSA for Isotope production Cyclotron, 98.5MHz, 12x1kW units, D=93% (90% with regulation overhead)
Uppsala group, WP in I.FAST program
Magnetron, R&D at various groups, =60-80% within reach
e.g. Wang et al, J-Lab, IPAC 2019; A.Dexter, Lancaster U., LINAC-2014; B.Chase, Fermilab, JINST-2015
Klystrons, >70% within reach
e.g. CLIC two stage multi-beam klystron, J.Cai, I.Syratchev, IEEE Trans, 2020
Solid state amplifiers (SSA) at various groups, =60-90% depending of freq.
Example: study 1GHz for CLIC drive beam; 6 cavities, 30 beamlets; 25+140kV; sat=82%
https://indico.cern.ch/event/1407353/
I.FAST efficient RF workshop, July 23-25, 2024, Toledo:

## Slide 28: Accelerator Magnets with High Temperature Superconductor Coils
magnets with High Temperature Superconductor (HTS) coils:
medium fields for all applications (high fields in block config.)
ReBCO and Bi-2212 materials are studied
no ohmic losses, can replace power hungry large aperture dipoles/quads
cryogen free conduction-cooling possible (no He)
much improved cryogenic efficiency at elevated temperatures (e.g. 4.5K…15K instead 2K)
today expensive materials
field ramping and field quality difficult (wide tapes)
solenoid test magnet, 18T @ 12K
PSI/CHART, B.Auchmann et al

## Slide 29: Accelerator Magnets with Permanent Magnet Material
B = 1.35 T g = -40.6 T/m
Dipole and Quad for SLS2.0, S.Sanfilippo et al (PSI)
permanent magnets:
extremly compact  low emittance lattices
no power consumption
no cooling, thus no heat introduced, no vibrations from cooling loop
field tuning difficult
use of rare earth materials

## Slide 30: Pulsed Magnets for beam Transfer Channels in lead: GSI, S. Heberer, P. Gehrke, P.Spiller et al
 | Prototype Quadrupole
Gradient | 80 T/m
Length | 0.65 m
Pulse length | 90 ms (beam 1 ms)
Peak current | 400 kA
Peak voltage | 17 kV
Energy @17 kV | 65 kJ
Inductivity | 535 nH
Capacitor | 450 mF
Forces | 200 kN
Engineering model of the prototype quadrupole magnet incl. support
low average power; high field; compact; energy recovery in capacitive storage (power supply)
complexity added by pulsing circuit; field precision potentially challenging

## Slide 31
other aspects of sustainability - heat recovery
- rare earths, critical materials - carbon footprint of components, construction, operation - carbon footprint of tunnel dominates

## Slide 32: Recover High Quality Power from Heat?
produce work  electrical power?
example: T=40C: efficiency 8%
T=95C: efficiency 20%
convert heat to higher T level for heating purposes
example: T=40C, Tuse =80C, COP=5: W=10kW, QC=40kW, QH=50kW
(availabe for heating)
use heat directly at available temperature
example: Tuse=50C …80C : heating
Tuse=25C…50C: green houses, food production
1 [electrical power]
0.95 [mechanical power]
0.3…0.4 [heat]
the quality of power
heat pumps at MAX-4
[Björn Eldvall / E.ON, Martin Gierow / Kraftringen]

## Slide 33: Biology/Nature is more efficient …
An increase in temperature from 8.6 to 13.7 oC
doubled the growth rate in salmon smolt.
Weight (average) in grams
Days
T = 5 C
A.Kiessling

## Slide 34: Powering accelerators from local PV renewable energy, C.Martins ESS
AC
DC
DC
DC
AC
DC
DC
DC
Power Converter
load (magnets, RF amp’s)
AC grid
~
AFE: Active Front End
DC
DC
Power Converter
AC grid
~
load (magnets, RF amp’s)
DC
DC
Conventional scheme:
PV injected into the AC grid (4 stages)
New scheme:
PV injected into power converters (2 stages)
ηPV≈0.98x0.97x0.97x0.95 = 87.6%
ηPV≈0.98x0.95 = 93.1%
For P=0.5MW ->
savings ≈ 20k€/year
Concept:
Install PV panels near accelerators’ “wasted land”;
Connect them to main power converters for accelerator magnets or RF amplifiers, using high efficiency DC/DC conversion
can redirect the PV energy back to the AC grid when accelerator not running
Up to 15-20% renewable energy utilization possible with no transmission losses and high conversion efficiency
Lower capital cost & lower payback time
Feasibility study for ESS case: up-to 2MW installed PV

## Slide 35: Critical Materials: Niobium for Superconducting Cavities, B.List, DESY
RRR (Residual Resistivity Ratio) is an indicator of purity
is defined as the ratio of its electrical resistivity at room temp 273 K to its resistivity at cryogenic temperature
RRR>=300 achieved by 6x vacuum remelting
estimate by B.List (DESY):
  Niobium RRR>300, from China: 98kg CO2-e / kg;
  (stainless steel ca 5..7 kg CO2 / kg) -> 10% of total GHG for ILC250 accelerator! -> large impact reduction potential
M. Hörmann, J. Less-Common Met. 139(1988)1 DOI:10.1016/0022-5088(88)90324-4
electron beam melting machine
impurities after n melting cycles
cavities based on thin film superconductor can reduce CO2 footprint (and operate at higher temperature), but technology is not ready for large scale deployment today

## Slide 36
Topics:
rare earths: benefits and issues
assessing carbon footprint, env. impact, societal impact …
supply chains and certification
recycling
https://indico.desy.de/event/35655/

## Slide 37
Introduction next slide - an example of the complex assessment of many factors for rare earth materials:
„normalised impacts“ per kWh generated from different types of wind power stations with/without rare earths from various sources
material mining: precarious conditions for workers
material mining: environmental pollution
material processing: pollution, toxicity
other materials needed … and more

## Slide 38: excerpt: Comparison of Wind Generator Types, Petra Zapp (IEK-STE)
0,0E+00
5,0E-05
1,0E-04
1,5E-04
2,0E-04
2,5E-04
DFIG
DDSG
BO
magnet
MP
magnet
DDPMSG DDPSMG DDPSMG
MW
magnet
normalized impacts [PE]
aluminum
concrete
permanent magnet
copper
cast iron, steel
stainless steel
plastics & chemicals
transport, energy & waste
A. Schreiber, J. Marx and P. Zapp: Comparative life cycle assessment of electricity generation by different wind turbine types; Journal of Cleaner Production 2019 Vol. 233 Pages 561-572
Influence of RE origin (ore type, mining location, specific site conditions) on environmental impacts per 1 kWh electricity generated by 3 MW wind power plant
DFIG: DDSG:
doubly-fed induction generator direct driven synchronous generator
DDPMSG: electrically excited and direct drive permanent
magnet synchronous generator
Electricity generation by DDPMSG with
magnet produced
(Bayan Obo) has
from
higher
environmental
impacts
permanent Chinese RE normalized compared to
U.S. Mountain Pass (→ 20%)
Mt. Weld (Aus) (→ 33%)
Electricity generation by Australian DDPMSG is 8% better than by DFIG

## Slide 39: Electromagnet Operation vs. Manufacturing Footprint, B.Shepherd, STFC
Power usage at nominal operating point
  CLARA 1: 385 W
  CLARA 2: 2.01 kW
  FEBE: 3.72 kW
UK electricity carbon intensity 2022: 193 gCO₂e / kWh
(and improving every year!)
Highly dependent on fuel mix:
Sweden 21g; France 102g; USA 432g; Germany 481g; Switzerland 153g (source: Electricity Maps)
Assume operated for 5 years, 250 days per year, 16 hours per day
Total impact of operation (note: cooling not included)
CLARA 1: 1.49 tCO₂e
CLARA 2: 7.76 tCO₂e
FEBE: 14.4 tCO₂e
Much greater than manufacture impact
600
500
400
300
200
100
0
2000
2005
2010
2015
2020
2025
Carbon intensity
[gCO₂e/kWh]
Year
 |  |  | ma
0
2
4
total impact over 5 years [tCO₂e]
6 8 10
12
14
16
CLARA 1
CLARA 2
FEBE
nufacture operation
Ben Shepherd • Electromagnets vs Permanent Magnets • Rare Earth LCA workshop, 6-8 Feb 2023

## Slide 40: CO2 Construction Footprint, example CLIC, B.List et al
5
CLIC tunnel (drive beam option), 5.6m diameter
estimate: 12.4m2 concrete
-> 31 t/m concrete
CLIC tunnel (klystron option), 10m diameter
estimate: 44.8m2 concrete
-> 112 t/m concrete

## Slide 41: The Future – Fluctuating Energy Sources
courtesy: FRAUNHOFER-INSTITUT FÜR SOLARE ENERGIESYSTEME ISE, Karlsruhe (2020)
residual power
production of power
solar, wind
release from storage
variation: x5!
use of power
industry, traffic etc
energy storage
simulation: April 2050, sustainable energy system, Germany
full RI operation at times of high grid production
reduced operation or standby modes with fast performance recovery otherwise

## Slide 42: Comment on Energy Production (actually Conversion)
binding energy of known isotopes
The Sun (:: wind, PV)
fusion reactor
fission reactor
radioactive decays (geothermal energy)
With accelerator driven systems (ADS) nuclear power can be made safer and more sustainable.
For fusion reactors synergetic R&D in the field of accelerators, like RF power generation, s.c. magnet - and vacuum technology.

## Slide 43: Summary High Intensity Particle Accelerators
Grid to Beam
State of the art 20%, up to 50% reachable for s.c. linacs & high beam power; cyclotrons provide solutions for E<1GeV, e.g. ADS systems
Technology
s.c. magnets & high Q cavities are efficient, higher temperature operation (HTS)
efficient RF sources, permanent magnets, heat recovery & photovoltaics
other: heat recovery, critical materials, managed lifecycle, carbon footprint, energy procurement, advanced energy production

## Slide 44: Thank you for your attention.