## Slide 2: Injection and extraction CAS on intensity limitations in hadrons beams – Part 1
Y. Dutheil, CERN, Geneva, Switzerland (SY-ABT-BTP) with material from past and current members of the ABT group as well as F. Tecker

## Slide 3
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The material is used for the sole purpose of illustration for teaching or scientific research. The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.
Copyright statement and speaker’s release for video publishing

## Slide 4: Injection-Extraction @CERN
CERN ABT group
  Accelerator Beam Transfer, website
  The ABT group is in charge of the design, development, construction, installation, exploitation and maintenance of injection and extraction related equipment and beam-transfer systems

## Slide 5: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 6: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 7: Introduction
Accelerators have limited ranges of energies
  A synchrotron have a typical range of energy of 20
    LHC from 450GeV to 7000TeV for protons (x15)
    SPS from 14GeV to 450GeV for protons (x30)
  Particles get accelerated in a chain of accelerators
Injection and extraction between stage needs careful consideration
  to maintain the beams properties, in particular brightness
  To deliver beams with required properties to fixed target experiments
The focus of this lecture
  General principle of injection/extraction for hadron synchrotrons
  Focus on high-intensity applications
  Second part focused on examples and experience from CERN complex

## Slide 8: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 9: Basic principle of injection

## Slide 10: Basic principle of injection
t
kicker field
intensity
injected
beam
Kickers produce fast pulses, rising their field within the particle-free gap in the circulating beam (temporal separation)

## Slide 11: Basic principle: Kicker
Aperture dimensions constrained by beam size at kicker location.
Short rise time: < 100 ns –few μs: low inductance.
Maximise horizontal kick: small vertical aperture.
B
HV conductor
Vertical aperture, Vap
Ferrite
HV
Return conductor
Horizontal
aperture, Hap
μr
μ0

## Slide 12: Basic principle of injection
t
kicker field
intensity
injected
beam
Kickers produce fast pulses, rising their field within the particle-free gap in the circulating beam (temporal separation)
Septa compensate for the relatively low kicker strength, and approach closely the circulating beam (spatial separation)

## Slide 13: Basic principle: septum

## Slide 14: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 15: Fast injection: concept
Septum + kicker work together to put beam onto reference trajectory.
Several trains can be stacked (e.g. from smaller ring to larger).
Slow bumpers may be used to minimize necessary kicks.
Applications: PS, SPS, LHC, etc. (“Bread and butter” of injection.)
Also applies to extraction systems
t
kicker field
intensity
injected
beam
‘boxcar’ stacking

## Slide 16: Injection techniques : Fast injection
Example of the LHC injection
Injected beam
Septum
Kicker
MSIs (P8)
MQY (superconducting LHC quadrupole)
MKIs

## Slide 17: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 18: Normalized phase space: concept
Hill’s equation describes oscillator whose amplitude and frequency vary with s coordinate.
E
x
E
x
ds
~K(s0)
~K(s1)

## Slide 19: Normalized phase space: concept
Hill’s equation describes oscillator whose amplitude and frequency vary with s coordinate.
E
x
E
x
ds
~K(s0)
~K(s1)

## Slide 20: Normalized phase space: concept
Hill’s equation describes oscillator whose amplitude and frequency vary with s coordinate.
E
X
dμ
s1
E
X
dμ
s0

## Slide 21: Normalized phase space: math
x(s)
x’(s)
Area = pe
Area = pe
Real phase space
Normalised phase space



## Slide 22: Fast injection: normalized phase space
Seen from the ring
  in the normalized transverse phase space in the plane of injection

## Slide 23: Fast injection: normalized phase space
Seen from the ring
  in the normalized transverse phase space in the plane of injection

## Slide 24: Fast injection: normalized phase space
Seen from the ring
  in the normalized transverse phase space in the plane of injection

## Slide 25: Fast injection: normalized phase space
Seen from the ring
  in the normalized transverse phase space in the plane of injection

## Slide 26: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 27: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 28: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 29: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 30: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 31: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 32: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 33: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 34: Dipole error and filamentation
Filamentation
  Mismatch between the injected position and ring closed orbit leads to a dipole oscillation around the closed orbit
  Mismatch between the injected shape and ring closed solution leads to a quadrupole oscillation of the beam
  Both errors lead to filamentation, and a reduction of the beam brightness
Turn after turn the brightness of the beam decreases as its emittance increases
  This effect is due to non-linear behaviour: particles at different distances from the center do no rotate at the same speed

## Slide 35: Dipole error and filamentation
If injection oscillation is left uncorrected, it might disappear after several turns.
Turn #
BPM signal over many turns

## Slide 36: Dipole error and filamentation
If injection oscillation is left uncorrected, it might disappear after several turns.
However, it has been “exchanged” for an r.m.s. emittance blow-up.
orbit
emittance
Turn #
Turn #
BPM signal over many turns

## Slide 37: Dipole error and filamentation
Example of such effect observed, at the SPS to LHC injection
SPS
TI8 transfer line
First arc of LHC (P8 to P7)

## Slide 38: Dipole error and filamentation
In numbers the coordinates for the misinjected (new) beam are
The mean action over all the particles is
The emittance increase is
[1] V. Kain, Emittance Preservation, CAS17 injection/extraction, https://doi.org/10.23730/CYRSP-2018-005.507

## Slide 39: Dipole error and filamentation
  Mismatch between the injected beam and closed orbit -> injection oscillations
  Non-linearities -> particles at different transverse amplitudes rotate at different speeds.
  Beam distribution “wraps around” closed orbit.
  Rms emittance increases + injection oscillations are damped.
  Effect can be partially mitigated by using transverse damper -> pick-up + kicker feedback system inside ring.
  Emittance increase is moderated by the ratio of damping time from the feedback system () to the filamentation time ()
[1] V. Kain, Emittance Preservation, CAS17 injection/extraction, https://doi.org/10.23730/CYRSP-2018-005.507

## Slide 40: Dipole error and filamentation
LHC Damper in Cell 6, right of P4
Example of LHC damped injection oscillation from ADT system commissioning

## Slide 41: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 42: Betatron error and filamentation
SPS
LHC
Regular lattice (FODO) (elements all powered in series with same strengths)
Final
matching
section
SPS to LHC Transfer Line (3 km)
Extraction
point
Injection
point
Initial
matching
section
Independently powered (tuneable) quadrupoles
Independently powered (tuneable) quadrupoles and (in this case) passive protection devices

## Slide 43: Betatron error and filamentation
Mismatch in optical parameters will lead to emittance blow-up via filamentation:
x
x’
Turn 0
Turn N
Time

## Slide 44: Betatron error and filamentation
Mismatch in optical parameters will lead to emittance blow-up via filamentation:
x
x’
Turn 0
Turn N
Time

## Slide 45: Betatron error and filamentation
Mismatch in optical parameters will lead to emittance blow-up via filamentation:
x
x’
Turn 0
Turn N
Time

## Slide 46: Betatron error and filamentation
Betatron mismatch
Using the parameter such that and
Coordinates in the normalised phase space of the ring become
Resulting emittance increased depend on the mismatch factor
[1] V. Kain, Emittance Preservation, CAS17 injection/extraction, https://doi.org/10.23730/CYRSP-2018-005.507

## Slide 47: Betatron error and filamentation
Quadrupole pick-up measurement is vert challenging and not presently used at CERN [1]
Emittance measurement comparison between rings is particularly challenging
  Example of emittance measurement in the PSB-to-PS using special optics [2]
  Very small differences in the beam halo population measured between SPS and LHC could come from mismatch [3]
Intensity limitations
  Intercepting measurements such as wire scanner cannot be used for the highest intensity beam [4-5]
[1] A. Sounas, M. Gasior, T. Lefevre, BPM TECHNOLOGIES FOR QUADRUPOLAR MOMENT MEASUREMENTS, HB2018, Daejeon, Korea
[2] W. Van Goethem*, E. Maclean, G. Franchetti, A. Huschauer, F. Asvesta, H. Rafique, Zero Dispersion Optics in the PS, July 2024, CERN, https://indico.cern.ch/event/1433323
[3] M. Rakic, Assessing the origin of the LHC beam halo, IPAC25, https://indico.cern.ch/event/1558252/#3-assessing-the-origin-of-the
[4] M. Sapinski∗, T. Kroyer, OPERATIONAL LIMITS OF WIRE SCANNER ON LHC BEAM , BIW08, Tahoe City, California
[5] E. de la Fuente, et. al., IMPEDANCE AND THERMAL STUDIES OF THE CERN SPS WIRE SCANNERS AND MITIGATION OF WIRE HEATING, IPAC24, Nashville, TN, USA
[1]

## Slide 48: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 49: Injection protection challenges at the LHC
Transferred high intensity beam can be very destructive
LHC beam in numbers
  Up to 4.8 MJ per injection (288 bunches at 2.3E11 ppb)
  Up to ~700 MJ per extraction
Individual injection/extraction system failure must be accounted for
Damages on a vacuum chamber of TT40 magnet (SPS-LHC transfer line) [1]
[1] A Bertarelli, Beam-Induced Damage Mechanisms and their Calculation, 2014 Joint International Accelerator School: Beam Loss and Accelerator Protection, Newport Beach, CA, USA
Outside of the vacuum chamber
Inside of the vacuum chamber, beam impact side
Inside of the vacuum chamber, side opposite to the beam impact

## Slide 50: Injection protection challenges at the LHC
Prevention measures
Fast interlock where possible
  Slow magnets and septa may fail slowly enough to be detected and inhibit the beam transfer >~1 ms
  Slow changes in beam characteristics may be detected through beam loss measurement
Fail-safe kicker triggering design
Commissioning and setup with low intensity
  All machines are commissioned, and systems functionality validate with low intensities (takes about 5 weeks for the LHC)
LHC control and power electronics for the dump system in UA63

## Slide 51: Injection protection challenges at the LHC [1]
A system of 3 collimators (2 jaws each) per plane at 60° phase advance from each other is installed at the end of the SPS-to-LHC TLs [2]
  optimized ratio: provided protection/number of collimators.
  Intercept large amplitude oscillations and attenuate escaping intensity below damage limit of LHC aperture  collimator geometry (material and active length)
[1] C. Bracco, Injection: Hadron Beams, CAS Beam Injection, Extraction and Transfer, 2017, Erice, Italy
[2] V. Kain, “Machine protection and beam quality during the LHC injection process”, CERN-THESIS-2005-047

## Slide 52: Injection protection challenges at the LHC [1]
Losses at injection beyond the core of the beam may be limiting
[1] C. Bracco, Injection: Hadron Beams, CAS Beam Injection, Extraction and Transfer, 2017, Erice, Italy
[2] B. Salvachua, STUDY OF THE PERFORMANCE AND BEAM LOSS LIMITATIONS DURING INJECTION OF HIGH-INTENSITY LHC PROTON BEAMS, IPAC24
[3] Y. Dutheil, Losses for LHC beams, up to LHC injection, JAP23, Montreux, Switzerland
Transverse
Longitudinal
Injection losses limited LHC intensity in the early part of the proton run in 2023 due to losses of <0.1 % [2-3]

## Slide 53: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 54: Injection protection challenges at the FCC-hh
Considerations
  LHC used as injector for the FCC
  Injection energy = 3.3 TeV (x7 HL-LHC)
  Bunch population = 1.1E11 ppb
  LHC can be filled with ~2800 bunches but, in order to limit the stored energy of the injected beam into the FCC to 5 MJ one can extract/inject 90 bunches at the time  reduce kicker flattop! [6]
trise injection kicker defined by the target filling factor assuming a target filling factor of 80%  0.28 μs
The LHC is emptied to fill FCC by pulsing the extraction/injection kickers at high frequency. Required kicker recharging time driven by synchronisation of two machines to common frequency
[1] W. Bartmann, BEAM TRANSFER TO THE FCC-hh COLLIDER FROM A 3.3 TeV BOOSTER IN THE LHC TUNNEL, IPAC15, Richmond, VA, USA
[2] C. Bracco, Injection: Hadron Beams, CAS Beam Injection, Extraction and Transfer, 2017, Erice, Italy

## Slide 55: Layout
Introduction
Basic principle of injection
  Kicker and septum
Fast injection concept
  Reminder on normalized phase space
  Dipole error and filamentation
  Betatron error and filamentation
  Injection protection challenges at the LHC
  Injection protection challenges at the FCC-hh
Multi-turn injection concept
Extraction
Transfer
Injection

## Slide 56: Multi-turn injection concept
Principle
  Injected beam is injected in a small part of the available phase space
  The injected trajectory is moved relative to the closed orbit during the injection process
  Allows to accumulate intensity and `paint` the phase space with a beam smaller than the available ring acceptance, typically from a linac to a ring
Challenges
  Complex manipulation of the injected beam and ring closed orbit during the injection process
Applications
  At CERN PSB until LS2
  At GSI SIS18 heavy ions injection

## Slide 57: Multi-turn injection concept
In the case of the PSB (pre-LS2) the beam is injected in the horizontal plane and the ring fractional tune is close to 0.25

## Slide 58: Multi-turn injection concept
In the case of the PSB (pre-LS2) the beam is injected in the horizontal plane and the ring fractional tune is close to 0.25

## Slide 59: Multi-turn injection concept
In the case of the PSB (pre-LS2) the beam is injected in the horizontal plane and the ring fractional tune is close to 0.25

## Slide 60: Multi-turn injection concept [1]
Other example at the GSI SIS18, injection of heavy ions from the UNILAC
Conclusion
  Disadvantages inherent in using an injection septum:
    Width of several mm reduces aperture
    Beam losses from circulating beam hitting septum:
      Typically 30 – 40 % for the CERN PSB injection pre-LS2
    Limits number of injected turns to 10 - 20
  Allows to accumulate intensity into a ring, from a much smaller beam source, typically a linear accelerator
  Is complex to optimize, with few observables as individual beamlets cannot be measured
[1]S. Appel, O. Boine-Frankenheim, and F. Petrov, ‘Injection optimization in a heavy-ion synchrotron using genetic algorithms’, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, vol. 852, pp. 73–79, Apr. 2017, doi: 10.1016/j.nima.2016.11.069.

## Slide 61: Further reading and ressources
ABT group is on the 865 building, my office 865/1D28
CAS 2017 on Beam injection, extraction and transfer at https://indico.cern.ch/event/451905/
  Overlooked here, timing and synchronization by RF expert H. Damerau next week
  Detailed talk on resonant slow extraction by P. Bryant https://indico.cern.ch/event/451905/contributions/2159064/
  Exotic extraction methods that discuss all the possibilities overlooked here by B. Goddard https://indico.cern.ch/event/451905/contributions/2159103
This CAS lecture on Kickers and Septa by M. Barnes https://indico.cern.ch/event/1018359/contributions/4312229
CERN GIS machine portal https://gis.cern.ch/gisportal/Machine.htm

## Slide 62
Thank you