## Slide 1: Cooling of High-Intensity Beams
M. Steck, GSI Darmstadt
Intensity Limitations in Hadron Beams,
Hotel Rila, Borovets, Bulgaria
15 - 27 June 2025

## Slide 2
Observation of Cooling
Xe54+ beam at 400 MeV/u cooled with electron current 200 mA
measured with residual gas ionization beam profile monitor
longitudinal Schottky noise
vertical profile (vertical emittance)
horizontal profile
(horizontal emittance)
longitudinal momentum distribution
injection of new beam
cooling in six-dimensional phase space
time

## Slide 3
Beam Cooling
Beam cooling is synonymous for a reduction of beam temperature.
Temperature is equivalent to terms as phase space volume, emittance and momentum spread.
Beam Cooling processes are not following Liouville‘s Theorem:
` in a system where the particle motion is controlled by external conservative forces the phase space density is conserved ´
(This neglects interactions between beam particles.)
Beam cooling techniques are non-Liouvillean processes which violate the assumption of a conservative force.
e.g. interaction of the beam particles with other particles (electrons, photons, matter)

## Slide 4
Beam Cooling
Beam cooling increases the phase space density and can support an intensity increase of weak beams, particularly secondary beams (rare isotopes, antiprotons).
It is not a technique to achieve ultimate intensities, the cooled beam has smaller emittance and energy spread, which makes it more susceptible to instabilities and results in stronger Coulomb interaction, i.e. intrabeam scattering, space charge.
It can support techniques which require good beam quality for efficient manipulation of the beam and improve performance, an intensity increase can result due to improved efficiency of beam manipulations.

## Slide 5
Cooling Force
Generic (simplest case of a) cooling force:
non conservative, cannot be described by a Hamiltonian
For a 2D subspace distribution function
cooling (damping) rate
in a circular accelerator:
Transverse (emittance) cooling
Longitudinal (momentum spread) cooling
vx,y,s velocity in the rest frame of the beam

## Slide 6
Beam Temperature
Where does the beam temperature originate from?
The beam particles are generated in a ‘hot’ source
In a standard accelerator the beam temperature is not reduced (thermal motion is superimposed the average motion after acceleration)
but: many processes can heat up the beam
e.g. heating by mismatch, space charge, intrabeam scattering, internal targets, residual gas, external noise
at rest (source) at low energy at high energy

## Slide 7
Beam Temperature Definition
Longitudinal beam temperature
Transverse beam temperature
Particle beams can be anisotropic:
e.g. due to different cooling strength in 2D subspaces
Don‘t confuse: beam energy  beam temperature
(e.g. a beam of energy 100 GeV can have a temperature of 1 eV)
Distribution function
dependent on s

## Slide 8
Benefits of Beam Cooling
Improved beam quality
  Precision experiments
  Luminosity increase
Compensation of heating
  Experiments with internal target
  Colliding beams
Intensity increase by accumulation
  Weak beams from the source can be enhanced
  Secondary beams (antiprotons, rare isotopes)
Xe54+ 15 MeV/u
effect of intrabeam scattering and internal gas target
cooling off
cooling on
time
beam momentum

## Slide 9
Electron Cooling
momentum transfer by Coulomb collisions
cooling force results from energy loss in the co-moving gas of free electrons
superposition of a cold intense electron beam with the same velocity
ve║ = ec= ic = vi║
Ee=me/MiEi
e.g.: 220 keV electrons cool 400 MeV protons
or 400 MeV/u ions
electron temperature
kBT  0.1 eV
kBT║  0.1 - 1 meV
acceleration section
deceleration section

## Slide 10
Electron Cooling Systems
ESR Electron Cooler/GSI
1990
Medium Energy: 250 keV
First Electron Cooling System
NAP-M/BINP
1974
Electron Energy: 35 keV
proposed by G.I. Budker, Novosibirsk, in 1966

## Slide 11
Simple Derivation of
the Electron Cooling Force
Analogy: energy loss in matter (electrons in the shell)
faster ion
slower ion
in reference frame of the beam
Rutherford scattering:
Energy transfer:
Energy loss:
Minimum impact parameter:
from:
Coulomb logarithm LC=ln (bmax/bmin) 10 (typical value)
electron target
b
db

## Slide 12
Characteristics of the Electron Cooling Force
cooling force F
for small relative velocity:  vrel
for large relative velocity:  vrel-2
increases with charge:  Q2
|F|  vrel
|F|  1/vrel2
maximum of cooling force
at effective electron temperature

## Slide 13
Electron Cooling Time
cooling time
cooling rate (-1):
slow for hot hadron beams  -3
decreases with energy  -2 ( is conserved)
linear dependence on electron beam intensity ne and cooler length =Lec/C
favorable for highly charged ions Q2/A
independent of hadron beam intensity
cooling rate is constant and maximum at small relative velocity
F  vrel   = t = prel/F = constant
for large relative velocities
for small relative velocities
first estimate: (Budker 1967)

## Slide 14
protons 400 MeV (Q=1)
Xe54+ 350 MeV/u (Q=54)
Ie= 100 mA
Ie= 250 mA
Ie= 500 mA
Longitudinal Cooling
measurement time 20 s
measurement time 650 s
Ie= 250 mA

## Slide 15
Electron Beam Properties
electron beam temperature
is determined by the thermal cathode temperature kBTcat
transverse temperature kBT = kBTcat , can be reduced by transverse magnetic expansion with ( Bc/Bgun)
longitudinal temperature kBT║ = (kBTcat)2/4E0  kBT
lower limit :
typical values:
transverse kBT  100 meV (1100 K)
with magnetic expansion kBT  1 meV
longitudinal kBT║  0.1 - 1 meV

## Slide 16
single particle cyclotron motion
cyclotron frequency
cyclotron radius
electrons follow the magnetic field line adiabatically  transverse magnetic expansion results in a reduction of the transverse temperature
Electron Motion in
Longitudinal Magnetic Field
another important consequence: for interaction times which are long compared to the cyclotron period the ions do not sense the transverse electron temperature  magnetized cooling ( Teff  T║  T)
B
rc  10 m
 e-

## Slide 17
standard multiturn injection in SIS18 (GSI) Au65+ at 11.4 MeV/u
fast accumulation by repeated multiturn injection with electron cooling
fast transverse cooling
intensity increase by a factor of  10
in 5 seconds
limitations:
space charge tune shift, recombination (REC)
Accumulation of Low Energy Heavy Ions by Electron Cooling before Acceleration
horizontal vertical
profile
beam size
horizontal-longitudinal stacking supported by electron cooling In LEIR (CERN) Au54+ at 4.2 MeV/u
beam accumulation

## Slide 18
Atomic Physics Limitation of Electron Cooling
losses by recombination (REC)
loss rate
Continuum
bound states
EKIN
K
L
M
Radiative Electron Capture (REC)
change of the ion charge results in particle loss
 different orbit
emission of a photon
AQ+ + e-  A(Q-1)+ + h
-1 = -2 REC ne
Dielectronic Recombination (DR)
Aq+ + e-  [A(q-1)+]**  A(q-1)+ + h

## Slide 19
Recombination Coefficient of Incompletely Stripped Heavy Ions
SIS18, GSI measurement at the injection energy 11.4 MeV/u
LEAR result, J. Bosser et al. EPAC 98 increased recombination rate for Pb53+
recombination of incompletely stripped ions is hard to predict,
it determines the lifetime of the cooled ion beam and limits accumulation
LEAR, CERN lead ion accumulation for LHC
beam lifetime is inversely proportional to the recombination coefficient
theoretical value for REC

## Slide 20
Limits of Beam Accumulation
accumulation saturates when injection rate is balanced by loss rate
loss-1 = inj-1
various process result in finite beam lifetime beam
losses due to atomic interaction in vacuum (ionization, capture)
nuclear lifetime of rare isotopes (can range from microseconds to years)
interaction with electron beam (radiative electron capture)
equilibrium intensity Neq is achieved when
Ninj/Trep = Neq(1 - exp(-Trep/beam))/Trep
production/injection rate Ninj/Trep
loss rate Neq(1-exp(-Trep/beam))/Trep
beam accumulation is most beneficial for low intensity or secondary beams with sufficiently long lifetime
Trep=0.4 s
saturation
beam
beam lifetime
Trep=350 ms

## Slide 21
Slow Extraction by Charge Change
septum magnet installed in UHV
electron capture in the cooling system provides a cooled beam for ultraslow extraction at any energy at which beam can be stored and cooled
(depending on the ring acceptance)
small emittance
good control of extraction rate
extraction time minutes to hours

## Slide 22
Electron Cooled Beams in Equilibrium with Intrabeam Scattering (IBS)
p/p  N0.3
x,y  N0.5
different ions (Q,A)
different energies (, )
IBS: total phase space volume increases with ion beam intensity and ion charge

## Slide 23
Intensity Limit of Cooled Ion Beam
p/p  N1/3
x  N2/3
y  N1/3-2/3
≥ 
≥ 
longitudinal stability
transverse stability
space charge tune shift
electron cooling of U89+ at 75 MeV/u, including bunched beam
number of ions / ring circumference N/B
bunched
unbunched
with increasing intensity the cooled beam approaches the unstable regime

## Slide 24: Low Intensity, High Brilliance Beam
The phase space density below the transition point is dramatically increased
Intrabeam scattering must be absent for low ion beam intensity.
For higher intensity the cooling rate cannot be increased corresponding to the IBS heating rate.
for small particle number:
increase of phase space density by 4 orders of magnitude
beam temperature for C6+ at 4800 MeV is below 1 meV
momentum spread reduction for less than 1000 particles
(Schottky noise)

## Slide 25
Collective Effects in High Intensity Cooled Beams
Ar18+ at 400 MV/u cooled with 300 mA electron current
2107 cooled ions
width of the Schottky signal corresponds
to a momentum spread of p/p= 3  10-5
6108 cooled ions
double peak structure with signal suppression
peak distance increases with particle number N1/2
long tails of particle distribution
electron cooled beam in TSR
this beam is stable, no increased loss rate

## Slide 26
Electron cooling with electrostatic acceleration is limited in energy (5-10 MeV).
A bunched electron beam offers the extension of the electron cooling method to higher energy (linear rf accelerator to increase the electron energy).
ion bunch (some ten ns) or coasting ion beam
electron bunches (some ns)
continuous electron beam
continuous (or bunched) ion beam
new scheme
traditional
Low Energy RHIC e-Cooler (LEReC) project at BNL
Bunched Beam Electron Cooling
high intensity bunches (production, transport)
momentum spread and emittance of bunches
beam alignment
magnetized  non-magnetized (magnetic shielding)
synchronization of electron and ion bunches
super-conducting
rf gun
5 MeV, 250 kW beam dump
two counter-propagating
ion beams
two opposite cooling sections
issues:

## Slide 27
LEReC is the first electron cooler based on the RF acceleration of electron beam .
State of the art electron accelerator which uses photocathode high-current gun, high-power laser and several RF cavities.
Electron beam parameters suitable for cooling were successfully generated and transported to the cooling sections in RHIC.
First electron cooling of hadron beams using a bunched electron beam was demonstrated on April 5, 2019.
Both longitudinal and transverse cooling was achieved.
Cooling of ion bunches in two separate RHIC rings (Yellow and Blue) using single electron beam was demonstrated.
LEReC cooling sections
demonstration of cooling
A. Fedotov et al.
Low-Energy RHIC electron Cooler (LEReC) at BNL

## Slide 28
x
x'
Stochastic Cooling Fluctuations in Phase Space
compression of total phase space volume by reduction of locally empty phase space volume
x'
x
cooling
phase space is not homogeneously filled with particles  fluctuations of local particle density
2D phase space x-x‘

## Slide 29
First cooling method which was successfully used for beam preparation
Conditions:
Betatron motion phase advance (pick-up to kicker): (n + ½) 
Signal travel time = time of flight of particle (between pick-up and kicker)
Sampling of sub-ensemble of total beam
Principle of transverse cooling:
measurement of deviation from ideal orbit
is used for correction kick (feedback)
S. van der Meer, D. Möhl, L. Thorndahl et al. (1925 – 2011) (1936 - 2012)
pick-up
kicker
amplifier
deviation
kick
Stochastic Cooling

## Slide 30
For exponential damping ( ):
correction kick
(unlimited time resolution)
correction kick with bandwidth W
Nyquist  the time resolution for a system of bandwidth W is T = (2W)-1
Correction kick
correction kick
cooling rate
in time domain
Stochastic Cooling
-
-
time
position

## Slide 31
Stochastic Cooling
some refinements of cooling rate formula
noise: thermal or electronic noise adds to the beam signal
mixing: change of relative longitudinal position of particles due to momentum spread
cooling rate
M mixing factor
U noise to signal ratio
cooling heating
maximum of cooling rate
with wanted mixing
and unwanted mixing
(kicker to pick-up)
(pick-up to kicker)
further refinement (wanted  unwanted mixing):

## Slide 32
Mixing
pick-up (at s1)
pick-up
kicker
(at s2)
kicker
 half a turn from pick-up to kicker
 half a turn from kicker to pick-up
unwanted mixing (from pick-up to kicker)
wanted mixing (from kicker to pick-up)
 eff ~ 0
 k-pu  0, (T(p/p)rms)-1  1
pick-up
kicker
mixing is determined by the ion optical functions

## Slide 33
Requirements Stochastic Cooling
large bandwidth (typically one octave in the GHz range)
good transfer function in gain and phase
high sensitivity (high impedance) of pick-ups and kickers
low electronic noise (cold pick-ups, low noise amplifiers)
large, but adjustable gain
special ion optical properties of the ring betatron phase advance between transverse pick-up and kicker small momentum slip factor (large wanted and little unwanted mixing) for Palmer cooling: large dispersion value at pick-up

## Slide 34
Longitudinal Stochastic Cooling
transmission line
short circuit at all harmonics of the revolution frequency
notches at harmonics
of the revolution frequency
with 180º phase jump
1) Palmer cooling
pick-up in dispersive section detects horizontal position
 acceleration/deceleration kick corrects momentum deviation
2) Notch filter cooling
filter creates notches at the harmonics of the nominal revolution frequency
 particles are forced to circulate at the nominal frequency
3) ToF cooling
simplified scheme without notches allows efficient pre-cooling

## Slide 35
Comparison of Longitudinal Cooling Methods
Palmer cooling
Time-of-Flight cooling
Notch filter cooling
Ar18+ 400 MeV/u longitudinal momentum distribution versus time
large momentum capture range
fast cooling
good final momentum spread
drawback: horizontal heating needs to be compensated
by horizontal cooling
large momentum capture range
slower cooling
moderate final momentum spread
simple set-up
no special lattice requirement
reduced momentum capture range
good cooling rate
smallest final momentum spread
most elaborate rf hardware
issue of notch filter stability
measured at the ESR heavy ion storage ring
Schottky signal observed at 245 MHz (h=124)

## Slide 36
Basic Studies of Stochastic Cooling
summary of initial stochastic cooling studies at CERN
with (anti-)protons
noise limit regime (depending on gain)
mixing limit regime
  N
particle number
cooling time
(normalized to 1 GHz bandwidth)
 cooling rate decreases for high intensity beams

## Slide 37
Antiproton Accumulation by Stochastic Cooling
kicker array
cryogenic microwave amplifier
microwave electronics
power amplifiers (TWTs)
momentum distribution of accumulated antiproton beam
accumulation of 8 GeV antiprotons at accumulator ring, FNAL, shut down 09/2011
a similar facility AC/AA at CERN was operated until 11/1996
with stochastic cooling:
accumulation of up to 6×1011 antiprotons
about 60 mA

## Slide 38
Nickel target
Proton beam 71012 protons every 2 sec
120 GeV
Debuncher (stochastic cooling)
Accumulator (stochastic cooling)
8 GeV
8 GeV
1 TeV
Tevatron
150 GeV
Main injector
8 GeV
Recycler (stochastic and electron cooling)
61011
= 2108
41012
= 4109
1108
= 1
1108
= 300
until 2005
Electron cooling in the Recycler Ring resulted in faster cooling and a factor of 3 more accumulated antiprotons
Fermilab’s Antiproton Production Chain

## Slide 39
High Energy Electron Cooling
electron cooling of 8 GeV antiprotons
cooling with 0.2 A, 4.4 MeV electron beam
FNAL Recycler electron cooling system
electron cooling time of order ten minutes
stochastic cooling time ≥ N/2W
20 m long
solenoid section
Pelletron
high voltage tank

## Slide 40
Stochastic Cooling for Bunched Heavy Ions
longitudinal pickup
3 tanks with longitudinal (narrow band) kicker units
longitudinal kicker open for injection and ramping (left), closed during cooling (right)
horizontal and vertical pickups
70 GHz carrier with 16 GHz local oscillator
RHIC
ion collider

## Slide 41: RHIC Luminosity Increase
For Uranium-on-Uranium collisions the cooling increased the integrated luminosity per store by a factor of 5
The transverse emittances were reduced by x 4 with a cooling time of ½ hour
luminosity with/without stochastic cooling
beam emittance during store
M. Brennan et al.
luminosity of ions colliding at 100 GeV/u is limited by intrabeam scattering in the intense beam of highly charged ions

## Slide 42
Increase of Stochastic Cooling Rate
A more powerful cooling or cooling of large particle number requires an increase of the bandwidth W of the cooling system -1  2W/N
Electronic cooling systems were developed for 8 and 16 GHz bandwidth, but larger bandwidth systems are not available
Alternative approaches are proposed to provide faster cooling at relativistic energies

## Slide 43
Coherent Electron Cooling
Modulator
Kicker
Dispersion section
( for hadrons)
Electrons
Hadrons
l2
l1
High gain FEL (for electrons)
Eh
E < Eh
E > Eh
Eh
E < Eh
E > Eh

The Coherent Electron Cooling system has three major subsystems
    modulator: the ions imprint a “density bump” on the electron distribution
    amplifier: FEL interaction amplifies a density bump by orders of magnitude
    kicker: the amplified & phase-shifted electron charge distribution is used to correct the velocity offset of the ions
A combination of electron and stochastic cooling concepts
proposed for fast cooling at highest energies energy range several 10 – 100 GeV
electron-ion collider
BNL-EIC

## Slide 44
Optical Stochastic Cooling Concept
first experimental demonstration with 100 MeV electron beam in IOTA (FNAL) Nature 608 287-292 (2022)
option for cooling hadron beams of highest energy
benefit:
high bandwidth of optical cooling system

## Slide 45
energy 400 (-550) MeV/u bandwidth 0.8 GHz (range 0.9-1.7 GHz)
p/p = 0.35 %  p/p = 0.01 % e = 10  10-6 m  e = 2  10-6 m
electrodes installed in the
ultrahigh vacuum inside magnets
combination of signals from electrodes
power amplifiers for generation of correction kicks
fast pre-cooling of hot rare isotopes
Stochastic Cooling of Rare Isotopes at GSI

## Slide 46
Fast stochastic pre-cooling
One trace every 120 ms
5.52 s in total
Subsequent electron cooling
Inj.
3 s
5 s
Primary Uranium beam
heated in thick target
stochastic pre-cooling + final electron cooling
immediately after injection
Combination of Stochastic and Electron Cooling
Stochastic pre-cooling reduces the total cooling time to a few seconds,
electron cooling only takes 10 - 60 s

## Slide 47
62 injections: 2×106 205Tl81+ ions
accumulation over 40 minutes
this accumulation scheme requires two cooling systems and a large momentum acceptance of the ring, one cooling system cools the injected beam and the second cooling system the stacked beam on a different orbit
injection orbit stochastic cooling
stack orbit electron cooling
p/p  1.6%
a powerful combination for the accumulation of (long-lived) rare isotope beams
Beam Accumulation of a Rare Isotope Beam
longitudinal stacking for beams transferred between ring accelerators

## Slide 48: Equilibrium Beam Parameters of the Cooled Beam in the ESR
Electron cooling results in
smaller momentum spread and smaller emittance.
The equilibrium is a balance between the cooling rate and the heating rate by intrabeam scattering.
calculated IBS-heating/cooling rate [s-1]
longit. transv.
stochastic cooling 0.9 - 2.2 0.5 - 1.3
el. cool. [25 mA] 2.0 - 6.0 1.4 - 3.3
el. cool. [250 mA] 18 - 58 7 - 10
limited by Intrabeam Scattering
electron cooling is more powerful in producing cold beams,
it provides higher (more than an order of magnitude) cooling rate for cold ion beams

## Slide 49
Cooling Methods of Hadron Beams
Stochastic Cooling Electron Cooling
Useful for: low intensity beams low energy
all intensities
hot (secondary) beams warm beams (pre-cooled)
high charge high charge
full 3 D control bunched beams
Limitations: high intensity beams space charge effects
/problems beam quality limited recombination losses
bunched beams (ions) high energy