## Slide 1
`
Instrumentation and Cryogenic Electrical Circuit
Juan Gansauskas Galvez
Magnetic and Electromagnetic Systems Group
On behalf of the Technology Unit
CNPEM’s Superconducting Wavelength Shifter (SWLS)
Technical Design Review
4–5th November 2024

## Slide 2
Overview of the SWLS circuit
Cryogenic Electrical Circuit
  Current Leads
  Links and Splices
Cryostat Instrumentation
Measurement, Control and Automation
Outline

## Slide 3
Overview of the SWLS circuit
Operating current
Operating current: 228 A
  Circuit rated for 300 A and 1 kV
Two power supplies
  Power Supply – Today 16:20 CET
Main and side coils current controlled separately
  Electromagnetic Design – Tomorrow 14:00 CET
External energy dissipation
  Quench Protection – Today 17:00 CET

## Slide 4
Cryogenic Electrical Circuit
Current Leads
Positive, negative and balance
Balance lead may experience full current
Ballast required for external energy extraction
Links
NbTi wire connecting coils and to the leads
Coils wound with excess wire to minimize splices
Splices
Soft-soldering links into a copper stabilizer
Includes one three-wired splice
Positive
Negative
Balance
NbTi Link
Splice
Ballast
Project premisse:
Complete redundancy in the insulation of the circuit wires
Bare wire
Teflon heat-shrink tubing
Enamel insulation
Fiberglass sleeve

## Slide 5
Current Leads – Overview
Hybrid conduction-cooled design
Resistive part: Brass alloy
Low (L/A)opt
Qc,min = 11.31 W @ 228 A (per lead)
6 W @ 0 A (per lead)
HTS part: Custom model from HTS-110
300 A @ 70 K
< 50 mW @ 4.2 K – 70 K (per lead)
Stainless steel ballast
Assembly:
SRDK-415D flange, 45° necks
One assembly w/ positive and balance leads
One assembly w/ negative lead
Positive and Balance leads
Negative lead

## Slide 6
Vacuum power feedthrough
Brass resistive part
Copper flexible termal-electric link
60 K Thermalization
Current Leads – Overview
Copper terminal
SS ballast
Bi-2223 tapes
4 K Thermalization

## Slide 7
Current Leads – Mounting
Indium from the current tab interfaces gets easily in the way when bolting.
It also seems to creep over time.
Sapphire washer that was short-circuiting through it
Indium
“Melted” bolt discovered after a test run
SS M4 bolt
FRP washer
Invar washer
Nylon bush
Retaining ring
Sapphire washer
Former mounting method: “insulated bolt”
Is Indium foil recommended, even though the washers are susceptible to cracking?
We suspect that the indium may not have creeped, but rather melted

## Slide 8
Current Leads – Mounting
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
The gap allows force transfer from the clip to the sapphire washers
Teflon alignment pin
SS clip
FRP spacer
HTS lead terminal
Current tab
Sapphire washer
NbTi link

## Slide 9
Current Leads – Simulation results
Simulated:
4.94 K @ 228 A
Experimental:
4.72 K @ 228 A
Vertical cryostat HTS lead
SWLS HTS lead
Simulated:
4.25 K @ 228 A
HS @ 3.5 K
HS @ 3.5 K
HS @ 50 K
Air-side near RT
HTS hot end @ 52.3 K
Resistive part
HTS part
HS @ 50 K
11.2 W

## Slide 10
Current Leads – Vertical Cryostat
Vacuum power feedthrough
Brass resistive part
Copper flexible termal-electric link
60 K Thermalization
HTS part
4 K Thermalization
Voltage Taps tab

## Slide 11
Links and Splices – NbTi link
SnPb
Current tab – NbTi link interface
Vertical Cryostat concept
Reliable soldering procedure developed and validated experimentally
The Formvar insulation burns away during soldering

## Slide 12
I
I
Links and Splices – Splices
The Formvar insulation burns away during soldering
“Shake-hands” splice between NbTi links
Tinned Cu wire
Copper “crucible”
SnPb
Reliable soldering procedure developed and validated experimentally
“Praying hands” concept
“Praying hands” concept
1
2
3
4

## Slide 13
Links and Splices – Splice Box
“Splice box” concept
Nylon Clip
FRP base
Threaded hole for sensor mounting
The gap allows force transfer from the clip to the copper crucible
Iside
Imain
Ibalance
The NbTi link could pass straight through this crucible, or we can make a splice

## Slide 14
Links and Splices – Test results
Splice box test setup in the vertical cryostat
Splice box test validations
Thermal performance
  Crucible @ 3.7 K w/ HS @ 3.5 K
  Little change between 0 A and 300 A
Resistance measurements
  Rsplice < 10 nΩ
  Rtab ≈ 150 nΩ
Mechanical performance
Quench behavior
Typical current tab resistance measurement
Typical splice
resistance measurement

## Slide 15
Cryostat Instrumentation – Overview
The SWLS instrumentation system performs many different functions, and comprises different instruments...
System operability
System health and safety
Specific functionalities
...which interfaces with the cryostat across 16 feedthrougs...
3 power feedthroughs
12 instrumentation feedthroughs
4 vacuum feedthroughs
...with 180 instrumentation wires...
Up to 32 4-wire temperature sensors
  17 for constant monitoring
  8 for warm-up control
  7 for tests and wiggle room
38 Voltage Taps
7 Heater circuits
...that leads to the measurement, control and automation systems
They will be briefly addressed later
Sensor wire: PhBr 36 AWG
Sensor extension: Cu 34 AWG
Voltage Taps: Cu 34 AWG, 2.6 kV
Heater leads: Cu 30 AWG
Sensor types: Diode and RTD
Magnetic field
Radiation incidence
Required accuracy
In this presentation, the instrumentation from “the cryostat and within” will be the main focus
Overall considerations:
Avoid ground faults and short circuits
Prioritize ease of installation and rugdeness

## Slide 16
Instrumentation – Suspended Structure
Feedthroughs: Central neck
Dedicated feedthroughs for sensors, heaters and VTs
116 instrumentation wires
Up to 20 temperature sensors
  10 for constant monitoring
  6 for warm-up control
  4 for tests and wiggle room
26 Voltage Taps
5 Heater circuits
Before integration:
Splice box assembly
Complete instrumentation installation
Wires’ 4 K thermalization (when applicable)
Wires bundling
After integration:
Wires’ 20 K and 60 K thermalization in the central neck
Wires routing through central neck
Feedthrough connection

## Slide 17
Instrumentation – Suspended Structure
Sensors
Voltage Taps
(redundant pair)
Splices
Heaters
Cartridge heaters
The redundant Voltage Taps are independently routed, thermalized and fedthrough
Cold Mass

## Slide 18
Instrumentation – Suspended Structure
Supports and Beam Chamber
Sensors
Heaters
“Surface heater” (TBD)

## Slide 19
Instrumentation – CL Assemblies
Sensors
Voltage Taps
(redundant pair)
Feedthroughs: Assembly flanges
Dedicated feedthroughs for sensors and VTs
32 instrumentation wires
Up to 6 temperature sensors
  4 for constant monitoring
  2 for tests and wiggle room
8 Voltage Taps
20 on the negative side
Before integration:
Complete instrumentation installation
Wires’ 4 K (when applicable) and 60 K thermalization
Wires bundling and routing
Feedthrough connection
After integration:
HTS cold end w/ NbTi link mounting

## Slide 20
Instrumentation – Thermal shields
20 K shield
60 K shield
Sensors
Heaters
Feedthroughs: Cryostat vacuum chamber
One for sensors, one for heaters
Before integration:
Shield body instrumentation installation
Wires bundling
After integration:
Shield lid instrumentation installation
Wires’ 20 K (when applicable) and 60 K thermalization
Wires routing
Feedthrough connection
Suspended structure thermalization and routing
10 instrumentation wires
2 sensors
1 Heater circuit

## Slide 21
Instrumentation – Vacuum
Pirani sensor
Cold cathode sensor
Mechanical + turbomolecular pumps
Ion pump

## Slide 22
Instrumentation – Thermalization
Courtesy of Lake Shore Cryotronics
Heat-sink bobbin
Instrumentation wires
Stycast
Heat-sink bobbin concept
Heat-sinking guaranteed
Compact design
Easy to install/uninstall
Great electrical insulation w/ fiberglass
Some interchangeability is lost
May require aditional solders in the heat-sinked wires
20 K Shield
60 K Shield
Suspended structure instrumentation wire thermalization example

## Slide 23
Measurement, Control and Automation
Interlock signals are relay contacts, active-low logic
Data acquisition and device configuration over Ethernet
Fast input for quench detection trigger timestamping
Automation architecture

## Slide 24
Measurement, Control and Automation
Warm-up control
PID robust against parameters variation
Efficient warming-up (avoid on/off)
Avoid large temperature gradients
  Fast and slow response sensors
Many safety checks to avoid burn-out
  Communication status
  Temperature variation
  Vacuum level
  ...
Setpoint;
Max temp. gradient;
PID gains (kp, ki, kd);
Open/closed loop;
Heater (de)activation
PLC
PID Controller
Heating System
1
Temperature monitor
+
-
r(k)
y(k)
u(k)

## Slide 25
Measurement, Control and Automation
Lakeshore 240-8P had better cost effectiveness
MKS 937B is the standard option in Sirius
Many MEAN WELL power supplies in stock
CompactLogix is the standard option in Sirius machine interlock
Type | Model | Qty | Manufacturer
Temperature | 240-8P | 4 | Lakeshore
Vacuum pressure | 937B | 1 | MKS Instruments
Heater power supply | SPV-300-48 | 7 | MEAN WELL
Quench detector | QDS-WLS | 1 | CNPEM
Magnet power supply | DRS-UDC | 1 | CNPEM
Interlock controller | CompactLogix 5380 | 1 | Rockwell Automation
Quench Protection – Today 17:00 CET
Power Supply – Today 16:20 CET
Instrumentation and Control electronics

## Slide 26
cnpem.br
Thank you!