## Slide 1
A Reconfigurable FPGA-based ML Library for Kernel Methods
  —
    Yousef Alnaser1, 2 , Jan Langer1, Anna Zuchna2
    1 Fraunhofer-Institut für Elektronische Nanosysteme ENAS, Technologie-campus 3, 09126 Chemnitz
    2 Technische Universität Chemnitz, Str. der Nationen 62, 09111 Chemnitz
Logobereich

## Slide 2: Introduction
Kernel Methods Intuition
    Linear Regression
  Finds the best-fit line with least prediction error.
    Ridge Regression
  Introduce a bias to the estimator to resolve overfitting.
    Kernel Regression
  Better fits data than linear estimators. But may lead to overfitting.
    Kernel Ridge Regression
  Fits data better, and resolves overfitting by introducing a bias to the estimators
Kernel Ridge Regression (KRR) Example
Very useful for non-linear and complex data

## Slide 3: Introduction
Kernel Matrix Complexity
Radial Basis Kernel (RBF)
Scale poorly for large datasets

## Slide 4: ML FPGA Library for Kernel Methods
Hardware acceleration of kernel ML
Why this library?
    Main Advantages
      Up to 30× faster than Python CPU libraries
      Partial reconfiguration
        Support different kernels
        Reduce Library Size
      Modular design: easy to extend with new solvers and kernels
      Works with big data, no FPGA knowledge needed
Accelerated kernel learning from Python — without hardware complexity.
Kria SOM
Alveo V80
VCK5000 Versal
FPGA Library
KRR
SVM
GP
PCA
Modular, hardware-accelerated blocks for common kernel methods
Plug-and-play Python interface via PYNQ
Runs on various edge and accelerator cards
from fpgakernel import SVM
model = SVM(‘rbf’)
model.fit(X, y)

## Slide 5: Use Case
Kernel Ridge Regression
Profiling
    Complexities:
      Lines 1, 2, & 7 have Quadratic Complexity
        Runs on FPGA fabric (HW)
      The remaining lines have Linear Complexity
        Runs on ARM cores (SW)
Formulation
Only operations with quadratic complexity are accelerated

## Slide 6: Introduction
HW/SW Partitioning
On-the-fly calculation  High memory BW requirements
Matrix Tiling/Partitioning  Reduced BW requirements
    Operations of Interest:
      Kernel-Matrix (KM) Construction
      Matrix-Vector (MV) Multiplication

## Slide 7: Accelerator Implementation
Design Overview
Accelerator hardware
      Kernel Matrix (KM) Construction
      Reconfigurable Kernel Module
      Matrix-Vector (MV) Multiplication
      Implemented in HLS in 300 LoC
      Compile-time configurable
      Run-time compatible with any arbitrary dataset
© Markus Jürgens

## Slide 8: Accelerator Implementation
Common Operations in Supported Kernels
Kernel Function | Equation
RBF | 
Laplacian | 
Linear | 
Polynomial | 
Sigmoid | 
Kernel Function | Equation
RBF | 
Laplacian | 
Linear | 
Polynomial | 
Sigmoid | 
Table 1 – Supported Kernels
Fig. 4 – Kernel Implementation

## Slide 9: Accelerator Implementation
Common Operations in Supported Kernels
Kernel Function | Equation
RBF | 
Laplacian | 
Linear | 
Polynomial | 
Sigmoid | 
Kernel Function | Equation
RBF | 
Laplacian | 
Linear | 
Polynomial | 
Sigmoid | 
Table 1 – Supported Kernels
Fig. 4 – Kernel Implementation
Common operations are combined in a single implementation

## Slide 10: Accelerator Implementation
Kernels Calculations
Fig. 4 – Kernel Implementation
Fig. 5 – Reconfigurable modules for supported kernels
Common operations  kernel specific operations
…

## Slide 11: Accelerator Implementation
Matrix Partitioning
Macro-tiles
    Kernel Matrix
      : macro-tile of size
         only the upper triangle is computed and reused
      Input Matrix
      : partitioned into tiles each of size
      MV multiplication
      Once one is calculated, both equation are computed:
© Markus Jürgens
‘
Macro tiles for storage and BW

## Slide 12: Accelerator Implementation
Matrix Partitioning
Micro-tiles
      Each macro-tile computations is divided into micro-tiles of size
      All computations in a micro-tile are executed fully in parallel
© Markus Jürgens
Micro tiles for parallelism

## Slide 13: Use Case 2
Posterior mean:
Variance:
Gaussian Process
Profiling
    Complexities:
      Quadratic Complexity
        Runs on FPGA fabric (HW)
      Remaining operations
        Runs on ARM cores (SW)
    Approach:
      Same as before
      But is not square, and not triangular
Formulation
Same approach as KRR

## Slide 14: Results
Performance Evaluation
Comparison
      Python Cholesky (cubic complexity – not shown)
        From scikit-learn
        requires large memory storage
      Python CG – 30x slower for big data
        Precomputes the kernel matrix
        scikit-learn, SciPy and NumPy
        requires large memory storage
      Python Naïve - 80x slower
        Matrix partitioning to improve caching
        scikit-learn and NumPy
30x faster
Kria SOM

## Slide 15: Results
Utilization
Reduced library size. Tradeoff: increased resources

## Slide 16: Conclusion
Challenges
Partial Reconfiguration
      Rigid Resource Allocation
        Must accommodate the largest RM
      Manual Floorplanning
        Must manually assign PR regions
      Toolchain Limitations
        PR in Vivado is not well-documented and buggy
HLS
      Single-cycle accumulation of floating point
        Must be manually handled.
      Loop dependencies
        Predicts incorrect dependencies
Data Movement
      Manual Data handling
      Xilinx DMA LogiCore
        Requires large amount of storage, for big data

## Slide 17: Conclusion
Summary
Library
full matrix
ML Algorithms
KRR
GP
KM-MV
upper triangle
SVM
PCA
…
upper triangle
Impl. #1
Impl. #2
Impl. #3
What’s next?!
AI Engines
More Kernels

## Slide 18
Thank you for your attention
—
Logobereich
    Contact
    Yousef Alnaser
    yousef.alnaser@enas.fraunhofer.de