## Slide 2: HDLRegression – A reliable and efficient tool for FPGA regression testing
FDF 2025

## Slide 3: Inventas
Norway’s largest independent design center and product development company
Established in 1997
170 designers and engineers
2016 - Launched UVVM
2021 - Established UVVM Steering Group
2022 - Launched HDLRegression
Provider of UVVM methodology and IP
UVVM & HDLRegression webinars, training and presentations

## Slide 4: Topics
Motivation
HDLRegression
Practical Example

## Slide 5: Verification challenges
87 % of projects had at least one non‑trivial bug escape into production.
≈ 67 % missed their original schedule.
Verification can consume up to 50% of total project effort.
Debugging is the single largest time sink for FPGA verification engineers.
*2024 Wilson Research Group FPGA functional verification trends

## Slide 6: Why do these problems happen?
Late discovery  many teams still only do a quick test before going to the lab; bugs appear late and cost more.
Design complexity  SoC FPGAs, several clock domains, and embedded CPUs.
Ad-hoc scripts  manually maintained compile orders and test lists get outdated fast.
Unpredictable debug  one bad failing test can take days to fix.
Change ripple  a fix in one block breaks logic that previously worked.

## Slide 7: What is regression testing?
Re-running the same functional and non-functional tests after each change.
Confirms that behaviour we already validated still works.
When something that passed yesterday fails today, that’s a regression.
Must be fully automated and repeatable.
Usual split: quick sanity pack and full suite overnight.
Code
Test
Pass
Fail
Commit

## Slide 8: Benefits of regression testing
Early fault detection – re-run tests after every code or configuration change.
Foundation for CI pipelines – CI tools rely on healthy regression suite.
Lower cost of defects – issues fixed at commit-time are orders of magnitude cheaper than those found in the lab – or in the field.
Confidence to refactor and innovate – clean up code or add features without silently breaking existing functionality.

## Slide 9: Continuous regression – what it is & why it helps
Run tests each time we push code - we catch errors right away.
Pipeline runs only tests impacted by the change.
Small, quick set on every push; full set at night or before milestone.
Keep logs from every run – easy to see when a bug appeared.
Favours small and frequent commits – gives early feedback, easier to review, and easier to revert.

## Slide 10: Topics
Motivation
HDLRegression
Practical Example

## Slide 11: What is HDLRegression?
An open-source regression runner for VHDL/Verilog TB – written in Python 3.
Ultra-easy start-up – only a pragma comment in the TB; no refactor.
Framework independent – works with UVVM, OSVVM, Vunit, or in-house code.
Auto-detects ModelSim, Questa, Riviera-PRO, GHDL, NVC, and drives them for you.
Scales from quick unit tests to large, multi-library projects.
Goal: simplicity and efficiency  focus on writing good tests.

## Slide 12: One-line testbench change
Add one pragma comment at the top of the TB entity.
No other edits, naming rules, or file-structure constraints.
HDLRegression auto-discovers TB entities, architectures and built-in sequencer tests.
-- hdlregression:tb entity tc_tb is generic( GC_TESTCASE : string := "UVVM" ); end entity;

## Slide 13: Test Case
A sequence of actions controlled by the testbench sequencer.
Can test one or multiple functions/requirements.
Often test related functionality or a logical sequence of events.
--HDLRegression:TB entity tc_tb is generic ( GC_TESTCASE : string := "UVVM_TB"; GC_GENERIC_1 : natural := 1; GC_GENERIC_2 : natural := 2; GC_PATH : string := "" ); end tc_tb; architecture tb_arch of tc_tb is begin p_seq : process begin if GC_TESTCASE = "tc_1" then ... elsif GC_TESTCASE = "tc_2" then ... else ... end if;
report_alert_counters(FINAL); std.env.stop; wait;
end process; end architecture tb_arch;

## Slide 14: Simple Python script
6-12 lines of plain Python.
Import HDLRegression, list files & libraries, and call start().
Same script runs RTL and netlist simulations – just add the netlist files.
Use the same script to run locally and in CI pipelines.
Full Python language available.
from hdlregression import HDLRegression hr = HDLRegression()
hr.add_files("../src/*.vhd", "design_lib") hr.add_files("../tb/*.vhd", "test_lib")
hr.start()

## Slide 15: Test Group
A collection of test cases
Test cases in a test group verify associated functionality or modules.
Test case 1
Test case 2
Test case 3
Test case 4
Test case 5
Test case 6
Test Group 1
Test Group 2

## Slide 16: Command Line Interface
sim % python ../script/sim.py -h usage: test.py [-h] [-v] [-d] [-g] [-fr] [-c] [-tc TESTCASE] [-tg TESTGROUP] [-ltc] [-etj EXPORTTESTCASEJSON] [-ltg] [-lco] [-fc] [-sof] [-s SIMULATOR] [-t [THREADING]] [-ns] [--waveFormat WAVEFORMAT] [--showWarnError] [--noColor] [--wlf] HDLRegression CLI options options: -h, --help show this help message and exit -v, --verbose enable full verbosity -d, --debug enable debug mode -g, --gui enable simulator GUI mode -fr, --fullRegression run full regression -c, --clean clean before regression run -tc TESTCASE, --testCase TESTCASE run selected testbench[.architecture[.testcase]] -tg TESTGROUP, --testGroup TESTGROUP run selected testgroup(s) -ltc, --listTestcase list testcases -etj EXPORTTESTCASEJSON, --exportTestcaseJson EXPORTTESTCASEJSON export testcases to JSON file with the given path. Example: --exportTestcaseJson testcases.json -ltg, --listTestgroup list testgroups -lco, --listCompileOrder list compile order -fc, --forceCompile force recompile -sof, --stopOnFailure stop simulations on testcase fail -s SIMULATOR, --simulator SIMULATOR select simulator Modelsim/GHDL/NVC/Riviera_Pro/Vivado -t [THREADING], --threading [THREADING] run tasks in parallel -ns, --no_sim no simulation, only compilation --waveFormat WAVEFORMAT wave file format [VCD (default) or FST] --showWarnError Show error and warning messages during simulations. --noColor Disable terminal output colors. --wlf Dumps wave file in WLF format (Questa/Modelsim).

## Slide 17: Topics
Motivation
HDLRegression
Practical Example

## Slide 18
The DUT has two processes:
  A write process (p_write) that updates the memory content on the rising clock edge when cs (chip select) and wena (write enable) are active.
  A read process (p_read) that provides data (rdata) when cs and rena (read enable) are active.
entity mem_block is port ( clk : in std_logic; rst : in std_logic; cs : in std_logic; wena : in std_logic; rena : in std_logic; addr : in unsigned(2 downto 0); wdata : in std_logic_vector(31 downto 0); rdata : out std_logic_vector(31 downto 0); ready : out std_logic ); end entity;
...
p_write : process(all) is begin if rst = '1' then mem <= (others => (others => '0')); elsif rising_edge(clk) then if cs = '1' and wena = '1' then mem(to_integer(unsigned(addr))) <= wdata; end if; end if; end process p_write; p_read : process(all) is begin if rst = '1' then rdata <= (others => '0'); else if cs = '1' and rena = '1' then rdata <= mem(to_integer(unsigned(addr))); end if; end if; end process p_read;
Uses a simple bus interface (SBI) approach, where the module is always “ready”, i.e. no wait cycles are needed for read or write operations.
A simple memory block that allows writing data to and reading data from specific addresses.

## Slide 19
library uvvm_util; context uvvm_util.uvvm_util_context; library uvvm_vvc_framework; context uvvm_vvc_framework.vvc_framework_context; library bitvis_vip_sbi; context bitvis_vip_sbi.vvc_context; library bitvis_vip_clock_generator; context bitvis_vip_clock_generator.vvc_context; -- hdlregression:tb entity tc_tb is generic( GC_TESTCASE : string := "UVVM" ); end entity;
...
log(ID_LOG_HDR, "TC: " & GC_TESTCASE, C_SCOPE); if GC_TESTCASE = "random_write_and_read" then for idx in 1 to 5 loop v_wdata := random(32); v_addr := unsigned(random(3)); sbi_write(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_wdata, "Write to mem", C_SCOPE); sbi_check(SBI_VVCT, C_SBI_VVC_IDX, v_addr, not(v_wdata), "Check data in mem", scope => C_SCOPE); end loop;
elsif GC_TESTCASE = "tc_read_empty" then for idx in 1 to 15 loop v_addr := to_unsigned(idx, v_addr'length); v_exp_data := (others => '0'); sbi_check(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_exp_data, "Check data in mem", scope => C_SCOPE); end loop; else alert(TB_ERROR, "Unknown TC: " & GC_TESTCASE); end if; await_uvvm_completion(1 ms);
Sequencer test cases. Each test is run isolated.
Testbench use UVVM for verification:
Utility Library
VVC Framework
SBI VVC
Clock Generator VVC
Marked for HDLRegression as testbench

## Slide 20: Manual simulation flow
nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/types_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/adaptations_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/string_methods_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/protected_types_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/license_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/global_signals_and_shared_variables_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/hierarchy_linked_list_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/alert_hierarchy_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/methods_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/generic_queue_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/bfm_common_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/data_queue_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/rand_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/data_stack_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/data_fifo_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/func_cov_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_util:/proj/sim/hdlregression/library/uvvm_util --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_util/src/uvvm_util_context.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_data_queue_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_protected_types_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_generic_queue_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_data_fifo_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_data_stack_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_vvc_framework_support_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_uvvm_engine.vhd nvc -L/proj/sim/hdlregression/library --work=uvvm_vvc_framework:/proj/sim/hdlregression/library/uvvm_vvc_framework --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src/ti_vvc_framework_context.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_scoreboard:/proj/sim/hdlregression/library/bitvis_vip_scoreboard --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_scoreboard/src/generic_sb_support_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_scoreboard:/proj/sim/hdlregression/library/bitvis_vip_scoreboard --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_scoreboard/src/generic_sb_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_scoreboard:/proj/sim/hdlregression/library/bitvis_vip_scoreboard --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_scoreboard/src/predefined_sb.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/sbi_bfm_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/transaction_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/vvc_sb_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/vvc_cmd_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_target_support_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_queue_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/vvc_methods_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_vvc_framework_common_methods_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/vvc_context.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_vvc_entity_support_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_sbi:/proj/sim/hdlregression/library/bitvis_vip_sbi --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_sbi/src/sbi_vvc.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_clock_generator/src/vvc_cmd_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_target_support_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_queue_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_clock_generator/src/vvc_methods_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_vvc_framework_common_methods_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_clock_generator/src/vvc_context.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/uvvm_vvc_framework/src_target_dependent/td_vvc_entity_support_pkg.vhd nvc -L/proj/sim/hdlregression/library --work=bitvis_vip_clock_generator:/proj/sim/hdlregression/library/bitvis_vip_clock_generator --std=08 --stderr=error --messages=compact -M64m -H64m -a /UVVM/bitvis_vip_clock_generator/src/clock_generator_vvc.vhd nvc -L/proj/sim/hdlregression/library --work=demo_lib:/proj/sim/hdlregression/library/demo_lib --std=08 --stderr=error --messages=compact -M64m -H64m -a /proj/src/mem_block.vhd nvc -L/proj/sim/hdlregression/library --work=demo_lib:/proj/sim/hdlregression/library/demo_lib --std=08 --stderr=error --messages=compact -M64m -H64m -a /proj/tb/tc_tb.vhd nvc -L/proj/sim/hdlregression/library --work=demo_lib:/proj/sim/hdlregression/library/demo_lib --std=08 --stderr=error --messages=compact -M64m -H64m -e --no-save --jit tc_tb-tb -gGC_TESTCASE=random_write_and_read -r nvc -L/proj/sim/hdlregression/library --work=demo_lib:/proj/sim/hdlregression/library/demo_lib --std=08 --stderr=error --messages=compact -M64m -H64m -e --no-save --jit tc_tb-tb -gGC_TESTCASE=tc_read_empty -r

## Slide 21
Create a Python run script and import HDLRegression
from hdlregression import HDLRegression hr = HDLRegression()
hr.add_files("../UVVM/uvvm_util/src/*.vhd", "uvvm_util")
hr.add_files("../UVVM/uvvm_vvc_framework/src/*.vhd", "uvvm_vvc_framework")
hr.add_files("../UVVM/bitvis_vip_sbi/src/*.vhd", "bitvis_vip_sbi") hr.add_files("../UVVM/uvvm_vvc_framework/src_target_dependent/*.vhd", "bitvis_vip_sbi")
hr.add_files("../UVVM/bitvis_vip_scoreboard/src/*.vhd", "bitvis_vip_scoreboard")
hr.add_files("../UVVM/bitvis_vip_clock_generator/src/*.vhd", "bitvis_vip_clock_generator") hr.add_files("../UVVM/uvvm_vvc_framework/src_target_dependent/*.vhd", "bitvis_vip_clock_generator")
hr.add_files("../src/*.vhd"), "demo_lib") hr.add_files("../tb/*.vhd", "demo_lib")
hr.start()
Add all files and libraries used in TB and DUT
Call start() when finished adding files

## Slide 22: Terminal
sim % python ../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Parsing files, detecting dependencies and building test suite structure

## Slide 23: Terminal
sim % python ../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Compiling library: uvvm_util - OK -
Compiling library: uvvm_vvc_framework - OK -
Compiling library: bitvis_vip_scoreboard - OK -
Compiling library: bitvis_vip_sbi - OK -
Compiling library: bitvis_vip_clock_generator - OK -
Compiling library: demo_lib - OK -
Compiling libraries
Parsing files, detecting dependencies and building test suite structure

## Slide 24: Terminal
sim % python ../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Compiling library: uvvm_util - OK -
Compiling library: uvvm_vvc_framework - OK -
Compiling library: bitvis_vip_scoreboard - OK -
Compiling library: bitvis_vip_sbi - OK -
Compiling library: bitvis_vip_clock_generator - OK -
Compiling library: demo_lib - OK -
Starting simulations...
Running 2 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.random_write_and_read (test_id: 1)
Result: PASS (0h:0m:0s).
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
Number of tests in test-suite, current running test and test run result.
Compiling libraries
Parsing files, detecting dependencies and building test suite structure

## Slide 25: Terminal
sim % python ../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Compiling library: uvvm_util - OK -
Compiling library: uvvm_vvc_framework - OK -
Compiling library: bitvis_vip_scoreboard - OK -
Compiling library: bitvis_vip_sbi - OK -
Compiling library: bitvis_vip_clock_generator - OK -
Compiling library: demo_lib - OK -
Starting simulations...
Running 2 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.random_write_and_read (test_id: 1)
Result: PASS (0h:0m:0s).
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
-----------------------------------------------------------------------
Simulation run time: 0h:0m:0s.
SIMULATION SUCCESS: 2 passing test(s).
Regression summary
Number of tests in test-suite, current running test and test run result.
Compiling libraries
Parsing files, detecting dependencies and building test suite structure

## Slide 26: Terminal
sim % python ../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Starting simulations...
Test run not required. Use "-fr"/"--fullRegression" to re-run all tests.
No changes, no need to simulate

## Slide 27: Regression Run
sim % touch ../src/mem_block.vhd
sim % python ../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Compiling library: demo_lib - OK -
Starting simulations...
Moving previous test run to: ./hdlregression/test_2025-04-30_11.46.58.379030.
Running 2 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.random_write_and_read (test_id: 1)
Result: PASS (0h:0m:0s).
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
-----------------------------------------------------------------------
Simulation run time: 0h:0m:0s.
SIMULATION SUCCESS: 2 passing test(s).
Detecting changes, building test suite structure and compiling file(s).
Backup old test run and run affected tests

## Slide 28: Failing Test Case
sim % python../script/sim.py
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Compiling library: demo_lib - OK -
Starting simulations...
Moving previous test run to: ./hdlregression/test_2025-04-30_11.52.39.299812.
Running 2 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.random_write_and_read (test_id: 1)
Result: FAIL (0h:0m:0s)
Test run: sim_errors=1, sim_warnings=0.
Failing test case is marked as FAIL – will be simulated in each run until marked as PASS.

## Slide 29: Failing Test Case
Running 2 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.random_write_and_read (test_id: 1)
Result: FAIL (0h:0m:0s)
Test run: sim_errors=1, sim_warnings=0.
===========================================================================================================================================
UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"6", x"F849F6DD"): 'Check data in mem'. [11]
UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"6", x"F849F6DD"). Command received [11]
UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [11]
UVVM: ID_AWAIT_UVVM_COMPLETION 20.0 ns TB seq. await_uvvm_completion() => OK. All UVVM scoreboards are empty. Condition ...
UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command
UVVM: ID_BFM 32.5 ns SBI_VVC,1 sbi_write(A:x"3", x"253B1447") completed. 'Write to mem' [2]
UVVM: ID_CMD_EXECUTOR 32.5 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"3", x"DAC4EBB8") - Will be executed [3]
UVVM:
UVVM: =====================================================================================================================================
UVVM: *** ERROR #1 ***
UVVM: 42.5 ns SBI_VVC,1
UVVM: sbi_check(A:x"3", x"DAC4EBB8")=> Failed. Was x"253B1447". Expected x"DAC4EBB8".
UVVM: 'Check data in mem' [3]
UVVM:
UVVM: Simulator has been paused as requested after 1 ERROR
UVVM: *** To find the root cause of this alert, step out the HDL calling stack in your simulator. ***
UVVM: *** For example, step out until you reach the call from the test sequencer. ***
UVVM: =====================================================================================================================================
UVVM:
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
-------------------------------------------------------------------------------------------------------------------------------------------
Simulation run time: 0h:0m:0s.
SIMULATION FAIL: 2 tests run, 1 test(s) failed.
Log output from simulation
Run next test case and present final summary

## Slide 30: Test Case
sim % python ../script/sim.py -ltc
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
TC:1 - tc_tb.tb.random_write_and_read
TC:2 - tc_tb.tb.tc_read_empty
sim % py ../script/run.py -tc 2
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Starting simulations...
Running 1 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
-----------------------------------------------------------------------
Simulation run time: 0h:0m:0s.
SIMULATION SUCCESS: 1 passing test(s).
List all test cases in test-suite
Select test case to simulate

## Slide 31: Test Group
...
hr.add_files(tb_path, "demo_lib") hr.add_to_testgroup("long_tests", "tc_tb", "tb", "random_write_and_read") hr.add_to_testgroup("short_tests", "tc_tb", "tb", "tc_read_empty") hr.start()
sim % python ../script/sim.py -ltg =======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files... Building test suite structure... |---- long_tests | |-- tc_tb.tb.random_write_and_read |---- short_tests | |-- tc_tb.tb.tc_read_empty
Create test groups in regression script.
Any number of test groups, and any number of test cases in test group.
Format: <name>, <entity>, <architecture>, <tc>
List test groups

## Slide 32: Test Group
sim % py ../script/sim.py -tg short_tests
=======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
=======================================================================
Scanning files...
Building test suite structure...
Simulator: NVC
Starting simulations...
Running 1 out of 2 test(s) using 1 thread(s).
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
-----------------------------------------------------------------------
Simulation run time: 0h:0m:0s.
SIMULATION SUCCESS: 1 passing test(s).
Select test group to simulate

## Slide 33: Verbosity
sim % py ../script/sim.py –tc 2 -v
...
Starting simulations...
Running 1 out of 2 test(s) using 1 thread(s).
UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"1", x"00000000"): 'Check data in mem'. [2]
UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"1", x"00000000"). Command received [2]
UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [2]
UVVM: ID_CMD_EXECUTOR 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"1", x"00000000") - Will be executed [2]
UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command
UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"2", x"00000000"): 'Check data in mem'. [3]
UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"2", x"00000000"). Command received [3]
UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [3]
UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command
UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"3", x"00000000"): 'Check data in mem'. [4]
UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"3", x"
UVVM:
...
UVVM: ID_LOG_HDR 1172.5 ns tb_seq SIMULATION COMPLETED
UVVM: ------------------------------------------------------------------------------------------------------------
UVVM:
Running: demo_lib.tc_tb.tb.tc_read_empty (test_id: 2)
Result: PASS (0h:0m:0s).
------------------------------------------------------------------------------------------------------------------
Simulation run time: 0h:0m:0s.
SIMULATION SUCCESS: 1 passing test(s).
Select verbosity to get transcript in terminal

## Slide 34: GUI
sim % python ../script/sim.py –tc 1 –-gui =======================================================================
HDLRegression version 0.61.2
See /doc/hdlregression.pdf for documentation.
======================================================================= Scanning files... Building test suite structure... Setting up: Y:/project/sim/hdlregression/library/modelsim.ini. Compiling library: uvvm_util - OK - Compiling library: uvvm_vvc_framework - OK - Compiling library: bitvis_vip_scoreboard - OK - Compiling library: bitvis_vip_sbi - OK - Compiling library: bitvis_vip_clock_generator - OK - Compiling library: demo_lib - OK -
Run test case in GUI

## Slide 35: GUI and waves
-g / --gui CLI options opens ModelSim/Questa with project precompiled and test case loaded.
Work interactively in GUI while debugging.
GHDL / NVC dumps VCD/FST files.

## Slide 36
Create a Rust function - fibonacci
cargo new --lib fibonacci_plugin
cd fibonacci_plugin
[package]
name = "fibonacci_plugin"
version = "0.1.0"
edition = "2021"
[lib]
crate-type = ["cdylib"]
pub extern "C" fn fibonacci(n: u32) -> u32 { if n < 2 { return n; } let mut f0: u32 = 0; let mut f1: u32 = 1; let mut f_next: u32; for _ in 2..=n { f_next = f0.wrapping_add(f1); f0 = f1; f1 = f_next; } f1 }
Edit the Cargo.toml file to include crate-type for creating a shared library
Write the Rust function
Exposed as extern "C" and compiled into a shared library (.so).

## Slide 37
Rename .dylib file to .so
cd target/release
mv libfibonacci_plugin.dylib libfibonacci_plugin.so
cargo build --release
function fibonacci(n : natural) return natural is begin report "This function should not be called in pure VHDL" severity failure; end function fibonacci;
attribute foreign of fibonacci : function is "VHPIDIRECT fibonacci";
Build project
Write the VHDL function
- note the foreign attribute

## Slide 38
Write a test case that use the fibonacci function
if GC_TESTCASE = "random_write_and_read" then for idx in 1 to 5 loop v_wdata := random(32); v_addr := unsigned(random(3)); sbi_write(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_wdata, "Write to mem", C_SCOPE); sbi_check(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_wdata, "Check data in mem", scope => C_SCOPE); end loop; elsif GC_TESTCASE = "read_empty" then v_exp_data := (others => '0’);
for idx in 1 to 15 loop v_addr := to_unsigned(idx, v_addr'length); sbi_check(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_exp_data, "Check data in mem", scope => C_SCOPE); end loop;
elsif GC_TESTCASE = "fibonacci" then for idx in 1 to 15 loop v_wdata := std_logic_vector(to_unsigned(fibonacci(idx), v_wdata'length)); v_addr := unsigned(random(3)); sbi_write(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_wdata, "Write to mem", C_SCOPE); sbi_check(SBI_VVCT, C_SBI_VVC_IDX, v_addr, v_wdata, "Check data in mem", scope => C_SCOPE); end loop;
else alert(TB_ERROR, "Unknowk TC: " & GC_TESTCASE); end if;
await_uvvm_completion(1 ms);

## Slide 39
Use HDLRegression to link the .so at simulation time.
import sys import os from hdlregression import HDLRegression hr = HDLRegression()
hr.add_files("../UVVM/uvvm_util/src/*.vhd", "uvvm_util")
hr.add_files("../UVVM/uvvm_vvc_framework/src/*.vhd", "uvvm_vvc_framework")
hr.add_files("../UVVM/bitvis_vip_sbi/src/*.vhd", "bitvis_vip_sbi") hr.add_files("../UVVM/uvvm_vvc_framework/src_target_dependent/*.vhd", "bitvis_vip_sbi")
hr.add_files("../UVVM/bitvis_vip_scoreboard/src/*.vhd", "bitvis_vip_scoreboard")
hr.add_files("../UVVM/bitvis_vip_clock_generator/src/*.vhd", "bitvis_vip_clock_generator") hr.add_files("../UVVM/uvvm_vvc_framework/src_target_dependent/*.vhd", "bitvis_vip_clock_generator")
hr.add_files("../src/*.vhd"), "demo_lib") hr.add_files("../tb/*.vhd", "demo_lib") # Rust library shared_lib_path = os.path.abspath("./plugin/target/release/lib/fibonacci_plugin.so") # Set the simulator options to load the shared library sim_options = ["--load={}".format(shared_lib_path)] hr.start(sim_options=sim_options)

## Slide 40
sim % python ../script/sim.py -ltc ======================================================================================================================================================
HDLRegression version 0.59.0 See /doc/hdlregression.pdf for documentation. ====================================================================================================================================================== Scanning files... Building test suite structure... TC:1 - tc_tb.tb.random_write_and_read TC:2 - tc_tb.tb.read_empty TC:3 - tc_tb.tb.fibonacci √ sim % py ../script/sim.py -tc 3 -v ====================================================================================================================================================== HDLRegression version 0.59.0 See /doc/hdlregression.pdf for documentation. ====================================================================================================================================================== Scanning files... Building test suite structure... Simulator: NVC Compiling library: uvvm_util - OK - Compiling library: uvvm_vvc_framework - OK - Compiling library: bitvis_vip_scoreboard - OK - Compiling library: bitvis_vip_sbi - OK - Compiling library: bitvis_vip_clock_generator - OK - Compiling library: demo_lib - OK - Starting simulations... Running 1 out of 3 test(s) using 1 thread(s). Running: demo_lib.tc_tb.tb.fibonacci (test_id: 3) ...

## Slide 41: ... UVVM: ID_LOG_HDR 20.0 ns tb_seq TC: fibonacci UVVM: ------------------------------------------------------------------------------------------------------------------------------------------------ UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_write(SBI_VVC,1, x"7", x"00000001"): 'Write to mem'. [2] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_write(SBI_VVC,1, x"7", x"00000001"). Command received [2] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [2] UVVM: ID_CMD_EXECUTOR 20.0 ns SBI_VVC,1 sbi_write(SBI_VVC,1, x"7", x"00000001") - Will be executed [2] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"7", x"00000001"). Command received [3] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [3] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_write(SBI_VVC,1, x"0", x"00000001"): 'Write to mem'. [4] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_write(SBI_VVC,1, x"0", x"00000001"). Command received [4] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [4] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"0", x"00000001"): 'Check data in mem'. [5] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"0", x"00000001"). Command received [5] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [5] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_write(SBI_VVC,1, x"1", x"00000002"): 'Write to mem'. [6] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_write(SBI_VVC,1, x"1", x"00000002"). Command received [6] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [6] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"1", x"00000002"): 'Check data in mem'. [7] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"1", x"00000002"). Command received [7] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [7] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_write(SBI_VVC,1, x"2", x"00000003"): 'Write to mem'. [8] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_write(SBI_VVC,1, x"2", x"00000003"). Command received [8] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [8] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_check(SBI_VVC,1, x"2", x"00000003"): 'Check data in mem'. [9] UVVM: ID_CMD_INTERPRETER 20.0 ns SBI_VVC,1 sbi_check(SBI_VVC,1, x"2", x"00000003"). Command received [9] UVVM: ID_UVVM_CMD_ACK 20.0 ns tb_seq ACK received. [9] UVVM: ID_CMD_INTERPRETER_WAIT 20.0 ns SBI_VVC,1 ..Interpreter: Waiting for command UVVM: ID_UVVM_SEND_CMD 20.0 ns tb_seq ->sbi_write(SBI_VVC,1, x"1", x"00000005"): 'Write to mem'. [10]

## Slide 42: Documentation

## Slide 43: Key take-aways
Regression improves the verification flow.
Use CI pipelines for running regression on each push.
A reliable regression tool and self-checking TB is key.
HDLRegression is easy to use
  One pragma in the TB.
  One small Python script.
  Works with any verification FW.
  Fast feedback, CI-ready, scales with your projects.
  Open-source and free on GitHub

## Slide 44
Marius Elvegard
marius.elvegard@inventas.no
Inventas