## Slide 1
Architecting FPGAs for Low Power Leadership
22 May, 2025
CERN, Switzerland
Dr. Hardik Shah
Regional Sales Manager

## Slide 2: Lattice Semiconductor Overview
APPLICATIONS & MARKETS
#1
World’s largest volume supplier of FPGA
Tier 1
Supplier with 40+ years
of innovation
We enable secure control, flexible connectivity, and low power compute acceleration
COMMUNICATIONS & COMPUTING
45%
CONSUMER
9%
INDUSTRIAL & AUTOMOTIVE
46%
Chart: 
Applications & Markets percentages based on FY2024 revenue breakdown by reporting segment.
GROWING CUSTOMER BASE
WORLD CLASS SUPPLIER
GLOBAL SUPPORT

## Slide 3: Lattice insights – register and win
https://www.latticesemi-insights.com
The Official Lattice FPGA Training Program

## Slide 4: Dr. Hardik Shah
Let’s connect on LinkedIn

## Slide 5: Why low power ?
extended battery life
simplified heat sink requirements
reduced complexity of the PCB power network
the potential for smaller package sizes
increased component longevity
minimized heat-related measurement errors
}
Cost reduction

## Slide 6: How ?
Company strategy
Target market
Technology node
Architecture features
… Low Power Programmable Leader

## Slide 7: At what cost ?
Largest FPGA device
Fastest Fabric
Latest technology node

## Slide 8: Motivating Example (Data Acquisition System)
Edge processing
  Aggregator is often close to detector in a confined space
  Less data volume close to detector
  Requires low power and small size
Post Quantum Cryptography, Board Management Controller
  Low power, small footprint, flexibility and quick boot-up time
Detector
Detector
Detector
Detector
Aggregator
Aggregator
Server/Processor
CPU
GPU
ASICs
Peripherals
BMC/PQC
….

## Slide 9: Avant Families
DDR4, LPDDR4 memory interface
Fast and flexible IO: 1.8 Gbps MIPI D-PHY, 1.6 Gbps LVDS, 3.3 V support
Avant-E features, plus:
  12.5 Gbps SERDES: up to PCIe Gen3, 10GE
  Advanced Bitstream Authentication and Encryption
  SED/SEC
Edge +
12.5 Gbps SERDES
Avant-G features, plus:
  DDR5 memory interface
  25 Gbps SERDES (up to PCIe Gen4, 25GE)
  Advanced security (bitstream + user security)
Avant-X
eXtra Speed
Mid-range FPGA with 25 Gbps SERDES
Avant-G
General Purpose
Mid-range FPGA with
12.5 Gbps SERDES
Avant-E
Edge
Optimized for edge processing applications
General Purpose +
25 Gbps SERDES

## Slide 10: Lattice Nexus 2 Platform Key Capabilities
Chart: Lower Power Operating Power Consumption
Chart: Lower Power Operating Power Consumption
Chart: Lower Power Operating Power Consumption
Chart: Lower Power Operating Power Consumption
Chart: Lower Power Operating Power Consumption
Chart: Lower Power Operating Power Consumption
16G SERDES
PCIe Gen 4
10 Gb Ethernet
Generic 8b/10b, 64b/66b, 128b/130b
JESD204B, DP, SLVS-EC, CoaXPress, CPRI, eCPRI
Upgraded MIPI C/D-PHY
Up to 4.5Gbps MIPI D-PHY
Up to 7.98Gbps MIPI C-PHY
Split Tx/Rx for more Use Cases
Enhanced Memory Interfaces
DDR4, LPDDR4
Up to 2400Mbps
2x Bandwidth vs Nexus
Higher Performance Fabric
300MHz+ Timing Closure
Scale to 220K SLC
Lower dynamic power
Improved DSP
2x DSP per LC
4x INT8 per block
Advanced Security
Higher strength authentication (ECC521) & encryption (AES-GCM)
SHA3-512 PQC ready
PUF, Anti-Tamper

## Slide 11: Platform Positioning
Chart: Capacity K System logic Cells
| 65 | 100 | 160 | 220
Nexus 2 (16G, 2024, 16nm) | 2 | 2 | 2 | 2
Nexus (8G, 2019, 28nm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Avant (25G, 2022, 16nm) | 3 | 3 | 3

## Slide 12: Agenda
Introduction to Lattice Semiconductor
  Call to register at Lattice Insights
Low power why/how/at what cost?
Motivating example for low power usecase
Basics of power consumption in digital ICs
Techniques used to achieve low power consumption by Lattice
Summary

## Slide 13: Power Consumption
Static & Dynamic Power

## Slide 14: What Impacts Power Consumption?
Capacitance or Logic Density
Logic density (more logic = bigger capacitive load)
Process technology (impacts transistor characteristics)
Temperature
Power consumption increases exponentially with temperature
Transitions or Activity Factor (AF)
Number of status change per clock cycle
Higher activity factor = more power consumed
Notes: https://www.edn.com/how-to-design-an-fpga-architecture-tailored-for-efficiency-and-performance/

## Slide 15: Power Components in FPGAs
Static Power: Static power related to leakage current, is consumed in the absence of any design activity (no active clock). It is mainly related to leakage current associated with transistors in idle mode (Proportional to Junction temperature Tj).
Bias Power: Related to a voltage applied to the substrate and is independent of temperature (depends on technology node – constant – usually associated with static power)
Dynamic Power: Related to design activity and status change of internal registers or transistors. At a lower level it could be explained as switching capacitive loads between two different voltage states (independent of Tj, proportional to frequency).
Total Power: Total chip power is given by combining static, bias, and dynamic power of all blocks and power rails
Power = V x I
I = A.eBT + D + C.Vf
Static
Bias
Dynamic

## Slide 16: Architecture decisions for low Power
Selection of LUT4 vs LUT6
Selection of process node
Architecture features
… Low Power Programmable Leader

## Slide 17: LUT4 vs LUT6

## Slide 18: LUT4 Architecture Optimal for Small & Mid-Range FPGAs
LUT6 – is ~4X the size of a LUT4 in Silicon
LUT4 is faster performance vs LUT6
On the same technology LUT4 is 1/4th static power of LUT6
LUT6 – offers 4X distributed Memory per logic cell (64 bits vs 16 bits)
For the same design implementation
  More logic levels when using LUT4 vs LUT6
  Power advantage of LUT4 vs LUT6

## Slide 19: Why LUT4 has been the standard for so long?
Balance Between Complexity and Efficiency:
Routing Simplicity
Power Consumption:
  Bigger LUT => More transistors for logic => higher static power consumption
Notes: https://www.edn.com/how-to-design-an-fpga-architecture-tailored-for-efficiency-and-performance/

## Slide 20: Public Articles
Lattice Targets Low Power Edge AI with New Small FPGA
“Nexus 2’s focus on small FPGA use cases enabled Lattice to take advantage of a LUT4 architecture, which is better for static power and area efficiency while enabling sufficient performance for the targeted use cases.”
https://www.eetasia.com/embeddednews-lattice-targets-low-power-edge-ai-with-new-small-fpga/
How to design an FPGA architecture tailored for efficiency and performance
“Simply increasing the LUT size to a basic 6-LUT from a 4-LUT or 5-LUT is highly inefficient.“
https://www.edn.com/how-to-design-an-fpga-architecture-tailored-for-efficiency-and-performance/
Notes: https://www.edn.com/how-to-design-an-fpga-architecture-tailored-for-efficiency-and-performance/
https://www.eetasia.com/embeddednews-lattice-targets-low-power-edge-ai-with-new-small-fpga/

## Slide 21: Process node selection

## Slide 22: Process node selection: FD-SOI Benefits (Lattice Nexus™ Family)
Fully Depleted Silicon On Insulator (FD-SOI) Technology choice is one of the major factors that contribute to the power advantage for the Lattice Nexus platform
Significantly less leakage current – lower power
Reduced temperature dependency
Less Vt variability (threshold voltage for charge conduction)
High reliability due to smaller channel surface area
Back Biasing enables tuning the silicon for two operating modes:
  High performance
  Low Power option
Notes: https://www.edn.com/how-to-design-an-fpga-architecture-tailored-for-efficiency-and-performance/

## Slide 23: Software enabled high performance or low power operation
Ability to switch the device from High Performance (HP) to Low Power (LP) mode by changing the technology back bias via a performance grade selection.
Nexus Device options for same speed grade
(HP or LP)
Software controlled bias voltage

## Slide 24: Architecture features

## Slide 25: Device Architecture decision
Both Lattice Avant™ and Lattice Nexus™ integrate features to dynamically reduce power usage of a design.
Lattice Nexus™ features example:
  Dynamic Clock Control (DCC, DCS)
  PLL: Keep PLL in reset, VCO OFF
  LRAM: Shuts down the internal memory
  ADC: Disables the clocking within the block
  I/O Bank (Bottom bank): It allows you to turn OFF referenced and differential input.
Power calculator integrate EF (%)
  Estimate how much the block will be used for power consumption estimation
User logic
State Machine/soft processor to Control User Standby Mode
PLL
LRAM
BNKREF18
ADC
pllpd_en_n_i
dps_i
STDBYINR
STDBYINR
adc_en_i
Notes: https://www.edn.com/how-to-design-an-fpga-architecture-tailored-for-efficiency-and-performance/

## Slide 26: Quick boot-up for low power consumption
Lattice FPGAs can be entirely shut-down within the task period to save power
ti
ti+1
ti+2
tin
ON
ON
ON
ON
Task period
FPGA turned of
FPGA booting up
FPGA shutting down
Device | Configuration time
CertusPro™-NX | 30 ms
CrossLink™-NX | 8 ms
MachXO3™ | 1 ms

## Slide 27: Summary
Low power is the key focus of Lattice
  LUT4 vs LUT6
  Technology node selection with software controlled bias voltage
  Selective turn on/off of on-chip modules
  Quick boot-up of Lattice FPGA results in significant power savings
Register for Lattice Insights – 3 lucky draw winners to receive Lattice FPGA Evaluation board