## Slide 1: Case study
Technical Training: Cryostat Engineering for SC devices
CERN, 13-15 November 2024

## Slide 2: FCCee, RF cryogenic layout, 400 MHz Cryomodule
1 of 33 cryomodules per side

## Slide 3
~10m
730
Inlet ø100
Cavity ø740
He tank ø800
Cavity ø300
Cavity 1850
He tank volume ~0.28m3
Interconnections 400
400 MHz cavities, 2-cell
RF Coupler
tube length: 500
He vapor collector ø50
Cavity: copper, 3-mm thick
Cavity mass: 150 kg
Helium vessel: thickness TBD, st.steel (304L grade)
Helium vessel mass: (304L): 200 kg
Beam tube cone (304L)
RF coupler tube (304L)
Approximate mass of cavity/helium tank/RF coupler assembly: 500 kg
Ø200 x 2
4.2 K saturated liquid helium, 1.0 bar
Liquid in
vapor out
ø50
Beam tube cone,
thickness: 1 mm
500

## Slide 4: Task 1. Cryostat design
Conceptual design of a cryostats for the 400 MHz cryomodule containing 4 cavities. Make a schematic design (simplified sketch, use ppt or any other S/W tool), and make a preliminary engineering design as follows:
  Calculate helium tank thickness, for a maximum allowable pressure of 4 bar
  Calculate vacuum vessel: material, diameter and thickness
  Calculate thermal shielding: material, diameter, thickness. Propose a possible supporting principle.
  Design of the supporting system. Choose type (column, tie rods, etc.), make a conceptual design (materials and sizing for mechanical and thermal requirements). Consider maximum loads from road transport: vertical: 7 m/s2; lateral: 4 m/s2; longitudinal: 6 m/s2 and a minimum Safety Factor on 2 on σ0.2.
  Propose a possible assembly method of the cavities string inside the vacuum vessel
Calculate the static thermal performance (Heat Loads) and total cooling mass flow needs, for the following :
  Supporting system (no heat intercept)
  RF couplers (with active vapor cooling or not)
  Beam tubes cold to warm transitions (cones between 300 K and 4.2 K, no heat intercept). (neglect conduction path of bellows)
  Thermal radiation from vacuum vessel and thermal shielding (flat plate approximation). Calculate the radiation load in the absence of a thermal shield.
  Calculate liquid boil-off mass flows, liquefaction load for ideal vapor cooling of couplers, and thermal shield mass flow assuming Tin=50 K and Tout= 55 K.

## Slide 5: Task 1.1. Table of design parameters
Item | Description | Value | Comments
1 a. |  |  | 
1 b. |  |  | 
1 c. |  |  | 
1 d. |  |  | 
1 e. |  |  | 

## Slide 6: Task 1.2. Table of Static Heat Loads and mass flows
Source of HL | HL (W) @ 4.2 K |  | HL (W) @ 50 K | 4.2 K liquid boil-off (g/s) | Liquefaction load (g/s) | Thermal shield mass flow (g/s) (with Tin=50K, Tout=55 K )
Supports conduction |  |  | - |  | - | -
Beam tube cones conduction |  |  | - |  | - | -
RF Couplers conduction (uncooled) |  | - | - |  | - | -
RF Couplers conduction (ideal vapor cooling) | - |  |  |  |  | 
Radiation, with thermal shield @ 50 K |  |  |  |  | - | 
Radiation, without thermal shield |  |  | - |  | - | -
Radiation from beam tube cones |  |  | - |  | - | -
Totals |  |  |  |  |  | 

## Slide 7: Task 2. Cool-Down
The cool down from 293 K is obtained by boil-off of liquid helium at 4.2 K (1 bar) entered from the bottom of the helium vessels.
Calculate the liquid helium need (mass in kg) for cooling down to 80 K the mass of cavity+helium tank. Consider, during the CD process, an average effectiveness in the use of the sensible heat of helium vapor between 4.2 K and 50 K (exhaust temperature at the exit of the cavity). (Neglect, in the calculation, the contribution from static heat loads to the power balance).
Calculate the average cooling power for a cool down from 293 K to 80 K in 12 h, assuming that cavity/helium vessel are isothermal in the cooling process

## Slide 8: Task 2 Results
Item | Value | Comments
a. |  | 
b. |  | 

## Slide 9: Task 3. RF operation, helium boil-off and pumping
During RF operation of a cryomodule, a dynamic heat load 175 W is added to the static heat load calculated previously. Vapours are pumped back to the refrigerator through a 1’000 m long, DN200 smooth pipe, routed in a shielded and vacuum insulated transfer line.
Calculate the total boil-off rate in saturated helium at 4.2 K and 1 bar (g/s) for one cryomodule
Calculate the pumping pressure drop along the line, neglecting static heat loads along the line
Calculate the total pressure drop for 33 cryomodules all operating with the same dynamic load
If the cavities operate at 2K, 30 mbar, calculate the pressure drop along the line

## Slide 10: Task 3 Results
Item | Value | Comments
a. |  | 
b. |  | 
c. |  | 
d. |  |