## Slide 1
1Sapienza University of Rome
2INFN – Genoa
3INFN and University of Milan
4Tampere University
5CERN
Combined Function Magnets
D. Novelli1,2, L. Alfonso2, A. Bersani2, L. Bottura5, B. Caiffi2,
S. Farinon2, F. Mariani1, S. Mariotto3 , A. Pampaloni2, T. Salmi4
Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.
November 2024
Workshop at LASA

## Slide 2: Nested Configurations
Quad into dipole:
(ReBCO @20 K)
Dipole into quad:
(ReBCO @20 K)
Arc:
Combined function magnets: B1, B1+B2 and B1+B3
B ≈ 8…16 T; G ≈ 320 T/m; G’ ≈ 7100 T/m2
Aperture ≈ 160 mm
Final focus:
Combined function magnets: B1, B2, B1+B2 , B1+B3
B ≈ 4…16 T; G ≈ 100…300 T/m; G’ ≈ 12000 T/m2
Aperture ≈ 120…300 mm
The quadrupole into dipole configuration is the most efficient one, in accordance with US-MAP. Additionally, for combined function magnets in the muon collider, quadrupoles are generally required to be stronger than dipoles.

## Slide 3
As first approx. I used the same cable assumption of L. Alfonso.
Optimization of with ROXIE by
maximizingwith a weight of 1 and with a weight of 0.5
ROXIE
optimization
N1
N2
Starting from the experience of T.Ogitsu:
https://indico.cern.ch/event/1043242/contributions/4448798/attachments/2279860/3873498/MCM20210712SCFM.pdf
Asymmetric Dipole

## Slide 4
2
As first approx. I used the same cable assumption of L. Alfonso.
Optimization of with ROXIE by
maximizingwith a weight of 0.5 and with a weight of 1
ROXIE
optimization
Asymmetric Quadrupole
By also allowing the number of conductors to vary, it becomes again an asymmetric dipole.

## Slide 5: Python-Ansys Interface
a1_quad
w_quad
w_dip
30 mm
30 mm
Initialization
a1_quad loop
w_quad loop
w_dip
loop
Increment of 25mm
(from 25 to 100)
Increment of 10mm
(from 10 to 80)
Increment of 10mm
(from 10 to 80)
Current density
optimization
Save the output
End
When w_dip = 80 mm
When w_quad = 80 mm
w_dip = 10 mm
w_quad = 10 mm
a1_quad = 25 mm
If:
a1_quad = 100mm
w_quad = 80mm
w_dip = 80mm
256 Ansys simulations
for each temperature

## Slide 6: Stress Issue
Zoom-in on the displacements shows that this sector of the quadrupole moves inward
The Von Mises peak stress is on the inner part of the coil

## Slide 7: Stress Issue
To address the issue, we insert an infinitely rigid internal structure to enable the study of stress behavior in the coils.
Now the peak stress, in the same configuration discussed so far, is on the dipole in compression on the midplane (by changing the parameters, the maximum could be shifted).
Now that we have a stress distribution in the coils, we can run the code and add a column with the peak stress to the data.
With all information we will try to create B-G plots for the combined.

## Slide 8: B-G plot at 4.5K
w_dip
w_quad
Current density
optimization (10%)
Optimize J_quad​ and J_dip​ to be close to the critical current density:
….
while not ( 0.9 < f < 1.1 ):
…..
→ ANSYS input (a1, w_quad, J_quad, w_dip, J_dip)
Run ANSYS
ANSYS output →
f = J_c (B_peak) / J
if f > 1: J=J*1.1
else: J = J*0.9
…..
…..
the optimization acts on J_quad and J_dip
with corrections of 10%,
and the cycle closes when either
J_quad or J_dip is within 10% of J_c
What if we performed a
1% optimization ?
Only EM optimization

## Slide 9: B-G plot at 4.5K
w_dip
w_quad
Current density
Optimization (1%)
Optimize J_quad​ and J_dip​ to be close to the critical current density:
….
while not ( 0.99 < f < 1.01 ):
…..
→ ANSYS input (a1, w_quad, J_quad, w_dip, J_dip)
Run ANSYS
ANSYS output →
f = J_c (B_peak) / J
if f > 1: J=J*1.01
else: J = J*0.99
…..
…..
the optimization acts on J_quad and J_dip
with corrections of 1%,
and the cycle closes when either
J_quad or J_dip is within 1% of J_c
This optimization requires more computational effort, but the result is more understandable graphs.
Only EM optimization

## Slide 10: B-G plot at 10K
Current density
Optimization (1%)
Optimize J_quad​ and J_dip​ to be close to the critical current density:
….
while not ( 0.99 < f < 1.01 ):
…..
→ ANSYS input (a1, w_quad, J_quad, w_dip, J_dip)
Run ANSYS
ANSYS output →
f = J_c (B_peak) / J
if f > 1: J=J*1.01
else: J = J*0.99
…..
…..
the optimization acts on J_quad and J_dip
with corrections of 1%,
and the cycle closes when either
J_quad or J_dip is within 1% of J_c
This optimization requires more computational effort, but the result is more understandable graphs.
w_dip
w_quad
Only EM optimization

## Slide 11: B-G plot at 20K
Current density
Optimization (1%)
Optimize J_quad​ and J_dip​ to be close to the critical current density:
….
while not ( 0.99 < f < 1.01 ):
…..
→ ANSYS input (a1, w_quad, J_quad, w_dip, J_dip)
Run ANSYS
ANSYS output →
f = J_c (B_peak) / J
if f > 1: J=J*1.01
else: J = J*0.99
…..
…..
the optimization acts on J_quad and J_dip
with corrections of 1%,
and the cycle closes when either
J_quad or J_dip is within 1% of J_c
This optimization requires more computational effort, but the result is more understandable graphs.
w_dip
w_quad
The simulations with bore radius
75 mm and 100 mm are still running
Only EM optimization

## Slide 12: Stress and Cost considerations
Chart: A vs B – Cost and Stress limits
| 8.8801438000000008 | 13.051802 | 15.295169 | 17.641893 | 20.808011 | 22.201453999999998 | 8.4723203999999992 | 12.534839 | 15.898937 | 17.265322000000001 | 8.2364780999999994
4.5K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
10K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 150
20K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 200 | 200 | 200 | 200 | 200
Chart: B vs G – Cost and Stress limits
| 183.57185000000001 | 176.10811000000001 | 142.60284999999999 | 127.03422999999999 | 123.24435 | 110.91231999999999 | 300.55613 | 240.62540000000001 | 214.29068000000001 | 217.46244999999999 | 387.41356999999999
4.5K, 50mm | 8.8801 | 13.0518 | 15.2952 | 17.6419 | 20.808 | 22.2015 | 8.4723 | 12.5348 | 15.8989 | 17.2653 | 8.2365
10K, 50 mm | 7.39 | 11.1084 | 14.0071 | 16.27 | 17.9306 | 19.1014 | 7.8826 | 11.6979 | 14.3116 | 15.1888 | 18.1791 | 7.3812 | 10.8664 | 13.7135 | 15.7891 | 7.4527 | 10.8542 | 13.7017
10K, 100mm | 7.9883 | 10.7797 | 13.485 | 15.6594 | 17.2659 | 7.2379 | 11.1675 | 12.704 | 14.6144 | 7.0488 | 10.1936 | 12.8537
10K, 150mm | 7.2291
20K, 50mm | 6.682 | 9.1073 | 11.5484 | 13.3849 | 14.7099 | 15.636 | 5.9808 | 9.5808 | 11.7215 | 12.4127 | 14.7773 | 6.0213 | 8.9798 | 11.292 | 13.0505 | 6.3161 | 8.607 | 10.7811 | 5.9728 | 8.6003 | 10.6779 | 5.6597 | 8.2516 | 5.7007
20K, 100mm | 6.5423 | 8.9246 | 11.1055 | 12.8308 | 14.0973 | 5.878 | 9.1783 | 10.3916 | 11.8908 | 5.7907 | 8.4653 | 10.591 | 5.9543 | 8.4746 | 5.5732 | 5.6237
20K, 150mm | 5.9232 | 8.5643 | 10.7191 | 12.3929 | 5.8393 | 8.8512 | 10.0254 | 5.5579 | 8.0281 | 5.1438
20K, 200mm | 6.26 | 8.2865 | 10.3859 | 5.8742 | 8.4919
Chart: A vs G – Cost and Stress limits
| 183.57185000000001 | 176.10811000000001 | 142.60284999999999 | 127.03422999999999 | 123.24435 | 110.91231999999999 | 300.55613 | 240.62540000000001 | 214.29068000000001 | 217.46244999999999 | 387.41356999999999
4.5K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
10K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 150
20K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 200 | 200 | 200 | 200 | 200
Chart: B vs G – only Stress limit
| 183.57185000000001 | 176.10811000000001 | 142.60284999999999 | 127.03422999999999 | 123.24435 | 110.91231999999999 | 99.816574000000003 | 300.55613 | 240.62540000000001 | 214.29068000000001 | 217.46244999999999 | 387.41356999999999
4.5K, 50mm | 8.8801 | 13.0518 | 15.2952 | 17.6419 | 20.808 | 22.2015 | 23.1184 | 8.4723 | 12.5348 | 15.8989 | 17.2653 | 8.2365
10K, 50 mm | 7.39 | 11.1084 | 14.0071 | 16.27 | 17.9306 | 19.1014 | 21.2508 | 21.7222 | 7.8826 | 11.6979 | 14.3116 | 15.1888 | 18.1791 | 19.0332 | 19.8022 | 22.0551 | 7.3812 | 10.8664 | 13.7135 | 15.7891 | 17.9498 | 19.1361 | 19.8238 | 22.089 | 7.4527 | 10.8542 | 13.7017 | 15.7864 | 17.4134 | 19.1533 | 19.9404 | 20.3901
10K, 100mm | 7.9883 | 10.7797 | 13.485 | 15.6594 | 17.2659 | 18.4028 | 20.8599 | 21.3329 | 7.2379 | 11.1675 | 12.704 | 14.6144 | 17.5064 | 18.5037 | 19.262
10K, 150mm | 7.2291
20K, 100mm | 6.5423 | 8.9246 | 11.1055 | 12.8308 | 14.0973 | 14.9886 | 16.7789 | 17.1383 | 5.878 | 9.1783 | 10.3916 | 11.8908 | 14.1579 | 14.9297 | 15.5137 | 16.9314 | 5.7907 | 8.4653 | 10.591 | 12.6015 | 13.857 | 15.1991 | 15.4544 | 17.1777 | 5.9543 | 8.4746 | 10.7031 | 12.2774 | 13.5029 | 14.9431 | 15.5384 | 15.876 | 5.5732 | 8.0595 | 10.0915 | 11.6665 | 13.4475 | 14.3155 | 15.7647 | 16.1128 | 8.4276 | 9.7901 | 11.2265 | 13.1642 | 14.0167 | 15.4384 | 16.4276 | 9.575 | 10.9866 | 12.8876 | 13.7251 | 15.2548 | 15.5961 | 9.1758 | 11.0276 | 12.1388 | 13.9207 | 14.4858 | 15.9779
20K, 150mm | 5.9232 | 8.5643 | 10.7191 | 12.3929 | 13.6272 | 14.3728 | 16.243 | 16.5983 | 5.8393 | 8.8512 | 10.0254 | 11.4832 | 13.3386 | 14.1945 | 15.6254 | 15.9674 | 5.5579 | 8.0281 | 10.514 | 12.1741 | 13.4561 | 13.9563 | 15.7821 | 16.1323 | 5.1438 | 8.1219 | 10.2842 | 11.8138 | 13.0053 | 14.4037 | 15.456 | 16.4492 | 7.7126 | 9.6916 | 11.2229 | 12.9511 | 13.7964 | 15.2029 | 16.1826 | 9.3237 | 10.7092 | 12.6803 | 13.5108 | 15.024 | 15.9955 | 10.4811 | 12.4158 | 13.2319 | 14.7164 | 15.6698 | 14.8782
20K, 200mm | 6.26 | 8.2865 | 10.3859 | 11.9224 | 13.0081 | 8.4919 | 9.8716 | 11.3294 | 13.92 | 15.8215 | 7.816 | 9.8184 | 10.8103 | 12.4676 | 12.6389 | 14.0104 | 15.0436 | 13.3638 | 10.265
Chart: A vs G – only Stress limit
| 183.57185000000001 | 176.10811000000001 | 142.60284999999999 | 127.03422999999999 | 123.24435 | 110.91231999999999 | 99.816574000000003 | 300.55613 | 240.62540000000001 | 214.29068000000001 | 217.46244999999999 | 387.41356999999999
4.5K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
10K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 150
Chart: A vs B – only Stress limit
| 8.8801438000000008 | 13.051802 | 15.295169 | 17.641893 | 20.808011 | 22.201453999999998 | 23.118427000000001 | 8.4723203999999992 | 12.534839 | 15.898937 | 17.265322000000001 | 8.2364780999999994
4.5K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
10K | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 150
Manually excluding the points that exceed the cost (400 kEUR/m) and the stress (400 MPa) limits
We should optimize the stress instead of excluding the points manually

## Slide 13: B-G plot at 4.5K
w_dip
w_quad
Midplane pressure
optimization
Optimize (decrease) J_quad​ and J_dip​ to not exceed the maximum stress (400 MPa)
…..
while not ( 0.99 < f < 1.01 ):
…..
read the J from 1% optimization
→ ANSYS input (a1, w_quad, J_quad, w_dip, J_dip)
Run ANSYS
ANSYS output →
if stress > 400:
f = 400/stress
J=J*
…..
…..
the optimization acts on J_quad and J_dip
with quadratic dependence of J on stress,
and the cycle closes when the stress is below
400 MPa on both the dipole and the quadrupole.
The simulations with bore radius
75 mm and 100 mm are still running
Limitations on cost are still missing
EM and Stress optimization

## Slide 14: 3D plot
Is it useful to have a 3D representation of the 3 planes of interest?

## Slide 15: Conclusions
Do we exclude the asymmetric configuration a priori? We have seen the cos-theta, but what about the CCT? The nested configuration may be best for the B-G plot, allowing B2 values greater than B1, but to study specific configurations the asymmetric might be better.
We inserted an internal support to solve the problem of the coil wanting to enter the aperture. I assumed an internal support with infinitely rigid structure, so the thickness does not matter for the code, but it is relevant to the results. How thick do we consider the inner support?
The code throws simulations with w from 10 to 80 mm (step 10mm), bore diameter from 50 to 200 (step 50mm). How can we make the graphs more accessible? Could it be useful to add points with w from 1 to 10 mm in 1mm steps? Add aperture points?
Now I’m considering roebel cable, 150 MPa as Young module of the ReBCO tape, etc. Should I align with the dipole design considerations? What about the protection of these kind of magnets?
Is it possible to interface the new plots with the old A-B plots? It might be useful to have a relationship between the new work with the old work. Is there a way to analytically assess if we are on the right path with the combined?
Should we start focusing on a specific configuration? If so, nested or asymmetric?

## Slide 16
1Sapienza University of Rome
2INFN – Genoa
3INFN and University of Milan
4Tampere University
5CERN
Thank you
for your attention
D. Novelli1,2, L. Alfonso2, A. Bersani2, L. Bottura5, B. Caiffi2,
S. Farinon2, F. Mariani1, S. Mariotto3 , A. Pampaloni2, T. Salmi4
November 2024
Workshop at LASA

## Slide 17: Stress Issue
A “tooth” is formed that undergoes a peak of stress.

## Slide 18: Stress Issue
If we manually remove the “tooth,” it moves to the first zone not excluded.
This is due to the fact that wedges are infinitely rigid, and the coil wants to move inside.

## Slide 19
Bsum + plf2d