## Slide 1: Magnetic design of the large aperture HTS superconducting dipoles for the accelerator ring of the Muon Collider
1 INFN – Genova, 2 INFN LASA – Milano, 3 University of Milan, 4 CERN, 5 Università degli Studi di Genova, 6 Sapienza Università di Roma
T. Maiello1,4,5, L. Alfonso1, L. Balconi2,6, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1,5, F. Levi1, F. Mariani2,6, S. Mariotto2,3, D. Novelli1,6, A. Pampaloni1, D. Rinaldoni 4, C. Santini2, S. Sorti2,3, M. Statera2 , G. Vernassa2

## Slide 2: Requirements for the SC dipoles
Main characteristics:
Open midplane dipole to avoid deposition of the radiation from muon decay
10 T of central field
Rectangular aperture of 100 mm x 30 mm
Aperture
100 mm
30 mm
Proposed solution:
Magnet design based on metal insulated HTS racetracks

## Slide 3: Requirements for the SC dipoles
Field quality requirements:
Rectangular aperture of 100 mm x 30 mm
Rectangular good field region of 50 mm x 20 mm
Field quality: units in beam radius of 10 mm
0 mm
5 mm
15 mm
25 mm
Harmonic coils
First question: are these numbers confirmed, or can they be reduced?

## Slide 4: Requirements for the SC dipoles
Field Paths
10 mm
6.6 mm
3.3 mm
0 mm
Field quality requirements:
Rectangular aperture of 100 mm x 30 mm
Rectangular good field region of 50 mm x 20 mm
Field homogeneity 1% in the good field region
First question: are these numbers confirmed, or can they be reduced?

## Slide 5: HTS Cable Assumptions
Cu
SC
Substrates
The conductor consists of two tapes and one SS strip.
The SC is based on a commercial YBCO tape from Fujikura
Same assumption as for the collider studies

## Slide 6: Configurations
Several configurations were found to meet various magnetic requirements. Since 3 racetracks are required, the possibilities are:
no aligned
2 aligned
3 aligned

## Slide 7: 3 Aligned Magnetic Design
I [A] | Jeng [A/mm2] | B0 [T] | Bp [T] | Bp/B0
2336.12 | 721.02 | 10.00 | 12.49 | 1.25
Racetrack 1 | N conductors | N tapes
 | 205 | 410
Top [K] | T margin [K] | Mag Length [m] | Mec Length [m] | Yoke radius [m] | Coord. Point A [mm]
20 | >2.5 | ~1.3 | ~1.6 | 0.3 | (150.22;116.98)
Racetrack 2 | N conductors | N tapes
 | 205 | 410
Racetrack 3 | N conductors | N tapes
 | 205 | 410
B [T]
.
A
1
2
3

## Slide 8: 3 Aligned Magnetic Design
Margin in temperature

## Slide 9: 3 Aligned Magnetic Design
Results:
All harmonics greatly less then 10 units
The harmonics higher than the 7th order are negligible (less than 0.003 units)
The field homogeneity evaluated at x = 25 mm is about 0.029%
Field along paths
lower path
higher path
x [mm]
B [T]

## Slide 10: 2 Aligned Magnetic Design
I [A] | Jeng [A/mm2] | B0 [T] | Bp [T] | Bp/B0
2392.00 | 738.27 | 10 | 12.54 | 1.25
Racetrack 1 | N conductors | N tapes
 | 210 | 420
Top [K] | T margin [K] | Mag Length [m] | Mec Length [m] | Yoke radius [m] | Coord. Point A [mm]
20 | >2.5 | ~1.3 | ~1.6 | 0.3 | (159.53;105.00)
Racetrack 2 | N conductors | N tapes
 | 210 | 420
Racetrack 3 | N conductors | N tapes
 | 151 | 302
B [T]
.
A
1
2
3

## Slide 11: 2 Aligned Magnetic Design
Margin in temperature

## Slide 12: 2 Aligned Magnetic Design
Results:
All harmonics greatly less then 10 units
The harmonics higher than the 7th order are negligible (less than 0.003 units)
The field homogeneity evaluated at x = 25 mm is about 0.033%
Field along paths
x [mm]
lower path
higher path
B [T]

## Slide 13: 0 Aligned Magnetic Design
I [A] | Jeng [A/mm2] | B0 [T] | Bp [T] | Bp/B0
2347.61 | 724.47 | 10 | 12.33 | 1.23
Racetrack 1 | N conductors | N tapes
 | 219 | 438
Top [K] | T margin [K] | Mag Length [m] | Mec Length [m] | Yoke radius [m] | Coord. Point A [mm]
20 | >2.5 | ~1.3 | ~1.6 | 0.3 | (157.70;114.30)
Racetrack 2 | N conductors | N tapes
 | 210 | 420
Racetrack 3 | N conductors | N tapes
 | 155 | 310
B [T]
.
A
1
2
3

## Slide 14: 0 Aligned Magnetic Design
Margin in temperature

## Slide 15: 0 Aligned Magnetic Design
Results:
All harmonics greatly less then 10 units
The harmonics higher than the 7th order are negligible (less than 0.003 units)
The field homogeneity evaluated at x = 25 mm is about 0.016%
Field along paths
x [mm]
lower path
higher path
B [T]

## Slide 16: Preliminary Cost Model
Aperture
Conductor | 160 k€/m
Iron yoke | 14 k€/m
Mechanical structure | 3 k€/m
Assembly | 20 k€/m
Total cost | 197 k€/m
Costs hypothesis:
2500 €/kg of YBCO superconductor.
8 €/kg of iron.
10 €/kg of SS for mechanical structure and conservative configuration (total space filling)

## Slide 17: Future Studies
Since the iron pole is practically saturated, a future magnetic analysis involves studying various configurations by removing the pole and inserting holes inside the yoke to manage its saturation.
?
Nominal current: 2336.12 A
B [T]

## Slide 18
Thanks for your attention
1 INFN – Genova, 2 INFN LASA – Milano, 3 University of Milan, 4 CERN, 5 Università degli Studi di Genova, 6 Sapienza Università di Roma
T. Maiello1,4,5, L. Alfonso1, L. Balconi2,6, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1,5, F. Levi1, F. Mariani2,6, S. Mariotto2,3, D. Novelli1,6, A. Pampaloni1, D. Rinaldoni 4, C. Santini2, S. Sorti2,3, M. Statera2 , G. Vernassa2