## Slide 1: Preliminary mechanical design of the large aperture HTS superconducting dipoles for the accelerator ring of the Muon Collider
1 INFN – Genova, 2 INFN LASA – Milano, 3 University of Milan, 4 CERN, 5 Università degli Studi di Genova, 6 Sapienza Università di Roma
T. Maiello1,4,5, L. Alfonso1, L. Balconi2,6, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1,5, F. Levi1, F. Mariani2,6, S. Mariotto2,3, D. Novelli1,6, A. Pampaloni1, D. Rinaldoni 4, C. Santini2, S. Sorti2,3, M. Statera2 , G. Vernassa2

## Slide 2: Requirements for the SC dipoles
Main characteristics:
Open midplane dipole to avoid deposition of the radiation from muon decay
10 T of central field
Rectangular aperture of 100 mm x 30 mm
Aperture
100 mm
30 mm
Proposed solution:
Magnet design based on metal insulated HTS racetracks

## Slide 3: Mechanical Performance
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Lorentz forces effect evaluation:
This very simple model has the aim of evaluate the stress associated to the Lorentz forces, not for the dimensioning of the mechanical structure.
Infinitely rigid structure.
Homogenous material for racetracks:
Frictionless system.
1
5 mm

## Slide 4: Mechanical Performance
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Lorentz forces effect evaluation:
This very simple model has the aim of evaluate the stress associated to the Lorentz forces, not for the dimensioning of the mechanical structure.
Infinitely rigid structure.
Homogenous material for racetracks:
Frictionless system.
1
Racetrack | Fx [kN/m] | Fy [kN/m] | Peak
1 | 1793 | 140 | 150
2 | 1670 | -407 | 146
3 | 1546 | -2151 | 137
tot | 5009 | -2418 | /
Racetrack | Fx [kN/m] | Fy [kN/m] | 
1 | 1793 | 140 | 150
2 | 1670 | -407 | 146
3 | 1546 | -2151 | 137
tot | 5009 | -2418 | /
1
2
3
24442.8
.180E+08
.359E+08
.539E+08
.719E+08
.898E+08
.108E+09
.126E+09
.150E+09

## Slide 5: Stress management Strategy
A 5 mm vertical sector splitting the racetracks into two was inserted to reduce the stress. The position of each sector is the result of an optimization study.

## Slide 6: 3 Aligned
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Lorentz forces effect evaluation:
This very simple model has the aim of evaluate the stress associated to the Lorentz forces, not for the dimensioning of the mechanical structure.
Infinitely rigid structure.
Homogenous material for racetracks:
Frictionless system.
1
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  | Peak | 
1 | 1019 | 799 | 24 | 95 | 76 | 77
2 | 993 | 698 | -93 | -378 | 74 | 75
3 | 927 | 632 | -418 | -1797 | 72 | 71
tot | 5068 |  | -2567 |  | / | 
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  |  | 
1 | 1019 | 799 | 24 | 95 | 76 | 77
2 | 993 | 698 | -93 | -378 | 74 | 75
3 | 927 | 632 | -418 | -1797 | 72 | 71
tot | 5068 |  | -2567 |  | / | 
N cond
N cond
46
45
159
160
47
158
1
2
3
N rt
28842.7
.923E+07
.184E+08
.276E+08
.368E+08
.460E+08
.552E+08
.644E+08
.767E+08

## Slide 7: 3 Aligned
The new field homogeneity at x = 25 mm is about 0.058%.
I [A] | Jeng [A/mm2] | B0 [T] | Bp [T] | Bp/B0
2380.91 | 734.85 | 10.00 | 12.32 | 1.23
+2.0% | +2.0% | / | -1.4% | -1.4%
x [mm]
lower path
higher path
B [T]

## Slide 8: 2 Aligned
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Lorentz forces effect evaluation:
This very simple model has the aim of evaluate the stress associated to the Lorentz forces, not for the dimensioning of the mechanical structure.
Infinitely rigid structure.
Homogenous material for racetracks:
Frictionless system.
1
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  | Peak | 
1 | 949 | 524 | 53 | 142 | 71 | 70
2 | 798 | 338 | -144 | -1525 | 61 | 61
3 | 1169 | 1140 | -323 | -1081 | 90 | 89
tot | 4918 |  | -2878 |  | / | 
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  |  | 
1 | 949 | 524 | 53 | 142 | 71 | 70
2 | 798 | 338 | -144 | -1525 | 61 | 61
3 | 1169 | 1140 | -323 | -1081 | 90 | 89
tot | 4918 |  | -2878 |  | / | 
N cond
N cond
52
39
99
171
43
167
1
2
3
N rt
31054
.108E+08
.216E+08
.324E+08
.431E+08
.539E+08
.647E+08
.755E+08
.898E+08

## Slide 9: 2 Aligned
The new field homogeneity at x = 25 mm is about 0.036%.
I [A] | Jeng [A/mm2] | B0 [T] | Bp [T] | Bp/B0
2441.72 | 753.62 | 10.00 | 12.36 | 1.23
+2.1% | +2.1% | / | -1.4% | -1.4%
x [mm]
lower path
higher path
B [T]

## Slide 10: 0 Aligned
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Lorentz forces effect evaluation:
This very simple model has the aim of evaluate the stress associated to the Lorentz forces, not for the dimensioning of the mechanical structure.
Infinitely rigid structure.
Homogenous material for racetracks:
Frictionless system.
1
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  | Peak | 
1 | 961 | 532 | 48 | 107 | 72 | 72
2 | 893 | 529 | -209 | -1547 | 69 | 69
3 | 1044 | 1013 | -290 | -942 | 80 | 79
tot | 4972 |  | -2833 |  | / | 
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  |  | 
1 | 961 | 532 | 48 | 107 | 72 | 72
2 | 893 | 529 | -209 | -1547 | 69 | 69
3 | 1044 | 1013 | -290 | -942 | 80 | 79
tot | 4972 |  | -2833 |  | / | 
N cond
N cond
51
43
155
167
44
219
1
2
3
N rt
32852.1
.965E+07
.193E+08
.289E+08
.385E+08
.481E+08
.577E+08
.673E+08
.802E+08

## Slide 11: 0 Aligned
The new field homogeneity at x = 25 mm is about 0.030%.
I [A] | Jeng [A/mm2] | B0 [T] | Bp [T] | Bp/B0
2395.09 | 739.22 | 10.00 | 12.20 | 1.22
+2.0% | +2.0% | / | -1.0% | -1.0%
x [mm]
lower path
higher path
B [T]

## Slide 12
Thanks for your attention
1 INFN – Genova, 2 INFN LASA – Milano, 3 University of Milan, 4 CERN, 5 Università degli Studi di Genova, 6 Sapienza Università di Roma
T. Maiello1,4,5, L. Alfonso1, L. Balconi2,6, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1,5, F. Levi1, F. Mariani2,6, S. Mariotto2,3, D. Novelli1,6, A. Pampaloni1, D. Rinaldoni 4, C. Santini2, S. Sorti2,3, M. Statera2 , G. Vernassa2

## Slide 13: case
Very preliminary mechanical concept:
SS both inside and outside of the racetrack.
Threads to convey the preload from outside.

## Slide 14: 3 Aligned
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  | Peak | 
1 | 1019 | 799 | 24 | 95 | 76 | 77
2 | 993 | 698 | -93 | -378 | 74 | 75
3 | 927 | 632 | -418 | -1797 | 72 | 71
tot | 5068 |  | -2567 |  | / | 
Racetrack | Fx [kN/m] |  | Fy [kN/m] |  |  | 
1 | 1019 | 799 | 24 | 95 | 76 | 77
2 | 993 | 698 | -93 | -378 | 74 | 75
3 | 927 | 632 | -418 | -1797 | 72 | 71
tot | 5068 |  | -2567 |  | / | 
N cond
N cond
46
45
159
160
47
158
1
2
3
N rt
To get an idea of what happens to the mechanics using a test was done and the variation of the values is so small that with the precision shown in the tables the numbers do not change
28844.4
.923E+07
.184E+08
.276E+08
.368E+08
.460E+08
.552E+08
.644E+08
.767E+08