## Slide 1: Data Processing with FPGAs: Parallel Computing on Compact Configurable Logic
iCSC 2025
Peter Hinderberger Technical University of Munich (TUM)
March 27, 2025

## Slide 2: Key Contents
1 Field-Programmable Gate Array
  Principles and Structure
  Building Blocks
2 Design Principles
  Design Flow
  VHDL „Hello World“
  High Level Synthesis
3 Parallel Processing
  Paradigms of Parallelism
  Neural Networks on FPGAs
4 Summary

## Slide 3: Introduction
Understand the principles of Field-Programmable Gate Arrays, their advantages and challenges
Know the differences between hardware and software programming and the basic principles of Hardware Description Language
Know what parallel processing means in the context of configurable logic
What to expect, and what not to expect
About me
PhD Student: FPGA-based onboard data processing for a small satellite-based tracking calorimeter
MSc. Applied and Engineering Physics
Born 1992 in Schwäbisch Gmünd, Germany
Hobbies: Hunting, Fishing, Sports, Sailing, Movies, Gaming…

## Slide 4: Field-Programmable Gate Arrays
Introduction and Overview

## Slide 5: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
Principles
?
From: stock.adobe.com

## Slide 6: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
Principles
?
From: stock.adobe.com

## Slide 7: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
“Gate Array” = Array of basic logical components
“Field-Programmable” = (Re-)Programmable wiring
Main components:
Flip Flops = Registers
Look-Up Tables (LUT)
Block RAM (BRAM)
Digital Signal Processors (DSP)
Clocking Structure
Input/Output Ports
Principles
From: Khan et.al., 2024
From: www.xilinx.com

## Slide 8: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
“Gate Array” = Array of basic logical components
“Field-Programmable” = (Re-)Programmable wiring
Main components:
Flip Flops = Registers
Look-Up Tables (LUT)
Block RAM (BRAM)
Digital Signal Processors (DSP)
Clocking Structure
Input/Output Ports
Principles
From: Khan et.al., 2024
From: www.xilinx.com
FF
CLK
RST
D
CE
Q

## Slide 9: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
“Gate Array” = Array of basic logical components
“Field-Programmable” = (Re-)Programmable wiring
Main components:
Flip Flops = Registers
Look-Up Tables (LUT)
Block RAM (BRAM)
Digital Signal Processors (DSP)
Clocking Structure
Input/Output Ports
Principles
From: Khan et.al., 2024
From: www.xilinx.com
LUT
A0
A1
A2
A3
A4
A5
Q

## Slide 10: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
“Gate Array” = Array of basic logical components
“Field-Programmable” = (Re-)Programmable wiring
Main components:
Flip Flops = Registers
Look-Up Tables (LUT)
Block RAM (BRAM)
Digital Signal Processors (DSP)
Clocking Structure
Input/Output Ports
Principles
From: Khan et.al., 2024
From: www.xilinx.com
36kb per Block, O(Mb) per Device

## Slide 11: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
“Gate Array” = Array of basic logical components
“Field-Programmable” = (Re-)Programmable wiring
Main components:
Flip Flops = Registers
Look-Up Tables (LUT)
Block RAM (BRAM)
Digital Signal Processors (DSP)
Clocking Structure
Input/Output Ports
Principles
From: Khan et.al., 2024
From: www.xilinx.com

## Slide 12: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
Advantages:
Large data bandwidth, high number of GPIO ports
Low power consumption
Reconfigurability
Adaptability
Arbitrary granularities of optimization and control
Latency!
Principles
From: Khan et.al., 2024
From: www.xilinx.com

## Slide 13: Field-Programmable Gate Arrays
FPGA: Field-Programmable Gate Array
Challenges:
Complex system: High number of specialized components
FPGAs are configurable Hardware: VHDL/Verilog
Lower clock speeds: O(100 MHz)
On-chip memory
Principles
From: Khan et.al., 2024
From: www.xilinx.com

## Slide 14: Recent Examples from Particle Physics
LHCb: Real-Time Cluster Finding at the Silicon Pixel Detector Bassi et. al., 2023, IEEE Transactions on Nuclear Science 70, 1189–1201
ALICE: Hardware cluster finding algorithm in the HLT Engel et. al., 2017, J. Phys.: Conf. Ser. 898 032018
CMS L1 Trigger: Tracklet Algorithm Bartz et. al., 2017, EPJ Web of Conferences 150, 00016
ATLAS L0 Muon Trigger Y. Mitsumori and on behalf of the ATLAS collaboration, 2023, JINST 18 C02019 Ospanov et. al., 2021, EPJ Web of Conferences 251, 04031
NA62 RICH detector L0 Trigger and DAQ @SPS Barbanera et. al., 2017, Journal of Instrumentation, 12, C01023-C01023
Belle-2, AMBER, PANDA…
+ Growing use for space applications
Examples @Cern

## Slide 15: Design Principles
Or: How to approach an FPGA

## Slide 16: Design Principles
Difference to Programming:
Concurrent statements!
Combinational Logic  Sequential Logic
Combinational
Combinational
Sequential
Code  Circuit!
Concurrent
Hardware Description Languages (HDL)

## Slide 17: Design Principles
Things to think about
Setup and Hold Times
+ Timing!
Difference to Programming:
Concurrent statements!
Combinational Logic  Sequential Logic
Combinational
Combinational
Sequential
Concurrent
From: nandland.com

## Slide 18: Design Principles
Things to think about
Difference to Programming:
Concurrent statements!
Combinational Logic  Sequential Logic
Combinational
Combinational
Sequential
Concurrent
Some Logic
Reg
Reg
Clock
Setup and Hold Times
+ Timing!

## Slide 19: Design Principles
Difference to Programming:
Concurrent statements!
Combinational Logic  Sequential Logic
Combinational
Combinational
Sequential
Concurrent
Things to think about
Some Logic
Reg
Reg
Clock
Some Logic
Reg
Setup and Hold Times
+ Timing!

## Slide 20: Design Principles
Difference to Programming:
Concurrent statements!
Combinational Logic  Sequential Logic
Combinational
Combinational
Sequential
Concurrent
+ Timing Constraints
+ Component Parameters
+ Number of Components
…
Things to think about

## Slide 21: Design Principles
FPGA Design Flow
HDL Code
HDL Testbench

## Slide 22: Design Principles
FPGA Design Flow
Synthesis
Derive Circuit
HDL Code
HDL Testbench
Simulate

## Slide 23: Design Principles
FPGA Design Flow
Synthesis
Derive Circuit
Implementation
Place and Route
HDL Code
HDL Testbench
Simulate

## Slide 24: Design Principles
FPGA Design Flow
Synthesis
Derive Circuit
Implementation
Place and Route
HDL Code
HDL Testbench
Simulate
Timing Successful?

## Slide 25: Design Principles
FPGA Design Flow
Synthesis
Derive Circuit
Implementation
Place and Route
Bitstream
HDL Code
HDL Testbench
Adapted from: Stilkerich et. al., 2014
100110110101100001000111101100010101010000111101010011000000000111101111011
Simulate

## Slide 26: Design Principles
FPGA Design Flow
Synthesis
Derive Circuit
Implementation
Place and Route
Bitstream
Verify
HDL Code
Simulate
HDL Testbench
Simulate
Simulate
Adapted from: Stilkerich et. al., 2014
100110110101100001000111101100010101010000111101010011000000000111101111011

## Slide 27: Hardware Description Language
General Layout of a VHDL Module
How to Code

## Slide 28: Hardware Description Language
General Layout of a VHDL Module
Choose packages to use (including own)
How to Code

## Slide 29: Hardware Description Language
General Layout of a VHDL Module
Entity Declaration
How to Code

## Slide 30: Hardware Description Language
General Layout of a VHDL Module
Architecture Head Definition of
Types, Constants, Signals, and Wires
Functions and Procedures
Attributes
Components
How to Code

## Slide 31: Hardware Description Language
General Layout of a VHDL Module
Architecture Body
How to Code

## Slide 32: Let’s code a MAC
type t_word is array (0 to 10) of std_logic_vector(7 downto 0); signal message : t_word := std_logic_vector(“HelloWorld”);

## Slide 33: Let’s code a MAC
type t_word is array (0 to 10) of std_logic_vector(7 downto 0); signal message : t_word := std_logic_vector(“HelloWorld”);

## Slide 34: Let’s code a MAC
type t_word is array (0 to 10) of std_logic_vector(7 downto 0); signal message : t_word := std_logic_vector(“HelloWorld”);
A
B
Acc
Out
Multiply-Accumulate

## Slide 35: Let’s code a MAC
type t_word is array (0 to 10) of std_logic_vector(7 downto 0); signal message : t_word := std_logic_vector(“HelloWorld”);
Multiply-Accumulate
A
B
Acc
Out
Python:
accumulator = 0
while clock:
accumulator += A * B

## Slide 36
Entity Declaration Architecture Head and First Assignments

## Slide 37
Architecture Body Resulting Circuit
Some Logic
Reg
Reg
Clock
LUT
A0
A1
A2
A3
A4
A5
Q
FF
CLK
R
D
CE
Q

## Slide 38
Architecture Body Simulation Result
Some Logic
Reg
Reg
Clock

## Slide 39
Architecture Body – With Pipeline Register Resulting Circuit
Some Logic
Reg
Reg
Clock
Some Logic
Reg

## Slide 40
Architecture Body – With Pipeline Register Simulation Result
Some Logic
Reg
Reg
Clock
Some Logic
Reg

## Slide 41: High-Level Synthesis
Describe on a higher abstraction level using C/C++
A software engineer’s perspective
C/C++
C/C++ Simulation
HDL
C/RTL Co-Simulation
Synthesis Implementation Bitstream
FPGA
Control
Resource consumption
Understanding of synthesized hardware
Design speed
Simplicity

## Slide 42: High-Level Synthesis
Describe on a higher abstraction level using C/C++
A software engineer’s perspective
C/C++
C/C++ Simulation
HDL
C/RTL Co-Simulation
Synthesis Implementation Bitstream
FPGA
Control
Resource consumption
Understanding of synthesized hardware
Design speed
Simplicity

## Slide 43: High-Level Synthesis
Support: Keras, limited: PyTorch, ONNX
Growing range of features, currently:
  MLP
  CNN
  RNN
  GNN
Backends: Intel, Vitis, Catapult, oneAPI
HLS4ML: Neural Networks for FPGAs
C/C++
C/C++ Simulation
HDL
C/RTL Co-Simulation
Synthesis Implementation Bitstream
FPGA
Python
fastmachinelearning.org
Alternative: MATLAB/SIMULINK

## Slide 44: Parallel Processing
What does “parallel” actually mean?

## Slide 45: Paradigms of Parallelism
Data-Parallel
“Single Instruction, Multiple Data (SIMD)” Vectorization
Easily implemented
Pipeline-Parallel
Different tasks… …at the same time …on different parts of the data
Inherent to FPGAs
Subtype of task-level parallelism
General
From: Xilinx, UG1399
A1
A2
A3
B1
B2
B3
C1
C2
C3
A1
…
Serial
Data- Parallel
A2
A3
B1
B2
B3
Source: https://www.planet-wissen.de/gesellschaft/wirtschaft/ industrialisierung_in_deutschland/pwiedasfliessbandeineerfolgsgeschichte100.html
C1
C2
C3

## Slide 46: Paradigms of Parallelism
FPGA-specific
Image adapted from: Xilinx, UG1399
Possible Bottlenecks:
Data transport, Interfaces
On-chip memory
Stream-based data transfer
Task-level parallelism
Buffering: FIFOs (First In First Out)
Pipelining on all levels of granularity

## Slide 47: Combination of Paradigms
Serial Execution:
+ Task-Level Parallelism, exploiting independence of B and C:
+ Pipeline-Level Parallelism (Macroscopic):
An Example
Images From: Xilinx, UG1399
+ Pipeline-Level Parallelism (Microscopic):

## Slide 48: Combination of Paradigms
Serial Execution:
+ Task-Level Parallelism, exploiting independence of B and C:
+ Pipeline-Level Parallelism (Macroscopic):
An Example
Images From: Xilinx, UG1399
+ Pipeline-Level Parallelism (Microscopic):

## Slide 49: Neural Networks on FPGAs
Matrix multiplications  Highly parallel
Quantization: Fixed-point favorable Floating-point possible
Performance often comparable to GPUs
Some Remarks

## Slide 50: Neural Networks on FPGAs
Limitations: On-chip weight memory MAC units (DSP or LUT)
Model compression and optimization for FPGAs:
Pruning
Knowledge distillation
Choice of Quantization
Choice of Activation Function
Some Remarks

## Slide 51: Neural Networks on FPGAs
Limitations: On-chip weight memory MAC units (DSP or LUT)
Model compression and optimization for FPGAs:
Pruning
Knowledge distillation
Choice of Quantization
Choice of Activation Function
Some Remarks
arXiv:1506.02626

## Slide 52: Neural Networks on FPGAs
Limitations: On-chip weight memory MAC units (DSP or LUT)
Model compression and optimization for FPGAs:
Pruning
Knowledge distillation
Choice of Quantization
Choice of Activation Function
Some Remarks
https://medium.com/vafion/knowledge-distillation-9a0bf514fbeb

## Slide 53: Neural Networks on FPGAs
Limitations: On-chip weight memory MAC units (DSP or LUT)
Model compression and optimization for FPGAs:
Pruning
Knowledge distillation
Choice of Quantization
Choice of Activation Function
Some Remarks
Idea: Use LUTs as ultrafast “multipliers” in binary neural networks (BNN)

## Slide 54: Recent Examples from Particle Physics
Giasemis et.al. 2025: Comparative Analysis of FPGA and GPU Performance for Machine Learning-Based Track Reconstruction at LHCb
FPGA vs. GPU for a Multilayer Perceptron
HLS4ML
Xilinx Alveo U50 and U250 (Kintex UltraScale+)
Feed Forward Network:
Max. number of parallel instances of a simple network
8 bit quantization
RelU Activation
FPGA-based Data Processing @CERN
Notes: Used in GNN-based track reconstruction for the LHCb Vertex Locator (VELO)

## Slide 55: Recent Examples from Particle Physics
Giasemis et.al. 2025: Comparative Analysis of FPGA and GPU Performance for Machine Learning-Based Track Reconstruction at LHCb
FPGA vs. GPU for a Multilayer Perceptron
HLS4ML
Xilinx Alveo U50 and U250 (Kintex UltraScale+)
Feed Forward Network:
Max. number of parallel instances of a simple network
8 bit quantization
RelU Activation
FPGA-based Data Processing @CERN
Better Performance
Lower Power Consumption
Notes: Used in GNN-based track reconstruction for the LHCb Vertex Locator (VELO)

## Slide 56: Recap

## Slide 57: Summary
Field-Programmable Gate Arrays
= Configurable Hardware ≠ Software
 Matrix of basic, low-level digital components
+ Extreme flexibility and perfectly optimized, specialized computing
+ High degree of (inherent) parallelism on all levels of granularity
- Programming needs different way of thinking
- High verification and debugging effort
Parallelism:
Macro- and microscopic pipelining
Data and task-level parallelism
Streaming, buffering
FIFO = First In First Out

## Slide 58
Contact: peter.hinderberger@tum.de
Thank You!
Contact: peter.hinderberger@tum.de
Notes: Find better image

## Slide 59: Resources
Kastner: Parallel Programming for FPGAs - The HLS Book
Gazi: A Tutorial Introduction to VHDL Programming
Gazi & Arli: State Machines using VHDL – FPGA Implementation of Serial Communication and Display Protocols
Snider: Advanced Digital System Design using SoC FPGAs
LaMeres: Quick Start Guide to VHDL
Bruno & Eschemann, 2024: The FPGA Programming Handbook
FPGA in Space Exploration: https://fpgainsights.com/blog/fpga-in-space-exploration-powering-satellites-and-spacecraft/
Woods: FPGA-based Implementation of Signal Processing Systems
Teubner: Data Processing on FPGAs
Vitis High-Level Synthesis User Guide (UG1399)
www.nandland.com

## Slide 60: Field-Programmable Gate Arrays
Components of a Xilinx Kintex UltraScale FPGA
FF
Images from: Xilinx online component documentation

## Slide 61: Field-Programmable Gate Arrays
Configurable Logic Block (CLB) (x4):
Look-Up Table (LUT) + flip flop/register
Can be used as distributed memory
Block RAM (BRAM):
36 kB or 2 x 18 kB per block
Adjustable width x depth
Signal Processor (DSP):
27x18-bit multiplier, 48-bit accumulator
Several features and capabilities
Components of a Xilinx Kintex UltraScale FPGA
FF
Images from: Xilinx online component documentation

## Slide 62: Field-Programmable Gate Arrays
Concurrent and flexible
Use available area as you like
Use different clocking regions
Suitable as:
Highspeed interface and glue logic
Specialized accelerator
All-in-one solution
Limit: Clock speed, Area (= Resources)
Some General Example
Processing Stage 1
Processing Stage 2
Processing Stage 3
Control Logic Status Registers
Some Independent Logic
Buffer
Online Test Functionality
Softcore Processor

## Slide 63: Types of Parallelism
Pipeline vs. Data:
Pipeline-parallelism should always be employed
Throughput increase >> Area consumption
More intermediate registers  Higher possible clock frequency
Data-parallelism: Use according to application and available area
Notes: Image from: Teubner: Data Processing on FPGAs

## Slide 64: Different Hardware Architectures in Comparison
GPU:
Originally: Mainly for image and video processing
Simple programming (e.g. CUDA, OpenCL)
Massively parallel, high performance
Floating point
High power consumption
High volume
High on-chip memory
Others:
Application-Specific Integrated Circuits (ASICS)
Specialized Accelerators: Tensor Processing Unit (TPU), Vision Processing Unit (VPU), Analog Matrix Processor (AMP) etc.
FPGA:
Multi-purpose, extremely parallel, highly specialized
Complex+efficient, or simpler programming
Reprogrammable (compared with ASICs)
Lower clock frequencies (compared with CPUs)
Fixed-point
Low power consumption
Low volume
Lower on-chip memory
+ Cost, volume, design effort, available experience...
Choice is not always simple!
Main Opponents

## Slide 65: Field-Programmable Gate Arrays
1980s PROM (Programmable Read-Only Memory), PLD (Programmable Logic Device)
1983 Altera EP300: Erasable EPROM using UV light
1985 XC2064: First commercially available FPGA (Xilinx) 8x8 configurable logic blocks with one LUT and three inputs each
1992 Patent: Naval Surface Warfare Center, 600,000 reprogrammable gates
1990s Growth, main usage in networking and telecommunications, later also industrial and automotive use In Physics: „Glue logic“, close to hardware
Now Vast range of applications, e.g. data centers or machine-learning Kintex Ultrascale KU060: 663,360 CLBs, 1080x36Kb BRAM, 2760 DSP slices…
History