## Slide 2: HI-ECN3 Target station and target complex design HI-ECN3 Irradiation Opportunities Workshop
J-L. Grenard, M. Calviani (CERN) – on behalf of HI-ECN3 WP4 Target Complex

## Slide 3: Content
Target complex overview
Target station design
Service building integration
Irradiation stations opportunities
Impact and timeline for implementation
Summary

## Slide 4: BDF/SHiP Target & Complex
New
Service Building
~ 700-1000 m2
ECN3
Beam Dilution System
New
Access Shaft
(material only)
88 m2
TCC8
Existing
Access Shaft
48 m2
B918
B911
New Target Complex
containing the Beam Dump Target

## Slide 5: BDF/SHiP Target
New
Service Building
~ 700 – 1000 m2
ECN3
Beam Dilution System
New
Access Shaft
(material only)
88 m2
TCC8
Existing
Access Shaft
48 m2
B918
B911
New Target Complex
containing the Beam Dump Target
13 x TZM blocks (580 mm)
5x W blocks (780 mm)
Baseline Design  To be improved during TDR
WP4
WP3
WP2
WP5+SHiP
WP4
WP6,WP7 +al.
WP4

## Slide 6: BDF Target complex integration
Target area
Confinement wall
Access chicane
Mobile Shielding
Above Coil Shielding
Magnetized
shielding
Water cooled proximity shielding
Target
Upstream Shielding
Collimator
Target station
SHIP experiment
Muon shield magnet
Diluted Proton beam from SPS
Space for shielding temporary storage
Beam instrumentation
Vacuum confinement

## Slide 7
BDF Target complex integration - shielding
~12 m
~8 m
~4.8 m
~ 180 m³ (~1400 t) of cast iron + US1010
~ 360 m³ (~800 t) of concrete / marble
Most of the shielding blocks recovered from other CERN facilities
Design of the target station will need to be frozen in Q3 2025

## Slide 8: BDF Target complex integration - extraction
~30m
Trolley mounted on stainless steel chain action rollers
Extraction towards the upstream side of the facility
The extraction of the target trolley would require a significant effort (~2 months to open and close the vessel)
Can only be performed during a YETS

## Slide 9: Target station vacuum confinement
Utilities feedthroughs (cooling, target instrumentation)
Mechanical design ready to build a prototype
Design of radiation tolerant gaskets
Decommissioning plan
Overall dimensions: ~6.36 x 2.05 x 2.95 m
Can be fully fabricated and tested at a contractor premises
Primary vacuum to optimize air activation around target
(Water containment in case of water leak)

## Slide 10: Opportunities for parasitic irradiation
BDF/SHiP offers the unique opportunity to access unprecedented radiation levels in mixed field – allowed due to the specific feature of the experiment
Priority is given to SHiP, so irradiation opportunities will have to be parasitic to the operation of the complex
Current budget does not include/foresee the addition of these items
Any irradiation station require an associated manipulation space for highly activated samples
None of the irradiation capabilities shown in the next slides are part of the target station baseline, but are intended as realistic possibilities
Input required by beginning of 2025 to act on the design

## Slide 11: Irradiations stations opportunities
High-fluence, in-vessel, irradiation module (BHFIM)
External activation station (BEAS, R2E@4m)
Internal activation/irradiation station (BIAS)
Rabbit irradiation station (BRIS)
12 m

## Slide 12: High-fluence, in-vessel, irradiation module (BHFIM)
In vessel module approximate overall size: 1 m (L) 150 mm (W) 900 mm (H)
Possible utilities could be connected via vacuum vessel door
Accessibility once a year during a YETS ~1month to extract the module
Samples could be handled in the surface target building hot/service-cell
Need a shielded cask for handling from underground to surface building

## Slide 13: Rabbit irradiation station (BRIS)
Rabbit D200mm connected to glove box / hot cell
Handling of ‘’small’’ samples (D150mm x L385mm)
Utilities could be connected on capsule
Accessibility all the time ~10 mins to recover a sample

## Slide 14: Rabbit irradiation station (BRIS)
Start in target area
Transition to shaft & target building
Reception in target service building
Reception station not included in the Project baseline, but building is foreseen to host it

## Slide 15: External activation station (BEAS, R2E@4m)
Maximum thickness including shielding station 1.2 m
Utilities
Accessibility every MD when no beam delivered in ECN3
Configuration change possible during TS

## Slide 16: Internal activation/irradiation station (BIAS)
Size limited to diameter ~200 mm
Could be located up to the edge of the vacuum vessel
Utilities
Accessibility every MD when no beam delivered in ECN3
Configuration change possible during TS

## Slide 17: Target service building
Building to support target station operation
Direct connection to the TCC8-ECN3 caverns
Cooling and ventilation systems of the target complex
Service cell to prepare the target station equipment for final disposal (part of baseline)
Space reservation for the potential material testing
~700-1000 m²
Work in progress
Optimization of volumes and process

## Slide 18: Irradiations stations opportunities - Summary
Name | Distance from target | Accessibility to recover the module | Size of module | Utilities capabilities
BEAS (R2E@4m) | ~4 m | SPS MD (when no beam for ECN3) | Max thickness 1.2 m | Yes (almost unlimited)
BIAS | ~1 m | TS | D200 mm | Yes (almost unlimited)
BRIS | ~1 m | Operation | D150xL385 mm | Yes (1 power circuit + 8 control signals)
BHFIM | ~5-10 cm | YETS | 1000x150x900 mm | Yes (limited)

## Slide 19: What would mean to add a longer distance irradiation station?
Major change for the civil engineering (new access shaft, access tunnel) and would have consequence on design of the foundations of the target service building
Any large CE structure would have to be included in the current design, since doing that a posteriori will be hardly implementable or will be very costly
Would likely have a significant impact on the ventilation system
Major radiation protection aspects would have to be taken in consideration (shielding, access system)
The HI-ECN3 timeline for design and construction of the current new CE structure is already tight and doesn't allow contingency the additional large new CE structure(s) unless a decision by management and budget & resources are made available immediately.
A consequent additional resources would be required to design properly this new facility

## Slide 20: Impact and timeline for implementation
Should be implemented as part of baseline target station construction
Could be implemented later post target station installation (during an EYETS, or LS)
As per expected residual dose rates of equipment (up to hundreds mSv/h) any changes (mechanical, electrical, shielding…) in the ‘’red box’’ can be foreseen
The design of the irradiation station shall take in consideration residual dose rates aspects in view of their maintenance

## Slide 21: Conclusions
We are still on time to implement a certain number of features to make the BDF target station compatible with future implementation of irradiations station(s)
Any large civil engineering modification need to be evaluated by end 2024, as IRP board is foreseen in mid 2025
Any interfaces part of the target station for the irradiation station(s) need to be implemented before end 2025
Any change in the shielding to implement the irradiation station(s) need to be implement before end 2025
The existing infrastructure should be ready and compatible with the handling of any highly activated equipment
External funding are required to implement interfaces for the future irradiations station(s)

## Slide 22
Thank you

## Slide 23: BDF Target complex integration extraction devlopment
Trolley mounted on full stainless steel chain action rollers
Extraction / insertion mechanism based on a motorized rigid chain

## Slide 24
Service building within the BDF/SHiP complex

## Slide 25
Shielded buffer zone
Material access
Cooling equipment
Service cell
with a movable roof
Power room
Personnel access
New lorry access
Service building – ground floor
HotCell
Access shaft

## Slide 26: Service building – 1rst level
30t overhead traveling crane
Control racks
Mobile shielded hatches
Filter room
Definition of the envelops by end of 2024