## Slide 1: Brief introduction on WP4.4 related study at USTC
Ming Shao

## Slide 2: STCF PID system
Cherenkov technology for STCF PID detector
Polar angle coverage ~22°-36° (endcap), ~34°-90° (barrel)
/K separation (4) for p<2GeV/c
400kHz physics event rate
Candidate technology: DTOF
Large area fused silica radiator
Multi-anode MCP-PMT
~15ps timing ASIC
Minimal material budget
Linear Accelerator
400 m
Damping Ring
150 m
Collier Rings
800-1000 m
A factory producing massive tau lepton and hadrons, to unravel the mystery of how quarks form matter and the symmetries of fundamental interactions
Ecm= 2-7 GeV， 0.51035 cm-2 s-1
Super Tau Charm Facility (STCF)

## Slide 3: DTOF R&D related to WP4.4.3
Requirements:
  Overall material budget <0.3 X0, as low as possible
  Fit in the limited space between tracker and ECAL
Plan:
  1st-version design (C fiber, Al honeycomb), 2024
  Prototyping & optimization, 2025
  Final design, 2026
Light-weight mechanical structure
Plan to join LHCb-TORCH group (Technical Associateship)
 Contribute to detector/electronics/mechanical etc.
Endcap PID
DIRC+TOF=DTOF
Barrel PID (DTOF option)

## Slide 4: DTOF R&D related to WP4.4.4
Requirements
  Roughness <1nm (reflectivity, error <0.1%)
  Absorption length >100m, 10% (>300nm)
Method
  Measuring laser intensity change after crossing fused silica
Optical characterization of fused silica
Plan
  Setup optical test stand in dark room, 2024~2025
  Test fused silica plates for endcap and barrel DTOF prototype, 2025-2026

## Slide 5: Thank you!