## Slide 1: Particle Accelerators in the XXI Century
Maurizio Vretenar CERN JUAS 2025

## Slide 2: This Seminar
This Seminar is intended as an “appetizer” to introduce you to the Science and Technology of Particle Accelerators
Goals:
Give a general overview of status and challenges of particle accelerator technologies and applications, with no maths;
Give some hints to guide your study and your future choices.
Outline:
Accelerators as instruments
Accelerator and innovation
Key accelerator challenges
Accelerators for society
The future…

## Slide 3: Accelerators: our door to the subatomic world
Extracting charged particles from an atom (protons, electrons, nuclei) and accelerating them we concentrate enormous amounts of energy in very small volumes
proton
Full LHC bunch (1.15 1011 protons) at interaction point (30 cm, 16x16 mm2): energy 1.3 105 J, energy density ≈ 0.5 1012 J/m3
For comparison: Li-ion battery 6 109 J/m3, Diesel fuel 4 1010 J/m3
Particle accelerators are our door to access the subatomic dimension… to study and exploit the atom and its components
LHC proton: 7 TeV
Yoghurt: 150 g, 120 cal.
TGV train: 400 tons, 200 m, 300 km/h
1 Joule is really tiny:
=1 W*s, cost ≈ 10-7 €

## Slide 4: Where does the energy go?
The accelerated particle can:
kick an electron out of the atom (ionization) – breaking of molecular bonds, generation of free chemical radicals acting at chemical and molecular level.
Excite the electron to a higher energy level, that comes back generating an X-ray (photon).
be deflected by the nucleus giving energy to the atom - increase of temperature, etc.
Interact with the nucleus, generating secondary particles (radiation) or breaking/modifying the nucleus.
Interact with other subatomic particles, generating new particles.
Limited to microscopic quantities by the small total energy.
Secondary beams, e.g. X-rays or neutrons, are used in applied science and medicine.
X-rays:
bremsstrahlung or synchrotron light
Neutrons:
spallation or other reactions
Particle-driven chemical processes are used for medicine and environment.
Penetration depth dependent on beam energy (Bragg peak)
Break molecules or DNA

## Slide 5
Particles can break and modify the nucleus, generating new atomic elements and transforming matter
Transforming matter, the dream of ancient alchemists
In high-energy collisions, energy can generate new particles
E = m c2
1. The dream of NUCLEAR PHYSICS
2. The dream of PARTICLE PHYSICS
The magic of creating matter
3. The dream of MEDICINE
The dream of observing and curing the body without blood
Particles deposit energy at a well-defined depth without damaging surrounding tissues.
Treatment and imaging using accelerators
Accelerators can fulfil old human dreams

## Slide 6: Accelerators can precisely deliver energy
A «beam» of accelerated particles is like a small “knife” penetrating into the matter
Particles can penetrate in depth
(different from lasers!).
A particle beam can deliver energy to a very precisely defined area, interacting with the electrons and with the nucleus.
Particle beams are used in medical and industrial applications,
e.g. to cure cancer, delivering their energy at a well-defined depth inside the body (Bragg peak)
Lasers and accelerators have comparable peak energy densities, but different interactions and penetration

## Slide 7: Innovation in Particle Accelerators
How old are particle accelerators?
How does their technology evolve?
Elwood Smith, NYT

## Slide 8: Modern particle accelerators are 97 years old
In 1928 a PhD Thesis introduced the basic concept of modern particle accelerators, using periodic acceleration provided by electric fields at Radio-Frequency (RF).
A major step from the previous DC (constant voltage) acceleration, limited to few MeV
Rolf Widerøe’s PhD thesis, 1928, University of Aachen – he was 26 years old!
Acceleration of potassium ions 1+ with 25kV of RF at 1 MHz  50 keV acceleration in an 88 cm long glass tube) “at a cost of four to five hundred marks”, less than 2’000 € today!
use of Radio-Frequency technology (at the time limited to 1-2 MHz) → marrying radio technology and accelerators.
Acceleration in a sequence of gaps separated by tubes → invention of periodic acceleration.
complete accelerator: ion source, RF accelerator, detector, in vacuum.
Ion source
Accelerating tube at
V=V0sinwt
Detector
RF generator
(from R. Wideroe’s thesis)
(image credit: Wikimedia commons)

## Slide 9: At the roots of innovation
What were the ingredients of Rolf Wideröe’s innovation?
He was young and curious (PhD student, fresh ideas and time available)
He was under pressure to complete his thesis («necessity is the mother of invention»)
He was merging information and experience from different fields (cross-fertilisation)
He was going all the way down to practical realisation (to «innovate»).
The Oslo Manual (OECD/Eurostat, 2005), defines innovation as “the implementation of a new or significantly improved product or process …”

## Slide 10: Innovation in the particle accelerator field
1931………….1945/48….1952…………..1965/90’s….…
Cyclotron: cyclic acceleration with magnets (Lawrence)
Application of WW2 radar technology to accelerators
Strong focusing
Superconducting magnets and acc. cavities
Succession of enabling technologies (technology leaps)
Energy
2009 Livingston plot, Symmetry magazine
(for colliders, energy to reach same c.o.m. energy in collision with proton at rest)
S. Livingston, 1959:
Accelerator energy increases by a factor of 10 every 6 years
(Moore’s law of accelerators)
XXI century
?
2008: the Large Hadron Collider
Colliders

## Slide 11: Particle Accelerators in 2025
Updated Livingstone-type chart (Wikipedia 2014, uploaded by J.Nash, Imperial College)
We have reached the end of exponential growth…
but the field has never been so flourishing!
TIARA Need for Accelerator Scientists report, 2013: 3’700 people engaged in accelerator science in Europe, growing to 5’000 by 2020.
As many as 50 ongoing accelerator construction or upgrade projects listed in the 2017 IPAC Conference (13 America, 11 Asia, 26 Europe).
?
How many particle accelerators there are in the world, and where are they?
Annual market for medical and industrial accelerators estimated (2018) at US$5.0 Billion/year, growing at 5%/year.

## Slide 12: Multiple challenges for accelerator science
12
For all XXth century, fundamental science has been the driving force for the development of new accelerators, with its continuous quest for high energies required to discover new particles.
In this early XXI century, we are moving to a new paradigm where together with particle physics applied science (photon and neutron science) and healthcare appear as driving forces for innovation.
Advanced medicine and new materials are key technology drivers of the XXIst century.
There are more than 35’000 particle accelerators in operation around the world:
Research |  | 6%
 | Particle Physics | 0,5%
 | Nuclear Physics, solid state, materials | 0,5%
 | Biology | 5%
Medical Applications |  | 35%
 | Diagnostics/treatment with X-ray or electrons | 33%
 | Radio-isotope production | 2%
 | Proton or ion treatment | 0,1%
Industrial Applications |  | 60%
 | Ion implantation | 34%
 | Cutting and welding with electron beams | 16%
 | Polymerization | 7%
 | Neutron testing | 3.5%
 | Non destructive testing | 2,3%
What is the role of accelerators in this transition?

## Slide 13: Accelerators in transition – for science and for society
Transition to new more sustainable technologies: lower use of natural, financial, and human resources.
Transition from basic science as main technology driver to a multiple system where basic and applied science, medicine and industry will together drive accelerator development.
Transition from a centralised configuration based on large laboratories to a distributed scheme (project clusters of small and large laboratories and industry)
Fundamental science
Applied science (photon and neutron sources)
Societal applications (medicine, industry, environment, etc.)
Limitations related to size, cost, energy.
New ideas and technologies
The electron linac for cancer radiotherapy, the most widespread accelerator in the world (> 12000 units)
innovation

## Slide 14: The big challenges for accelerator science
We need new ideas (innovation!) and a collaborative and creative environment for these ideas to grow
Making accelerator-based particle physics research sustainable over the long-term, increasing at the same time the benefits of particle accelerators for society are the main challenges to the accelerator community in this XXI century.
From the LHC (27 km) to the Future Circular Collider (90 km)
Sustainability translates into considering from an early design phase that resources are finite and use them conservatively and wisely with a view to long-term priorities, for the entire life cycle. New accelerator projects require Life Cycle Assessments (resources and emissions for construction / operation / decommissioning).
The goal is to reduce the overall environmental footprint of particle accelerators, minimising their impact as large consumers of energetical, environmental, financial, and human resources.

## Slide 15: Multiples challenges for accelerator R&D

## Slide 16: Increasing energy efficiency
Accelerators requires large amounts of energy to operate.
Low overall efficiency, between <1% (scientific accelerators) and 20-50% for high-intensity applications.
Due to high quality of the concentrated energy of a particle beam: from the electric grid the energy goes to several transformation (AC/DC, high voltage, radio-frequency, cryogenics, magnetic fields), each with a (low) characteristic efficiency, often from thermodynamics.
Large effort ongoing to develop components with better efficiency (e.g. superconductivity, permanent magnets, high-efficiency RF sources).
Power flow in the PSI cyclotron facility: 13% of power to production target, 87%% dissipated into heat.
Only a tiny fraction of power on target converted into beams (n, m) for physics.
Permanent magnet quadrupoles
High-efficiency upgrade of LHC klystrons : from 60% to 70% efficiency
Electrical power consumption (MW) for LHC and future projects (estimated) |  | 
 | normal | Stand-by
LHC | 122 | 89
HL-LHC | 141 | 101
ILC | 230 | 
CLIC 500 GeV | 235 | 167
CLIC 1.5 TeV | 364 | 190
FCC hh | 580 | 300?

## Slide 17: Economic sustainability and innovation
The economic environment and the priorities of a society define the budget to be invested in large scientific infrastructure (“Big Science”).
scaling of present technology
reduction in cost with new technologies
Moving along this line was made possible by new technologies
(colliders – antiproton production and storage – superconductivity)
Plot courtesy of P. Lebrun
collider
p-pbar
collider
superconducting
collider
FCC-ee

## Slide 18: Reducing environmental footprint: smaller accelerators
Synchrotrons: p/q=Br
Need to maximise magnetic field
Superconductivity is mandatory, the limitations is the critical current density Jc for SC magnets
Linear accelerators: W=El
Need to maximise electric field
Limitations: arcing between electrodes, field emission, etc.
(and RF power, proportional to V2 !)

## Slide 19: The magnetic field frontier in superconducting magnets
R&D towards a 20 T HTS dipole magnet, develop 10 kA cable.
REBCO (rare earth barium copper oxyde) deposition on stainless substrate, tape arranged in Roebel cables.
values of 900-1200 A/mm2 at 4.2 K , 18-20 T have been obtained
Three technologies under consideration
1. NbTi (Niobium Titanium as in the LHC): mature but limited to about 9T field.
2. Nb3Sn (Niobium Tin) technology has seen a great boost in the past decade (factor 3 in JC w/r to ITER) but is not yet used in an accelerator – The HL-LHC upgrade will be the first one.
3. HTS (High-Temperature Superconductor) technology still in the experimental phase (Production quantities, homogeneity and cost need to evolve!) but can be a disruptive technology for future high-field magnets.
Right: layered structures with sections of different conductors
Left: new magnet designs are required for HTS
Courtesy L. Rossi, CERN

## Slide 20: The electric field frontier – superconducting cavities
Bulk Nb
Multi-layer
SRF Thin Film
TRENDS:
Nitrogen infusion process (FNAL) and other doping techniques: high Q operation, gradients ∼45 MV/m
Coating of Nb with a thin layer of Nb3Sn (allows operation at larger , improved cryogenic efficiency)
Coating of Cu cavites with Nb by HiPIMS (High Power Impulse Magnetron Sputtering,
Long-term goal: 60 → 90 MV/m

## Slide 21: The electric field frontier – normal conducting cavities
Pulsed systems, characterised by a BreakDown Rate (BDR), pulses lost because of vacuum arcing in the structure
Most advanced results by the Compact Linear Collider (CLIC) study based at CERN (X-band, 12 GHz)
Large international collaboration to understand the physics of breakdown phenomena.
100 MV/m gradient can be achieved (and exceeded)
… but power scales as the square of gradient! High gradient means smaller dimensions but higher power consumption.

## Slide 22: New acceleration techniques using lasers and plasmas
Accelerating field of today’s RF cavities or microwave technology is limited to <100 MV/m
  Several tens of kilometers for future linear colliders
Plasma can sustain up to three orders of magnitude much higher gradient
  SLAC (2007): electron energy doubled from 42GeV to 85 GeV over 0.8 m  52GV/m gradient
Lasers can produce huge transverse electric fields (TV/m !)
Can we convert the transverse fields into longitudinal and use them for acceleration?
(1) Micro/Nano-Accelerators
(2) Plasma Accelerators
Use a plasma to convert the transverse electrical field of the laser (or the space charge force of a beam driver) into a longitudinal electrical field, by creating plasma waves.
The «accelerator on a chip»
Send THz Laser into Dielectric Waveguide (Micro-Accelerator)

## Slide 23: A plasma-based linear collider?
Main challenges
W.P. Leemans & E. Esarey, Physics Today, March 2009
HALHF:

## Slide 24: Other options for high energy: muon collider
Colliding muons:
Muons are leptons, similar to electrons but heavier (207 times),
produced by pion decay or electron/positron annihilation, have a lifetime of only 2.2 ms.
Muon production complex
Muon acceleration complex
Neutrino radiation
Good in term of power/luminosity, potential for cost savings
Many critical technical challenges requiring R&D

## Slide 25: Accelerators for society
The Economist, October 2013

## Slide 26: Accelerators for medicine and industry
26
>35000 accelerators in use world-wide:
  44% for radiotherapy
  41% for ion implantation
  9% for industrial applications
  4% low energy research
  1% medical isotope production
  <1% research
Treating cancer
Making better semi-conductors
“Curing” materials:
sterilisation; carbon dating; treating flue gases or water; etc
Microanalysis of materials, mass spectroscopy, PIXE, etc
PET and SPECT medical imaging
Radiotherapy electron linac
Proton cyclotron for radioisotope production
The IBA Rhodotron for production of intense electron beams
A commercial system for ion implantation
A tandem accelerator for material and artwork analysis

## Slide 27: Particle accelerators: a formidable tool for medicine
Particles beams can activate nuclei generating radiation that can destroy cancerous cells or be detected from outside.
The energy deposited by a proton or ion beam has a well-defined peak (Bragg peak) inside the body: destroys the cancer cells with minimum damage to other tissues.
Accelerators realise the old dream of a bloodless surgery and imaging: penetrate into the human body to treat diseases and to observe internal organs without using surgical tools.
≈ 16’000 particle accelerators operating for medicine worldwide, in cancer therapy and imaging
M. Vretenar | NIMMS
Notes: One step back

## Slide 28: Treating cancer with particle beams
5 – 25 MeV e-beam
Tungsten target
>14,000 in operation worldwide!
Electron Linac (linear accelerator) for X-ray radiation therapy of cancer
Proton Cyclotrons and Ion (Carbon) synchrotrons for particle therapy of cancer
Different from X-rays, protons and ions deposit their energy at a given depth inside the tissues, minimising the dose to the organs close to the tumour. (“Bragg peak”)
>150 centres for protons, 12 for carbon

## Slide 29: Environmental applications of accelerators
Low-energy electrons can break molecular bonds and be used for:
Flue gas treatment (cleaning of SOx from smokes of fossil fuel power plants)
Wastewater and sewage treatment
Treatment of marine diesel exhaust gases (removal of SOx and NOx).
150 kV electron accelerator to break the high order molecules that are then cleaned by a water jet (scrubber)
Hybrid Exhaust Gas Cleaning Retrofit Technology for International Shipping (HERTIS)
A project based on a patent from INCT Warsaw promoted by a collaboration of research institutions (including CERN), accelerator industry, shipyards, maritime companies, maritime associations (Germany, UK, Switzerland, Poland, Latvia, Italy).
From engine
To air
Testing on a tugboat at Riga shipyard, 5.07.2019

## Slide 30: Accelerators for art
particle accelerator
particle beam
Emission of radiation of characteristic energies (X-rays, g, particles…)
Radiation detection and spectral analysis
Ion Beam Analysis (e.g. PIXE, Proton Induced X-ray Emission)
A beam of particles (protons) from an accelerator is sent on a sample (e.g. a painting)
The atoms are excited and emit different types of radiation (X-rays, gammas, etc.)
Different atomic elements emit X-rays at different energies – Spectral analysis from one or more detectors allows determination of the chemical composition (e.g. of the pigments).
Ritratto Trivulzio by Antonello da Messina, 1476 – analysis at INFN-LABEC (Florence)
2 m
Portable PIXE system based on an RFQ linac built by CERN and LABEC

## Slide 31: Some conclusions - at the roots of innovation
Particle accelerators are facing a critical moment in their evolution.
The expectations on accelerators from basic science, applied science, medicine and industry are increasing but some of our technologies are still the same as Widerøöe’s invention almost 100 years ago.
There is today a lot of space and encouragement for innovative ideas!
But what are the ingredients of innovation? Remember the first slide on Widerøe’s invention:
  Merge inputs from different science and technology fields (look around you!)
  Challenge the established traditions (but respect experience!)
  Take risks (but foresee mitigations!)
The 4 industrial revolutions (4th still ongoing!)
Image credit: B. Horvath, S. Mundi, 2018
Particle accelerators can become crucial actors of the
4th industrial revolution
allowing industry and medicine to exploit technologies based on subatomic particles
Dimensions: chemistry/molecule physics/electrons physics/atoms physics/subatomic level

## Slide 32: Some final words…
Particle accelerators are a vibrant and growing field, in full transition from basic science to applied science and to wider societal applications.
But to drive this transition and to push further the frontiers of accelerators we need fresh ideas, technology jumps, and (why not!), some change in paradigm.
The secret for the success are novel ideas by young people developed in a collaborative environment, jumping across borders between different scientific fields.
To achieve these goals, we need multinational research programmes with wide support from governments and scientific communities, but above all…
Thank you for your attention! maurizio.vretenar@cern.ch