## Slide 1
Derive the general expression of the transit time factor of an accelerating gap of length L, with constant accelerating field, in which the field is oscillating at fRF and that accelerate particles with relativistic factor β.
Remembering that the light wavelength in free space is given by RF=c/fRF, for which value of the accelerating gap length L, T is equal to zero?
Calculate the numerical value of T for L=10 cm, fRF=1 GHz and ultra-relativistic electrons (β=1).
Calculate the accelerating voltage as a function of the gap length L assuming an injection phase on crest (inj=0)
EXERCISE 1: TRANSIT TIME FACTOR

## Slide 2
We consider now the acceleration between two electrodes fed by an RF generator
Ez
source
z
z
gap
RF ACCELERATION: ENERGY GAIN
-L/2
+L/2
Hyp. of symmetric accelerating field
Peak gap voltage
T<1
Transit time factor
Injection phase
Average accelerating field in the gap
Average accelerating field seen by the particle
t=z/v

## Slide 3
EXERCISE 1: SOLUTION
z
-L/2
+L/2
It is equal to zero when
Numerical calculation

## Slide 4
= =
Very small accelerating gaps for low beta particles
Total accelerating voltage

## Slide 5
A proton beam is injected into a DTL (Alvarez structure) working at fRF=300 MHz, with a kinetic energy Win=4 MeV. Calculate:
the distance between the first two centers of the accelerating gaps (Lgaps) assuming a constant velocity of the proton beam between the first two gaps and a negligible increase of the velocity due to the accelerating field;
if the structure is composed by 40 accelerating gaps (Ngaps) and the average accelerating voltage per gap is Vacc=0.5 MV, calculate final proton beam kinetic energy.
EXERCISE 2: ALVAREZ STRUCTURES
REMEMBER
proton rest energy m0_pc2=E0_p=938 MeV
velocity of light c=2.998e8

## Slide 6
Alvarez's structure can be described as a special DTL in which the electrodes are part of a resonant macrostructure.
ALVAREZ STRUCTURES
The DTL operates in 0 mode for protons and ions in the range =0.05-0.5 (fRF=50-400 MHz, RF=6-0.7 m) 1-100 MeV;
The beam is inside the “drift tubes” when the electric field is decelerating. The electric field is concentrated between gaps;
The drift tubes are suspended by stems;
Quadrupole (for transverse focusing) can fit inside the drift tubes.
In order to be synchronous with the accelerating field at each gap the length of the n-th drift tube Ln has to be:
Ez
z
© Encyclopaedia Britannica, inc
(protons and ions)

## Slide 7
EXERCISE 2: SOLUTIONS
RF=c/fRF=0.9993m
in=(Win+E0_p)/E0_p=1.0043
βin=sqrt(1-1/in^2)= 0.0921
Lgaps=βinRF=92 mm
Wfin = Win +qNgaps*Vacc=24 MeV

## Slide 8
EXERCISE 3: ALVAREZ STRUCTURES AND TRANSIT TIME FACTOR
Particles at β=0.5 are accelerated through an ideal DTL operating at fRF=400 MHz. Assuming a uniform accelerating RF field (ERF) along the gap, calculate the accelerating gap length (L) that maximize the energy gain of the accelerated particles.

## Slide 9
EXERCISE 3: SOLUTIONS
Maximum energy gain when:
The energy gain as a function of L oscillates

## Slide 10
A SW cavity is feed by an RF generator with constant power, calculate after how much time the field in the cavity is 90% the field at full regime supposing that the cavity operate at fRF=1.3 GHz and has an equivalent Q factor of 10000.
EXERCISE 4: FILLING TIME

## Slide 11
SW CAVITIES : FILLING TIME AND DISSIPATED POWER
Time domain
FILLING TIME
Prefl to the generator (it that has to be protected!)
Pdiss 1/Q
One needs several filling times to completely fill the cavity
Let us now consider the case of a cavity powered by a source (klystron) in pulsed mode at a frequency fRF=fres. The accelerating voltage has an exponential behavior and reach the steady state regime asymptotically with a certain filling time (F) that is proportional to the quality factor of the resonator.
The reachable Vacc for a given power is proportional to Q but, on the other hand, the filling time is Q
[MV]
Example:
  Q10000
fRF=1 GHz
F=3.1 s
To reach a given voltage the required power is inversely proportional to the Q-factor

## Slide 12
EXERCISE 4: SOLUTION

## Slide 13
A -mode structure, operating at fRF=400 MHz, is made up of N=8 cells and is used to accelerate protons. Each single cell has a shunt impedance R=3 M and a length Lcell=15 cm. Calculate:
the total shunt impedance of the -mode structure;
the accelerating voltage if the total dissipated power into the cavity is Pdiss=1 MW;
the average accelerating field;
the average  of the proton beam accelerated by this structure.
EXERCISE 5:  MODE STRUCTURES

## Slide 14
MULTI-CELL SW CAVITIES
R
nR
In a multi-cell structure there is one RF input coupler. As a consequence the total number of RF sources is reduced, with a simplification of the layout and reduction of the costs;
The shunt impedance is n time the impedance of a single cavity
They are more complicated to fabricate than single cell cavities;
The fields of adjacent cells couple through the cell irises and/or through properly designed coupling slots.
Pin
.
Pin
(electrons or protons and ions at high energy)

## Slide 15
QUALITY FACTOR
SHUNT IMPEDANCE
The shunt impedance is the parameter that qualifies the efficiency of an accelerating mode. The highest is its value, the larger is the obtainable accelerating voltage for a given power. Traditionally, it is the quantity to optimize in order to maximize the accelerating field for a given dissipated power:
ACCELERATING VOLTAGE (Vacc)
DISSIPATED POWER (Pdiss)
STORED ENERGY (W)
  NC cavity Q104
  SC cavity Q1010
The R/Q is a pure geometric qualification factor. It does not depend on the cavity wall conductivity. R/Q of a single cell is of the order of 100.
  NC cavity R1M
SW CAVITIES PARAMETERS: R, Q, R/Q
  SC cavity R1T
SHUNT IMPEDANCE PER UNIT LENGTH
Example:
  R1M
Pdiss=1 MW
Vacc=1MV
For a cavity working at 1 GHz with a structure length of 10 cm we have an average accelerating field of 10 MV/m

## Slide 16
MULTI-CELL SW CAVITIES:  MODE STRUCTURES
The N-cell structure behaves like a system composed by N coupled oscillators with N coupled multi-cell resonant modes.
The modes are characterized by a cell-to-cell phase advance given by:
.
The multi cell mode generally used for acceleration is the , /2 and 0 mode (DTL as example operate in the 0 mode).
The cell lengths have to be chosen in order to synchronize the accelerating field with the particle traveling into the structure at a certain velocity
Ez
z
Ez
z
0 mode
 mode
For ions and protons the cell lengths have to be increased along the linac that will be a sequence of different accelerating structures matched to the ion/proton velocity.
For electron, =1, d=RF/2 and the linac will be made of an injector followed by a series of identical accelerating structures, with cells all the same length.
(electrons or protons and ions at high energy)
EXAMPLE: 4 cell cavity operating on the -mode

## Slide 17
EXERCISE 5: SOLUTION
1) RTOT=N*Rcell=24 M
2) Vacc=sqrt(RTOT*Pdiss)=4.9 MV
3) Eacc=Vacc/(Lcell*N)=4.08 MV/m
4) βin =2*Lcell /RF=0.4
being
RF=c/fRF=0.7495 m

## Slide 18
Exercise 6: TW STRUCTURES
B) Demonstrate that if we define the shunt impedance per unit length as:
the accelerating field “seen” by an ultrarelativistic particle (z=ct) along the structure can be expressed as:
A) Demonstrate that if we define the attenuation constant as:
the power flow along the structure scales as:
C) Demonstrate that the total accelerating voltage is given by:

## Slide 19
TW CAVITIES PARAMETERS: r, , vg
Similarly to the SW cavities it is possible to define some figure of merit for the TW structures
Group velocity [m/s]: the velocity of the energy flow in the structure (1-2% of c).
Shunt impedance per unit length [/m]. Similarly to SW structures the higher is r, the higher the available accelerating field for a given RF power.
Field attenuation constant [1/m]: because of the wall dissipation, the RF power flux and the accelerating field decrease along the structure.
Working mode [rad]: defined as the phase advance over a period D. For several reasons the most common mode is the 2/3

## Slide 20
TW CAVITIES: EQUIVALENT CIRCUIT AND FILLING TIME
In a TW structure, the RF power enters into the cavity through an input coupler, flows (travels) through the cavity in the same direction as the beam and an output coupler at the end of the structure is connected to a matched power load.
If there is no beam, the input power, reduced by the cavity losses, goes to the power load where it is dissipated.
In the presence of a large beam current, however, a fraction of the TW power is transferred to the beam.
In a purely periodic structure, made by a sequence of identical cells (also called “constant impedance structure”),  does not depend on z and both the RF power flux and the intensity of the accelerating field decay exponentially along the structure :
The filling time is the time necessary to propagate the RF wave-front from the input to the end of the section of length L is:
L
Differently from SW cavities after one filling time the cavity is completely full of energy

## Slide 21
Exercise 6: SOLUTION
A)
B)
C)
z
z+dz
PF(z)
PF(z+dz)
pdissdz

## Slide 22
A SLAC-type TW structure accelerate ultra-relativistic electrons. The structure length is L=3m and it can be simplified as a structure with a group velocity is vg=1.1% the velocity of light. Calculate:
the filling time;
if we suppose that the structure has a field attenuation constant =0.2 m-1, calculate the total accelerating voltage if the accelerating field at the beginning of the structure is EINPUT=20 MV/m;
Calculate the average accelerating field
if the average dissipated power per unit length in the structure, corresponding to the previous value of the accelerating field, is pdiss= 4 MW/m calculate the shunt impedance per unit length.
Exercise 7: TW STRUCTURES

## Slide 23
TW CAVITIES PARAMETERS: r, , vg
Similarly to the SW cavities it is possible to define some figure of merit for the TW structures
Group velocity [m/s]: the velocity of the energy flow in the structure (1-2% of c).
Shunt impedance per unit length [/m]. Similarly to SW structures the higher is r, the higher the available accelerating field for a given RF power.
Field attenuation constant [1/m]: because of the wall dissipation, the RF power flux and the accelerating field decrease along the structure.
Working mode [rad]: defined as the phase advance over a period D. For several reasons the most common mode is the 2/3

## Slide 24
TW CAVITIES: EQUIVALENT CIRCUIT AND FILLING TIME
In a TW structure, the RF power enters into the cavity through an input coupler, flows (travels) through the cavity in the same direction as the beam and an output coupler at the end of the structure is connected to a matched power load.
If there is no beam, the input power, reduced by the cavity losses, goes to the power load where it is dissipated.
In the presence of a large beam current, however, a fraction of the TW power is transferred to the beam.
In a purely periodic structure, made by a sequence of identical cells (also called “constant impedance structure”),  does not depend on z and both the RF power flux and the intensity of the accelerating field decay exponentially along the structure :
The filling time is the time necessary to propagate the RF wave-front from the input to the end of the section of length L is:
L
Differently from SW cavities after one filling time the cavity is completely full of energy

## Slide 25
Exercise 7: SOLUTION
1) L=3;  tF=L/vg=909.7 ns
2)
3) Eacc=Vacc/L=15 MV/m
4) r=Eacc^2/pdiss=56.5 M/m

## Slide 26
A constant impedance TW structure, accelerates ultra-relativistic electrons (β=1). The cavity has the following parameters: =0.25 m-1 ; shunt impedance r=65 MOhm/m and a total length of 2 m. Calculate:
the input power to have an energy gain of the particles of 60 MeV
if the group velocity vg is 1% the speed of light, which is the filling time of the structure?
Exercise 8: TW STRUCTURES

## Slide 27
Exercise 8: SOLUTION
1)
2) tF=L/vg=667 ns

## Slide 28
A multi cell SW cavity, operating on the -mode at 1 GHz, accelerates protons at β=0.5. The cavity is a 9 cell structure. Assuming a negligible variation of the particle velocity through the cavity itself calculate:
the distance between the centers of the accelerating cells;
assuming a shunt impedance of the single cell (R) of 1 M, calculate the dissipated power to have a peak accelerating voltage on the overall structure of Vacc=10 MV;
Calculate the maximum average accelerating field;
If the cavity is fed by 4 s rf pulses with a repetition rate of 100 Hz, calculate the Duty Cycle.
EXERCISE 9:  MODE STRUCTURES AND DUTY CYCLE

## Slide 29
RF STRUCTURE AND BEAM STRUCTURE: NC vs SC
The “beam structure” in a LINAC is directly related to the “RF structure”. There are two possible type of operations:
CW (Continuous Wave) operation  allow, in principle, to operate with a continuous (bunched) beam
PULSED operation  there are RF pulses at a certain repetition rate (Duty Cycle (DC)=pulsed width/period)
SC structures allow operation at very high Duty Cycle (>1%) up to a CW operation (DC=100%) (because of the extremely low dissipated power) with relatively high gradient (>20 MV/m). This means that a continuous (bunched) beam can be accelerated.
NC structures can operate in pulsed mode at very low DC (10-2-10-1 %) (because of the higher dissipated power) with, in principle, larger peak accelerating gradient(>30 MV/m). This means that one or few tens of bunches can be, in general, accelerated. NB: NC structures can also operate in CW but at very low gradient because of the dissipated power.
Bunch spacing
RF pulses
RF power
t
Amplitude
103-108 RF periods
time

## Slide 30
EXERCISE 9: SOLUTION
1)
2)
RTOT=N*R=9 M
Pdiss=Vacc^2/RTOT=11.1 MW
3)
LTOT=d*N=67.4 cm
Eacc=Vacc/LTOT=14.8 MV/m
4)
DC=Timp/Tperiod=4e-6/0.01=4e-4 (0.04%)

## Slide 31
A RF accelerating structure operating at fRF=400 MHz, is used to accelerate protons at an input nominal kinetic energy Win=10 MeV. Assuming that the nominal synchronous phase s=-/6 and that the average accelerating field is Eacc=2 MV/m, calculate the maximum kinetic energy of the protons that is possible to capture in the RF bucket (assuming that it is injected at a phase corresponding to the synchronous one).
EXERCISE 10: energy acceptance

## Slide 32



s
-s
To study the longitudinal dynamics at large oscillations, we have to consider the non linear system of differential equations without approximations. In the adiabatic acceleration case it is possible to easily obtain the following relation between w and  that is the Hamiltonian of the system related to the total particle energy:
APPENDIX: LARGE OSCILLATIONS AND SEPARATRIX
For each H we have different trajectories in the longitudinal phase space
the oscillations are stable within a region bounded by a special curve called separatrix: its equation is:
the region inside the separatrix is called RF bucket. The dimensions of the bucket shrinks to zero if s=0.
trajectories outside the RF buckets are unstable.
we can define the RF acceptance as the maximum extension in phase and energy that we can accept in an accelerator:
Small amplitude oscillations
RF bucket

## Slide 33
EXERCISE 10: SOLUTION
in=(Win+E0_P)/E0_P=1.0107
βin=sqrt(1-1/in^2)= 0.1449
WMAX=Win+w=10.362 MeV

## Slide 34
Exercise 11: low energy electrons
An electron beam generated by a DC gun at 40 keV is directly accelerated by a TW structure. Calculate the minimum accelerating field needed to capture the beam, assuming an operating frequency of 6 GHz and a final fin equal to 1.
If the accelerating field is twice the minimum accelerating field, what is the final phase (fin) with respect to the accelerating field of a particle injected at in=-/2?

## Slide 35
LONGITUDINAL DYNAMICS OF LOW ENERGY ELECTRONS: PHASE SPLIPPAGE
The accelerating field of a TW structure can be expressed by
The equation of motion of a particle with a position z at time t accelerated by the TW is then
It is useful to find which is the relation between  and  from an initial condition (in) to a final one (fin)
Suppose that the particle reach asymptotically the value fin=1 we have:

Eacc
in
in
fin
fin=1
z
Eacc
Should be in the interval [-1,1] to have a solution for fin
This quantity is >0
This limits the possible injection phases (i.e. the phase of the electrons that is possible to capture)
We always have that

## Slide 36
Where RF=c/fRF=0.05 m, E0=0.51 MeV and in can be calculated as follows:
in=(Win+E0_e)/E0_e=1.078
βin=sqrt(1-1/in^2)= 0.374
substituting we obtain
The final phase is given by:
EXERCISE 11: SOLUTION

Eacc
in
in
fin
fin=1

Eacc
in
in
fin
fin=1

## Slide 37
A DTL (Alvarez structure) working at fRF=300 MHz accelerate protons with an injection energy Win=4 MeV, permanent magnet quadrupoles are inside the drift tubes and the focusing system is equivalent to a FODO lattice, as sketched below. The quadrupoles inside the drift tubes have a length LQ=5 cm.
If the average accelerating field per cell is Eacc=2 MV/m and the nominal synchronous phase S=-/6, calculate, using the “smooth approximation” approach, the quadrupole gradient (G) that is necessary to have, in the first cells, of the structure in order to achieve a transverse phase advance per period () equal to /3, supposing that the period of the FODO (LP) is exactly twice the distance between two accelerating gaps.
Exercise 12: transverse beam dynamics
proton rest energy m0c2=E0=938 MeV
velocity of light c=2.998e8

## Slide 38
SMOOTH APPROXIMATION OF TRANSVERSE OSCILLATIONS
In case of “smooth approximation” of the LINAC (we consider an average effect of the quadrupoles and RF) we obtain a simple harmonic motion along s of the type ( is constant):
Phase advance per unit length (/Lp)
Magnetic focusing elements (for a FODO)
RF defocusing term
If we consider also the Space Charge contribution in the simple case of an ellipsoidal beam (linear space charges) we obtain:
I= average beam current (Q/TRF)
rx,y,z=ellipsoid semi-axis
f= form factor (0<f<1)
Z0=free space impedance (377 Ω)
Space charge term
For ultrarelativistic electrons RF defocusing and space charge disappear and the external focusing is required to control the emittance and to stabilize the beam against instabilities.
G=quadrupole gradient [T/m]
l=quadrupole length
NB: the RF defocusing term f sets a higher limit to the working frequency
Lp
l

## Slide 39
Exercise 11: transverse beam dynamics
RF=c/fRF=0.9993m
in=(Win+E0_P)/E0_P=1.0043
βin=sqrt(1-1/in^2)= 0.0921
L_gaps=βinRF=92 mm
LP=2*Lgaps=184 mm
K0=(/3)/LP=5.69 m-1