## Slide 1
Exercises for Beam Diagnostics
JUAS 2025, ESI-Archamps at CERN
Peter Forck (GSI and University Frankfurt)

## Slide 2
Exercise #12: Beam diagnostics design for a proton facility
RFQ-LINAC
DTL-LINAC
proton source on U = 100 kV
Imax=50mA, Imin=0.1µA
tpulse=1ms, repetitions 1s
transverse size:  = 5 mm
bunch length:
bunch = 100 of rf
Ekin= 3 MeV
experiment
Ekin= 100 MeV
facc= 300 MHz
transverse: =2mm
bunch length:
bunch = 100 of rf

## Slide 3
Exercise #12: Beam diagnostics design for a proton facility
RFQ-LINAC
DTL-LINAC
proton source on U = 100 kV
Imax=50mA, Imin=0.1µA
tpulse=1ms, repetitions 1s
transverse size: =5mm
bunch length:
bunch = 100 of rf
Ekin= 3 MeV
experiment
Ekin= 100 MeV
facc=300 MHz
Tune: Qx = 4.28, Qy = 3.22
Bunch length: bunch = 200 of rf
trans. size: x =5…3 mm
transverse: =2mm
bunch length:
bunch = 100 of rf
1st synchrotron
l = 200 m
Ein = 100 MeV, Eout= 1 GeV
0.76 s < trev < 1.6 s
Imax = 1012 protons
2.57MHz< facc<5.25MHz  4 bunches

## Slide 4
Exercise #12: Beam diagnostics design for a proton facility
experiment:
fast extraction
4 bunches within 0.7 s
RFQ-LINAC
DTL-LINAC
proton source on U = 100 kV
Imax=50mA, Imin=0.1µA
tpulse=1ms, repetitions 1s
transverse size: =5mm
bunch length:
bunch = 100 of rf
Ekin= 3 MeV
experiment
Ekin= 100 MeV
experiment:
slow extraction
1s extraction
facc=300 MHz
HEBT
length 300 m
transverse: =2mm
bunch length:
bunch = 100 of rf
trans. size:
x=5 …3 mm
Tune: Qx = 4.28, Qy = 3.22
Bunch length: bunch = 200 of rf
trans. size: x =5…3 mm
1st synchrotron
l = 200 m
Ein = 100 MeV, Eout= 1 GeV
0.76 s < trev < 1.6 s
Imax = 1012 protons
2.57MHz< facc<5.25MHz  4 bunches

## Slide 5
Exercise #12: Beam diagnostics design for a proton facility
experiment:
fast extraction
4 bunches within 0.7 s
RFQ-LINAC
DTL-LINAC
proton source on U = 100 kV
Imax=50mA, Imin=0.1µA
tpulse=1ms, repetitions 1s
transverse size: =5mm
bunch length:
bunch = 100 of rf
Ekin= 3 MeV
experiment
Ekin= 100 MeV
2nd synchrotron
l = 2200 m
Ein = 1 GeV, Efinal = 100 GeV
7.3 µs < trev < 8.4 s
Imax = 1013 protons
5.25 MHz < facc < 6.00 MHz
( complete filling 40 bunches)
experiment:
slow extraction
1s extraction
facc=300 MHz
HEBT
length 300 m
transfer from 1st synchrotron:
10 x 4 bunches within 0.7 s
Tune: Qx = 20.28, Qy = 18.22
Bunch length: bunch = 200 of rf
trans. size: x =3…1 mm
transverse: =2mm
bunch length:
bunch = 100 of rf
trans. size:
x=5 …3 mm
1st synchrotron
l = 200 m
Ein = 100 MeV, Eout= 1 GeV
0.76 s < trev < 1.6 s
Imax = 1012 protons
2.57MHz< facc<5.25MHz  4 bunches
Tune: Qx = 4.28, Qy = 3.22
Bunch length: bunch = 200 of rf
trans. size: x =5…3 mm

## Slide 6
Exercise #13: Beam diagnostics design for a LINAC FEL
photo electron source
within rf-gun
facc= 1 GHz
1st LINAC
facc= 1 GHz
Ekin= 7 MeV
trans = 100 µm
long = 100 ps
Qbunch = 100 pC
1st bunch compressor
2nd bunch compressor
undulator
beam dump
SASE:
X-ray  =1 nm
Ekin= 0.5 GeV
trans = 100 µm
long = 100 ps
trans = 100 µm
long = 1 ps
Ekin= 5 GeV
trans = 10 µm
long = 10 ps
trans = 10 µm
long = 100 fs
2nd LINAC
facc= 3 GHz
Mode 1: Singh-bunch
Mode 2: 100 bunches, 50 ns spacing
Charge per bunch: Qbunch = 100 pC
laser

## Slide 7
Exercise #12: Beam diagnostics design for a proton facility
Now your task:
Step 1: Please form 4 groups for protons and 5 groups including the LINAC FEL
(group1: LINAC, group2: 1st synchrotron, group3: HEBT line, group4: 2nd synchrotron)
Step 2: Review the beam properties and the requirements for the diagnostics
Step 3: Chose appropriate beam instrumentation for beam measurements
(You might form sub-groups to share the work)
Step 4: Summarize your results and prepare a presentation of your results
Step 5: Present your results in the lecture room (including possible open topics…),
duration about 3 min + 3 min questions & answers
If you have any question, remark, comment, doubt, disagreements ….
Please ask me at any time (moreover, I will pass the rooms regularly)
Or ask the other groups on the requirements for their facility part
Meeting for presentation: about 11:15

## Slide 8
The following slides discusses exercises inactively.
These exercises discussed here are also given
in the written exercises document
Some slides from the lecture are included
as relevant for the exercise
Some more information are complied in addition

## Slide 9
Fast, Flying Wire Scanner
In a synchrotron one wire is scanned though the beam as fast as possible.
Fast pendulum scanner for synchrotrons; sometimes it is called ’flying wire’:
From https://twiki.cern.ch/twiki/
bin/viewauth/BWSUpgrade/
injection
extraction
particle
detector
synchrotron
Scanners used as
reference method!
scanner

## Slide 10
Usage of Flying Wire Scanners
Material: carbon or SiC  low Z-material for low energy loss and high temperature.
Thickness: down to 10 μm  high resolution.
Detection: High energy secondary particles with a detector like a beam loss monitor
Proton impact on
scanner at CERN-PS Booster:
Secondary particles:
Proton beam → hadrons shower (π, n, p...)
Electron beam → Bremsstrahlung photons.
Rest mass:
m± = 140 MeV/c2
m0 = 135 MeV/c2
Kinematics of flying wire:
Velocity during passage typi. 10 m/s = 36 km/h & typical beam size  10 mm
 time for traversing the beam t  1 ms
Challenges: Wire stability for fast movement with high acceleration
U. Raich et al., DIPAC 2005
rotating
wire
rotation
beam
scintillator
photo
multiplier
ADC
A
D
motor
position
encoder
computer
shower
vacuum tube

## Slide 11
Exercise #7: Transverse profile by flying wire scanner
Assume a beam of 1012 protons at 1GeV stored in a synchrotron.
The beam size 10 x 10 mm2 with ρbeam=const (for simplification), the revolution time is 1.0 μs.
The wire is made of Carbon with 50 x 50 μm2 and scanned with v =10 m/s.
[Carbon is light material of ρ=2.2 g/cm3 density therefore low stopping power.]
The energy loss is dE/ dx= 4.29 MeV/cm.
Assumptions: rectangular beam and wire, no betatron oscillations.
beam
dbeam
= 10 mm
wire scanned with v = 10 m/s
thickness x = 50 µm
x = 50 µm
Movement for distance x = 50 µm
within tx= x / v = 5 µs
beam: circulates in synchrotron with trev = 1 µs
Basic question:
Does the beam survive and wire the scan?

## Slide 12
Exercise #7: Transverse profile by flying wire scanner 1/3
Calculate the relative energy loss per passage through the wire!
Calculate the average energy loss during the scan! How many passages an ion does in average?
Is this device nearly ‘non-destructive’  Are the particles lost?
Result: Energy loss for one passage:
time to move by one wire thickness of x = 50 µm:
average numbers of passages: , total time for the scan:
Proton’s energy loss: =
i.e. lower than typical longitudinal acceptance i.e. beam survives
Assume a beam of 1012 protons at 1GeV stored in a synchrotron.
The beam size 10 x 10 mm2 with ρbeam=const (for simplification), the revolution time is 1.0 μs.
The wire is made of Carbon with 50 x 50 μm2 and scanned with v =10 m/s.
[Carbon is light material of ρ=2.2 g/cm3 density therefore low stopping power.]
The energy loss is dE/ dx= 4.29 MeV/cm.

## Slide 13
Result: Energy loss for one passage:
average numbers of passages:
Total energy , total power
power per mm: i.e. on the border
 more realistic calculations required
Role of thumb: The maximum power rate to prevent for destruction is about 1 W/mm.
Is the wire destroyed?
Exercise #7: Transverse profile by flying wire scanner 2/3
Assume a beam of 1012 protons at 1GeV stored in a synchrotron.
The beam size 10 x 10 mm2 with ρbeam=const (for simplification), the revolution time is 1.0 μs.
The wire is made of Carbon with 50 x 50 μm2 and scanned with v =10 m/s.
[Carbon is light material of ρ=2.2 g/cm3 density therefore low stopping power.]
The energy loss is dE/ dx= 4.29 MeV/cm.

## Slide 14
Modification of wire thickness due to sublimation
Exercise #7: Transverse profile by flying wire scanner: Example
Example of thinning at LHC
with 1.51013 protons at 3.5 TeV,
slower scan v = 5 cm/s
Example of thinning at SPS
with Pb82+ impact
slow scan v = 2 cm/s
Min. thickness 4 µm
B. Sapinski, Proc. BIW 2012

## Slide 15
Mechanical realization of a
flying wire scanner
Exercise #7: Transverse profile by flying wire scanner: Example
B. Dehning, Proc. HB 2016

## Slide 16
Assume a beam of 109 Uranium (mass 238 amu, nucl. chrage Z=92) ions at 1GeV/u stored.
The beam size 10x10 mm with ρbeam=const (for simplification), the revolution time is 1.0 μs.
The wire is made of Carbon with 50x50 μm and scanned with v=10 m/s.
The energy loss is dE/dx= 35640 MeV/cm (instead 4.29 MeV/cm for protons as dE/dx  Z2 ).
Why is the energy loss so much larger?
Are the particles lost? Is the wire destroyed? Repeat the same calculation for this case!
What happens for not fully stripped ions (i.e. ions with some bound electrons)?
What is an appropriate method of profile determination for the Uranium case?
Result: Energy loss for one passage:
i.e. for Uranium after one passage
out for longitudinal acceptance
beam is lost during scan!
Result: Energy deposition in the wire
is significantly higher than destruction level
 the wire is destroyed!
Exercise #7: Transverse profile by flying wire scanner 3/3

## Slide 17
Ionization Profile Monitor at GSI Synchrotron
Non-destructive device for proton synchrotron:
beam ionizes the residual gas by electronic stopping
gas ions or e- accelerated by E -field 1 kV/cm
spatial resolved single particle detection
One device per plane
Realization at GSI synchrotron:
Typical vacuum pressure:
Transfer line: N2 10−8... 10−6 mbar  3108...31010cm-3
Synchrotron: H2 10−11...10−9 mbar  3105...3107 cm-3
beam
300 mm flange
MCP:
100 x 48 mm2
175
mm
175mm
63 wires,
2.1mm spacing
HV feedthru
R
voltage divider
+ 6 kV
+ 5 kV
+ 4 kV
+ 2 kV
+ 3 kV
+ 1 kV
0 kV
MCP
anode
position readout
HV electrode
ion
e.g. H+
beam

## Slide 18
Low Current Measurement for slow Extraction
Slow extraction from synchrotron: lower current compared to LINAC,
but higher energies and larger range R >> 1 cm.
Particle counting:
max: r ≃ 106 1/s
Energy loss in gas (IC):
min: Isec  1 pA
max: Isec  1 μA
Sec. e− emission:
min: Isec  1 pA
Max. synch. filling:
Space Charge Limit (SCL).
Particle detector technologies for ions of 1 GeV/u, A = 1 cm2:
Particles per second
injection
extraction
synchrotron
Scint., IC & SEM
Notes: 18

## Slide 19
GSI Installation for SEM, IC and Scintillator
IC in Ar-gas at 1 bar
SEM in vacuum
Feed-through with Ø 200 mm flange
IC
Scintillator
SEM
beam
gas filled
PMT
P. Forck et al., DIPAC’97
Notes: 19

## Slide 20
Ionization Chamber (IC): Electron Ion Pairs
Energy loss of charged particles in gases  electron-ion pairs  low current meas.
Example: GSI type:
W-value
is the average energy
for one e- -ion pair:
Gas | Ionization Pot. | W-value
He | 24.5 eV | 42.7 eV
N2 | 15.5 eV | 36.4 eV
O2 | 12.5 eV | 32.2 eV
Ar | 15.7 eV | 26.3 eV
CO2 | 13.7 eV | 33.0 eV
GSI realization:
Energy calculation dE/dx with SRIM or LISE
Current measurement via
current-to-frequency converter IFC
diameter 55 mm
Length x
2x 3.2 mm
Voltage:
UHV = 1 kV
Gas: 80% Ar + 20% CO2
Notes: 20

## Slide 21
Exercise #4: Slow Extraction Current Measurement 1/2
Assume a beam of Ni = 1.25·1012 protons extracted from a synchrotron within t = 1 s
The current should be measured by an ionization chamber of 0.5cm length filled with Ar
The average energy to create a ion-electron pair is W = 26.3 eV
The energy loss is dE/dx = 2.58 keV/cm
Calculate the ion-electron pairs per proton and the secondary current within the IC!
The energy loss (described by Bethe-Bloch equation ) scales with dE/dx  Zp2
Assume a beam of Ni = 1.8·1010 Uranium with Zp=92 extracted within 1 s
Calculate the ion-electron pair per proton and the secondary current within the IC!
The energy loss per Uranium is
The same calculation as above leads to i.e. saturation of the IC and a SEM is better!
The energy loss dE/dx of a proton is
With the average energy for one ion electron pair W, the number of pair is
For the extraction ions Ni per second the amount is
or a current of .

## Slide 22
Low Current Measurement for slow Extraction
Slow extraction from synchrotron: lower current compared to LINAC,
but higher energies and larger range R >> 1 cm.
Particle counting:
max: r ≃ 106 1/s
Energy loss in gas (IC):
min: Isec  1 pA
max: Isec  1 μA
Sec. e− emission:
min: Isec  1 pA
Max. synch. filling:
Space Charge Limit (SCL).
Particle detector technologies for ions of 1 GeV/u, A = 1 cm2:
Particles per second
injection
extraction
synchrotron
Scint., IC & SEM
Notes: 22

## Slide 23
Secondary Electron Monitor (SEM): Electrons from Surface
For higher intensities SEMs are used.
Due to the energy loss, secondary e− are emitted from a metal surface.
The amount of secondary e− is proportional to the energy loss
Sometimes they are installed permanently in front of an experiment.
It is a surface effect:
Sensitive to cleaning procedure
Possible surface modification by radiation
Example: GSI SEM type:
Advantage for Al: good mechanical properties.
Disadvantage: Surface effect!
e.g. decrease of yield Y due to radiation
 calibration versus IC required to reach 5%.
Material | Pure Al (99.5%)
# electrodes | 3
Active surface | 80 x 80 mm 2
Distance between electrodes | 5 mm
Applied volatage | + 100
CO2 | 13.7 eV
Notes: 23

## Slide 24
Exercise #3: Slow Extraction Current Measurement 2/2
Assume a beam of Ni = 1.25·1012 protons extracted from a synchrotron within 1 s
The current should be measured by an SEM
For Aluminium plates the secondary electron yield is Y = 27.4 e-/(MeV/mg/cm2)
The energy loss (frequently used units!) is dE/ρdx = 1.77 keV/(mg/cm2)
Calculate the electrons per proton and the secondary current emitted by the SEM!
The energy loss (described by Bethe-Bloch equation ) scales with dE/dx  Zp2
Assume a beam of Ni = 1.8·1010 Uranium with Zp=92 extracted within 1 s
Calculate the electron per Uranium and the secondary current by the SEM!
The secondary electrons for one proton is a proton is
this corresponds for an extraction Ni proton within t = 1s to a current of
The scaling of the energy loss is
with the number of Uranium per t = 1 s it is
 Flying wire

## Slide 25
Summary for Beam Profile
Different techniques are suited for different beam parameters:
e−-beam: typically Ø 0.01 to 3 mm, protons: typically Ø 3 to 30 mm
Intercepting  non-intercepting methods
Direct observation of electrodynamics processes:
Optical synchrotron radiation monitor: non-destructive, for e−-beams, complex, limited res.
X-ray synchrotron radiation monitor: non-destructive, for e−-beams, very complex
OTR screen: nearly non-destructive, large relativistic γ needed, e−-beams mainly
Detection of secondary photons, electrons or ions:
Scintillation screen: destructive, large signal, simple, all beams
Ionization profile monitor: non-destructive, expensive, limited resolution, for protons
Residual fluorescence monitor: non-destructive, limited signal strength, for protons
Wire based electronic methods:
SEM-grid: partly destructive, large signal and dynamic range, limited resolution
Wire scanner: partly destructive, large signal and dynamics, high resolution, slow scan.

## Slide 26
Beam Structure of a pulsed LINAC
Pulsed LINACs and cyclotrons used for injection
to synchrotrons with tpulse 100 s:
One distinguish between:
Mean current Imean
→ long time average in [A]
Pulse current Ipulse
→ during the macro pulse in [A]
Bunch current Ibunch
→ during the bunch in [C/bunch]
or [particles/bunch]
Remark: Van-de-Graaff (ele-static):
→ no bunch structure
Question:
What is the pulse structure of a beam within a synchrotron?
What does this means for beam current measurement?

## Slide 27
Passive Transformer (or Fast Current Transformer FCT)
Simplified electrical circuit of a passively loaded transformer:
A voltages is measured: U = R · Isec = R /N · Ibeam ≡ S · Ibeam
with S sensitivity [V/A],
equivalent to transfer function or transfer impedance Z
Equivalent circuit for analysis of sensitivity and bandwidth
(disregarding the loss resistivity RL)
beam

## Slide 28
Ibeam
Excurse: Time Domain  Frequency Domain
Time domain: Recording of a voltage as a function of time:
Frequency domain: Displaying of a voltage as a function of frequency:
Instrument:
Spectrum Analyzer
Fourier
Transformation:
Instrument:
Oscilloscope
Care: Fourier Transformation of time domain data contains amplitude and phase
courtesy company Keysight
voltage
time
frequency

## Slide 29
The spectrum analyzer determines the frequency spectrum of a signal:
Steps for an analog device:
Low pass filter, typ. f < 3 GHz
Mixing with
scanning local oscillator
Difference frequency by narrow
band pass filter, width typ.  1 kHz
Rectification  units W or dBm
Scan duration typically  1 s
i.e. averaging signal over many turns
Parameter to be chosen:
Reference level Pref [dBm]
Center frequency fLO = fcenter
Span fspan = fstop - fstart
Resolution bandwidth fres
i.e. band-pass filter width
Video bandwidth fvideo i.e. data smoothing
Sweep time tsweep
U
t
RF
IF
LO
input amp.
low pass
filter
mixer
band pass filter  fres
IF gain
amplitude
detector
video
filter fvideo
voltage controlled oscillator  fspan
display
 tsweep
Excurse: Basic Detection Instrument: Analog Spectrum Analyzer

## Slide 30
Steps for an digital, ‘real time’ device:
Low pass filter, typ. f < 3 GHz
Down mixing with
fixed local oscillator
IF filtering
Digitalization: some 10 MSa/s, 16 bit
FFT calculation with
various parameters, windowing, filter ...
Parameter to be chosen:
FFT parameter, windowing
digital filters
time window
Most often given in traditional parameters
reference level Pref [dBm]
Span fspan = fstop - fstart
Resolution bandwidth fres
RF
IF
LO
input amp.
low pass
filter
mixer
band pass filter
0.1 .... 10MHz
IF gain
ADC e.g.
 10 MSa/s
FFT
calc.
local
oscillator
display
A
D
FFT
data
treatm.
Excurse: Basic Detection Instrument: Digital Spectrum Analyzer
The spectrum analyzer determines the frequency spectrum of a signal:

## Slide 31
2π flow
=R/L
2πfhigh
=1/RCS
Time domain description:
Droop time: τdroop= 1/( 2πflow ) = L/R
Rise time: τrise = 1/( 2πfhigh ) = 1/RCS (ideal without cables)
Rise time: τrise = 1/(2π fhigh ) (with cables)
RL: loss resistivity, R: for measuring.
beam current
signal
baseline
Baseline: Ubase  1 - exp(-t/droop)
positive & negative areas are equal
Bunch train:
Response of the Passive Transformer: Rise and Droop Time
time
time
time
time
beam current
output volt.
test
pulse
beam bunch

## Slide 32
Exercise #3: Transformers for a pulsed LINAC 1/4
Assume a beam with 1 ms macro-pulse length at a LINAC
The current should be measured by a current transformer
The maximum droop should be 3% within 1 ms .
Calculate the required droop time constant and the lower cut-off frequency flow !
Core size: ri = 30 mm, ro = 60 mm, length l = 40 mm
Permeability of the core: µr = 105 (µ0 = 4π·10-7 Vs/Am)
Passive transformer with R = 1 kΩ termination, RL = 10 Ω loss resistivity
Calculate the number of winding for the given droop and the sensitivity [V/A]!
Hint: 1. Calculate the required inductance L:
2. The inductance of a core with N windings is:
Result: for t = 1 ms = 32 ms
cut-off frequency: = 4.9 Hz
Result: Inductance via  = 244
Sensitivity V/A
 Flying wire

## Slide 33
General Noise Sources
Any electronics is accompanied with noise due to:
Thermal noise as given by the thermal movement of
electrons described by Maxwell-Boltzmann distribution
Within resistive matter
average movement cancels Umean = < U > = 0
but standard deviation remains:
this is white noise i.e. no frequency dependence
kB Boltzmann constant, T temperature, R resistivity, f bandwidth
Maxwell-Boltzmann distribution:
Example: Maxwell-Boltzmann distribution of a free electron gas
Shot noise as given by the fluctuations of finite amount of electrons
for most electronics not important due to large amount of electrons
Flicker noise or ‘1/f - noise’ as given by trapping of electrons in matter
pink noise due to a frequency , ‘corner-frequency’ fc  3 kHz i.e. 1/f-noise = thermal noise
Disturbance by Electro-Magnetic Interference EMI:
Not noise but pick-up of electro-magnetic waves from the environment
leads unwanted signal deformation and depends on the surrounding
R
at T

## Slide 34
signal only
S/N=2
signal only
S/N=2
noise only
Excurse: Signal to Noise Consideration
The minimum noise is given thermal noise:
R is the input Ohmic resistor  input of a low-noise amplifier (realistic noise figure 2-3 x Ueff)
f is the bandwidth of the signal chain
Simulation:
Broadband ‘white’ noise
For Signal-to-Noise = 2
(Noise: std. deviation, signal: maximum)
 peak just visible
For Signal-to-Noise = 4
 peak well visible
Filtering improves S/N
here: n=50 taps moving average
 bandwidth restriction
sample
signal only
S/N=4
filtered
signal only
S/N=4
sample
Ueff

## Slide 35
Core size: ri = 30mm, ro = 60 mm, length l = 40 mm
Permeability of the core: µr = 105 (µ0 = 4π·10-7 Vs/Am)
Passive transformer with R = 1 kΩ termination, RL = 10 Ω loss resistivity
The upper cut-off frequency is fhigh = 100 kHz, the lower flow = 100 Hz, R is at T=300 K
Use Unoise = (4kB·T·R·Δf)1/2 and kB = 1.4·10-23 J/K, bandwidth Δf = fhigh - flow
Calculate the thermal noise contribution for a resistor at T=300 K!
Calculate the threshold concerning the beam current for a signal-to-noise ratio of S/N = 1!
Result: Thermal noise
Beam current for S/N=1 : Sensitivity
Exercise #3: Transformers for a pulsed LINAC 2/4
Assume a beam with 1 ms macro-pulse length at a LINAC
The current should be measured by a current transformer
The maximum droop should be 3% within 1 ms .
Flying wire

## Slide 36
‘Active’ Transformer with longer Droop Time
Active Transformer or Alternating Current Transformer ACT:
uses a trans-impedance amplifier (I/U converter) to R  0  load impedance i.e. a current sink
+ compensation feedback
 longer droop time τdroop
Application: measurement of longer t > 10 μs e.g. at pulsed LINACs
The input resistor is for an op-amp: Rf/A << RL
 τdroop = L/(Rf /A+RL) ≃ L/RL
Droop time constant can be up to 1 s!
The feedback resistor is also used for range switching.
An additional active feedback loop is used to compensate the droop.

## Slide 37
Operational Amplifier Principle
Operational Amplifier: Chips used as a simple equivalent circuit,
but has complex built-in electronics
Without feedback: Uout = gol ∙ ( U+ - U- )
Open loop gain: gol  104
With feedback: compensation of both inputs
Examples of applications:
Inverting voltage amplifier: Uout = g ∙ Uin = -R2 / R1 ∙ Uin
Current-to-voltage converter: Uout = - R ∙ Iin
i.e. feedback leads current sink at inverting input
U+
Uout
U-
Uout
Uin
Uout
Iin

## Slide 38
Excurse: Trans-impedance Amplifier = I/U Converter
Current-to-voltage converter: Ua = - R ∙ Ie  - Zt ∙ Ie Zt is called trans-impedance
i.e. feedback leads current sink at inverting input
Counteraction between
Current resolution
Time resolution
Uout
Iin
Zt [V/A] | 105 | 107 | 109 | 1011
Full scale | 100A | 1A | 10nA | 100pA
Bandwidth fcut [kHz] | 500 | 400 | 50 | 1.1
Risetime trise 10 to 90% | 0.7s | 0.9s | 7s | 300s
Equivalent input noise Noise/full-scale (rel.) Rel.to thermal noise | 10nA 10-4  1 | 450pA 2∙10-4  1 | 3.7pA 3∙10-4  1.6 | 0.8pA 10-3  10
 Flying wire

## Slide 39
As for the previous example: Assume a beam with 1 ms macro-pulse length at a LINAC
The current should be measured by current transformer
Core size: ri = 30mm, ro = 60 mm, length l = 40 mm
Permeability of the core: µr = 105 (µ0 = 4π·10-7 Vs/Am)
The maximum droop should be 3% within 1 ms
The upper cut-off frequency is 100 kHz, the resistor is at T = 300 K
Active transformer with open-loop ampl. A = 106 and Rf = 1 MΩ feedback, RL = 10 Ω
Calculate the inductance for the given droop time!
Calculate the number of winding and the sensitivity!
Calculate the threshold concerning the beam current for a signal-to-noise ratio of S/N = 1!
Result: Inductance via = 24
Sensitivity V/A
Noise: &
Minimum beam current:  unrealistically low due further noise
Exercise #3: Transformers for a pulsed LINAC 3/4
 Flying wire

## Slide 40
Passive Transformer (or Fast Current Transformer FCT)
Simplified electrical circuit of a passively loaded transformer:
A voltages is measured: U = R · Isec = R /N · Ibeam ≡ S · Ibeam
with S sensitivity [V/A],
equivalent to transfer function or transfer impedance Z
Equivalent circuit for analysis of sensitivity and bandwidth
(disregarding the loss resistivity RL)
beam

## Slide 41
Assume a beam with 1 µs pulse length behind a synchrotron to be measured by a transformer
Core size: ri = 30mm, ro = 60 mm, length l = 40mm
The maximum droop should be 3% within 1 µs
Permeability of the core: µr = 103 due to µr  1/f for f > 100 kHz (µ0 = 4π·10-7 Vs/Am)
The upper cut-off frequency is 100 MHz, the resistor is at T=300 K
Fast passive transformer with R = 50 Ω termination
Calculate the droop time and the lower cut-off frequency!
Calculate the inductance for the given droop time!
Calculate the number of winding and the sensitivity!
Calculate the threshold concerning the beam current for a signal-to-noise ratio of S/N = 1!
Result: for t = 1 µs  = 33 µs
cut-off frequency: = 4.9 kHz
Inductance via = 19  20
Sensitivity V/A
Noise:  min.
Exercise #3: Transformers for a pulsed LINAC 4/4
 Flying wire

## Slide 42
Design Criteria for a Current Transformer
Criteria:
1. The output voltage is U  1/N  low number of windings for large signal.
2. For a longer droop time, a large inductance L is required due to τdroop = L/R:
L  N2 and L  μr (μr 105 for amorphous alloy)
3. For a large bandwidth the integrating capacitance Cs should be low τrise = √LsCs
Depending on applications the behavior is influenced by external elements:
Passive transformer: R = 50 Ω, τrise  1 ns for short pulses
Application: Transfer between synchrotrons : 100 ns < tpulse < 10 μs
Active transformer: Current sink by I/U-converter, τdroop  1 s for long pulses
Application: macro-pulses at LINACs : 100 μs < tpulse < 10 ms
General:
The beam pipe has to be intersected to prevent the
flow of the image current through the torus
The torus is made of 25 μm isolated flat ribbon
spiraled to get a torus of 15 mm thickness,
to have large electrical resistivity
Additional winding for calibration with current source

## Slide 43
70
180
Linear Ampl.
Right
channel
Technical Realization of a Shoe-Box BPM
Technical realization at HIT synchrotron of 46 m length for 7 MeV/u 440 MeV/u
BPM clearance: 180x70 mm2, standard beam pipe diameter: 200 mm.

## Slide 44
Shoe-box BPM for Proton Synchrotrons
Frequency range: 1 MHz < frf < 10 MHz  bunch-length >> BPM length.
Signal is proportional to actual plate length:
In ideal case: linear reading
Shoe-box BPM:
Advantage: Very linear, low frequency dependence
i.e. position sensitivity S is constant
Disadvantage: Large size, complex mechanics
high capacitance
Size: 200x70 mm2

## Slide 45
Example of Transfer Impedance for Proton Synchrotron
The high-pass characteristic for typical synchrotron BPM:
Uim(ω)=Zt(ω)·Ibeam(ω)
Large signal strength  high impedance
Smooth signal transmission  50 
Parameter for shoe-box BPM:
C=100pF, l=10cm, β=50%
fcut= ω/2π=(2πRC)-1
for R=50   fcut= 32 MHz
for R=1 M  fcut= 1.6 kHz

## Slide 46
Exercise #8: Signal Estimation for a broad-band BPM 1/2
Assume a shoe-box BPM of length l=20 cm, radius a=10 cm and capacitance C=100 pF The beam velocity is β= 0.5 and the bunch length is σt= 100 ns.
Assume a position linear sensitivity of S=1/a i.e. UΔ/UΣ = x/a.
Calculate the transfer impedance for half-cylindrical plate and termination of R = 1 MΩ!
Calculate the sum voltage UΣ for Ibeam = 1 A !
Calculate the different voltage for x = 1 mm displacement!
What are the corresponding values for a termination with R = 50 Ω?
The transfer impedance is not constant, what does it mean? Use Zt(50Ω)=Zt(1MΩ)/20 .
Result: Transfer impedance for R= 1 M:
Sum voltage for Ibeam = 1 A: U = 2 Zt  Ibeam = 13.3 V
Difference voltage for x = 1 mm: U = Zt  Ibeam = 67 mV
Result: Sum voltage for Ibeam = 1 A: U = 2 Zt (50)  Ibeam = 670 mV
Difference voltage for x = 1 mm: U = Zt (50)  Ibeam = 3.3 mV

## Slide 47
Signal Shape for capacitive BPMs: differentiated ↔ proportional
Depending on the frequency range and termination the signal looks different:
High frequency range ω >> ωcut:
 direct image of the bunch. Signal strength Zt  A/C i.e. nearly independent on length
Low frequency range ω << ωcut:
 derivative of bunch, single strength Zt  A, i.e. (nearly) independent on C
Example from synchrotron BPM with 50  termination (reality at p-synchrotron : σ>>1 ns):

## Slide 48
Calculation of Signal Shape (here single bunch)
The transfer impedance is used in frequency domain! The following is performed:
1. Start: Time domain Gaussian function Ibeam(t) having a width of σt
2. FFT of Ibeam(t) leads to the frequency domain Gaussian Ibeam(f) with σf=(2πσt)-1
3. Multiplication with Zt(f) with fcut=32 MHz leads to Uim(f) =Zt(f)∙Ibeam(f)
4. Inverse FFT leads to Uim(t)

## Slide 49
Exercise #8: Signal Estimation for a broad-band BPM 2/2
Assume a shoe-box BPM of length l=20 cm, radius a=10 cm and capacitance C=100 pF The beam velocity is β= 0.5 and the bunch length is σt= 100 ns.
Assume a position linear sensitivity of S=1/a i.e. UΔ/UΣ = x/a.
Compare the signal strength to the thermal noise (using the theoretical minimum):
The thermal noise voltage at T=300 K is given by
Unoise = (4kB·T·R·Δf)1/2 and kB=1.4·10-23 J/K within the bandwidth Δf = 100 MHz !
Calculate Ueff for R=1 MΩ and R=50 Ω termination !
A displacement of x = 1 mm should be detected.
What is the minimum beam current Ibeam to achieve a Signal-to-Noise Ratio S/N=2 !
How can the position resolution be improved significantly? What is the physical reason?
Result: Thermal noise for R = 1 M:
Thermal noise for R = 50 :
Result: For R = 1 M & U = 2 Unoise(1M):
For R = 50  & U = 2 Unoise(50):
(not realistic because BPM from a low pass filter f cut (1M)=1.6 kHz: realistic Ibeam = 5mA)

## Slide 50
Voltage Spectrum for the BPM and Train of Bunches, R=50 Ω
What is the voltage spectrum for the case of a bunch train with σt=100 ns and facc=1 MHz ?
How is the spectrum modified if only part of the buckets are filled?
The spectrum consists of line separated by facc.
The envelope is given by the voltage signal of a single bunch.
Side bands appear
the power at facc is
reduced.

## Slide 51
Signal strength for long bunches is Usignal=Zt(f>fcut) ·Ibeam=7 mV
A baseline shift occur i.e. no dc-transmission
What is the spectrum and the signal shape for a termination with R=1 M
Sketch and discuss the signal voltage for the case of a bunch train with σt=100 ns !
The cut-off frequency is
fcut=1/(2πRC)=1.6 kHz
 the proportional shape is recorded
Reason for this choice: larger signal independent on bunch length
However: larger thermal noise due to Ueff=(4kB·T·Δf·R)1/2
Voltage Spectrum for the BPM and Train of Bunches, R=1 MΩ

## Slide 52
Numerical Value of Usignal(t) for Shoe-box BPM
2.2.4 What is the voltage for the case of a single bunch with σt=1, 10 and 100 ns and
a current of max. value Ibeam=1mA? (start with σt=1ns, other case only estimation)
Assume a value of the transfer impedance | Zt(f>fcut) |=7  above fcut=32 MHz.
For short bunches σt=1 ns → σf=1/2σt = 160 MHz
i.e. main component above fcut  proportional shape
 Usignal=Zt (f>fcut) ·Ibeam= 7 mV for the σt=1 ns case
For long bunches with σt=100 ns → σf=1/2σt = 1.6 MHz
i.e. all frequencies below fcut  derivative shape
 Usignal≈ 0.3 mV for the σt=100 ns case (i.e. a factor 23 lower!)
For the σt=10 ns the signal must be calculated:
 Usignal≈ 3 mV for the σt=10 ns case

## Slide 53
Exercise #6: Transverse profile by flying wire scanner
Assume a beam of 1012 protons at 1GeV stored in a synchrotron.
The beam size 10x10 mm with ρbeam=const (for simplification), the revolution time is 1.0 μs.
The wire is made of Carbon with 50x50 μm and scanned with v=10 m/s.
[Carbon is light material of ρ=2.2 g/cm3 density therefore low stopping power.]
The energy loss is dE/ dx= 4.29 MeV/cm.
Calculate the relative energy loss per passage through the wire!
Calculate the average energy loss during the scan! How many passages an ion does in average?
Is this device nearly ‘non-destructive’  Are the particles lost?
The maximum power rate to prevent for destruction is 1 W/mm.
Is the wire destroyed?
Repeat the same calculation assuming 109 stored Uranium ions!
The energy loss is now dE/ dx=35640 MeV/cm.
Why is the energy loss so much larger?
Are the particles loss? Is the wire destroyed?
What happens for not fully stripped ions (i.e. ions with some bound electrons)?
What is an appropriate method of profile determination for the Uranium case?