## Slide 1
Exercise as preparation for the exam
JUAS 2025, ESI-Archamps at CERN
Peter Forck (GSI and University Frankfurt)

## Slide 2
Program of today’s interactive Session
Possible subjects of interactive session for exam preparation:
Discussion and some examples from pervious exams
General questions and answers to beam diagnostics
Discussion of polls presented during lecture and some further polls
Further exercises form exercise document as interactive discussion
(‘Exercises_instrumentation.pdf’ posted in INDICO
‘Answers_instrumentation.pdf’ will be posted today)
After topic 1, please decide on the topic 3 or 4 as not all can be realized!
Contributions (questions, comments, remarks) are required from your side.
This session is your event!

## Slide 3
Style of the Lecture and Expectation to You
My perspective concerning the style of the lecture:
Presentation of the basics
Some extension to cover recent developments to make it actual
Possible problem: How to distinguish between both?  Exams questions only on basics
Usage of the book:
Description in more detailed manner than on the slides
Might of usage later on when you are working at a accelerator
 might be not so useful for the exam
Exam preparation:
Review the slides
Answer the polls again, you might answer some more presented questions
Try to work on the printed exercises (might be too much for Monday)
 Look to the schematic plots and diagrams and
 Explain the topic yourself or your colleagues

## Slide 4
Results of last Years’ Examinations in Beam Instrumentation
Distribution of marks in the last years, 20 points maximal.
2021
µ=14.3
=2.2
2020
µ=14.2
=3.3
2019
µ=14.0
=3.5
2018
µ=15.2
=3.3
2017
µ=13.2
=4.2
2016
µ=12.4
=4.0
2022
µ=15.3
=4.0
2019 to 2024: Distribution of mean value and standard deviation
2023
µ=14.0
=3.0
2024
µ=15.5
=2.5

## Slide 5
Exercise Example (a bit too simple): Types of BPMs
 expected answer
rating: 100 %
Assume a proton synchrotron with facc = 1 MHz acceleration frequency.
Which type of BPM would you install? Give the main reason for your choice.
Answer 1:
Linear-cut BPMs are installed in most low-frequency synchrotrons.
The main reason is the linearity of the position sensitivity.
Additionally: For a high impedance termination, a large signal can achieved due to the low fcut
Answer 2:
Button BPMs are generally a good choice and are e.g. installed at LHC.
The reason is that the beam pipe diameter and shape in only weekly modified to prevent for any wake-field excitation.
 unexpected answer
rating: almost 100 %
Answer 3:
Button BPM.
 wrong answer
rating: 0 %
 partly answered
rating:  30 %
Answer 4:
Linear-cut BPM.
Not correct: For a typical bunch length and beam pipe size, the frequency components are much smaller than the cut-off frequency of the beam pipe (interpreted as a hollow wave-guide).
However: Bunch length was not specified. It could be important for short bunches
(e.g. LHC, facc = 200 MHz). Moreover, wake-field contributions were not discussed in the lecture.

## Slide 6
Faraday Cup or active transformer, the beam power is sufficient low for a Faraday Cup,
and the beam current sufficient high for a transformer
Give an appropriate method for current measurement for a proton accelerators:
(a) Behind the ion source, Ekin = 100 keV, Ibeam = 100 mA, pulse duration of tpulse = 1 ms.
(b) Behind the ion source with the same parameter as under a) but a Ibeam = 10 nA.
Faraday Cup, the current is too low for a transformer
(c) Behind a proton LINAC, Ekin = 100 MeV, Ibeam = 100 mA, pulse duration of tpulse =1 ms.
(d) Permanent monitoring during the 1 s long acceleration within a synchrotron from
Ekin = 100 MeV  1 GeV, circulating beam Ibeam  100 mA.
(e) The circulating current within a synchrotron after acceleration and de-bunching
Active transformer due to the high beam power
DCCT for a permanent monitoring, or using a FCT and integrating the bunch signal
DCCT no other choice
(f) Fast extraction from a synchrotron in a transport line of 1012 protons within 1 μs.
Passive transformer, well suited for a bunched beam detection,
Faraday Cup not possible because above pion production threshold.
Ionization chamber
(g) The same parameters as under f) but with a duration of 10 s by ’slow extraction’.
Exams Example, Exercise #2: Current Measurements for Proton Beam

## Slide 7
Exam Example: Ionization Profile Monitor IPM (1/2)
The properties of an IPM should be discussed (3 points out of 20):
(a) For what purpose IPMs are used?
IPMs are used for non-invasive profile measurement either at high current LINACs (to prevent for material destruction) or within a synchrotron to measure the undisturbed beam
Due to the beam’s energy loss, residual gas atoms or molecules are ionized. With the help of an external electric field, the residual gas ions or electrons are accelerated towards an single particle detector with spatial resolution.
The electric field of the beam is comparable to the external electric field. The trajectory of a residual gas ion or electron is influenced such that the spatial distribution does not reflect the particle distribution.
An additional external magnetic field can be applied which guide the electrons on their trajectory towards the detector.
(b) Describe briefly the principle of an IPM.
(c) Which modification is required for intense beams and why?

## Slide 8
Ionization Profile Monitor at GSI Synchrotron
Non-destructive device for proton synchrotron:
beam ionizes the residual gas by electronic stopping
gas ions or e- accelerated by E -field 1 kV/cm
spatial resolved single particle detection
One device per plane
Realization at GSI synchrotron:
Typical vacuum pressure:
Transfer line: N2 10−8... 10−6 mbar  3108...31010cm-3
Synchrotron: H2 10−11...10−9 mbar  3105...3107 cm-3
beam
300 mm flange
MCP:
100 x 48 mm2
175
mm
175mm
63 wires,
2.1mm spacing
HV feedthru
R
voltage divider
+ 6 kV
+ 5 kV
+ 4 kV
+ 2 kV
+ 3 kV
+ 1 kV
0 kV
MCP
anode
position readout
HV electrode
ion
e.g. H+
beam

## Slide 9
Exam Example: Ionization Profile Monitor IPM (2/2)
The cyclotron radius is µm The radius rc determine now the spatial resolution of the IPM. (The value of 70 µm is acceptable as the resolution of an MCP is in the same order of magnitude.)
Due to the limited resolution as given by the MCP of about 100 μm, IPMs do not deliver sufficient spatial resolution for an electron beam of typically size σ < 100 μm.
(d) Assume and electron is emitted from the residual gas atom with an kinetic energy of Ekin,⊥ = 5 eV perpendicular to an external magnetic field of B = 0.1 T.
Calculate the cyclotron radius. Why is this quantity of importance?
(You might need: electron mass mec2 = 511 keV, elementary charge e = 1.6 · 10−19 C, velocity of light c = 3 · 108 m/s.)
(e) IPMs are seldom used at high energetic electron accelerators. Can you guess why?

## Slide 10
Electron Detection and Guidance by Magnetic Field
e− detection in an external magnetic field
cyclotron radius
for eV & B = 0.1 T  rc  100 µm
Ekin from atomic physics, 100 µm resolution of MCP
Time-of-flight: 1 - 2 ns  2 - 3 cycles.
B-field: Dipole with large aperture
 IPM is expensive & large device!
Ion detection mode:
Electron detection mode:
 broadening by beam’s electric field
7 1010 charges
per 10 m bunch

## Slide 11
Beam Quantities and their Diagnostics I
LINAC & transport lines: single pass  Synchrotron: multi pass
Electrons: always relativistic  Protons/Ions: non-relativistic for Ekin < 1 GeV/u
Depending on application: low current  high current
Overview of the most commonly used systems:
Beam quantity |  | Transfer line | Synchrotron
Current I | General Special | Transformer, dc & ac Faraday Cup Particle Detectors | Transformer, dc & ac Pick-up Signal (relative)
Profile xwidth | General Special | Screens, SEM-Grids Wire Scanners, OTR Screen MWPC, Fluorescence Light | Ionization Profile Monitor Wire Scanner, Synchrotron Light Monitor
Position xcm | General Special | Pick-up (BPM) Using profile measurement | Pick-up (BPM)
Transverse Emittance εtrans | General Special | Slit-grid Quadrupole Variation Pepper-Pot | Ionization Profile Monitor Wire Scanner Transverse Schottky

## Slide 12
Beam Quantities and their Diagnostics II
Destructive and non-destructive devices depending on the beam parameter.
Different techniques for the same quantity  Same technique for the different quantities.
Remark: In most cases no diagnostics device installed inside the rf-cavities (except cyclotron)
Beam quantity |  | Transfer line | Synchrotron
Bunch Length Δφ | General Special | Pick-up Secondary electrons arrival Electro-optical laser mod. | Pick-up Wall Current Monitor Streak Camera Electro-optical laser mod.
Momentum p and Momentum Spread Δp/p | General Special | Pick-ups (Time-of-Flight) Magnetic Spectrometer | Pick-up (e.g. tomography) Schottky Noise Spectrum
Longitudinal Emittance εlong | General Special | Buncher variation Magnetic Spectrometer | Pick-up & tomography
Tune and Chromaticity Q, ξ | General Special | --- --- | Exciter + Pick-up Transverse Schottky Spectrum
Beam Loss rloss | General | Particle Detectors | 
Polarization P | General Special | Particle Detectors Laser Scattering (Compton scattering) | 
Luminosity L | General | Particle Detectors | 

## Slide 13
Questions related to Particle Detectors for Beam Current
What happens if a particle in a transfer line loses 10 % of is kinetic energy
e.g. by passing through a ionization chamber? What happens if the energy loss is 1 %?
To which physical processes does the word ‘scintillation’ refers?
What is a photo-multiplier?
What is an ionization chamber?
Can ICs be used for other purposes as beam current measurement as well?
What is the physics process of the energy loss of electrons with Ekin > 10 MeV in matter?
Example of questions at the end of the chapter on
beam current measurement
 Question to lecture
Notes: 13

## Slide 14
Quiz for Scintillation and OTR Screen Profile Measurement
What is the basic physics of scintillation?
What are the important properties of scintillation from a inorganic material?
What is a the basic physics of optical transition radiation?
Is transition radiation emitted in other (non-optical) wavelength region as well?
What might be a resolution limit of screen measurements?
Do you know about other challenges or limitations for screen measurements?
Example of questions at the end of the chapter on
transverse profile measurement
 Question to lecture
Notes: 14

## Slide 15
Quiz related to Beam Emittance and Slit-Grid Method
What is meant by beam quality = emittance, i.e.
what type of quantitative description is used?
What is the geometrical meaning of a phase space distribution for -  12  <xx’>  0 ?
Expectation: Is the emittance of a 10 MeV electron beam smaller or larger than a proton beam?
Describe shortly the measurement principle of a slit-grid method!
Do you know variances of the slit-grid method?
Why is a slit-grid measurement of 100 MeV electron and proton beam not meaningful?
Example of questions at the end of the chapter on
Emittance measurement
 Question to lecture
Notes: 15

## Slide 16
Quiz related to BPM Signals
What is the cause of the wall current and wall current density?
What is its connection to the beam bunches?
What is the usage of the transfer impedance?
What is the frequency dependence of the transfer impedance and why is it so?
What is baseline shift?
Transfer impedance: Do you know other quantities of similar type?
How you determine the beam position?
Why it is clever to normalize the difference to the sum signal for position calculation?
What are the typical acceleration frequencies at electron and proton
LINACs, synchrotrons and cyclotrons?
Example of questions at the end of the chapter on
Beam position monitors
 Question to lecture
Notes: 16

## Slide 17
Summary of longitudinal Measurements
Longitudinal  transverse correspondences:
position relative to rf  transverse center-of-mass
bunch structure in time  transverse profile in space
momentum or energy spread  transverse divergence.
Determination uses:
Broadband pick-ups:  position relative to rf, mean energy
 emittance at transfer lines or synchrotron via tomography
assumption: bunches longer than pick-up.
Particle detectors:  TOF or secondary e− from wire
 for non-relativistic proton beams
reason: E-field does not reflect bunch shape.
Streak cameras:  time resolved monitoring of synchrotron radiation
 for relativistic e−-beams, tbunch < 1 ns
reason: too short bunches for rf electronics.
Laser scanning:  Electro-optical modulation of short laser pulse
 very high time resolution
Beam deflection:  Transverse deflection of primary beam
 very high time resolution, but most expensive ‘device’.

## Slide 18
Exercise (previous exam): Methods of Bunch Length Measurement
The beam has a non-relativistic velocity and a bunch of 1 ns length leads to a prolongation of the wall current; an example was discussed in the slides. Therefore, a Bunch Shape Monitor must be used.
A Bunch Shape Monitor is based on the emission of secondary electron from an intersecting wire and it deflection within a resonator operated in phase with the acceleration rf.
For the following accelerators and beam parameters, an appropriate method for bunch shape measurement (bunch shape is a synonym for longitudinal profile) should be chosen; give the main argument for your choice.
In each case, the RMS bunch length is  = 0.1 tacc of the acceleration period tacc = 1/facc:
Proton accelerator:
a) After a LINAC providing an energy of 10 MeV accelerated with facc = 100 MHz.
b) In a synchrotron with a beam energy of 100 MeV & acceleration frequency of facc = 1 MHz.
The bunch length is 100 ns. It can be monitored by the time-dependent signal from an FCT (and example was discussed during the lecture in chapter 2 and 6) or a BPM.
c) In a transfer line at an energy of 1 GeV following extraction within one turn from a synchrotron with a bunch length of roughly 10 ns.
As for the synchrotron case an FCT, WCM or BPM is suited. (Synchrotron light monitors are not suited for such proton energy resp. Lorentz factor ).

## Slide 19
The parameter are typical for a synchrotron light source. A streak camera can be used as discussed in the lecture.; its functionality should be described briefly….
For the following accelerators and beam parameters, an appropriate method for bunch shape measurement (bunch shape is a synonym for longitudinal profile) should be chosen; give the main argument for your choice.
In each case, the RMS bunch length is  = 0.1 tacc of the acceleration period tacc = 1/facc:
Electron accelerator:
a) In a synchrotron with a beam energy of 1 GeV &acceleration frequency of facc = 500 MHz.
b) At the end of a LINAC (as Free Electron Laser) of 10 GeV and a bunch length of  = 100 fs.
The bunch length after this typical FEL-LINAC is too short for a streak camera.
Electro-optical modulation: Close to a beam, a birefringent crystal is installed. Here the electrical field of the bunch leads a rotation of the polarization change. A polarized laser beam passes this crystal and analyzed with a polarizer. The change of polarization is a measure for the strength and time dependence of the bunch’s electric field.
Alternatively, transverse deflection cavity: A deflecting cavity can be used. Here the electron beam is deflected transversally within a cavity operated by a mode providing a transvers reflection. The phase of the mode is chosen such that the reference particle crosses the cavity at the zero-crossing of the sine wave. Tt acts as a time-to-space converter. After some drift the deflection is monitored on a scintillation screen.
Exercise (previous exam): Methods of Bunch Length Measurement

## Slide 20
Bunch Structure using secondary Electrons for low Ekin Protons
Secondary e− liberated from a wire carrying the time information.
→ Bunch Shape Monitor (BSM)
Working principle:
insertion of a 0.1 mm wire at  10 kV
emission of secondary e− within less than 10 ps
secondary e− are accelerated
toward an rf-deflector
rf-deflector as ’time-to-space’ converter
detector with a thin slit
slow shift of the phase
resolution  10 ps  1o @ 280 MHz
Measurements are comparable
to that obtained with particle detectors.
SEM: secondary electron multiplier

## Slide 21
Bunch Length Measurement for relativistic Electrons
injection
extraction
Streak camera
e- synchrotron
acc.
freq. frf
rf cavity
Electron bunches are too short (t < 100 ps) to be covered by the bandwidth of
pick-ups (f < 3 GHz  trise > 100 ps) for structure determination.
 Time resolved observation of synchr. light with a streak camera: Resolution  1 ps.
Scheme of a streak camera:

## Slide 22
Bunch Length Measurement by electro-optical Method
FELs  bunch length below 1 ps is achieved, i.e. below the resolution of streak camera
Short laser pulses with t  10 fs and electro-optical modulator
Electro optical modulator: birefringent, rotation angle depends on external electric field
Relativistic electron bunches: transverse field E lab =  E rest carries the time information.
LINAC
LINAC
EO monitor
Undulator
Bunch compressor
Measurement by scanning
Short laser pulses t < 10 fs
and delay line
 scanning method
Further methods used!
 conclusion
crystal
beam

## Slide 23
Bunch Length by rf-Deflection: Principle
Transversal deflection of the bunch i.e. time-to-space conversion
From D. Xiang, IPAC’12
Size of the streak given by
k is determined by the rf-power

## Slide 24
Program of today’s interactive Session
Possible subjects of interactive session for exam preparation:
Discussion and some examples from pervious exams
General questions and answers to beam diagnostics
Discussion of polls presented during lecture and some further polls
Further exercises form exercise document as interactive discussion
(‘Exercises_instrumentation.pdf’ posted in INDICO at Tuesday 28st of February;
‘Answers_instrumentation.pdf’ posted in INDICO at Friday 3rd of March)
Please decide on the topic as not all can be realized!
Contributions (questions, comments, remarks) are required from your side.
This session is your event!