## Slide 1: RF Engineering Transmission Lines II & Pillbox Resonator I
Christine Völlinger (CERN) & Manfred Wendt (BNL)

## Slide 2: Transmission Lines and Waveguides
Wave patterns in guided wave systems depend on the number of conductors used.
Source: Ma, Electromagnetic Waves and Applications Part III, univ. lecture
“Open” two-wire system (TEM)
Coaxial line (TEM)
E-field ---H-field
Picture: Coaxial loads for the SPS 200 MHz cavity © CERN
Uniform waveguides rectangular, round, random cross-section (all non-TEM)
TEM-propagation = 2 conductor system
Source: Saad, Microwave Engineers Handbook, vol. 1, Artech House
E-field
---H-field
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer

## Slide 3: Hollow Waveguides
Waveguides exist in different shapes. They are just hollow metallic tubes with uniform cross-sections.
The metallic waveguide is a completely enclosed system without any radiation losses.
Further, losses due to a dielectric layer, as we have seen for the coaxial line do not exist, equally the inner conductor of the coaxial line is eliminated.
Waveguides present a one-conductor system, so no TEM-mode propagation is possible. Propagation happens in TE-mode (Transverse-Electric) and TM-mode (Transverse-Magnetic). These modes have a lower frequency limit, the so-called cut-off frequency below which propagation is not possible. The cut-off frequency depends on the dimensions of the waveguide cross-section.
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
Rectangular waveguide
Circular waveguide
Arbitrarly shaped cross-section waveguide

## Slide 4: Waveguides & Boundary conditions
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
Rectangular waveguide
Circular waveguide
Arbitrarly shaped cross-section waveguide
Waves are following the waveguide shape, even if it is bend.
For this, the propagating waves (formerly unbound) now need to fulfil boundary conditions on the walls of the waveguide.
Remember? From EM-field description, we know that:
 on perfect conducting surfaces, the tangential electric field has to vanish to fulfill the boundary
condition. We speak of an “electric wall”: Etangential = 0.
 the walls of a waveguide can approximated as a perfect conductor (exception: loss calculation).

## Slide 5: Circular (round) Waveguides (1/6)
Like all transmission lines, also the circular waveguide is characterized by a propagation constant, an attenuation constant and a characteristic impedance.
These quantities are derived by field theory analysis (see lecture of A. Mostacci). Propagation is usually assumed in z-direction.
This leads to the so-called cut-off frequencies for the different modes:
z
R
For a perfect conducting tube (no resistive attenuation) with radius R, we obtain propagation constants for the TE-mode and the TM-mode:
 Roots of the Bessel-function for TM-mode
 Roots of the derivative of the B.F. for TE-mode
Notes: In 1897, the physicist John William Strutt, better known as Lord Rayleigh gave the mathematical proof that wave propagation in waveguides must be possible. This was a novum as until then, people believed that two conductors would be necessary for the transfer of electromagnetic energy. Rayleigh also gave the theory of the TE- and TM-mode patterns and the cut-off frequency, he was, however, not able to provide experimental proof at the time. The waveguide was then essentially forgotten again until the 1930s.

## Slide 6: Circular (round) Waveguides (2/6)
Recall the Bessel function and the derivative of the Bessel function with their roots:
Source: Pozar, Microwave Engineering, 4th ed., Wiley
= 1st root of Bessel function of first type
= 2nd root of Bessel function of first type
= 1st root of derivative of Bessel function of first type

## Slide 7: Circular (round) Waveguides (3/6)
Let’s see an example.
z
R= 60 mm
 Calculating cut-off frequencies for a circular waveguide with R = 60 mm.
TM-mode
TE-mode
Frequencies where these modes start propagating.
Source: Pozar, Microwave engineering, 4th ed., Wiley
Chart of cut-off frequencies relative to fc of TE11-mode:

## Slide 8: Circular (round) Waveguides (4/6)
Waveguide modes and field patterns
Simulaton pictures: courtesy E. Jensen, source pictures and chart: Pozar, Microwave engineering, 4th ed., Wiley
2nd mode is TM01. Magnetic field is transverse.
1st mode is TE11. Electric field is transverse.
Mode has 2 polarisations (orientations of the electrical field).

## Slide 9: Circular (round) Waveguides (5/6)
Waveguide modes and field patterns
Simulaton pictures: courtesy E. Jensen, source pictures and chart: Pozar, Microwave engineering, 4th ed., Wiley
3rd mode is TE21. Electric field is transverse
6th mode is TE31. Electric field is transverse.
4th mode is TM11. Magnetic field is transverse.
Further field plots can e.g. be found here: Lee, Lee and Chuang, Plot of Modal Field Distribution in Rectangular and Circular Waveguides. IEEE, Trans. Microwave Theory and Techniques, Vol. MTT-33, no. 3, March 1985

## Slide 10: Circular (round) Waveguides (6/6)
What is actually happening if the wave frequency in a waveguide is below cut-off?
Remember? Propagation constant is defined:
Now for frequencies below cut off, β would become complex:
This is called an evanescent wave = a wave that cannot propagate.
Then, the propagation constant γ becomes fully real, and the wave is damped even in the loss-less case (α=0), since the propagation is following:

## Slide 11: Rectangular Waveguides (1/6)
All field quantities are derived by field theory analysis (see lecture of A. Mostacci).
Wave propagation is usually assumed in z-direction.
The rectangular waveguide is characterized by a propagation constant, attenuation constant and a characteristic impedance.
We distinguish again between TE-modes and TM-modes. TEM-modes do not exist in a waveguide.
We will see that the hollow rectangular waveguide can propagate TE- and TM-modes, and that these modes have cut-off frequencies below which propagation is not possible, similar to the TE- and TM-modes of the circular waveguide.
The derivation of the cut-off frequency is straightforward, please refer to textbooks, if you are interested.
The field components are obtained by the separation method.
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
z
b
a
a > b

## Slide 12: Rectangular Waveguides (2/6)
TE-modes are characterized by a zero electric field in propagation direction. The electric field is in the transverse plane, only.
TE-modes
The mode with the lowest cut-off frequency is called the dominant mode.
Note that if n=m=0, all field components become zero, there is no TE00 mode.
A waveguide is called overmoded, if more than one mode is propagating in the waveguide at the same time.
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
x
b
a
a > b
y
z
Each mode has a cut-off frequency:
TE10-mode is the mode with the lowest cut-off frequency:

## Slide 13: Rectangular Waveguides (3/6)
TM-modes
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
x
b
a
a > b
y
z
TM-modes are characterized by a zero magnetic field in propagation direction. The magnetic field is in the transverse plane, only.
There is no TM00-mode, neither do TM01 or TM10 exist. For n=m=0, all field components become zero.
Note that TE10-mode remains the dominant mode, it is the mode with the lowest cut-off frequency.
Also in this case, each mode has a cut-off frequency (identical to TE):
TM11 has as cut-off frequency:

## Slide 14: Rectangular Waveguides (3/6)
TM-modes
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
x
b
a
a > b
y
z
TM-modes are characterized by a zero magnetic field in propagation direction. The magnetic field is in the transverse plane, only.
There is no TM00-mode, neither do TM01 or TM10 exist. For n=m=0, all field components become zero.
Note that TE10-mode remains the dominant mode, it is the mode with the lowest cut-off frequency.
Also in this case, each mode has a cut-off frequency (identical to TE):
TM11 has as cut-off frequency:

## Slide 15: Rectangular Waveguides (4/6)
Field pattern for TE01-mode
source: Zinke/Brunswig, Hochfrequenztechnik, 5th ed., Springer
E-field ---H-field
What do we actually see?
View from front
(x/y-plane)
Wall currents and displacement
currents inside the waveguide.
Side view broad
(x/z-plane)
Side view narrow
(y/z-plane)

## Slide 16: Rectangular Waveguides (5/6)
Fundamental and higher waveguide modes
and field patterns for TE-modes
TE11-mode
TE21-mode
Simulaton pictures: courtesy E. Jensen, field pattern source: Pozar, Microwave engineering, 4th ed., Wiley
TE10-mode

## Slide 17: Rectangular Waveguides (6/6)
Fundamental and higher waveguide modes
and field patterns for TM-modes
Simulaton pictures: courtesy E. Jensen, field pattern source: Pozar, Microwave engineering, 4th ed., Wiley, TM31-mode from Lee et al., MTT-33, 1985
TM31-mode
TM11-mode
TM21-mode

## Slide 18: Coaxial line installation
Amplifiers of the 200 MHz travelling wave system in the CERN SPS and their coaxial power lines leading to the underground installation (feeder lines)
Quiz!
Test your knowledge.

## Slide 19: Quiz no. 4
Waveguides are used for TEM signal transport
  - true - false
In a waveguide, lossy wall-currents exist in…?
  - circular waveguides due to the shape of their outer conductor - rectangular waveguides due to the shape of their outer conductor - rectangular waveguides only, but not in circular waveguides and not in elliptical waveguides - all waveguides

## Slide 20: Quiz no. 4
Waveguides are used for TEM signal transport
  - true - false (correct answer)
In a waveguide, lossy wall-currents exist in…?
  - circular waveguides due to the shape of their outer conductor - rectangular waveguides due to the shape of their outer conductor - rectangular waveguides only, but not in circular waveguides and not in elliptical waveguides - all waveguides (correct answer)

## Slide 21: Cavity resonators
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
Microwave resonators can be built from waveguides by closing the open ends.
We call this an RF-resonator or a cavity.
A cavity stores electric and magnetic energy inside the hollow body.
The frequency of the electromagnetic field resonance depends on the cavity dimensions.
Same as with the rectangular and the circular waveguide, the electromagnetic field has to fulfil the boundary conditions on the resonator walls. The field builds up in resonant modes.
Cavities that are used for the acceleration of particles in our accelerators are mostly of a cylindrical and flat shape. This is why we call them pillbox cavities.
We will later see how resonances can be excited in cavities by feeding RF-signal in, and how such a cavity can be used in accelerators for particle acceleration.

## Slide 22: Cavity resonators and Q-value (1/2)
Resonators are classified by their quality factor Q.
The quality factor (or Q-value) can be used as a measure of “how well the cavity is resonating” (more details will come).
High Q-value is desired in accelerating cavities; Q-value is one of the accelerator efficiency figures-of-merit.
Q-value reduces e.g. due to the power dissipated in the metallic walls or other loss mechanisms.
The connection of the cavity resonator to the outer world will reduce its Q-value as well (we say “it loads the cavity with an additional loss mechanism).
If the cavity is filled with a dielectric, this will produce additional losses  we don’t have this in accelerators.
define
= unloaded Q

## Slide 23: Cavity resonators and Q-value (2/2)
Example: measurements taken on the PS 80MHz pillbox cavity
We tested this cavity for Q-deterioration and shifting of its fundamental mode (~80 MHz).
Q-values obtained from 3-dB-measurement (see dashed red lines, method will be introduced later).  Plot on the top has a higher Q-value than the plot below.

## Slide 24: Rectangular Cavity Resonators (1/3)
E-field
Picture source: Caspers, JUAS lecture 2021
From the field pattern of the TE10-mode in the rectangular waveguide  imagine that the resonant field in a rectangular resonator will build up in a similar way.
The field is building up in a standing wave pattern, using sine and cosine functions.
From the boundary condition on the resonator wall, the electric field has to be zero, thus we can see multiples of electric field maxima.
The mode indices are counting the maxima of the field along one axis (we see either a TExyz or a TMxyz- mode.
The mode shown is a TE101-mode.
x
y
z
Waveguide TE10-mode
Source: Pozar, Microwave engineering, 4th ed., Wiley

## Slide 25: Rectangular Cavity Resonators (2/3)
Formulae for a rectangular resonator
(for derivation see lecture of A. Mostacci or textbooks).
TE101-mode is the lowest resonant mode, hence also the dominant mode in this resonator.
resonant wavelength:
Resonant frequencies for TEmnl-mode and TMnml-modes:
Q-value for TE101:
Source: Pozar, Microwave Engineering, 4th ed., Wiley
c
c

## Slide 26: Rectangular Cavity Resonators (3/3)
E-field
x
y
z
Picture source: Caspers, JUAS lecture 2021
b
c
a
For the case a=c, the formulae simplifies strongly.
resonant wavelength:
Q-value for TE101:

## Slide 27: Pillbox Cavity Resonators (1/6)
A cylindrical cavity resonator can be seen as a section of circular waveguide shorted at both ends.
From the TE11-mode (dominant mode for circular waveguide)  TE111-mode is the dominant TE-mode for a cylindrical cavity.
TM010-mode is the dominant TM-mode for a cylindrical cavity.
TM010-mode mode is used for acceleration as it has a large electric field along the z-axis.
Electric field is described by Besselfunction J0.
TM010-mode and pillbox mode indices?
z
Ez
-B
Picture source: Caspers,
JUAS lecture 2021
Pillbox cavity is flat compared to a “long” cylindrical cavity.
Also, beam-pipe connection is needed.
Simulation: P. Kramer

## Slide 28: Pillbox Cavity Resonators (2/6)
Mode indices of a pillbox cavity are as follows:
The electric field on the cavity’s axis following the Besselfunction J0
The first mode-index gives the order of the Bessel function.
The second mode-index indicates the root of the Bessel function which is the number of its zero-crossings.
The third mode-index is the number of half waves (maxima) along the z-axis.
Ez
Picture source: Caspers, JUAS lecture 2021
Ez
TM010
h
a
J2
J1
J0
Besselfunctions
h
h
Source: Pozar, Microwave engineering, 4th ed., Wiley

## Slide 29: Pillbox Cavity Resonators (3/6)
Ez
Picture source: Caspers, JUAS lecture 2021
Ez
h
a
Formulae for a circular cavity resonator (for derivation see lecture of A. Mostacci or textbooks).
Resonant frequencies for TEnml-mode:
Resonant frequency for TMnml-modes:
Note that the TM010- mode is independent of the cavity height h (until the TE111 mode shows up, roughly at 2a/h=1).

## Slide 30: Pillbox Cavity Resonators (4/6)
Recall the Bessel function and the derivative of the Bessel function with their roots:
Source: Pozar, Microwave Engineering, 4th ed., Wiley
= 1st root of Bessel function of first type
= 2nd root of Bessel function of first type
= 1st root of derivative of Bessel function of first type

## Slide 31: Pillbox Cavity Resonators (5/6)
Ez
Ez
TM010
h
a
For the case of the TM010-mode, we have no dependence on cavity height, so we get a much simpler formulae:
Remember? Skindepth is:

## Slide 32: Pillbox Cavity resonators (6/6)
Resonant chart for a general cylindrical cavity showing the excited modes as a function of cavity dimensions.
1st TE-mode is TE111
1st TM-mode is TM010, and shows up for ratios (2a/h)2 > 1
(2a/h)2
Source: Pozar, Microwave engineering, 4th ed., Wiley

## Slide 33
Thank you for your attention.

## Slide 34
Let’s have a break!

## Slide 35: Further reading…
POZAR, David M., “Microwave Engineering”, 4th edition, Wiley and sons.
ZHANG, Keqian, “Electromagnetic Theory for Microwaves and Optoelectronics”, 2nd edition, Springer.
BHAT, Shiban, “Stripline-like transmission Lines for Microwave Integrated Circuits”, New Age International Publishers.
HOFFMANN, “Integrierte Mikrowellenschaltungen”, Springer.
SAAD, “Microwave Engineer’s Handbook”, Vol.1, Artech House Inc.