## Slide 1: RF Engineering Scattering (S)-Parameters
Christine Völlinger & Manfred Wendt – CERN

## Slide 2: Outline and Objectives
A brief recap on electrical networks
  A simplified way to describe electrical, electronics and RF circuits
  Electrical network composed out of lumped and distributed elements
  Two-port RC-filter example using admittance (Y) parameters
Introduction to scattering (S) parameters
  General concept of incident / reflected waves scattered at the ports of an RF network
  Reference impedance
  -port and -port S-parameters
  Properties of the S-matrix: reciprocity, symmetry, losses
  A few S-matrix examples for RF networks with -, -, -, and -ports
  S-parameters in practice: the SnP Touchstone file format
  Cascading (“chaining”) 2-port S-matrizes
  General -port networks
JUAS Proc. 2024 II.2.x.y.z, p. nnn
Please note the references to the JUAS proceedings!

## Slide 3: Electrical Networks (1)
The electromagnetic behavior or RF circuits and systems, like any other electrical / electronics circuit or system can be described by Maxwell’s equations
  These equations need to be solved, taking all the boundaries and materials into account
However, this is far too complicated and inconvenient for most practical situations!
  simplified electrical network description based on approximative lumped or distributed elements
    With given characteristics and values of each circuit element represented by a symbol in an electrical network, following the laws of Ohm and Kirchhoff. Here some examples:
lumped, passive, non-linear
diode
lumped, active, non-linear
transistor
npn transistor
distributed, passive, linear
transmission-line
lumped, passive, linear
resistor
inductor
capacitor
JUAS Proc. 2024 II.2.7.1, p. 829

## Slide 4: Electrical Networks (2)
Complex electrical, electronics and RF systems are divided into functional blocks, i.e., networks, with -ports, each port has two terminals
  The two-port network is most popular, typical examples for two-port networks are filters, attenuators, amplifiers, etc.
The characteristic behavior of the -port network is defined by a set of parameters, linked to their ports.
  A two-port network has four parameters as port voltages (, ) and port currents (, ), two are independent, the other two are dependent parameters.
  Various combinations of dependent and independent port voltages and currents exist, accordingly various matrix definitions for linear -port networks exist, known as -, -, - and - parameters.
2-port network
1
1’
2
2’
- parameters
, : dependent , : independent
JUAS Proc. 2024 II.2.7.1, pp. 829/830

## Slide 5: Electrical Networks (3)
It is more convenient to express the parameters for linear networks in the frequency domain
  Avoids solving differential equations! Example: Simple RC two-port network
    Only for time-invariant and linear networks!
Voltage/current-based network parameters fail at high frequencies!
  Now voltages and currents are a function of frequency (or time) AND space (location): ,
    Originating from time/space varying EM-fields
  Example: RC two-port network embedded between transmission-lines
    While it is still possible to solve the network problem, it becomes complicated and cumbersome based on and
  The circuit may become unstable or might be damaged, when operating on a short or open end for characterizing the network parameters
  Due to parasitic effects, a reliable measurement of and becomes almost impossible.
Resolution: RF scattering parameters based on power-waves for linear networks which include distributed elements
  The magnitude of a traveling wave is independent of the location in a lossless transmission-line
- parameters:
- parameters:
linear two-port
JUAS Proc. 2024 II.2.7.1, p. 830

## Slide 6: Principle of Scattering (S)-Parameters
Analogy to optical waves
  Light falls on a car window
    Some parts of the incident light is reflected (you see the mirror image)
    Other parts of the light is transmitted through the window (you can still see objects inside the car)
  Optical reflection and transmission coefficients of the window glass define the ratio between reflected and transmitted light.
Similar in RF networks: The scattering (S)-parameters of an -port RF network (DUT) is characterized by incident and reflected / transmitted (power) waves.
JUAS Proc. 2024 II.2.7.1, p. 831

## Slide 7: Generalized S-Parameters
for an arbitrary -port microwave or RF network are defined by a set of normalized complex voltage waves:
  as incident and reflected / transmitted power waves at the port of the network, defined by the terminal voltage and current , and an arbitrary reference impedance
    Please note the complex notation implies linear, time-invariant networks describe in the frequency-domain
Today, for most practical cases the RF network, also called “device under test” (DUT) is characterized by a vector network analyzer (VNA), connected with coaxial cables (transmission-lines) with a characteristic impedance of to the ports.
  Usually the S-parameters are defined for a port reference impedance:
  Some VNAs with a physical reference impedance of allow a mathematical port impedance conversion to adapt to a port reference impedance
incident wave at port :
reflected wave at port :
: conjugate complex
-port (DUT)
JUAS Proc. 2024 II.2.7.2, pp. 831/832

## Slide 8: S-Parameters – -port
Electrical / electronics networks
  -port electronics circuits
  Defined by voltages or and currents or at the port terminals
  Characterized by circuit matrices, e.g., , , , etc.
RF / microwave networks
  -port RF DUT circuit or subsystem, e.g., filter, amplifier, transmission-line, hybrid, circulator, resonator, etc., which may include distributed elements
  Defined by incident and reflected / transmitted waves at a reference plane (physical position) at the ports.
  Characterized by a scattering parameter (S-parameter) matrix of the reflected and transmitted power waves, typically as a function of the frequency
  Normalized to a reference impedance of typically
1
1’
1-1’ reference plane (port 1)
R
L
C
e.g., any complex load
DUT (device under test)
1-port RF network (DUT) example
S-Parameters allow to characterize the DUT with the measurement equipment located at some physical distance
All high frequency effects of distributed elements are included with respect to the reference plane
JUAS Proc. 2024 II.2.7.3, pp. 832/833

## Slide 9: S-Parameters – -port (1)
Analysis of the forward S-parameters:
  -port networks still can be fully characterized with a -port VNA, but always remember:
  ALWAYS: Terminated unused ports in their characteristic impedance!
1
1’
port 1
DUT
2
2’
port 2
  Independent parameters:
  Dependent parameters:

## Slide 10: S-Parameters – -port (2)
1
1’
port 1
DUT
2
2’
port 2
Analysis of the reverse S-parameters:
  Examples of 2-ports DUT: filters, amplifiers, attenuators, transmission-lines (cables), etc.
  ALL ports ALWAYS need to be terminated in their characteristic impedance!
  Independent parameters:
  Dependent parameters:
JUAS Proc. 2024 II.2.7.4, pp. 833-835

## Slide 11: S-Parameters – -port (3)
Linear equations for a -port network (DUT):
  with:
signal flow graph (SFG)
of a -port network
port1: with
port 2:
port 1
port 2
JUAS Proc. 2024 II.2.7.4, pp. 835/836

## Slide 12: S-Parameters – -port (1)
Reflection coefficient and impedance at the -port of a RF network (DUT):
Power reflection and transmission for a -port network (DUT):
with all ports terminated in their characteristic impedance and
Here the US notation is used, where power . European notation (often): power These conventions have no impact on the S-parameters, they are only relevant for absolute power calculations
JUAS Proc. 2024 II.2.7.5, p. 837

## Slide 13: The Scattering Matrix
Waves traveling towards the n-port:
Waves traveling away from the n-port:
The relation between and () can be written as a system of linear equations ( the independent variable, the dependent variable)
  in compact matrix form follows
one-port | 
two-port | 
three-port | 
four-port | 
one-port | 
two-port | 
three-port | 
four-port | 
JUAS Proc. 2024 II.2.7.5, p. 837/838

## Slide 14: Quiz (1)
Select all correct answers
  Y- and Z-parameters of electrical networks require a reference impedance
  Scattering parameters of RF networks are based on normalized, complex power waves incident and reflected / transmitted at their ports
  DUT stands for “Device Under Test”, as acronym for the RF network to be characterized
  S-parameters are only defined for a reference impedance of .
  Unused ports in a S-parameter measurement setup always need to be terminated in their characteristic port impedance

## Slide 15: S-Matrix Properties
A port of the network is matched if:
  i.e., no reflections!
A -port is reciprocal if:
  Most passive components are reciprocal, e.g., resistor, capacitor, inductor, transformer, etc.
    But not components with inhomogeneous material properties, e.g., magnetized ferrites, plasma, etc.
  Active components, like amplifiers are non-reciprocal
A -port is symmetric if:
  It needs to be reciprocal, and input and output reflection coefficient need to be equal.
A -port is passive and lossless if the matrix is unitary:
  Example: passive, lossless -port:
conjugate transpose (Hermitian) : identity matrix
transpose
Matrix symmetry
Matrix symmetry and electrical symmetry
JUAS Proc. 2024 II.2.7.6, p. 838/839

## Slide 16: Examples for Symmetry and Reciprocity
Without prof: The S-matrix is always reciprocal for symmetric networks.
1’
1
2’
2
symmetry
1’
1
2’
2
with:
with:
-network
voltage-divider network
JUAS Proc. 2024 II.2.7.6, p. 840/841

## Slide 17: Numerical lossless / lossy Example
1’
1
2’
2
-port series-network
lossless | lossy
JUAS Proc. 2024 II.2.7.6, p. 841

## Slide 18: Quiz (2)
Prompts |  | Possible Answers
matched | A4 | 
symmetric | B3 | 
reciprocal | C6 | 
passive and lossless | D2 | 
Prompts |  | Possible Answers
matched | A4 | 
symmetric | B3 | 
reciprocal | C6 | 
passive and lossless | D2 | 

## Slide 19: Quiz (3)
Mark all correct answers for the S-parameters of a 2-port RF network
  and are independent parameters
  is the input reflection coefficient
  and are the incident waves at port 1 and port 2, respectively.
  and are the transmitted waves between port 1 and port 2, and vice versa.
  and are the forward and reverse transmission gains.
  To characterize the S-parameters at port 2, port 1 needs to be terminated in its characteristic port impedance.
-port
port 1
port 2

## Slide 20: S-Matrix Examples – -port
Examples for -port S-matrices are any simple, passive (complex) impedances
  Any R, L, C, RL, RC, LC and RLC circuit or any combinations of those elements leading to a single port network, which of course also my include distributed (transmission-line) elements
  “Special” cases are:
    (matched, ideal termination)
    (ideal short)
    (ideal open)
  If an active element is involved, e.g., a reflection amplifier
Strictly speaking, a simple RF resonator, e.g., a “pill-box” cavity, is a -port
  One coaxial or waveguide port as RF power coupler, plus two beam (waveguide) ports.
However, for many practical cases it can be treated as -port
  The mode of interest, e.g., TM010, is trapped with no or negligible fields contribution near the beam-ports
  We consider only a single coupler to characterize, e.g., the TM010 mode in terms of a -port S-parameter measurement
    Typically applying an RLC-parallel equivalent circuit
JUAS Proc. 2024 II.2.7.7.1, pp. 842/843

## Slide 21: S-Matrix Examples – -port
Ideal (matched: ) transmission-line of length
  For a lossless transmission-line:
  For a lossless line of length :
Ideal attenuator
: propagation constant
: attenuation constant in [Np/m] : phase constant [rad/m]
: attenuation
: attenuation in dB : attenuation in neper
-attenuator:
-attenuator:
SFG example: 3 dB attenuator
port 1
port 2
port 1
port 2
signal flow graph (SFG):
JUAS Proc. 2024 II.2.7.7.2, pp. 843/844

## Slide 22: S-Matrix Examples – -port
Ideal amplifier (gain stage)
Low-noise RF transistor
  Avago VMMK-1218
  E-pHEMT GaAs FET
    The S-parameters are different at other frequencies and operational conditions
    The transistor requires impedance matching networks at in- and output
: voltage gain
: voltage gain in dB
port 1
port 2
Datasheet Avago VMMK-1218:
port 1
port 2
JUAS Proc. 2024 II.2.7.7.2, pp. 844/845

## Slide 23: S-Matrix Examples – -port
-port resistive power divider
  The transfer-loss between -ports is 6 dB.
Ideal circulator
  Matched, but not reciprocal
port 1
port 2
port 3
port 1
port 2
port 3
Isolator, based on the circulator
  Terminating, e.g., port 3 internally results in a -port, called isolator
port 1
port 2
JUAS Proc. 2024 II.2.7.7.3, pp. 845/846

## Slide 24: S-Matrix Example – -port
Ideal directional coupler
  Matched, symmetric, infinite isolation
  Distinguishes between forward and reflected signal power on the main line port 1-2
    Forward power at coupled port 3
    Reflected power at coupled port 4
port 1
port 2
port 4
port 3
input
isolated
transmitted
coupled
https://en.wikipedia.org/wiki/Power_dividers_and_directional_couplers
double-symmetry
JUAS Proc. 2024 II.2.7.7.4, pp. 846/847

## Slide 25: S-Matrix Example – 4-port
Ideal, lossless TEM directional coupler
  The coupled port 3 is in-phase with the input port 1
  The main line output port 2 is in quadrature phase ( phase delay) with the input port 1
  Lossless TEM direction coupler:
Lossless conditions:
JUAS Proc. 2024 II.2.7.7.4, pp. 847/848

## Slide 26: S-Parameters in Practice
In practice, S-parameters are a function of the frequency:
  Some instruments or applications can also provide time-domain S-parameters
In most real-world practical situations, S-parameters are acquired by a measurement, e.g., characterization of a RF component or sub-system by a VNA.
  By characterizing the DUT over a range of frequencies, in steps of
Also, numerical RF analysis tools (Qucs, ADS, Microwave Office, etc.) generate S-parameters through linear RF circuit / systems simulations.
  Numerical EM software tools (CST, HFSS, etc.) and PCB tools (Cadence Allegro) can also generate S-parameters
Both application types, VNA measurements and RF/EM simulation software exchange S-parameters on a file basis
  The SnP Touchstone ASCII file format is de-facto the industry standard for S-parameters
  Example Touchstone s2p file:
JUAS Proc. 2024 II.2.7.8, pp. 848/849

## Slide 27: SnP Touchstone S-Parameter Files
-port VNA file
! header
# format
frequency
[dB]
[deg]
Touchstone v1.1 example file
v2.0 is different, file ext. *.ts
The file name extension specifies the number of ports
  Attention: NOT equal to the number of columns! The carriage return (CR) is different between s1p, s2p and s3p, s4p files!
The comment header (!) includes general information, e.g., type of instrument, measurement time, etc.
The format line (#) defines the format (mag[dB]/angle[deg], mag/angle, real/imag), stimulus units and the reference impedance
The column delimiter varies, e.g., space, comma, semicolon, etc.
  Column order in the example file: f_Hz S11_dB S11_deg S21_dB S21_deg S12_dB S12_deg S22_dB S22_deg
JUAS Proc. 2024 II.2.7.8, p. 849

## Slide 28: T-Parameters
Cascading e.g., -port S-parameter networks is important to characterize a larger RF system.
  Solution: Scattering transfer (T) parameters, which directly relates the waves at input and output
  T-parameters enable cascaded -port networks by simply multiplying their matrices:
  Relation between -port T-parameters and S-parameters:
with:
with:
JUAS Proc. 2024 II.2.7.9, pp. 850/851

## Slide 29: ABCD-Parameters
Also called “chain” parameters, used for cascading networks based on V and I
  Useful for chaining a mix of lumped elements and transmission-lines
  Chaining 2-port ABCD-parameter networks:
  Relation between -port ABCD-parameters and S-parameters:
JUAS Proc. 2024 II.2.7.10, pp. 851/852
Please try to follow
Example II.2.7.3
JUAS Proc. 2024 II.2.7.10, p. 852/853

## Slide 30: General -Port Networks
A general -port may include ports of different technologies, i.e., waveguides, as well as TEM transmission-lines, such as coaxial lines, microstrip lines etc.
  In the frequency range of interest different modes may propagate at each physical port, e.g., several waveguide modes in a rectangular waveguide and/or higher order modes in a coaxial line..
  Each EM-mode must then be represented by a distinct modal port.
    This is very important in EM-simulation to ensure the absorption of the energy for all modes!
  The number of modal ports needed generally, increases with frequency, as more waveguide modes can propagate.
physical -port
modal -port
: -polarization of the circular mode
JUAS Proc. 2024 II.2.7.11, pp. 853-855

## Slide 31: Summary
The scattering (S) parameters are based on incident and reflected normalized complex voltage waves (power waves), defined at the ports of a RF network.
S-Parameters are used to characterize a linear, time-invariant RF component, circuit or sub-system as function of frequency under realistic operational conditions
  The S-parameters are given in a matrix notation, and have complex values
The characteristic of the S-matrix may provide additional details about the network, such as reciprocity, symmetry, losses.
Typically, the S-parameters matrix of a RF network is acquired by measurement characterization with a vector network analyzer (VNA), or by a numerical analysis, e.g., circuit analysis or electromagnetic simulation software
The S-parameter matrices of a set of networks can be converted to transfer (T) parameter matrices to enable a simple cascading of those networks
The number of logical, modal ports might be higher than the number of physical ports for a general RF network utilizing various transmission-line technologies.

## Slide 32: Backup Slides

## Slide 33: The Scattering Matrix (2)
Its simplest form is for a passive 1-port network:
  with the reflection coefficient:
Most popular is the 2-port network:
  An unmatched load, present at port 2 with a reflection coefficient transfers to the input port as:
reference plane
-port
port 1
-port
port 1
port 2

## Slide 34: Numerical lossless / lossy Examples
It is evident, this ideal -port coupler is symmetric and reciprocal
It also is matched:
But is it lossless or lossy?
1’
1
2’
2
-port series-network
-port ideal directional coupler
lossless | lossy

## Slide 35: Numerical lossless / lossy Examples
Multiply matrix columns by itself with the conjugate complex
  and test for
1’
1
2’
2
-port series-network
-port ideal directional coupler
lossless | lossy

## Slide 36: Numerical lossless / lossy Examples
Multiply all different matrix columns with the conjugate complex
  and test for
1’
1
2’
2
-port series-network
-port ideal directional coupler
lossless | lossy