## Slide 1: RF Engineering Introduction to the Smith Chart
Christine Völlinger & Manfred Wendt – CERN

## Slide 2: Outline and Objectives
Signals and reflections on transmission-lines
  Reflections effects of pulse signals on transmission-lines due to characteristic-termination impedance mismatch
  Standing waves on transmission-lines for continuous wave (CW) sinusoidal signals, definition of the reflection coefficient
  Relation between reflection coefficient, standing wave ration and return loss
The Smith chart
  Refresher: Visualization of a complex impedance in the frequency domain
  Definition of the Smith chart, mapping the complex impedance / admittance plane with the complex reflection coefficient
  Basic facts and important points on the Smith chart
  Examples for a and series circuit, and for a transmission-line terminated with a series circuit.
  Operation of a transformer based on a transmission-line as a (normalized) impedance inverter
Smith chart exercise (if time permits…)
JUAS Proc. 2024 II.2.x.y.z, p. nnn
Please note the references to the JUAS proceedings!

## Slide 3: Transmission-lines
TEM: coaxial cable, PCB stripline, micro-stripline, co-planar waveguide, etc.
  but also, TE / TM: waveguides (rectangular, circular, elliptical)
Transport RF energy (EM waves) from a RF source to a load.
Physical length becomes relevant for
Reflections occur if the load impedance is not matched to the characteristic impedance of the TL
!
load
RF source
transmission-line, here: TEM coaxial
with losses no losses
Remember: The characteristic impedance is defined by the cross-section geometry and is typically a real number with the unit

## Slide 4: TL: Signal visualization in time-domain
Circuit simulator applet: https://www.falstad.com/circuit/
  Load file: IdealTL_DCswitched_Z050-RL.txt
    Change the load resistor value: RL = 50, 100, 25 Ω
    Operate the switch and observe the signals at the beginning, and at the end of the transmission-line.
  Load file: IdealTL_pulsed_Z050-RL.txt
    Change the load resistor value: RL = 50, 100, 25 Ω
    Observe the signal waveforms! Can you predict the values?!
      (Press Run/STOP and hover with the mouse over the waveform)
JUAS Proc. 2024 II.2.6, p. 807

## Slide 5: TL: Operating with sinusoidal signals (FD)
For a single frequency, continues wave (CW) signal on a transmission-line
  Superposition of forward and backward b traveling waves
  standing waves
Reflection coefficient
  is related to the impedance ratio:
    The load impedance can be complex
  is a complex number
Reflections also originate due to discontinuities of the TL along
  Same does not prevent reflections! EM-field effect!
waves
E-fields
voltages
impedances
matched:
pure travelling waves
open:
standing waves
short:
standing waves
JUAS Proc. 2024 II.2.6.1, pp. 810/811
transmission-line
load
source
(sine-wave generator)
p1
p2
incident wave:
reflected wave:
here: for a lossless TL ()

## Slide 6: TL: Voltage Standing Wave Ratio (VSWR)
The voltage standing wave ratio (VSWR) expresses the ratio between the maximum and minimum voltage of a standing wave along a transmission-line
  The VSWR is a function of the frequency.
The return loss (RL) is another way to express reflection effects
with:
 |  | Return Loss [dB] | Refl. Power | Inc. Power
0.0 | 1.00 |  | 0.00 | 1.00
0.1 | 1.22 | 20.0 | 0.01 | 0.99
0.2 | 1.50 | 14.0 | 0.04 | 0.96
0.3 | 1.87 | 10.5 | 0.09 | 0.91
0.4 | 2.33 | 8.0 | 0.16 | 0.84
0.5 | 3.00 | 6.0 | 0.25 | 0.75
0.6 | 4.00 | 4.4 | 0.36 | 0.64
0.7 | 5.67 | 3.1 | 0.49 | 0.51
0.8 | 9.00 | 1.9 | 0.64 | 0.36
0.9 | 19.00 | 0.9 | 0.81 | 0.19
1.0 |  | 0 | 1.00 | 0.00
 |  | Return Loss [dB] |  | 
0.0 | 1.00 |  | 0.00 | 1.00
0.1 | 1.22 | 20.0 | 0.01 | 0.99
0.2 | 1.50 | 14.0 | 0.04 | 0.96
0.3 | 1.87 | 10.5 | 0.09 | 0.91
0.4 | 2.33 | 8.0 | 0.16 | 0.84
0.5 | 3.00 | 6.0 | 0.25 | 0.75
0.6 | 4.00 | 4.4 | 0.36 | 0.64
0.7 | 5.67 | 3.1 | 0.49 | 0.51
0.8 | 9.00 | 1.9 | 0.64 | 0.36
0.9 | 19.00 | 0.9 | 0.81 | 0.19
1.0 |  | 0 | 1.00 | 0.00
symbols: incident (forward) wave: reflected (backward) wave:
JUAS Proc. 2024 II.2.6.1, pp. 810/811

## Slide 7: Reminder: Circuit Vocabulary
Resistance, impedance, reactance are inverse proportional to conductance, susceptance, admittance
resistor, with: resistance
conductor, with: conductance
inductor, with: inductance
reactance
capacitor, with: capacitance
susceptance
complex impedance
example:
complex admittance
example:
or
complex impedance
or
complex admittance
suceptance
reactance
JUAS Proc. 2024 II.2.6.2, pp. 811/812

## Slide 8: Reminder: The complex -Plane
Different ways to visualize
  magnitude / phase
  real / imaginary
  complex -plane
    Plot in the complex plane with as parameter
complex impedance plane
JUAS Proc. 2024 II.2.6.2, p. 813

## Slide 9: The Smith Chart (1)
The Smith chart is a calculation tool, divided in 2 parts:
  A transformation of the complex, normalized impedance and admittance planes on a circle.
  A set of “rulers” below, for additional computations
    VSWR, return and reflection loss, etc.
At a 1st look the Smith chart is quite overwhelming
  In this introduction the focus is on the complex z-plane
JUAS Proc. 2024 II.2.6.3, p. 814

## Slide 10: The Smith Chart (2)
The Smith chart (in impedance / admittance coordinates) represents the complex -plane (in polar coordinates) within the unit circle.
It is a conformal mapping of the complex -plane on the -plane by applying the transformation:
⇒ the real positive half plane of is thus transformed (Möbius) into the interior of the unit circle!
complex -plane
complex -plane
JUAS Proc. 2024 II.2.6.3, p. 815

## Slide 11: The Smith Chart (3)
In the classic paper Smith chart the impedance is normalized: to a reference impedance , typically, to the characteristic impedance of the coaxial cable transmission-lines used in RF / microwave engineering: .
The normalized form of the transformation follows then as:
The Smith chart is a parametric graph
  with the frequency as parameter
  and the normalized, complex impedance and complex reflection coefficient as variables
    also, the normalized, complex admittance is mapped and can be used as variable.
In the past
  The Smith chart was used as a calculation tool for impedance matching, e.g., antennas to transmitters or receivers, amplifier input / output stages, couplers of accelerating cavities, etc.
At presence, the Smith chart is still popular
  for visualization purposes, e.g., vector network analyzer (VNA) measurement of input / output impedances (display of the scattering parameters), in software tools, etc., usually using the un-normalized impedance
  for the optimization of the coupling between RF source and a cavity resonator.
JUAS Proc. 2024 II.2.6.3, p. 815

## Slide 12: Quiz (1)
No signal reflections are observed at the end of a transmission-line, this means:
The Smith chart transforms the complex impedance plane onto the complex Gamma (reflection coefficient) plane within the unit circle.

## Slide 13: The Smith Chart (4)
In the Smith chart, the complex reflection factor is expressed in linear polar coordinates, representing the ratio of backward vs. forward traveling waves.
is the ratio between backward and forward wave
(implied forward wave )
JUAS Proc. 2024 II.2.6, p. 816

## Slide 14: The Smith Chart (5)
mismatch losses
available source power
The distance from the center of the directly proportional to the magnitude of the reflection factor and permits an easy visualization of the matching performance.
  In particular, the perimeter of the diagram represents total reflection: .
  (power dissipated in the load) = (forward power) – (reflected power)
JUAS Proc. 2024 II.2.6.3, p. 816

## Slide 15: The Smith Chart – “Important Points”
Important Points:
Short Circuit
Open Circuit
Matched Load
On the circle : lossless element
Upper half: ”inductive” = positive imaginary part of
Lower half: ”capacitive” = negative imaginary part of
  Outside the circle, : active element, e.g., tunnel diode reflection amplifier
Short Circuit
inductive
capacitive
Matched Load
Open Circuit
JUAS Proc. 2024 II.2.6.3, p. 816

## Slide 16: The Smith Chart – Basic Example (1)
Complex impedance based on lumped element components
Calculate for a given frequency, e.g., :
Calculate the normalized impedance
  Locate in the Smith chart
  Retrieve
Repeat for other frequencies…
incident wave
reflected wave
with:
reactive
resistive
JUAS Proc. 2024 II.2.6.3, pp. 817/818

## Slide 17: The Smith Chart – Basic Example (2)
…and for different component values and circuit combinations
incident wave
reflected wave
with:
incident wave
reflected wave
with:
JUAS Proc. 2024 II.2.6.3, pp. 817/818

## Slide 18: Quiz (2)
Prompts |  | Possible Answers
Point A | A5 | 
Point B | B4 | 
Point C | C1 | match
Point D | D3 | Point in the capacitive half plane
Point E | E6 | 
 |  | Point in the inductive half plane
Prompts |  | Possible Answers
Point A | A5 | 
Point B | B4 | 
Point C | C1 | 
Point D | D3 | Point in the capacitive half plane
Point E | E6 | 
 |  | Point in the inductive half plane
Smith chart (simplified)
A
B
C
D
E

## Slide 19: Quiz (3)
Trace with marker points in the simplified Smith chart for an RL series impedance
  There is no frequency related to points A and B
Smith chart (simplified)
A
B
Please try to complete
Exercise II.2.6.2
JUAS Proc. 2024 II.2.6.3, p. 820

## Slide 20: The Smith Chart – TL Transformer (1)
S-parameter of a lossless transmission-line:
  Phase delay (electrical length) of with: (wave number)
backward transmission
coefficient S12
forward transmission
coefficient S21
incident wave
reflected wave
The lossless transmission-line adds a phase delay of , seen at its input, , to the reflection coefficient at its output:
This results in a transformation of the impedance at the end of the line to a different impedance at the input of the line
  The Smith chart offers an effective, simple graphical way to calculate this transmission-line based impedance transformation
JUAS Proc. 2024 II.2.6.4.3, pp. 825/826

## Slide 21: The Smith Chart – TL Transformer (2)
@
Based on the previous example
Calculate the normalized impedance for locate the point in the Smith chart.
  Notice the corresponding value of , and read the -length value on the rim
Add by rotating by
  From to
    The phase is subtracted, therefore clockwise rotation!
Notice the value of and read the corresponding value of the normalized impedance
  Calculate the transformed impedance
  What is the equivalent circuit, and what are the component values?
    …and what is the physical length of the transmission-line?
      assuming a coaxial cable as transmission-line with a dielectric constant of
JUAS Proc. 2024 II.2.6.4.3, pp. 825/826

## Slide 22: The Smith Chart – TL Transformer (3)
A transmission-line of length transforms a reflection at the end of the line to its input as
This results the unitless, normalized impedance at the end of the line to be transformed into: at the beginning of the line
A short circuit at the end of the -transformer is transformed to an open, and vice versa
  This is the principle of the -resonator.
when adding a transmission-line
to some terminating impedance we rotate
clockwise through the Smith-Chart
impedance
impedance
JUAS Proc. 2024 II.2.6.4.3, pp. 827

## Slide 23: A Smith Chart matching Exercise
A network analyzer measurement of a RF amplifier, operated at shows a reflection coefficient of
  Locate in the paper Smith chart
  What is the un-normalized impedance ?
  What is the lumped-element series equivalent circuit and what are the element values the make up ?
  What circuit element , and its value, is required to match the impedance to ?
    Please use the paper Smith chart and find the value of the normalized matching impedance
    Then de-normalize the value and calculate the value of the lumped element.

## Slide 24
Locate on the circle ANGLE OF REFLECTION COEFFICIENT IN DEGREES
  Mark with a line
Locate on the ruler RFL. COEFF, E or I
  Mark the point crossing the -line

## Slide 25
Follow the real part circle to on the real axis RESISTANCE COMPONENT ()
Follow the imaginary part to to the positive imaginary axis CAPACITIVE REACTANCE COMPONENT ()
De-normalize the impedance for
  capacitive

## Slide 26: Impedance Matching
As the imaginary part of the impedance is negative, the lumped-element equivalent series-impedance circuit is a RC series circuit
  We are in the lower, capacitive half plane of the Smith chart
We need to compensate the capacitive element by an inductive series element to get
  This is called a “dual” network:
  This is equivalent with the Smith chart operation:

## Slide 27: Final Remarks
The Smith chart is a special type of a parametric plot for the complex impedance or admittance, mapped to the complex reflection coefficient.
The use of the Smith chart can be viewed in two ways:
  As a calculation and impedance matching tool as originally envisioned.
    However, today this will happen rather rarely!
    Please notice: All the examples presented are based on the paper-style Smith chart, which is always based on an unitless, normalized impedance
  As a visualization tool for the complex impedance, along with the reflection coefficient
    Still very popular and useful for displaying and analyzing on a vector network analyzer, also used in data-sheets, and RF simulation and education software.
    Here the Smith chart utilizes the actual complex impedance in units of ! Markers on the parametric trace give all relevant information, including the element values of a selected equivalent circuit.
Old, but excellent information on transmission-lines and standing waves:
  https://www.youtube.com/watch?v=I9m2w4DgeVk
  https://www.youtube.com/watch?v=DovunOxlY1k&t=38s
Smith chart education software (only for MS-Windows):
  https://www.fritz.dellsperger.net/smith.html

## Slide 28: Backup Slides

## Slide 29: Navigation in the Smith Chart (1)
This is a “bilinear” transformation with the following properties:
Generalized circles are transformed into generalized circles
  circle circle
  straight line circle
  circle straight line
  straight line straight line
Angles are preserved locally
    a straight line is equivalent to a circle with infinite radius
    a circle is defined by 3 points
    a straight line is defined by 2 points

## Slide 30: Navigation in the Smith Chart (2)
 | Up | Down
Red circles | Series L | Series C
Blue circles | Shunt L | Shunt C
Shunt L
Shunt C
Series C
Series L
in red: impedance plane ()
in blue: admittance plane ()

## Slide 31: Navigation in the Smith Chart (3)
Red arcs | Resistance
Blue arcs | Conductance
Con-centric circle | Transmission line going Toward load Toward generator
Red arcs | 
Blue arcs | 
Con-centric circle | Transmission line going Toward load Toward generator
Toward load
Toward generator