## Slide 1: Eigenmodes simulation of a cylindrical resonator with CST
Michela Neroni*
Acknowledgments: Andrea Mostacci, Christine Vollinger, Manfred Wendt
*michela.neroni@cern.ch

## Slide 2: Eigenmodes simulation of a cylindrical resonator with CST
CST Studio Suite: the Eigenmode solver
Model geometry
Simulation set-up
Eigenmodes results
Field plots
Figures of merit: Q, R/Q

## Slide 3: CST Studio Suite: the Eigenmode solver
CST Studio Suite® is an Electromagnetic Field Simulation Software. It includes different modules for design and optimization of accelerator devices operating in a wide range of frequencies. https://www.3ds.com/products/simulia/cst-studio-suite
With the Eigenmode solver, the Maxwell’s eigenvalues problem is solved. The problem involves finding the eigenvalues and eigenmodes of the equations which correspond to the medium’s resonant frequencies and associated electric and magnetic field distributions.
Other electromagnetic simulation software exits:
ANSYS HFSS (Tutorial JUAS23 and described in the JUAS proceedings) it has a free student version: https://www.ansys.com/academic/students/ansys-electronics-desktop-student
JUAS proceedings: chapter II.2.5, pp. 794-806

## Slide 4
CST Studio Suite: the Eigenmode solver

## Slide 5
CST Studio Suite: the Eigenmode solver
1
2
3
4

## Slide 6
CST Studio Suite: the Eigenmode solver
Save the project with the name ‘Cavity-JUAS25’

## Slide 7: Model geometry
Properties
l_cavity = 310 mm
d_cavity = 296 mm
l_port = 92 mm
d_port = 96 mm
What is the fundamental mode?
Is this a pillbox cavity?
* Pozar, Microwave engineering, 4th ed., Wiley
cavity
port
port
h
a

## Slide 8: Model geometry
Let’s build the model…
From Modeling, select the cylindrical shape.
Press ESC to open a dialog box where the coordinates can be inserted.
To symmetrically center the cylinder respect to the origin of the axis
1
2
Select material as vacuum
When typing a variable, a new window will pop up and you will be able to select the variable type, unit and value
3

## Slide 9: Model geometry
Let’s build the model…
Spacebar to fit the full model into the view
You can access the cavity geometry here
You can access and modify the created variables under the Parameter List
Click here to activate the rotation

## Slide 10
The input and output ports can be built following the same procedure.
Model geometry
l_port = 92 mm
d_port = 96 mm

## Slide 11
Model geometry
The output port can be created mirroring the input port with respect to the XY plane
Select the input_port under Components
1
Click on Transform  Mirror
2
3

## Slide 12
Model geometry
You can rename the second port as “output_port”
The model is now complete!

## Slide 13
Model geometry
After creating the three cylinders, let’s unite them
Select the cavity and the two ports
1
Click on Boolean  Add
2

## Slide 14
Simulation set-up
After finalizing the 3D geometry, we can move to the Simulation tab.
We would need to define, from the Settings at the top left:
1- Frequency
2- Background
3- Boundaries

## Slide 15
Simulation set-up
Click on Frequency
Let’s choose a range of Frequency from 0 to 1 GHz
1
2

## Slide 16
Simulation set-up
1
2
Click on Background

## Slide 17
Simulation set-up
Let’s impose the condition of zero tangential electric field at the wall
Click on Boundaries
1
2

## Slide 18
Simulation set-up
Click on Setup Solver to input the Eigenmodes simulation settings
1
We want to see the first three eigenmodes
Adaptive mesh refinement process will refine the mesh until convergence criterium is satisfied.
Click on Start to run the simulation
3
Select 3 modes to be checked during the mesh adaptation
2

## Slide 19
Eigenmodes results
You can see the results of frequencies of the first three resonant modes in the Messages tab, or under 1D Results, Mode Frequencies in the Navigation Tree.
To distinguish which type of modes we obtained, we need to look at the field pattern. A TM mode would have a component of electric field on the propagation axis-z.

## Slide 20
Field plots
Let’s have a look to the field pattern of each mode
The E-field, H-field and other quantities for each mode can be found in the Navigation Tree, under 2D/3D Results.

## Slide 21
Field plots
From the 2D/3D Plot toolbar, you can change the view and plot the field on a plane
We can look at the E-field of the first mode on the YZ plane to understand if it has a longitudinal component.

## Slide 22
Mode 1 and 2 are modes (two possible polarizations of the same mode) because the electric field has no longitudinal component.
Mode 3 is mode. The electric field is longitudinal.
mode used for particles acceleration!
It is not a pillbox cavity because the fundamental mode (lowest cut-off frequency) corresponds to a TE mode!
Field plots

## Slide 23
From the RF lectures…
C. Vollinger – RF Engineering lecture (22nd February)
Mode's chart
mode is the fundamental one if
shows up for ratios . This mode is independent of the cavity height h  pillbox cavity
*
* Pozar, Microwave engineering, 4th ed., Wiley
Field plots
 We will focus on Mode 3 () for the following Q-factor and R/Q calculations.

## Slide 24
Figures of merit: Q, R/Q
The Q factor can be calculated by making use of the perturbation method:
The electromagnetic problem is solved ignoring the losses as a first step. Including the information on the material conductivity of the walls, we introduce a power dissipation which can be calculated from the H-field of the mode and the conductivity of the wall material.
From the RF lectures…
Power dissipated in the resonator (through the walls). It is directly related to the magnetic field H:
The unloaded Q factor it’s a measure of the resonance quality.
Energy stored in the cavity

## Slide 25
See A. Mostacci “Introduction to RF” – JUAS 2025
Surface current density
Figures of merit: Q, R/Q
Circumferential H-field on XY plane
Mode 3
MHz
Mode 3
MHz

## Slide 26
Figures of merit: Q, R/Q
Click on Result Templates
1
2
3
4
5
Select Q-factor (Perturbation) and Mode 3 (the one of interest for acceleration)
We consider stainless-steel walls with conductivity

## Slide 27
Figures of merit: Q, R/Q
From the Result Template, the Q factor can be evaluated:
1
2

## Slide 28
Another important figure of merit for accelerators is the R over Q.
Figures of merit: Q, R/Q
From the RF lectures…
C. Vollinger – RF Engineering lecture (21st February)
CST uses the so called “Linac definition” of R-over-Q (different solvers can use a different definition):
It is a measure of the cavity ability to convert the stored energy into acceleration. It is related to the cavity geometry (useful for cavities design).

## Slide 29
Figures of merit: Q, R/Q
Click on Result Templates
1
2
3
Select R over Q and Mode 3.
Direction Z for field integration
Transient time factor  consider particle velocity 
4

## Slide 30
Figures of merit: Q, R/Q
2
From the Result Template, the R-over-Q can be evaluated:
1
The actual R-over-Q of the cavity is
Normal conducting accelerating cavities R/Q

## Slide 31
Additional exercises
Vary the cavity length and radius to test yourself in guessing the fundamental mode.
Try to change the material electrical conductivity to observe how the Q factor changes. What happens to the R/Q?

## Slide 32
References
CST Studio Suite®, https://www.3ds.com/products/simulia/cst-studio-suite
Mostacci, A., “Introduction to RF”, JUAS24, Archamps, February 2024
Vollinger, C. et Wendt, M., “RF Engineering”, JUAS24, Archamps, February 2024
Pozar, D. M., “Microwave Engineering”, 4th edition, Wiley and sons
Wendt, M., “RF Training: Numerical Analysis”, CAS Advanced, Sevrier, November 2022
Udongwo, S. et al., “Numerical Simulations”, CAS 2023, RF for Accelerators, Berlin, June 2023
Migliorati, M., “Simulation of a Pillbox cavity with CST”, JUAS18, Archamps, February 2018
CST Studio Suite® 2024 Help