## Slide 2: High Intensity ECN3 (HI-ECN3) Project: SPS Beam Dump Facility
M. Fraser (SY-ABT-BTP) presenting on behalf of the HI-ECN3 Project Team
214th TE-TM meeting, CERN, Geneva, Switzerland
4th November 2024
https://hiecn3.web.cern.ch

## Slide 3
Beam Dump Facility (BDF) / SHiP
R. Jacobsson
Direct search for Feebly Interacting Particles (FIPs) at a new Beam Dump Facility to be installed in ECN3 to exploit 4×1019 protons (400 GeV/c) per year for 6×1020 POT over 15 years to overcome the small cross-section of ultra-rare events:
SHiP Physics Proposal: Rep. Prog. Phys. 79 (2016) 124201 published 2016
SPS Beam Dump Facility Comprehensive Design Study: CERN-2020-002 published 2020
High energy → production of charmed and beauty mesons
High ppp & POT → overcome small production cross-section of rare events of hidden particles
High ρ, Z & A → maximize p+ interaction
Shortest λ → force absorption of K & π to reduce muon & neutrino background

## Slide 4
SHiP’s bow wave is made of & …
R. Jacobsson
C. Ahdida et al., Findings of the Physics Beyond Colliders ECN3 Beam Delivery Task Force, CERN-PBC-REPORT-2023-001
Expected background:
< 1 event for 6×1020 POT
Richard will discuss the SHiP magnet systems in detail

## Slide 5
Study Project Approved Project
Upgrade of beam intensity at North Area and SHiP beam-dump (BDF/SHiP) experiment approved recently…
… with ~ 62 MCHF (over 7 years) reserved for the High Intensity upgrade of ECN3 (HI-ECN3) project in CERN’s Medium-Term Plan ratified by CERN Council in June 2024.
Approved together with ~ 170 MCHF for consolidation of the North Area (NA-CONS project)
The HI-ECN3 project is a part of CERN’s…
“…broad diverse scientific programme, complementary to the collider and carried out mainly at the injectors: continuously upgraded and expanded (e.g. recently the ECN3 beam intensity upgrade at the North Area).”
Fabiola Gianotti
For more information on the competitive ECN3 decision process:
C. Ahdida et al., Findings of the Physics Beyond Colliders ECN3 Beam Delivery Task Force, CERN-PBC-REPORT-2023-001
G. Arduini, C. Vallée, J. Jaeckel (eds.) Post-LS3 Experimental Options in ECN3, CERN-PBC-REPORT-2023-003

## Slide 6
Francesco VELOTTI & Laurie NEVAY
Rui FRANQUEIRA XIMENES
Jean-Louis GRENARD
Francois BUTIN
Claudia AHIDIDA
Project Safety Officer (PSO): Melania AVERNA
Project & Experiment Safety Support (PESS) Correspondent: Jamie CURRIE
Fernando PEDROSA
Luigi ESPOSITO
Experiment Project Leader: Richard JACOBSSON
SHiP Experiment Safety Correspondent: Letizia DI GIULIO
PL: Matthew FRASER
DPL: Claudia AHDIDA
HI-ECN3 Project Structure
TE in WP2
TE-MSC: TCC2 magnets / BDF dilution system
TE-MPE: Machine protection
TE in WP5
TE-CRG: Dismantling NA62 LKr calorimeter / cooling of SHiP muon shield
TE in WP4
TE-MSC: Magnetised hadron stopper
TE in SHiP Collaboration
TE-MSC: SHiP spectrometer magnet
TE in WP3
TE-MPE: Machine protection

## Slide 7
North Area Consolidation & Upgrade
Transfer Tunnel (TT) 20:
inc. TT20 TED
TDC2: TT20 splitters
TCC2 Targets:
T2 / T4 / T6
SPS Slow Extraction from
Long Straight Section 2 (LSS2)
Timeline = completion in LS3 (2026-2029) and LS4
NA-CONS consolidation project
TCC8: T10 / TAX
→ BDF
New Beam Dump (TIDVG4)
HI-ECN3 project
Timeline = completion after LS3
~ 1.7 km !
EHN1
EHN2
CERN Prévessin Site
ECN3

## Slide 8
HI-ECN3 Operation
Operation out to late 2040s:
beyond HL-LHC
(frequency & length of LS’s TBC)
HI-ECN3
Commissioning
HI-ECN3
Operation
Today
NA available exclusively for EHN1/2 from mid-2029:
Test-beam users & other POT demanding experiments
(e.g. AMBER, MuonE)
ECN3 beam to dump in P42 for commissioning of TCC2
whilst construction ongoing
CERN Accelerator Schedule
NA-CONS
NA-CONS Phase II
(TBC)
NA-CONS Phase I
M. Lamont, Updated schedule for CERN’s accelerators, CERN Bulletin, 4 October 2024
HI-ECN3
TDR Phase

## Slide 9
HI-ECN3 Project Timeline
TDR Phase
(Facility)
TDR extension?
Long Shutdown 3
Upgrades to NA with NA-CONS
LS4
Below freezing design for SCE!
(Detailed design for consultant before contractor Invitation to Tender)
July 2026
Critical path:
CE procurement & works
Dismantling
Beam on BDF Target

## Slide 10
How many protons for BDF / SHiP? (i)
Short 7.2 s SHiP cycles with a 1.2 s FT (~ 1 s spill) vs. 14.4 s SFTPRO period
SPS Page 1 during BDF prototype target test at T6 in 2018

## Slide 11
How many protons for BDF / SHiP? (ii)
Protons to ECN3 (BDF/SHiP)
Protons to TCC2 (other NA users)
North Area needs
~ 51019 protons/year…
a la CNGS (~41019 p+/y)
… but, slow extracted…
…unprecedented !
T. Prebibaj et al., SPS Operation and Future Proton Sharing Scenarios for the ECN3 facility, CERN-PBC-Notes-2023-001
Possible after ~ 10 years of
SX R&D with bent crystals

## Slide 12
Slow Extraction from LSS2 in SPS

## Slide 13
LSS4 gonio R&D:
~ 55% loss reduction
To be deployed operationally in 2024
Crystal Shadowing of electrostatic septa
L. Esposito et al., Progress on optimised TECA and MVRA production, SLAWG #76: Crystal shadowing and production, August 2024
F. M. Velotti et al., Phys. Rev. Accel. Beams 22, 093502 (2019)
down
To SPS
x
s
ZS
Unaffected beam
Deflected beam
up
TECS (LSS2)
(...)
Deflected beam
TECA (LSS4)
To TT20
circulating
deflected
LSS2 gonio already operational with 20% loss reduction
Thin, bent silicon crystal ~ 2 mm thick, 2 mm long

## Slide 14
Objective: achieve an even higher loss reduction factor (x10?!) with advanced crystal technology (multiple thin, bent crystals aligned for Volume Reflection) installed in SPS
Crystal Shadowing of electrostatic septa (ii)
L. Esposito et al., Progress on optimised TECA and MVRA production, SLAWG #76: Crystal shadowing and production, August 2024
F. M. Velotti et al., Phys. Rev. Accel. Beams 22, 093502 (2019)

## Slide 15
Beam Transfer across the North Area

## Slide 16
Field-free region
Horizontally deflected by the B-field
Continues straight: no B-field
Losses (~5%)
Shared delivery:
splitting
16
T2
T4
T6
TT23
TT24
TT25
H2
H4
H6
H8
P4
P42
M2
EHN1
ECN3
EHN2
LSS2
P41, P61
SPS
TCC8
NA62
TT21
TT22
SFTPRO shared Beam Delivery to ECN3

## Slide 17
T2
T4
T6
TT23
TT24
TT25
H2
H4
H6
H8
P4
M2
EHN1
ECN3
EHN2
LSS2
SPS
No interaction with TCC2 Target
No splitting
in TDC2
TT21
TT22
Dedicated Beam Delivery to ECN3: commissioning
P4 Beam Dump
TBIU
target
TBID
Dedicated delivery:
no splitting
B

## Slide 18
T2
T4
T6
TT23
TT24
TT25
H2
H4
H6
H8
P4
P42
M2
EHN1
ECN3
EHN2
LSS2
P41, P61
SPS
TCC8
No interaction with TCC2 Target
BDF/SHiP
No splitting
in TDC2
TT21
TT22
Dedicated Beam Delivery to ECN3

## Slide 19
BDF/SHiP in ECN3
L. Krzempek, BDF-SHiP Integration in ECN3, EDMS #2936008
ECN3
TCC8
Existing
Access Shaft
B918
B911
Beam from SPS
~ 300 kW (avg.)
~ 2.3 MW (spill)
1 second spill
4 Hz sweep
New
Access
Shaft
BDF’s Target Complex
containing a “thick” high-Z target (Mo/W)
Beam Dilution System
New Target
Service Building
SHiP experiment

## Slide 20
Civil Engineering Scope
New target building: adjacent to building 911 → B. 754 / BB85
New access shaft (PA855), connecting tunnel to ECN3 and access building→ B. 758 / BA85
Underground excavations: in Target complex (TCC8) and Experimental Area (ECN3)

## Slide 21
NA62 in ECN3
ECN3
B918
B911
TCC8
T10
Target
K12 beam line
T10
XTAX
Dismantling will start immediately in LS3 to allow civil engineering works to get underway ASAP

## Slide 22: NA62 Dismantling: an example
*F. Duval, Plans for the NA62 dismantling at LS3C#8, 24 July 2024
Expert technical support from Johan BREMER (TE-CRG)

## Slide 23
TCC2 Upgrades

## Slide 24
Upgrade of TCC2 T4 Target System for BDF/SHiP (i)
Looking downstream from on top of T4 target
H6
H8
To ECN3
To avoid scattering BDF/SHiP beam on air the ECN3 side of XTAX will be replaced by a fixed absorber with a vacuum chamber
Urgent design effort ongoing !

## Slide 25
Today, operation of EHN1 (H6/H8 test beams) is coupled with ECN3 (NA62)
Secondary particles for EHN1 are selected using magnet wobbling system, whilst protons not interacting with the target are transmitted to NA62
x
s
T4 Target
To EHN1: H8
T4 XTAX
To ECN3: NA62
To EHN1: H6
F. Metzger et al, Beam line and parameters, 30th SHiP collaboration meeting, ALU Freiburg, 1 – 4 October 2024
Upgrade of TCC2 T4 Target System for BDF/SHiP (ii)

## Slide 26
T4
A pulsed magnet allows us to decouple proton beams on the dedicated HI-ECN3 cycle in the horizontal plane (in addition to vertical separation to avoid target)
To EHN1: H8
To ECN3: NA62
To EHN1: H6
F. Metzger et al, Beam line and parameters, 30th SHiP collaboration meeting, ALU Freiburg, 1 – 4 October 2024
Upgrade of TCC2 T4 Target System for BDF/SHiP (iii)

## Slide 27
TCC8 / ECN3

## Slide 28: BDF Dilution System
Y. Dutheil, SPS BDF CDS, CERN Yellow Report, CERN-2020-002
Present baseline:
Slow sweep = 4 Hz over a 1 second spill
/2 scheme: independently powered laminated dipole magnets:
  2H + 2V magnets (~ 0.5 mrad, 0.7 Tm per plane)
  de-phased by 90 degrees to give circular spill
Beam profiler(s) to check beam position, size & sweep post-operation
Challenge: protection of the target critical, loss of dilution during single spill will likely damage the target
Independent interlock system needed for redundancy:
  Independent DCCTs measurement current in dilution dipole magnets
  Dedicated “live” beam position monitoring of beam during its sweep
Failure 2H OR 2V
Failure 1H OR 1V
Failure 1H AND 1V
Failure Scenario:

## Slide 29: BDF Target Baseline Design
Baseline beam parameters of the BDF Target operation. https://doi.org/10.23731/CYRM-2020-002
~ 4.0×1019 p+/y
13 x TZM blocks (580 mm)
5x W blocks (780 mm)
~ 1500 mm
Baseline design:
Water-cooled, Mo & W blocks (cladded with Ta)
Tested with beam in 2018 & PIE
TDR phase needed to improve CDS design:
Alternatives to water-cooling to avoid cladding and the risk of development of free radicals (hydrogen)
Helium-cooled pure W design now being prototyped: tests in TCC2 planned in 2025 and 2026
D250 mm

## Slide 30: BDF Target Complex in TCC8 (i)
30
~12 m
~8 m
~4.8 m
Diluted Proton beam from SPS

## Slide 31: BDF Target Complex in TCC8 (ii)
Target area confinement wall (details under study with FIRIA study)
Access chicane
SHiP muon shield MS1
Diluted Proton beam from SPS
Beam instrumentation ?
Magnetised hadron stopper (shielding)

## Slide 32
Summary
BDF/SHiP has been approved to search directly for dark matter at the North Area
CERN has reserved budget in its Medium-Term Plan for the construction of a new facility in ECN3 under the project named HI-ECN3 to fully exploit the investment being made in the North Area Consolidation project
Some ~ 10 years of R&D will converge into a Technical Design Report to realise a slow extracted beam power of 300 kW (avg.) to the North Area
HI-ECN3 TDR will be published in 2026, building on the SPS BDF Comprehensive Design Study published in 2020
First beam on target expected in 2031 to give SHiP at least 2 years of beam before LS4

## Slide 34: NA-CONS / HI-ECN3 Synergy
GRAD team supported by CERN STAFF experts
EP ECN3 Experiment Technical Coordinator (TC)
Richard JACOBSSON
WP2 Coordination Meetings
Francesco VELOTTI
WP3 Coordination Meetings
Rui XIMENES
WP4 Coordination Meetings
Jean-Louis GRENARD
WP5 Coordination Meetings
Francois BUTIN
WP6 Coordination Meetings
Claudia AHDIDA
WP7 Coordination Meetings
= adhoc NA-CONS WC4
Fernando PEDROSA
Technical Design Study
Frequency is choice of WPL ~ Biweekly
Project Coordination & Integration
Project Management
Adhoc Meetings
Project Team Meetings
Claudia AHDIDA /
Matthew FRASER
~ Weekly
ICEA
Francois BUTIN /
Jean-Louis GRENARD
~ Biweekly
Joint with NA-CONS ICEA when relevant
HI-ECN3 TCC
Claudia AHDIDA /
Matthew FRASER
~ Monthly
Joint with NA-CONS TCC when relevant
Project Board Meetings
Matthew FRASER
~ Adhoc
NA-CONS / HI-ECN3
Steering Committee Meetings
Roberto LOSITO
~ Quarterly
Reviews:
C&S, Safety, Technical etc.
Joint NA-CONS when relevant
TBC
CERN Management
IEFC
Brennan GODDARD
when reporting requested
ATS-MB
Mike LAMONT
when reporting requested
NA62 TC
Decommissioning
Hans DANIELSSON
ICL
(upstream TCC2)
EN-ACE
Joint NA-CONS / HI-ECN3 TCC meeting series: critical for advancement of TCC2 upgrades fro BDF & implicated systems, next items include P42 dump and BA82
HI-ECN3 ICEA:* first dedicated agenda on integration to take place in two weeks (impacted NA-CONS items already discussed in ICEA for many months) co-chaired by Francois Butin and Jean Louis Grenard
WP7.1 NA-CONS Synergism: collecting and documenting impacted systems and NA-CONS WPs key role played by Fernando PEDROSA & Thomas ZICKLER (timing, magnets, power converters, BA82, etc.)
*M.A Fraser & Y. Kadi, ICEA Mandate for the HI-ECN3 Study Project, Memorandum, EDMS#3018359, 25 Jan 2024

## Slide 35
Prompt Radiation in TCC8
Cross-sectional view
Side view
Shielding design is well optimized for the prompt radiation
Avg. intensity of 5.6×1012 p/s
(-20 cm < x < 80 cm)
(13260 cm < z < 134380 cm)
(-20 cm < x < 80 cm)
(13260 cm < z < 13380 cm)
C. Ahdida et al., RP Studies for CERN's HI-ECN3 Facility, presented at SATIF-16, 29 May 2024

## Slide 36
Prompt Radiation in TCC8
Cross-sectional view, target level
Along x-axis, working height
Upstream of vessel w/o upstream shielding Preliminary worst case manual intervention scenario
The shielding design contains well the high residual dose rates reaching in the central target region several 10 Sv/h after 1 month of cool-down
The residual dose rates outside the shielding are < 1 µSv/h
1 month cool-down
x [0,40]
x_beam = 26 cm
Shielding removed
After opening vessel & removing shielding, residual dose rates of several 100 µSv/h are expected
Supervised Radiation Area on the sides
Further optimization by movable shielding
Total POT 6×1020
(13240 cm < z < 13390 cm)
(15 cm < y < 45 cm)
(13240 cm < z < 13390 cm)
1 month
(-15 cm < x < 80 cm)
100 rem = 1Sv
C. Ahdida et al., RP Studies for CERN's HI-ECN3 Facility, presented at SATIF-16, 29 May 2024

## Slide 37
Environmental Aspects
C. Ahdida et al., RP Studies for CERN's HI-ECN3 Facility, presented at SATIF-16, 29 May 2024
Muon prompt radiation aboveground downstream ECN3
Dose from air releases
Used max. dose coefficients from different age groups
Positions of nearby population groups
Effective dose estimates
Dose from stray radiation
Release point
Annual limit of Non-designated Area on CERN domain and at CERN fence (1 mSv/y) as well as dose objective for members of the public (10 uSv/y) is by far met
CERN fence
H-3 release due to air activation of ~80 kBq
POT 4×1019 per year
Annual effective dose from muons