## Slide 1
Active control in Nanophotonics
for
Super-resolution Imaging
Bergin Gjonaj

## Slide 2
Acknowledgments
Asaf David
Yochai Blau
Doron Shterman
Guy Bartal
APRL Group
Jochen Aulbach
Patrick Johnson
Allard Mosk
Kobus Kuipers
Ad Lagendijk

## Slide 3
Outline
Background
  Microscopy over time
  Nanophotonics promises for microscopy
  Control - shaping optical wavefronts
Proof of concept for new microscopy
  Controlling nanophotonic/plasmonic wavefronts
  Focusing and scanning microscopy
Super-resolution
  Platforms for super-resolution
  Silicon Plasmonics

## Slide 4
Microscopy
We started like this
Few Nobels later
(Nikon Storm)

## Slide 5
Bright field – Dark field

## Slide 6
TIRF & Confocal
Total internal reflection
  Evanescent excitation
  Surface specific
Scanning technique
  Focused excitation
  Focused detection

## Slide 7
Structured illumination
Two different gratings generate a third one
If resolution does not allow to resolve one of the gratings, You can still deduce it from the other two.
Sample
Structured illumination

## Slide 8
Near field Probes
No more lenses
  Detect with a scanning probe
  Resolution is given by the probe size

## Slide 9
Aperture NSOM Light coupled into optical fiber
Scattering NSOM Light collected by
lens/parabolic mirror
Advantages:
No Background
Disadvantages:
Limited resolution ()
Near – field techniques
Advantages:
Resolution (~2-20 nm)
Disadvantages:
Far field |Bacground
Scanning Sample
Notes: Expand on nearfield

## Slide 10
Single molecule localization
If two single molecules are well separated in space
  You can localize them by their center of mass

## Slide 11
PALM, STORM STED
If molecules are separated
in time or space
  You can sum up an image
  (switching, activating)
If molecules are separated
in energy
  You can scan an image
  (saturation, depletion)
Betzig et al, Science 2006
Hell et al, Optics Letters 1999

## Slide 12
Outline
Wavefront shaping in Nanophotonics (spatial resolution)
  Controlling waves in nanophotonic systems
  Focusing and scanning microscopy / Super-resolution
  Goal: towards nanolocalized Raman excitation
Wavefront shaping in scattering media (spatio-temporal)
  Controlling speckle in time
  Spatio-temporal focusing at targets
  Goal: towards burning/imaging targets inside tissue

## Slide 13
Optical microscopy: optimizations
Optics
  Oil/water immersion objectives
Illumination
  Dark Field, Phase Contrast (DIC)
  Total Internal Reflection (TIRF)
  Optical Coherence Tomography (OCT)
  Structured Illumination (SIM)
Detection
  Fluorescence,
  Confocal, Near-Field
Light-matter interaction
  STED, PALM, STORM
  Nonlinear, Photo-acoustic
The microscope slide

## Slide 14
The generalized microscope slide
  More Control!
Conventional
  Passive, compensated
  Cheap and standard
Nanophotonic
  Active, focusing, filtering
  Super, hyper, meta lens
Natural
  Omnipresent, random, light scattering
  Thin slicing ex-vivo, other waves
  More Control!

## Slide 15
Choo, Yablonovitch (Nat Photon, 2012)
Hillenbrand group (Nat Photon, 2012)
Novotny & Van-Hulst (Nat Photon, 2011)
More control in Nanophotonics
Resolution
  Hot spots 10 – 100 nm
  Fixed, No imaging
Required control
  Image formation

## Slide 16
Motivation
Why do you need new microcopies?
  Applied - latest transistors at 20nm
  Cannot be fluorescently labeled
  Fundamental – spectroscopy
  The spatial distribution provides the WHAT
  You need spectroscopy to provide the HOW

## Slide 17
The slide is the lens
Metamaterial slide
  Negative refraction materials
  Perfect lens
  Hyperbolic material
  Hyper lens
Plasmonics
  Short wavelengths
  Plasmonic lens
  Little success in bio imaging – We need more control!

## Slide 18
Wavefront Shaping – new control
Control the incident wavefront
  Use a spatial light modulator to shape the front
  Use feedback to find the right wavefront
  Achieve focusing from scattering media (paper)
  Achieve focusing to a different spot
Vellekoop, Opt. Lett. (2007 )

## Slide 19
The wavefront control
Planar front
Spatial Light Modulator (SLM)
Shaped front
(amp & phase)
10 000 channels

## Slide 20
Nanophotonics wavefront control
Is wavefront control in nanophotonics
applicable for microscopy?

## Slide 21
Surface Plasmon Polaritons (SPP)
Dielectric
Metal
Surface waves
Evanescent waves
Metal-dielectric interface
Sensing, SERS, Q. optics
Compared to photons:
Same energy (color)
Shorter wavelength
Momentum mismatch
Light
SPP

## Slide 22
Plasmonics for microscopy
Shorter wavelength
Better focusing
Improved resolution

## Slide 23
Plasmonic wavefront shaping
Gjonaj, Nature Photonics (2011)

## Slide 24
Amplitude design: bare gold
Resolution: 450 nm

## Slide 25
Launching SPPs: hole array
SPP plane waves propagate into the SPP arena
Polarization dependency
Formation of a standing SPP wave

## Slide 26
450 nm
425 nm
400 nm
375 nm
Fringe periodicity = 0.5*λSPP = 300 nm
Fringes and gratings

## Slide 27
Shift & tilt of the fringes (SSIM)
Gjonaj, Nano Letters (2012)

## Slide 28
SPP focusing

## Slide 29
The SPP focus (with feedback)

## Slide 30
Relocating the focus
Everywhere inside the SPP arena
Gjonaj, Nature Photonics (2011)

## Slide 31
Implementation: microscopy
Gjonaj, PRL (2013)

## Slide 32
Hole grating : SPP launching
Bare gold arenas : no feedback
Free space GF : calculation
Scatterers : to be imaged
Metal : functionalize
Nanostructered microscope slide

## Slide 33
Concept – Scanning the focus

## Slide 34
Plasmonic 2D imaging
White light
illumination
Focusing
and
scanning
Overlap with
SEM image

## Slide 35
White light
illumination
Deconvolution
Enhancing the focusing/resolution

## Slide 36
Possible read-outs
Single shot : detection psf
Integrated intensity : excitation psf
Pixel in the focus : confocal psf

## Slide 37
Gjonaj, PRL (2013)
Imaging point spread functions

## Slide 38
Reorganizing our thoughts
Concept
  Simple – scanning a focus to achieve imaging
  Nice – does not require labeling
  Competitive – delivers energy locally (nano-spectroscopy)
Resolution
  Lensing – From 450nm objective to ~ 200nm. Great
  Wavelength – From 633nm to ~ 600nm plasmonic. (n=1.1)
  Maturity – STED, PALM, STORM ~ 20nm. Unfit

## Slide 39
Improved waveguides – Si Nitrite
Air
Gold
Light (633nm)
SPP (600nm)
SiN
Silver
Light (532nm)
SPP (240nm)
Air
Next: New nanophotonics platforms
  Wavelength – From 633nm to ~ 180nm. (n=3.5)
  Losses – Propagation length > 1 micrometer.
  Interaction – Should excite a probe or a bio molecule

## Slide 40
Near field measurements
Gjonaj, David et al Nano Letters (2014)
Static focus due to the shape of the slits

## Slide 41
Wavelength 240nm; focus 66 nm
Gjonaj, David et al Nano Letters (2014)

## Slide 42
Improved waveguides – Si Nitrite
Air
Gold
SiN
Silver
Air
  Wavelength – From 600nm to ~ 240nm. Almost there
  Losses – Propagation length < 1 micrometer.
  Interaction – Should excite a probe or a bio molecule

## Slide 43
Super-resolution in Silicon domain
Thin Si waveguide
  Transparent
  Guided modes in 2D
  Propagation up to 10 um
Bulk Silicon
  Refractive index ~ 3.5
  Connection to Si Photonics
  Connection to lithography
  Absoption in the visible
  Hard to harvest light
IBM Research

## Slide 44
Focusing with Silicon
David, Gjonaj et al Optica (2015)

## Slide 45
Hybrid photonic plasmonic modes
Oulton et al Nat Photon (2008)
Si - SiO2 - Ag
60 - 8 - 300 nm
Air
Si
Metal
Air
Si
Metal
Si - SiO2 - Ag
60 - 4 - 300 nm
- SiO2 -
Single hybrid mode
  More photonic
  Wavelength 220 nm
  Propagation 5.3 um
Single hybrid mode
  More plasmonic
  Wavelength 184 nm
  Propagation 3.3 um
1D

## Slide 46
Resolution: contrast or size?
David, Gjonaj et al Optica (2015)
Si - SiO2 - Ag
60 - 8 - 300 nm
  Wavelength 220 nm
  Propagation 5.3 um
  Size (FWHM) 78 nm
Si - SiO2 - Ag
60 - 4 - 300 nm
  Wavelength 184 nm
  Propagation 3.3 um
  Size (FWHM) 66 nm
Intensity
Phase

## Slide 47
Tunability: better contrast focusing
Si - SiO2 - Ag
60 - 8 - 300 nm
  Wavelength 220 nm
  Propagation 5.3 um
  Size (FWHM) 78 nm
1
0
-p
p

## Slide 48
Tunability: better size focusing
David, Gjonaj et al Optica (2015)
Si - SiO2 - Ag
60 - 4 - 300 nm
  Wavelength 184 nm
  Propagation 3.3 um
  Size (FWHM) 66 nm
1
0
-p
p

## Slide 49
Orbital angular momentum (spiral)
1
0
-p
p
Spiral lens & circular polarization
  Angular momentum spiral = -1
  Angular momentum polarization = 1
  Net angular momentum L = 0

## Slide 50
Orbital angular momentum (circle)
Circular lens & circular polarization
  Angular momentum circle = 0
  Angular momentum polarization = 1
  Net angular momentum L = 1
David, Gjonaj, et al PRB (2016)

## Slide 51
Nano vortex relevance
Optical vortices are well known and used
    Hasman, et al Nano Letters (2011)
Nano vortices are new
  The size (60 nm) is comparable with quantum systems
  For example Quantum Dots
  Beyond the dipole transition
  Accessing new transitions (dipole prohibited)
David, Gjonaj, et al PRB (2016)

## Slide 52
Joining efforts
Active wavefront control
  Raster scanning
  (focus or vortex)
  Far field microscopy
  Flexibility
Silicon waveguides
  Wavelength 184 nm
  Propagation 3.3 um
  Resolution 66 nm
  CMOS compatibility Al

## Slide 53
  Microscopy is continuously growing
Nanoscopy is an actuality
  Limitations: Fluorecent labelling, invasiveness
  Open questions : Chips, nanospectroscopy (i.e. Raman)
Wavefront shaping is flexible control
  Microscopy by focusing and scanning (label free)
  Deliver energy suitably for spectroscopy
Resolution is enhanced in Photonic 2D waveguides
  Static focusing to ~60 nm with reasonable contrast
  Tunable by material properties (resolution, losses, CMOS)
Take home messages

## Slide 54
Upgrading an existing microscope
Multiplexed imaging

## Slide 55
Spatial light modulator: amplitude and phase
Grating 1 order 1
Grating 2 order 1
Phase
How to achieve it

## Slide 56
The generalized microscope slide
  More Control!
Conventional
  Passive, compensated
  Cheap and standard
Nanophotonic
  Active, focusing, filtering
  Super, hyper, meta lens
Natural
  Omnipresent, random, light scattering
  Thin slicing ex-vivo, other waves
  More Control!

## Slide 57
Optical bioimaging – label free
  Bright-field
  2 Photon
  fluorescence
  Optoacoustic
  microscopy
  SHG THG
  Nonlinear harmonic generation
  Overlaid
  contrast
D. Soliman, et al, Sci. Rep. (2015)
Ntziachristos group
  Principle: Scan a focused laser pulse
  Resolution: Size of the focus (~ 0.2 – 10 um)
  Depth: Mean free path (~ 0.1 – 1 mm )

## Slide 58
Bypassing diffusion (space – time)
  Acoustics
  M. Fink, IEEE (1992)
  A. Derode, et al, PRL (1995)
  Microwave
  G. Lerosey, et al, PRL (2004)
  G. Lerosey, et al, Science (2007)
  Optics (monochromatic)
  S. M. Popoff, et al, PRL 2010
  Optics (pulsed)
    D. J. McCabe, et al, Nat Com (2011)
    J. Aulbach, et al, PRL (2011)
    O. Katz, et al, Nat Photon (2011)

## Slide 59
Fink, et al. Rep. Prog. Phys. (2000)
Acoustics to optics
Johnson, et al. Phys. Rev. E (2003)

## Slide 60
Aulbach, Gjonaj, et al, Phys. Rev. Lett. (2011 )
Bypassing diffusion (space – time)

## Slide 61
  Laser pulse ~ 64 fs
  SLM segmentation N ~ 300
  Temporal focusing ~ 115 fs
  Intensity enhancement ~ 102 - 103
Aulbach, Gjonaj, et al, Phys. Rev. Lett. (2011)
Time focusing

## Slide 62
  Second Harmonic particles (size 200 nm)
Aulbach, Gjonaj, et al, Opt. Exp. (2012 )
Space-time addressing of targets

## Slide 63
SH images
(@ 2ω)
Autocorrelation
(@ 2ω)
Aulbach, Gjonaj, et al, Opt. Exp. (2012 )
Space-time focusing

## Slide 64
Part. # | τpulse(fs) | ηexp | ηmodel | ηcw
1 | 110 | 2.5 · 102 | 3.1 · 102 | 1.6 · 104
2 | 102 | 0.7 · 102 | 3.2 · 102 | 1.7 · 104
3 | 111 | 2.7 · 102 | 2.7 · 102 | 1.4 · 104
4 | 104 | 0.7 · 102 | 2.9 · 102 | 1.5 · 104
5 | 109 | 3.0 · 102 | 3.8 · 102 | 2.0 · 104
6 | 109 | 5.5 · 102 | 6.5 · 102 | 2.4 · 104
  The enhancement, η, depends on the SLM segmentation.
  We contained the SLM segmentation to N = 800,
  because above it (N > 1000) the particles are burned and destroyed
Reproducibility

## Slide 65
Kuzmin, et al, Biomed. Opt. Express. (2016 )
Biomedical opportunities
  Depth ~ 10 - 100 mean free paths
  Tissue equivalent 0.1 - 5 cm
65
Human brain tumour (dark)
Intra-operational THG image (40 mW)
Intra-operational (in depth)
  High tumour density: CUT MORE
  Low tumour density: CLOSE UP
Early stage (in depth)
  Degeneration: YES/NO
Can we burn inside?
Nanoparticle labelling ?
Can we image inside (THG)?
Focusing and memory effect?

## Slide 66
Challenges/requisitions:
  Diffusion of light by tissue
  Local power delivery
  Specificity – tumours only
  Photoacoustic contrast
  Multi-sensorial (light, sound)
  Single detector (image-free)
  Only optical diffusion
The right feedback

## Slide 67
Submitted VIDI proposal
Ant-burning of tumours

## Slide 68
Photoacoustics space-time focusing:
  Contrast agents: Hemoglobin – brain, eye, breast
          Melanin – skin, lymph nodes, circulating tumor cells
          External – dyes, plasmonic particles
  Imaging : SHG, THG, (memory effect - high res, limited range)
  Sensing: Oxygen saturation of Hemoglobin (sO2), temperature
Therapy, imaging & sensing
One case of success is sufficient!

## Slide 69
Generic
  Microscopy is important and is challenging
  ‘SIM is the future’ – Betzig said.
Specific to this work
  High index materials (n>3) are great for SIM
  A double Moire illumination is the way to go
  5x better resolution (down to 45nm)
  Relatively simple and fast
  The required control is feasible
Conclusions