## Slide 2
Jorg Wenninger
BE-OP-LHC
Solenoid spin compensation with bumps

## Slide 3: Introduction (1)
Recently new layouts of the IR with non-local solenoid compensations have been discussed at MDI meetings.
The compensation solenoid is moved out of the inner MDI region to ~10 m from the IP. The compensation solenoid field can be lowered (from ~5T to 2T), coupling of solenoid and compensation solenoid are avoided.
As a side effect, coupling compensation is no longer local and vertical orbit shifts appears in the IR.
  The horizontal crossing angle of the beam through the solenoid generates a vertical orbit deflection that is no longer contained within the MDI region.
K. Oide, https://indico.cern.ch/event/1476514/

## Slide 4: Introduction (2)
The new layout proposal for the IR has an impact on the n0 axis due to interleaved spin deflections around the s- and x-axis:
  Reduction of the asymptotic polarization to ~1% based on K. Oide’s tracking simulations.
  Systematic spin tune shifts affecting the energy systematic error – to be evaluated.
The spin direction could be restored with vertical orbit bumps on both sides of every IR.
  The bumps will have impact on the vertical emittance – to be checked.
Such a compensation scheme was used successfully at LEP.
Since Xsuite does not include spin tracking (coming soon?): for this study a simple tracking of the spin was setup (no n0 axis calculation!), benchmarked on LEP solenoid compensation.
  First step towards identifying compensation for FCCee.

## Slide 5: Part 1: LEP

## Slide 6: Solenoids at LEP
All 4 LEP experiments had solenoids of varying strength (NC and SC).
LEP had no anti-solenoids, the GLOBAL coupling was corrected using skew quadrupoles.
  There is evidently local coupling between solenoids and skews.
Experiment | BL (Tm)
L3 | 6.078
ALEPH (SC) | 10.082
OPAL | 2.613
DELPHI (SC) | 9.030
At 45.5 GeV, the spin rotation around the s-axis due to the ALEPH solenoid was 66 mrad.
Without compensation, the predicted asymptotic polarization was in the range 1-5% - in practice it was generally ~0%.
  Without compensation, the energy calibration program at the end of physics fills would have been impossible.

## Slide 7: Polarization & n-axis
Correlation between n-axis deviation from the vertical and expected polarization: for > 20 mrad the expected polarization is lowered to ~few %.
  Filled squares: linear approx. (SITF)
  Open squares : non-lin. (SODOM)
Average deviation of n0 from vertical direction

## Slide 8: Solenoid compensation
Compensation scheme to restore the spin axis using bumps at the beginning of the arcs on both side of every IP (nickname: “SolSpin”).
Took advantage of the 60 vertical betatron arc phase advance in use around the Z  long bumps, favorable spin phase advance.
Solenoid
Dispersion suppressor
Dispersion suppressor
Compensation bump
Compensation bump
Double pi-bump to rotate the spin vector out of the vertical.
Precession in the dispersion suppressor by Dns ~1.1 [2p].
Rotation by the solenoid.
Precession in the dispersion suppressor by Dns ~1.1 [2p].
Double pi-bump to rotate the spin vector back to the vertical orientation.

## Slide 9: Solenoid compensation
Predictions (SLIM)
Energy (ns) range
@ Z pole (45.6…GeV)

## Slide 10: Polarization wo/with SolSpin bumps
Two examples with polarization wo/with compensation bumps.
In the experiment on the left: ~4% polarization without compensation.
CERN/SL 94-08
PHD R. Assmann
Predicted impact of solenoids (linear):
E = 44.7 GeV, ns ~101.5
E = 44.7 GeV, ns ~101.5

## Slide 11: Compensation bumps
Vertical orbit
Vertical dispersion
L3
ALEPH
OPAL
DELPHI
Double pi-bump, ALEPH left side
Complete bump set
Dmy = 2p
Dns = 4p + p/2

## Slide 12: Impact on emittance/performance
The double pi-bumps at p phase advance contain well the vertical dispersion within the bump region, limiting the vertical emittance growth.
At the Z, the vertical bumps generate a vertical emittance of ey ~ 150 pm.
For a natural horizontal emittance of ex = 12-30 nm (wo/with wigglers) for the LEP 90/60 optics (optics with 90 phase advance in H and 60  V), this corresponds to ey/ex ~0.5-1.2%.
  At 45 GeV LEP operated with ey/ex ~1% in physics production.
At LEP no polarization in physics: polarization studies & energy calibration outside physics data taking  emittance growth not critical.

## Slide 13: Spin path arc to IP
Spin vector orientation assuming initial vertical direction from entrance of the left side compensation bump to the exit of the solenoid.
Color coded from dark blue (start) to yellow (end).
  Each point: one machine element.
Horizontal lines: spin deflections induced by vertical orbit correctors or offsets in quadrupoles.
Curved sections: precession in dipoles.
Start
Entrance solenoid
Exit solenoid
End of bumps
ns (mrad)
nx (mrad)

## Slide 14: Spin path IP to arc
Spin vector orientation from exit of the solenoid to the end of the right-side compensation bump.
Color coded from dark blue (start) to yellow (end).
Horizontal lines: spin deflections induced by vertical orbit correctors or offsets in quadrupoles.
Curved sections: precession in dipoles.
End
Exit solenoid
Start of bumps
ns (mrad)
nx (mrad)

## Slide 15: Original versus replay
LEP note 629, 1990
2024

## Slide 16: Impact of solenoids on spin tune @ LEP
The systematic spin tune shift due to the solenoids (and compensation bumps) and associated systematic error on the beam (or centre-mass) energy was estimated to be negligible for LEP.
The shift is difficult to check experimentally due to the long time required to ramp and compensate the solenoid ( energy drifts):
  One single check, no energy change within 0.44 MeV.
CERN/SL 93-26
! centre-of-mass energy !

## Slide 17: Part 2: FCCee

## Slide 18: Non-local solenoid compensation concept
Consider option “F” proposed at the MDI meeting 11.11.2024 (GHC lattice):
  https://indico.cern.ch/event/1476514/
Vertical deflection due to the horizontal crossing angle in the solenoid.
15 mrad (1.2 xing angle) in ~6-7Tm integrated field
Symmetric layout on the right side of the IP

## Slide 19: Non-local solenoid compensation geometry
Orbit around the IP – interleaved horizontal fields + solenoid(s).
~ -20 mrad
~ +20 mrad
~ +20 mrad
~ -20 mrad
~ +300 mrad each
Vertical bending due to solenoid + xing angle

## Slide 20: Non-local solenoid compensation
No MADX version of the geometry is available on Git.
  In discussion with H. Burkhardt for some ad-hoc madx scripts – but they are for the LCC lattice, not for the GHC.
The following slides show a first look at the geometry and the possible impact on polarization.

## Slide 21: Spin vector tracking
Tracking the spin vector through left side compensation solenoid, vertical orbit corrector, solenoid (+hor crossing angle), right side vertical orbit corrector, compensation solenoid.
  Color coded from dark blue (start) to yellow (end).
Due to the compensation solenoids at ~10m, the vertical orientation is well preserved.
Solenoid
+ xing angle
L-side vertical corrector
R-side vertical corrector
L-side Comp. solenoid
R-side Comp. solenoid

## Slide 22: Spin vector tracking - zoomed
Tracking the spin vector through left side compensation solenoid, vertical orbit corrector, solenoid (+hor crossing angle), right side vertical orbit corrector, compensation solenoid.
  Color coded from dark blue (start) to yellow (end).
There is a small deviation of the spin from the vertical at the exit of the region by ~10 mrad.
  Simplified check with discretized spin rotations confirms the deviation magnitude.
Due to the small values of the shift, it is very sensitive to details – need to confirm with further studies / geometry checks.
Dark blue: entrance
Yellow: exit
magenta: IP

## Slide 23: Discussion
The LEP solenoid compensation was used as benchmark to check / compensate the impact of the solenoids (+ compensation) for FCCee.
In the absence of a proper MADX sequence for the local solenoid compensation, a first exploratory investigation was performed.
  The spin deflections by the (compensation) solenoids are like those at LEP (~6-7 Tm vs 10 Tm).
  Despite the “not fully” local nature of the compensation, the compensation does also work for the polarization, leaving only a residual deviation of n0.
  Compensating bumps can be small !
SAD tracking by K. Oide yields only ~1% residual polarization (4 IPs !) which looks a bit pessimistic for the small imperfection. Confirmation / cross-check with BMAD needed !