## Slide 1: Pre-alignment voluntarily displacement
Vivien RUDE,
Vincent BARBARROUX
Patrick BESTMANN
2024-10-02

## Slide 2
Safety layers constraints :
  After the interconnections, the bellows can accept :
  1 mm of translation
  1 mrad of torsion
INPUT
Range :
  FRAS range : +/- 2.5 mm
  Jack range : +/10 mm
  Baseline : When the interconnection is complete, the jacks should be positioned within the mid-range

## Slide 3
Mechanical Coordinate system
D9
D10
    Primary axis : Y : Regression line corresponding to the mechanical cold bore axis (determined from mechanical mole)
    Secondary axis : Z : Normal vector of the plane [Conn-D9, Conn-D10, NConn-D9, NConn-D10]
    Origin : Projection of the central cold feet on Y axis
Conn
D9
Conn
D10
NConn
D10
NConn
D9
Magnet | Maximum residual from the regression line (except flanges) | 
 | in radial (mm) | in vertical (mm)
Q2a P3 | 0.4 | 0.6
Q2a #03 | 0.3 | 0.6
Q2a #05 | 0.4 | 0.3
Q2b P2 | 0.4 | 0.4
Q2b #04 | 0.2 | 0.3
Q3 #01 | 0.5 | 0.5
Z
X
Y
Regression line
Cold bore measurement

## Slide 4
D11
M
Delta Mechanical and Magnetic (axis and magnetic field)
Q3 #01
X
Z
Magnetic
field
+2.550 mrad
Mechanical direction
(Z axis)
 =0.60 mm
 =-0.12mm
Y
X
Magnetic axis
Mechanical axis
Mechanical axis
Magnetic axis
 =0.31 mm
 =0.39 mm
Y
Z
Top view
Side view
This rotation also occurs between the end cover and the magnetic axis. All the auxiliary lines are installed with respect to the Z-axis.
Magnetic
field
Mechanical direction
(Z axis)

## Slide 5
Delta Mechanical and Magnetic (Constant at warm and at cold)
Example : Q2#P3 in vertical

## Slide 6
Mechancial or magnetic axis ?
Q1
Top view
+0.60 mm
-0.12 mm
+0.53 mm
-0.26 mm
Q2a
Magnetic axis
Mechanical axis
Mechanical axis
Magnetic axis
Delta : close to 1 mm
X
Z
-0.316 mrad
Magnetic
field
Mechanical direction
(Z axis)
X
Z
Magnetic
field
+2.550 mrad
Mechanical direction
(Z axis)
Torsion : close to 3 mrad

## Slide 7
Vacuum Vessel
Cold mass
Mechanical axis warm
Vacuum Vessel
= R-vacuum vessel
Jack
Jack
floor
Cold feet
Jack
Jack
Jack
Jack
Cold mass
R-vacuum vessel
R-mechanical axis
(cold mass at cold)
Z (warm-cold)
 1.5 mm
Jack
Jack
Vacuum Vessel
Cold mass
R-vacuum vessel
R-mechanical axis
(cold mass at cold)
R-magnetic axis (at cold)
Jack
Jack
For cold element | R-vacuum vessel = R-mechanical axis (warm) |  | R-mechanical axis (cold) |  | R-magnetic axis (at cold) |  | R-rst | 
Tx (radial) |  | FSI or Tx = 0 |  | Tx = ... |  | Tx = 0 |  | 
Ty (longitudinal) |  | FSI or Ty = 0 |  | Ty = 0 |  | Ty = … |  | 
Tz (vertical) |  | FSI or Tz = -1.5 mm |  | Tz = ... |  | Tz = 0 |  | 
Rx (pitch) |  | FSI or Rx = 0 |  | Rx = ... |  | Rx = 0 |  | 
Ry (roll) |  | FSI or Ry = 0 |  | Ry = ... |  | Ry = 0 |  | 
Rz (Yaw) |  | FSI or Rz = 0 |  | Rz = ... |  | Rz = 0 or 180 ° |  | 
Scale |  | FSI or Scale = … |  | Scale = 1 |  | Scale = 1 |  | 
Constant
Constant
FSI or Constant
R-fiduciualisation
= R-mechanical axis (cold mass at warm)
= R-vacuum vessel
R-rst
How to manage the different coordinate system ?
R-vacuum vessel
R-cold mass at warm
R-mechanical axis (warm)
R-mechanical axis (cold)
R-magnetic axis (at cold)
R-rst
Mad-X

## Slide 8
Before the interconnection phase, the elements should be installed in their nominal positions
The longitudinal shift from Mad-X (R-rst) to the fixed cold foot of each component should be implemented
The warm-cold delta should be taken into account prior to interconnection.
The mechanical-magnetic delta should be taken into account prior to interconnection.
The direction of magnetic field should be taken into account prior to interconnection.
How to manage the deltas ?
  By longitudinal shift  Longitudinal shift from R-magnetic axis at cold to Rrst
  By vertical shift  Warm-cold delta (anticipation) Be careful not to apply it twice (shift + FSI)
  By bump : Three bumps exist :
    Bump : Beam Base alignment
    Bump : Optimization displacements (aperture)  mechanical-magnetic delta (MAB validation)
    Bump : Mechanical constraints
This implementation is not yet done on geode  On going
String Test ?
  100% magnetic ?
Open discussion

## Slide 9
Thank you
for your attention